## Slide 1: Test Chip of POC –Modular VR Feb/16, ’23 Long Wang, Srini Rajagopalan & DerChang Kau CPG/GEMS/Foundry Technology Engineering

## Slide 2: Modular PD Solution- Integrated VR tile
Goal
  Cost-effective solutions
    Reusable IP to reduce NRE: Si VR tile reusable Embedded in companion chiplets
    Versatile, integrity in advanced packaging solution with best in class packaging suppliers for OpEx
  Enhance End-to-End (E2E) power efficiency
    On-par or better electrical performance
Problem statement : Existing integrated VRs, FIVR, DLVR (LDO) are implemented on the same advanced nodes’ die as active circuits implemented (monolithic solution) .
  Advanced nodes’ die size could be reduced w/o IVRs (yield improving /cost saving)
  Power loss from MBVR (12V to 1.8V) in addition to loss from MB/Pkg parasitic (Rpath) results in lower overall E2E efficiency
VR tile Concept: utilizing 3DIC tech, disaggregation die of VR tile
  DLVR tile implemented on in-expensive notes’ die w/ utilizing High density DTC/ISC ( MIMs) to have self sufficient VR
  Off-The-Shelf (OTS) Si VR embedded in FO-EB

## Slide 3: Architectures for End-End power efficiency
12V 1.8V
1.8V 1.2V
12V 1.4V
1.4V 1.2V
5V 1.2V
12V 5V
Courtesy of Don Nguyen

## Slide 4: TC Architecture W/ High Density C ( Basedie/Interposer)
R jumper
TC Pkg substrate
Core1
PG
PG
PG
DLVR/DTC
DLVR/DTC
DLVR/DTC
DLVR/DTC
R jumper
DSC
Base die
Core2
Core3
Core4
DTC/ISC provides high density C on TSMC/Samsung notes
DTC/ISC provides high density C on TSMC/Samsung notes
OPVR
R jumper
TC Pkg substrate
VDM/ODI 1
PG
PG
PG
IVR/DTC
IVR/DTC
IVR/DTC
IVR/DTC
R jumper
DSC
FO-EB
VDM/ODI 2
VDM/ODI 3
VDM/ODI 4
RDL
Could use discreet IVR and discreet components embedded in FO-EB
OPVR
DC

## Slide 5: Next Steps
Resources
  Analog designers (2) : to facilitate DLVR/OPVR porting (FTiP)
  Silicon Layout designer (1) : implementing base-die design (FTiP)
  RTL engineers (2~3) (
  PD/PI engineers (2) : conducting analysis on PDN/VR (CCG? FTiP)
  Integration (1): testchip integration (FTiP)
  OSAT/SPIL enigneers (1 or 2) : enabling FO-EB technology (
  DFX engineers (1-architect) (
  Packaging designer (1) (
Funding ( FTE)
Testing

## Slide 6
Backup

## Slide 7: MTL-M Package and DIE Integration Overview
Vertical Stack
Vertical Stack
X