## Slide 1: High-Bandwidth, Energy-efficient DRAM Architectures for GPU systems
Mike O’Connor – November 2, 2015

## Slide 2: GPUs Demand High DRAM Bandwidth

## Slide 3: GPUs Demand High DRAM Bandwidth
2008: NVIDIA Tesla GT200
512-bits @ 2.2 Gbps

## Slide 4: GPUs Demand High DRAM Bandwidth
2010: NVIDIA Fermi
GF100
384-bits @ 3.7 Gbps

## Slide 5: GPUs Demand High DRAM Bandwidth
2013: NVIDIA Kepler
GK110
384-bits @ 6 Gbps

## Slide 6: GPUs Demand High DRAM Bandwidth
2013: NVIDIA Maxwell
GM200
384-bits @ 7 Gbps

## Slide 7: GPUs Demand High DRAM Bandwidth
2013: AMD Fury X
“Fiji”
4096-bits @ 1 Gbps

## Slide 8: GPUs Demand High DRAM Bandwidth
Future GPU with
4-stack HBM2
4096-bits @ 2 Gbps

## Slide 9: GPUs Demand High DRAM Bandwidth
4 TB/sec Exascale Node Target

## Slide 10: GPUs Demand High DRAM Bandwidth
Typical PC CPU
2 Channel DDR3-1600
51.2 GB/sec
CPUs, Not so Much

## Slide 11: GPUs Demand High DRAM Bandwidth
Newer High-End CPU
2 Channel DDR4-3200
102.4 GB/sec
CPUs, Not so Much

## Slide 12: Why Do GPUs Demand so Much Bandwidth?
Lots of compute
24 Streaming Multiprocessors each w/ 128 execution units
Lots of threads
64 warps of 32 threads per SM
 49,152 threads executing simultaneously on 3072 execution units
NVIDIA Maxwell GM200

## Slide 13: Why do GPUs Demand so Much Bandwidth?
Different Memory Hierarchies
6 MB Register File
(Holds state for many threads)
~2 MB L1 and Scratchpad
6 MB Register File
2.3 MB L1/Scratchpad
3 MB L2
8 MB L3
512K L2
128K L1
25.25K Register File (PRF)
Intel Core i7-4790
NVIDIA Maxwell GM200

## Slide 14: Why do GPUs Demand so Much Bandwidth?
Radically Different Memory Hierarchies per Thread
6 MB Register File
(Holds state for many threads)
~2 MB L1 and Scratchpad
1 MB L3
64K L2
16K L1
3.28K Register File (PRF)
Intel Core i7-4790
8 Threads
NVIDIA Maxwell GM200
49,152 Threads
128B Register File
48B L1/Scratchpad
64B L2

## Slide 15: Why do GPUs Demand so Much Bandwidth?
Radically Different Memory Hierarchies per Thread
6 MB Register File
(Holds state for many threads)
~2 MB L1 and Scratchpad
1 MB L3
64K L2
16K L1
3.28K Register File (PRF)
Intel Core i7-4790
8 Threads
NVIDIA Maxwell GM200
49,152 Threads
128B Register File
48B L1/Scratchpad
64B L2
On-Chip Storage:
240 bytes per thread
vs.
1,133,856 bytes per thread

## Slide 16: Whole Different Ballgame
vs. typical CPU
25x More Bandwidth
Less sensitive to latency
LESS regular access patterns
More sensitive to tRRD/tFAW

## Slide 17: I thought GPUs had regular/streaming accesses?
GPU warp = 32 Threads executed in SIMD manner
http://www.shopbuy.org/static/category/original/rope/14174435-seamless-heamp-rope-texture-pattern.jpg
http://www.shopbuy.org/static/category/original/rope/14174435-seamless-heamp-rope-texture-pattern.jpg
Nice, Coalesced load of 32 x 4B = 128B
LD r1, [r2+tid.x]

## Slide 18: I thought GPUs had regular/streaming accesses?
But a lot is happening in parallel…

## Slide 19: I thought GPUs had regular/streaming accesses?
But a lot is happening in parallel…
24 SM’s… 64 warps each…
Highly interleaved execution!
HA HA HA! I will bring Chaos to your puny DRAM system!

## Slide 20: CPU
Fewer threads, lower chance of bank conflicts
Typical CPU : 8 Threads
http://www.shopbuy.org/static/category/original/rope/14174435-seamless-heamp-rope-texture-pattern.jpg
http://www.shopbuy.org/static/category/original/rope/14174435-seamless-heamp-rope-texture-pattern.jpg
2 ranks/channel 8 banks per rank
 4 banks per thread

## Slide 21: GPU
Many different threads competing
NVIDIA Titan X: 1536 Warps
6 channels 16 banks per channel
 0.06 banks per warp

## Slide 22: What does this mean for Energy?
Low Accesses per Activate
 Average ~160 Bytes accessed per activate (5 x 32B)

## Slide 23: What does this mean for Energy?
Low Accesses per Activate
 High Accesses per Activate workloads are typically simpler functions like large data copies
Compositing Images

## Slide 24: What does this mean for Energy?
Low Accesses per Activate
 Many of the 1 Access/Activate workloads are are doing graph traversals of large graphs
Graph Analytics

## Slide 25: What does this mean for Energy?
Want to reduce row overfetch
DRAM device typically has 1-2KB row
- we only need 160B on average
Wastes ~84-92% of the energy on activate/precharge of a DRAM bank
Multiple devices in parallel (like a DIMM) make this even worse

## Slide 26: What does this mean for Performance?
Activate rate is a key
High-bandwidth I/O is nice, but…
Key aspect of performance is rate of activates - low tRRD and tFAW - high number of channels
Typical 2-channel, 2-rank DDR4 w/ tRRDeff=5.25ns: 762 M ACT/sec
HBM2 4-stack, 64-channel (w/ pseudochannels) w/ tRRDeff=4ns: 16 G ACT/sec

## Slide 27: Small DRAM Atoms
DRAM “atom” is smallest indivisible access
Basically a function of bus-width and burst-length
GPUs extensively use compression of graphics surfaces
Efficiency of compression a function of minimum access size
Efficient partial coverage

## Slide 28: What to GPUs need from DRAM?
High Bandwidth (w/ low access / activate)
Energy-efficient (largely because of high bandwidth)
Small minimum burst sizes (e.g. 16-32B)
Not necessarily concerned with:
Low-latency
Extremely large capacities
Lowest possible cost

## Slide 29: One Approach: High-Speed Signaling
Start with a commodity DRAM core
Since GPUs don’t need huge capacities, drop multi-rank support
Without multi-drop busses and sockets, push I/O data rates
Beef-up the DRAM core to keep up (reduce tRRD/tFAW if possible)
Basic approach behind GDDR DRAMs

## Slide 30: GDDR5
GDDR5 signals at up to 8 Gbps
GDDR5X soon going to 10-12 Gbps
Lots of board challenges
I/O energy efficiency not so great

## Slide 31: Challenges with High-speed Signaling
Limits on data rates with inexpensive board & package
High-data rates place demands on the DRAM core
- Cycle the DRAM core arrays faster
And/Or
- Sub-partition pieces of the DRAM array
And/Or
- Fetch more data from the array each time

## Slide 32: Another Approach: In-package Integration
3D Stacking technologies enable many more I/Os
What if instead of faster, we go wider…

## Slide 33: What is High-Bandwidth Memory (HBM)?
Memory standard designed for needs of future GPU and HPC systems:
  Exploit very large number of signals available with die-stacking technologies for very high memory bandwidth
  Reduce I/O energy costs
  Enable higher fraction of peak bandwidth to be exploited by sophisticated memory controllers
  Enable ECC/Resilience Features
JEDEC standard JESD235, adopted Oct 2013.
  Initial work started in 2010

## Slide 34: What is High-Bandwidth Memory (HBM)?
Enables systems with extremely high bandwidth requirements like future high-performance GPUs

## Slide 35: HBM Overview
Each HBM stack provides 8 independent memory channels
  These are completely independent memory interfaces
    Independent clocks & timing
    Independent commands
    Independent memory arrays
    In short, nothing one channel does affects another channel
4 DRAM dies with 2 channels per die
Optional Base “Logic” Die
Channel 0
Channel 1

## Slide 36: HBM Overview - Bandwidth
Each channel provides a 128-bit data interface
  Data rate of 1 Gbps per signal (500 MHz DDR)
  HBM2 bumps this to 2 Gbps per signal (1 GHz DDR)
  16-32 GB/sec of bandwidth per channel
8 Channels per stack
  128-256 GB/sec of bandwidth per stack
For comparison:
  Highest-end GDDR5-based today (NVIDIA GeForce GTX 980Ti)
    384b wide GDDR5 (12 x32 devices) @ 7 Gbps = 336 GB/s
  AMD Fury X with 4 stacks of HBM
    Four stacks of HBM @ 1 Gbps = 512 GB/s
  Future possible GPU with 4 stacks of HBM2
    Four stacks of HBM2 @ 2 Gbps = 1 TB/s

## Slide 37: HBM Overview - Bandwidth
Each channel provides a 128-bit data interface
  Data rate of 1 Gbps per signal (500 MHz DDR)
  HBM2 bumps this to 2 Gbps per signal (1 GHz DDR)
  16-32 GB/sec of bandwidth per channel
8 Channels per stack
  128-256 GB/sec of bandwidth per stack
For comparison:
  Highest-end GDDR5-based today (NVIDIA GeForce GTX 980Ti)
    384b wide GDDR5 (12 x32 devices) @ 7 Gbps = 336 GB/s
  AMD Fury X with 4 stacks of HBM
    Four stacks of HBM @ 1 Gbps = 512 GB/s
  Future possible GPU with 4 stacks of HBM2
    Four stacks of HBM2 @ 2 Gbps = 1 TB/s
At lower overall DRAM system power – ~6 pJ/bit vs.
~18 pJ/bit for GDDR5

## Slide 38: HBM Overview - Capacity
Per-channel capacities supported from 1-32 Gbit
  Stack capacity of 1 to 32GBytes
  Nearer-term, at lower-end of range HBM: 4 high stack of 2Gb dies = 1GBytes/stack HBM2: 4 high stack of 8Gb dies = 4GBytes/stack
8 or 16 banks per channel
  16 banks when > 4Gbit per channel (> 4GBytes/stack)
Not including optional additional ECC bits
  A stack providing ECC storage may have 12.5% more bits

## Slide 39: HBM Channel Overview
Each channel is similar to a standard DDR interface
  Data interface is bi-directional
    Still requires delay to “turn the bus around” between RD and WR
    Burst-length of 2 (32B per access)
  Requires traditional command sequences
    Activates required to open rows before read/write
    Precharges required before another activate
    Traditional dram timings still exist (tRC, tRRD, tRP, tFAW, etc.) – but are entirely per-channel

## Slide 40: HBM Channel Summary
Function | # of µBumps | Notes
Data | 128 | DDR, bi-directional
Column Command/Addr. | 8 | DDR
Row Command/Addr. | 6 | DDR
Data Bus Inversion | 16 | 1 for every 8 Data bits, bi-directional
Data Mask/Check Bits | 16 | 1 for every 8 Data bits, bi-directional
Strobes | 16 | Differential RD & WR strobes for every 32 Data bits
Clock | 2 | Differential Clock
Clock Enable | 1 | Enable low-power mode
Total | 193 | 

## Slide 41: New: Split Command Interfaces
2 semi-independent command interfaces per channel
  “Column Commands” – Read / Write
  “Row Commands” – ACT / PRE / etc.
Key reasons to provide separate row command i/f:
  100% column command bandwidth to saturate the data bus w/ BL=2
  Simplifies memory controller
  Better performance (issue ACT earlier or not delay RD/WR)
Still need to enforce usual ACTRD/WRPRE timings

## Slide 42: New: Single-Bank Refresh
Current DRAMs require refresh operations
  Refresh commands require all banks to be closed
  ~ 1 refresh command every few µsec
  Can consume 5-10% of potential bandwidth
  Increasing overheads with larger devices
Sophisticated DRAM controllers work hard to overlap ACT/PRE in one bank with traffic to other banks
  Can manage the refresh similarly
  Added “Refresh Single Bank” command
    Like an ACT, but w/ internal per-bank row counter
    Can be issued to any banks in any order
    Memory controller responsible for ensuring all banks get enough refreshes each refresh period

## Slide 43: New: RAS Support
HBM standard supports ECC
  Optional: Not all stacks required to support it
ECC and non-ECC stacks use same interface
  Key insight: Per-byte data mask signals and ECC not simultaneously useful
  Data Mask Signals can carry ECC data - makes them bi-directional on HBM stacks that support ECC
Parity check of all cmd/addr busses also supported

## Slide 44: Other HBM Features
HBM supports Temperature Compensated Self Refresh
  Temperature dependent refresh rates with several temperature ranges (e.g. cool/standby, normal, extended, emergency)
  Temperature sensor can be read by memory controller to adjust its refresh rates as well
DBIac Data Bus Inversion coding
Reduce number of simultaneously switching signals
  No more than 4 of 9 (DQ[0..7], DBI) signals switch
  DBI computation maintained across consecutive commands

## Slide 45: HBM2 – The next step
Evolution of HBM
Doubles bandwidth of I/O channel
Requires doubling burst-length and DRAM atom
Break up channel into two pseudo-independent half-wide channels
Pseudochannels add bank-level parallelism
Prevent DRAM atom size from increasing
Reduce DRAM row overfetch by cutting effective row in half

## Slide 46: High Bandwidth DRAM Energy Trends

## Slide 47: Conclusion
GPUs place significant requirements on the DRAM
Ideal GPU DRAM provides
energy efficient
high-bandwidth
to small quantities of data
Stacked memories like HBM2 are good, but need new innovations to get to Exascale-class nodes