## Slide 1: Setback scheme for multilevel cell in BiSM
Dany-Sebastien Ly-Gagnon, Derchang Kau
BiSM, MLC, read, setback, read disturb
4/28/2020
Multilevel cells need to read the cells without disturbing the VT state. However, if the cell thresholds after applying bias during read operation, the cell VT state may be altered due to the read operation.
Considering a cell with 2 bits per cell, which can be placed in 4 distinct VT states: P1, P2, N1, N2, using specific programming write conditions (polarity, PA/PW).
Adding a setback pulse that matches the write condition, in a read polarity that is consistent with the write operation:
  READ operation starts with V1, and if cell thresholds, I1/T1 setback condition is applied, in positive polarity.
  If cell did not thresholds with V1, read voltage V2 is attempted, and if cell thresholds, I2/T2 setback condition is applied, in positive polarity.
  If cell did not threshold upon V2, read voltage –V1 is attempted, and if cell thresholds, I1/T1 setback condition is applied in negative polarity.
  If cell did not threshold upon applying –V2, then terminate.
Considering a cell with 4 VT states: P1, P2, N1, N2
  The VT states are defined using positive (P1/P2) and negative pulses (N1/N2) and two different conditions for PA/PW: high VT (P2/N2) or low VT (P1/N1) PA/PW condition.
  The typical way to readout the cells would be to start from the lowest bias and iteratively trying the next higher bias until the cell thresholds, e.g. trying V1, V2, V3 read biases until the cell thresholds.
  Once the cell is read, the cell needs to receive a subsequent write operation to place VT at same level as prior to reading the cell.
V1
Vapplied
% cells threshold
V2
P1
P2
N1
N2
V3
V1
Vapplied
% cells threshold
V2
P1
P2
N1
N2
-V1
-V2
Vp1
Vp2
Vn1
Read sequence:
Time
0V
Bias
Cell VT distributions:
State | VT (in p polarity) | VT (in n polarity) | Write condition (PA/PW and polarity)
P1 (00) | 0<VT<V1 | -V3 < VT < -V2 | I1/T1 in P polarity
P2 (01) | V1<VT<V2 | -V3 < VT | I2/T2 in P polarity
P3 (10) | V2 < VT < V3 | -V1<VT<0 | I1/T1 in N polarity
P4 (11) | V3 < VT | -V2<VT<V1 | I2/T2 in N polarity

## Slide 2: State diagram and setback
V1
Vapplied
% cells threshold
V2
P1
P2
N1
N2
Vp1
Vp2
Vn1
Read sequence:
Time
0V
Bias
Cell VT distributions:
State | VT (in p polarity) | VT (in n polarity) | Read Setback (PA/PW and polarity)
P1 (00) | 0<VT<V1 | -V3 < VT < -V2 | I1/T1 in P polarity
P2 (01) | V1<VT<V2 | -V3 < VT | I2/T2 in P polarity
P3 (10) | V2 < VT < V3 | -V1<VT<0 | I1/T1 in N polarity
P4 (11) | V3 < VT | -V2<VT<V1 | I2/T2 in N polarity
N1
N2
P1
P2
-V3
-V1
-V2
V3
State diagram
BL/WL bias ramp to V1 in positive polarity
Threshold detection
Write back with I1/T1 in positive polarity
Data out is 00
BL/WL bias ramp to V2 in positive polarity
Threshold detection
Write back with I2/T2 in positive polarity
Data out is 01
yes
no
BL/WL bias ramp to V1 in negative polarity
Threshold detection
Write back with I1/T1 in negative polarity
Data out is 10
Data out is 11
yes
no
yes
no