## Slide 1: AR Update: Identify Checkpoint for MLC Decision Point(s)
Understand controlling & engineering intermediate PM state, without disturb
  Success criteria of nucleation/growth distribution look like?
  Components of variance quantified
  Understand source of within bit (trial to trial) sigma?
    How to control (process/device)?
  What is impact of scaling?
Understand controlling & engineering non-phase change state
  Paper models articulated with assumptions
    Experiments to validate models/test assumptions
    Focus on physics, not algorithm tweaking
  What is switching physics?
    What is source (where in stack, what is switching mechanism, what dictates speed)?
    How is state retained (retention/disturb)?
    What is impact of scaling?
    Source of switching must be few (<2)
Required to answer basic questions/understanding and/or convince black-box can be controlled
Study Plan
  Resource(s) allocated with this as primary job (DK/SR)
  Study Plan in place (DK + Resource)
  Scope contained (resources/silicon) until above questions answered
Strategic goal: EOY step up / down

## Slide 2: AR Update: Identify Checkpoint for MLC Decision Point(s)
Understand controlling & engineering intermediate PM state, without disturb
  Success Criteria including assumption and model for a working mid state (one model)
    Validate of mid state physically (αSDαPM) – data collected, analysis pending
    Defining success criteria of ‘amorphous’, ‘nucleation’ and ‘growth’ distribution – not start
  Model Validation
    Components of variance quantified – partially done, question raised on “initial state”, ie. is mid state amorphous PM
    Understand source of within bit (trial to trial) sigma – Same above
    How to control (process/device)? – Not Start
  What is impact of scaling?
    Amorphous, nucleation and growth distribution of scaled cell meeting success criteria – Not start, plan to use ATF silicon in Q4
    Scaling projection for array operation – Not start
Understand controlling & engineering non-phase change state
  Paper models articulated with assumptions – WIP; Two speculated “interfacial” models with physical abstract being quantified.
  Model validation
    TTT Fingerprint – wip; <10% of NPC bits available after pulse, most of mid-state bits exhibit partial crystalline behavior; no POR SD on single-chal si
    Empirical models segmentation for the source of memory window – not start, PFA vs. TTT planned (may compete with Lab resources)
    Reliability such as retention, disturb and cycling endurance – Not start, use exiting S26 and SC silicon in hand
    Model validation – not start, S26 based SD experiment segmentation (material composition and thickness variation, single chal preferred) for ∆VT tuning
  What is impact of scaling – not start, ATF based full stack and single chal experiment on SD
Required to answer basic questions/understanding and/or convince black-box can be controlled – some started by Sanjay, will need to piggy back from him with resources allocated.
Study Plan
  Resource(s) allocated with this as primary job – Fuga 33%, Hemant 50% + Roberto 100%. (Dany may swap with Hemant, Roberto may swap with and Phoebe. As you pointed out, this is a part of business processes for ‘transfer’). Process resources ZBB’d until ATF gate lifted
  Study Plan in place (DK + Resource) – Fuga owns it. We are 75% complete as I am revising study plan of Engineering amorphous PM states.
  Scope contained (resources/silicon) until above questions answered – Yes with RTD process constraint management kicked in (ie. no ATF SC flow and experiment).
Strategic goal: EOY step up / down – no visibility today. Will know in a couple week as I am regrouping the team.