## Slide 1: Ww08

## Slide 2: 2k x 4k STUDY PLANS
Intel Confidential
 | Q1 | Q2 | Q3
Tile circuit architecture | Study plan: Layout assessment of first pass CuA architecture; gross spec compliance assessment (Die size, Energy, Idle/Fsb power, DTS/AOS, Tmspec, Cspec) Success criteria: Most major circuit functions comprehended (e.g. spike mitigation, bl supply mux etc.); >90% circuit fit and signal/power route-ability; solutions identified to address major issues in next iteration | Study plan: Layout assessment of second iteration of CuA architecture; spec compliance assessment using spread sheet/ some simulations Success criteria: All circuit functions comprehended (e.g. AIR mode); >95% circuit fit and signal/power route-ability; solutions identified to address issues in next iteration | Study plan: Layout assessment of 3rd iteration of CuA architecture; spec and reliability assessment using simulations Success criteria: CuA meets die size and signal/power routing requirements; Other spec issues deemed solvable through design optimization or spec changes
Partition architecture | Study Plan: First pass partition level architecture, schematics and layout floor plan Success Criteria: Most major circuit functions comprehended. Spreadsheet/paper based layout fit assessment within 10% of die size goal. | Study plan: Layout assessment of partition architecture; spec compliance assessment using spread sheet/some simulations Success criteria: All circuit functions comprehended (e.g. AIR mode); >90% circuit fit and signal/power route-ability; solutions identified to address major issues in next iteration | Study plan: 2nd iteration of partition architecture; spec and reliability assessment using simulations. Success criteria: Partition meets die size and signal and power routing requirements; Spec issues deemed solvable through design optimization or spec changes

## Slide 3: CMOS STUDY PLANS
Intel Confidential
 | Q1 | Q2 | Q3
Pitch Cell X’tor | Strategy: Source drain inner junction engineering to reduce electric field at GIDL and Isubmax bias Success criteria: TCAD based DOE covers electrical field | Study plan: Layout assessment of second iteration of CuA architecture; spec compliance assessment using spread sheet/ some simulations Success criteria: All circuit functions comprehended (e.g. AIR mode); >95% circuit fit and signal/power route-ability; solutions identified to address issues in next iteration | Study plan: Layout assessment of 3rd iteration of CuA architecture; spec and reliability assessment using simulations Success criteria: CuA meets die size and signal/power routing requirements; Other spec issues deemed solvable through design optimization or spec changes
Partition architecture | Study Plan: First pass partition level architecture, schematics and layout floor plan Success Criteria: Most major circuit functions comprehended. Spreadsheet/paper based layout fit assessment within 10% of die size goal. | Study plan: Layout assessment of partition architecture; spec compliance assessment using spread sheet/some simulations Success criteria: All circuit functions comprehended (e.g. AIR mode); >90% circuit fit and signal/power route-ability; solutions identified to address major issues in next iteration | Study plan: 2nd iteration of partition architecture; spec and reliability assessment using simulations. Success criteria: Partition meets die size and signal and power routing requirements; Spec issues deemed solvable through design optimization or spec changes

## Slide 4: BACK UP

## Slide 5: ATF HIGH LEVEL FLOOR PLAN
Intel Confidential
IO
PERIPHERY
PART 0
PART 31
Tile 0
Tile 127
LWLs/LWLd/PCL CTRL DRVRS
GWLS DRVR/TERM CAPS
Tile Circuits: Decoders, VDM source followers, current mirrors, sense amp, mask logic, ..
Partition Circuits: Address drivers, PCL, VDM_DAC, iREF_DAC
PERIPHERY CIRCUITS: PL, Fuses, redundancy matching, HV regulators,..
IO CIRCUITS: PADS, Tx, Rx, DLL,..
GBLS DRVR/TERM ANALOG
PCL/LBLS & LBLd DRVRS
Not all of this termination edge fits under the array

## Slide 6
30s Tile Layout
POR TILE
2Kx4K Quilt
2Kx4K Interlock
2Kx4K Quilt x 2 slices
2Kx4K Interlock x 2 slices
Circuits fit better than 2Kx4K Quilt
Supply voltage worse than 2Kx4K quilt
Die Size lower than 2Kx4K quilt
Need one extra metal
Circuit Fit ??
Supply voltage lower than POR
Die Size higher than POR
Intel Confidential