## Slide 1: Bow Falls Scope and Complexity
based on 26.5nm array pitch SXP (Full Stack, SLC)
Scope | Module | What’s New | Risk | Interaction | Coupling
Array (Max) | HM, toppling | Films, Dry | H | CMP, film stack, etch/clean | H
 | 1st and 2nd Cut | FP/LP, clean | H | Liner/seal/fill | H
 | Liner/Seal | ALD films | H | Cell stack, clean, FP 2nd Cut, LP all cut, Fill (adhesion), CMP | H+
 | 193i overlay | Metro structures | M | Scribe to Array deltas | L
CMOS (Erv) | 79% HVT DR Shrink | HVT scaling, HVT DR | M | Interconnect | L
 | Interconnect scheme | 4 193i or +1 or +2 level metal | M | Cost/Energy | L
Design (Sandeep) | Device consolidation | Eliminate Low Vtn | M | Energy, sensing(VDM), Selection | H
 | 30% Energy reduction | Supply, Sensing, New Algo | H | Interconnect, array such as ESSR, Array metal, cell current | H
 | Modular Design | Quantized Z/L, gridded layout | M | DR, Within CUA and Partition logic | M
Test, System (Kiran) | Tester 4800MT/s | Hi Speed tester | M | Array vs. Speed testing decoupling | M
 | PHY definition | DDR5 | M | Backward compatibility | M
 | WD, 2X capability loss | Margin management | L | Space scaling and gap fill | H
Contingency | New Electrode | Stack re-configuration | M | Etch, clean, liner, seal | M
 | New PM | Film | H | Etch, clean, liner, seal | H
 | New SD | Film | H | Etch, clean, seal | H
 | New Fill (if WD) | Film, Tool (tbd) | H | Seal, CMP, Chop, 2nd Cut, DEB | H
 | -30% Array metal r | Film | H | Etch, clean, liner, seal | M
 | PQ vs. DSA | Film, integration and tools | M | HM/Patterning flow | M

## Slide 2: Array Scope
Key Assumptions in the table: Cell materials matched to ATF and POR Gap Fill feasible for space scaling
Impact of Cell stack change
  Changes to stack are inherently disruptive, impacting all segments (cuts -> HM -> CMPs, liner/seal) and therefore incur the greatest schedule impact (e.g., for S15, stack change = 2 qtr)
Impact of Gap fill change
  Gap fill changes impact seal, CMP, 2nd cut and DEB segments depending on 1st or 2nd cut gapfill.
Module | MTS & Change | incoming modules changes | Receiving module changes | Coupling Risk
Hard Mask | Films, Dry | Pitch reduction | CMP, FP/LP etch, chop, possible: FP/LP clean, seal | H (etch/clean, CMP)
1st Cut | FP/LP, clean | HM | Liner, possible:seal | H (profile)
2nd Cut | FP/LP, clean | HM | Liner, possible: seal | H (profile)
Liner | ALD films | FP etch, clean | LP etch, possible LP clean | VH (stack)
Seal | ALD films | FP/LP etch/clean | Possible: gap fill, CMP | VH (stack)
193 overlay | Metro structures | NA (reticles) | NA (reticles) | L

## Slide 3: CMOS Scope
Design rule changes include d2d, d2w, p2p, end cap, contact, c2g
HVT consolidation and shrink:
  One NMOST for select and deselect pitch cell; LG shrink from 7l to 5l
  One NMOST for tile control and partition logic circuit with LG shrink
  Two PMOST with LG shrink
No LVT shrink or DR change except dummy poly collapse & quantization of W and L
Impact of other changes?
  If LVT scaling required, then ~+1-2Q on schedule
  If LVT performance increase required, then ~+4Q on schedule
Module | MTS & Change | incoming modules changes | Receiving module changes | Coupling Risk
STI | HV Line/space | NA | Well Implant, GTA, Epi | M-H (Epi)
Well Implant | Dose | STI | VT implant, Tip/Halo | M
Poly patterning | HV Line/Space, Reg | STI | ReOx, spacer, NiSi, Epi | M-H (Epi)
Tip | Does, energy, tilt, twist | Vt, PTS implant/doping profile | Pitch cell and HVT Lg scaling | M
Halo | Dose, Energy, tilt, twist | Tip | NMOST Pitch cell | M
Contact | Size and Reg | STI corner, Spacer. salicde | M1 | M
M4 | Line/space (PQ) | V3 | AV0 | M

## Slide 4: Design Scope
Energy reduction
  VPP/VNN supply reduction
  Additional metal layers for wider signal spacing
  Cell current reduction
  TBD Design architecture improvements
  TBD Algorithm Optimization
Die Size
  Fitting tile circuits under the array
  Minimum socket size for both rowmux and colmux
  Partition termination and periphery area reduction
IO Speed
  4800 MT/s with the same LVCMOS as ATF
HVT consolidation
  Elimination of low Vt N device (Circuits impacted: BLVDM, Sense Amp, Regulators)
Modular design
  Gridded layout
  Quantized device sizes
Write Completion Time Reduction
  PCL modifications for data wait idle time elimination
  C-cell half patch decoding
Design Technology handshake
  CMOS/Design collaboration on CMOS DTS to meet product specs
  Cell/Array/Design collaboration on Cell DTS to meet product specs