## Slide 1: BWF CMOS Scope Assessment
Erv, Sandeep and DerChang, WW06, 2021
Boundary Conditions, Assumptions & Scaling Strategy
Technology scope, metric and assessment for
  Array Pitch Scaling: Cost reduction & DR Shrink
  2Kx4K: Additional shrink in Pitch Cell
Design challenges
  CUA of 2Kx4K
  Transistor consolidation

## Slide 2: Boundary Conditions, Assumptions & Scaling Strategy
Boundary conditions: ATF based algo, RWB and supply domains @ 1.5W power envelope
Cost:
  Array pitch scaling, 79% Shrink, to achieve 0.75X $/GB @ 15% CoT
BW @ Power envelope
  Write Cycle Time reduction
  Concurrency: 2Kx4K Tile
CMOS Scaling: Planar CMOS technology with transistor consolidation
  No oxide scaling, no materials change  Doping profile design, +ox/spacer optimization
  ‘Reuse’ ATF Low voltage transistors (dual VT)
  79% design rule shrink to match array pitch scaling
  Additional 5% scaling on pitch cell for 2Kx4K
  + Other cost reduction line items
Metric for scope:
  Traffic lights for risk indicators
  Learning cycles (LC) – complexity and schedule for decision
Modularity: Interactions and possibility of other unintended consequence
High | Med-High | Med | Low

## Slide 3: Array Pitch Scaling
Cost Reduction | LC | Engineering Scope | Modularity/Interaction
Non-Epi starting material | 2 | CZ-Wafer defect, doping profile, cost (%) | Well isolation, Vss busing, ESD and latchup - expecting to draft off of ATF
LVT CMOS consolidation From triple to dual VT |  | Redesign with dual Vt | ATF: 79.4% of high VT, 20.5% of med VT, 0.1% of low VT
HVT NMOST Consolidation From triple to single VT |  | Removal of BLWritev SF; Redesign sense amp and voltage regulators | ATF: 29.1% of high VT, 62.7% of med VT, 8.2% of low VT
HVT Pitch Cell nMOST Dedicated for Pitch cell |  | LXS, LYD, GXS, GYD use the same devices (Same L, different W) | Pitch cell nMOST: 38% of all Transistors in ATF
Triple Well: diode isolation of nMOST in Psub | 2 | Triple Well Doping Profile Engineering | Non-Epi
79% Design Rule Shrink | LC | Engineering Scope | Modularity/Interaction
Non-Pitch HVT | 3 | Doping optimization for Leff (Ron/Ioff) & inner junction leakage and reliability | Spacer engineering, Stack Gate, Contact & Transistor consolidation
Pitch HVT | 4 | Doping optimization for Leff & inner junction leakage and reliability | Spacer engineering, Stack Gate, Contact & Transistor consolidation
Isolations | 2 | Well Implant and trench optimization | Transistor scaling, Bandgap diode
Diffusion | 2 | S/D width, ∆Z | Trench oxide module, Endcap profile
Contact module | 2 | Contact to gate, landing, contact resistance | Spacer
V1/M2/V2/M3 | 2 | 193i, ~1% cost | 
V3/M4 | 2 | Pitch reduction | 

## Slide 4: Enabling 2Kx4K
75% Design Rule Shrink | LC | Engineering Scope | Modularity
Pitch HVT | 4 | · Doping optimization for Leff (Ron/Ioff) & inner junction leakage and reliability · Additional 10% LG reduction to achieve Ron and Ioff · 2D Field effect for gate control | · Spacer engineering, Stack Gate, Contact & Transistor consolidation · STI corner, gate wrap vs. “bird’s beak”, Endcap control
Isolations | 2 | Well Implant and trench optimization | Transistor scaling, Bandgap diode
Diffusion | 4 | S/D width, ∆Z | Trench oxide module, Endcap profile
Contact module | 2 | Con to gate, landing, contact R, 193i | Spacer, NESL
M1/V1/M2/V2/M3 | 2 | change M1 193i and tighter pitches for all | 
Adding M5/V4 | 2 | Dual PD layer for interlock connectivity 4% | 

## Slide 5: DESIGN CHALLENGES
Intel Confidential
Enablers | Risks | Risk Level | Next Steps
Interlock layout | Spike @ ED0 | low | Array sims - Q2
Decoder Channel length 7->5 | Leakage, reliability | high | Silicon assessment, simulations - Q2?
Narrow W Rowmux Select Device | Current delivery | high | Silicon assessment, cell current, supply voltage - Q2
Removal of BLWritev SF | Selection spike, Vt metrology | medium/high | Array sims - Q2
Removal of Growth SF | Growth current wave shape | medium/high | Array sims - Q2
Combination of Growth and Reset Mirrors | Headroom, variation | medium | Array sims - Q2
Half latch/dynamic level shifters | Energy/functionality | medium | Energy assessment based on floorplan - Q1; Leakage/coupling assessment - Q2
Removal of one WL SF and associated LS | Dual VDM functionality | high | ucode development and array functional sims - Q2
Tile Logic Channel length 9.7->7.6 | Leakage, reliability | medium/high | Silicon assessment, simulations - Q2?
 | Risks | Risk Level | Next Steps
Low voltage transistor consolidation | Power, performance | tbd | Design analysis - Q1/Q2
High voltage transistor consolidation | Blwritev selection, senseamp and regulator functionality | medium/high | Redesign and simulations - Q2
CUA FIT: 2k x 4k
TRANSISTOR CONSOLIDATION
Note: Above table based on tile fit. Partition work to start in late Q1

## Slide 6: Backup

## Slide 7: ATF32 HIGH LEVEL FLOOR PLAN
IO
PERIPHERY
PART 0
PART 31
CUA Tile Circuits: (~80%* of Core)
Decoders, VDM source followers, current mirrors, sense amp, mask logic and etc. (70% of ATF32)
Partition Circuits:
Address drivers, PCL, VDM_DAC, iREF_DAC
Tile 0
Tile 127
LWLs/LWLd/PCL CTRL DRVRS
GWLS DRVR/TERM CAPS
GBLS DRVR/TERM ANALOG
PCL/LBLS & LBLd DRVRS
Core/Partition: 118mm2
Periphery Circuit: 10mm2
PL, Fuses, redundancy matching, HV regulators,..
IO CIRCUITS: 4mm2
PADS, Tx, Rx, DLL,..
Scribe Lane: 3mm2
CUA
Pitch Cell:
WL: HVN Sel/HVP Desel
BL: HVP Sel/HVN Desel
50% of ATF32
Outside Pitch Cell:
~30% CUA area [20% of ATF32]
Scaling by floorplan
1/4th Tile (1K x 1K)
* Need to confirm
 | I/O, Scribe | Periphery | Partition cntl | Tile control | Pitch cell
ATF (134mm2) | 7mm2 (5%) | 10mm2 (7%) | 23mm2 (17%) | 28mm2(21%) | 66mm2 (50%)
Design Rule | 100% | 100% | 79% | 79% | 79%2
BWF (95mm2) | 7mm2 | 10mm2 | 18mm2 | 22mm2 | 41mm2

## Slide 8: Transistors consolidation for BWF
Collateral # | symbol | model | Tag by L | Type # | #/Tile | #/Die | Tox | Type | Channel | triple well | Assymetry
1 | nlvhvt4t | nhvt | Lmin 0.9 | 1 | 1418 | 8.60E+06 | 21 | N | high |  | 
2 | nlv4t | n | Lmin 0.9 | 2 | 158 | 2.22E+06 |  |  | med |  | 
3 | nlvlvt4t | nlvt | Lmin 0.9 | 3 | 0 | 1.16E+04 |  |  | low |  | 
4 | plvhvt4t | phvt | Lmin 0.9 | 4 | 1299 | 8.18E+06 |  | P | High |  | 
5 | plv4t | p | Lmin 0.9 | 5 | 119 | 1.89E+06 |  |  | med |  | 
6 | plvlvt4t | plvt | Lmin 0.9 | 6 | 0 | 9.13E+03 |  |  | low |  | 
7 | nhv4t | nhv | L=5.52 | 7 | 8352 | 3.74E+07 | 110 | N | high |  | 
8 | nhv4t | nhv | Lmin 9.7 | 8 | 1454 | 7.70E+06 |  |  | med |  | 
9 | nhvsw4t | nhv | L=8 |  | 0 | 1.28E+05 |  |  |  |  | 
10 | nhvlvt4t | nhvlvt | Lmin 9.7 | 9 | 121 | 8.55E+05 |  |  | low |  | 
11 | ntwhv5t | ntwhv | Lmin 9.7 | 10 | 713 | 3.58E+06 |  |  | med | yes | 
12 | ntwhvlvt5t | ntwhvlvt | Lmin 9.7 | 11 | 9 | 1.56E+05 |  |  | low |  | 
13 | ntwhv5t | ntwhv | L=7 | 12 | 260 | 1.13E+06 |  |  |  |  | 
14 | phv4t | phv | Lmin 9.7 | 13 | 1160 | 6.39E+06 |  | P | med |  | 
15 | phv4t | phv | L=7 |  | 8482 | 3.80E+07 |  |  |  |  | 
16 | phv4t | phv | L=8 |  | 9024 | 3.88E+07 |  |  |  |  | 
17 | phvlvt4t | phvlvt | Lmin 9.7 | 14 | 157 | 9.43E+05 |  |  | low |  | 
18 | ntwhvssh5t | ntwhvssh | L=7 | 15 | 8516 | 3.65E+07 |  | N | low | yes | yes
Dual Vt Low voltage nMOST (2)
Dual Vt Low voltage pMOST (2)
One Vt High voltage nMOST (1) Triple well = diode isolated well device
Dual Vt High Voltage pMOST (2)
Pitch cell High voltage nMOST (1)