## Slide 1: Model-Based Problem Solving (MBPS)
DerChang Kau, WW43, 2019
Problem solving process vs tools: Having the right tools is necessary but insufficient to solve problems. Don’t mistake a tool as a substitute for the process of problem solving!
MBPS methodology with single page RA/RM dashboard – What each step is, how to do it
    Develop Problem Statement
    Problem Characterization & Segmentation
    Develop Models
    Validate Models
    Identify Solutions
    Implement/Standardize Solutions
    Review Helpful Templates and Tips

## Slide 2: RA/RM Template
Issue/Owner | Models/Strategy | Results/Next Steps | 
Problem Statement: Quantified gap to goal & underline mechanism(s) if known. Problem statement is a clear & concise statement on the specific observations of an undesired result. A clear problem statement includes proven facts only and is supported by a concise exhibit that justifies the accuracy of the statement. Problem Characterization: Concise articulation to reflect the current status of problem solving (knowns and unknowns) The characterization is where we identify and organize key information to detail problem. Types of information includes impact, metrics for detection, success criteria, on known/unknown. Success Criteria: Determine what criteria must be met to release the line, release the containment restrictions and/or close the problem solving effort. Owners: Sponsors/Stakeholders: Phase: Maturity of the problem solving 1-Assumption 2-Symptom, Data Collection 3-Speculation with limited data 4-Segmentation 5-ID’d 6-Containment deployed 7-Root cause validated Risk: 1-Showstopper 1.5-High Risk/No Data 2-High Risk 2.5-No Data 3-Med Risk 4-Low risk 5-cert. | Models of Gaps What is Problem Segmentation? Problem segmentation is the process of narrowing down a problem into more manageable pieces in space and time to help determine where the problem is occurring. Segmentation is achieved by figuring out where the problem is NOT coming from to help the team focus all their efforts where the problem is more likely to originate. What is a Model? A model is a description of the contributing factors or conditions that must be met to create the observed symptoms of a problem statement. | Results: Frame each model in the form of: Model description, Supporting evidence, Conflicting evidence Model Validation is the process of designing and executing experiments or analyses to prove/disprove a model. Validated Model: has strong supporting evidence, little or no conflicting evidence, and is logically sound. This is likely at least one the root causes or contributing factors of your problem. Invalidated Model: has little or no supporting evidence and has strong conflicting evidence. Cannot be the root cause for your problem. | 
 | Strategy for gap-to-goal assessment: Integrated strategy to segment model, validate the solution for root cause elimination and/or containment patches | Next Step @ Quad 1 : Next steps @ Quad 2 : Critical Path and planning for milestone, use expected completion date to support the schedule and schedule logic | ECD

## Slide 3: Pitch Cell Scaling (50% of Die Size)
Issue/Owner | Models/Strategy | Results/Next Steps | 
Problem Statement: Scaling goal is 62.5% vs. 64% (1.5% gap) Pitch cell scaling requires both WL and BL decoders layout shrink in both dimensions at 79% (26.5/33.5) or 37.5% footprint reduction. Aggressive decoder LG scaling (from 7l to 5.5l) needed in order to meet cell operating current without cell CD scaling Other Deign Rule including d2d, d2w, c2g, poly2poly, poly end cap, contact size, contact enclosure (see Problem Characterization) will require doping profile and alignment integrity and process modules / integration assessment Problem Characterization: Preliminary DR change proposal enables 36% footprint reduction vs. 37.5% required Owners: Luo, Prashant, Baofu, Khaled Sponsors/Stakeholders: Sandeep, Eddie, Balaji, DerChang Phase 2-Data Collection or 3-Speculation with limited data Risk: 1.5 to 2.5 | Models of Gaps 79% linear shrink required aggressive LG scaling by both channel and Tip doping engineering Diffusion spacing design rule scaling uses STI depth, S/D and well doping engineering Other poly and contact design rule rely on patterning true spec characterization | Results: Preliminary Design Rule change proposal enables ~36% pitch decoder area scaling Key learning from TCAD simulation Ion/Ioff/BV/Isub DTS met at scaled Lg down to 218nm for decoder select devices The trade-off is higher VT and degraded Rout due to channel length modulation Started to see BVD degradation at Lg of 218nm [segmenting breakdown, punch through or reach through] | 
 | Strategy for gap-to-goal assessment: TCAD assessment of planar transistor design: 110Å oxide CMOS channel and tip doping for LG scaling. Metric validation on in Vt, Id-Vd, Id-Vg, Isub, GIDL meeting pitch cell electrical requirement. diffusion spacing design rule capability assessment using TC03 for initial risk assessment and segmentation for additional STI depth and well doping engineering. Contact and poly patterning and alignment true spec characterization using TC03. | Next Step @ Quad 1 : TCAD Scaling of on Pitch transistors [N/P] to ≤ 5.5l TCAD calibration to Si data [Process & e-test] Assess FEOL DR change proposals based on available Si process modules data Next steps @ Quad 2 : TCAD Scaling/DR of outside-Pitch under tile CuA [including LVT] Apply CuA learning to partition circuit scaling Plan for Si expts to test scaling limits and DR change proposals | ECD ww21 ww20 ww22 ww24 ww26 ww26
Pitch cell DR proposal | 33.5 | 26.5 | ratio
Cell Pitch | 0.67 | 0.53 | 79%
N-active to Well | 12 | 10 | 83%
P-active to Well | 12 | 10 | 83%
Active Spacing | 2.2 | 1.8 | 82%
WL select L NHV | 7 | 65.5 | 86%
WL desel L PHV | 8 | 6 | 75%
BL select L PHV | 7 | 65.5 | 86%
BL desel L NHV | 5.52 | 5.52 | 100%
WL select W NHV | 8.52 | 6.68 | 78%
WL desel W PHV | 3.16 | 2.44 | 77%
BL select W PHV | 8.52 | 6.68 | 78%
BL desel W NHV | 3.16 | 2.44 | 77%
Inverter Width | 4.24 | 2.4 | 57%
HV Endcap | 2.2 | 1.6 | 73%
Poly Spacing | 2.4 | 2 | 83%
Contact-to-Gate | 1.7 | 1.61.45 | 85%
Contact Size | 1.6 | 1.4 | 88%
Diff ovlp of contact | 0.1 | 0 | 0%
Contact Space | 2.4 | 2.4 | 100%
ww19.5

## Slide 4
Problem Characterization & Segmentation
Implement/ Standardize Solutions
Detection/Containment Strategy
Identify Solutions
Validate Models
Develop Problem Statement
Develop Models
MBPS Process
Structure the problem space: define right problem & define problem right
Identify key characteristics of the problem. Eliminate segments where the problem is not to narrow down the possible culprits
Note how Problem Characterization & Segmentation overlaps with Problem Statement, Develop Models and Validate Models
The flow thru the first four steps is not linear!
Develop hypotheses that describe the conditions that must be met to create the observed symptoms of a problem statement.
Experimentally test models in order to identify supporting and conflicting evidence until one or more models are validated.
Generate a set of alternative solutions
Decide upon and implement the selected solutions with understanding of intended and unintended consequences
Develop problem detection & containment strategies immediately and refine strategies at each step.