## Slide 1: Transform NVM Pathfinding World Class
DerChang Kau, Max Hineman & Cathy Labelle, WW24/2021
Phases of Ideation
TCAD and Modeling are part of “Team NVM Pathfinding”
Necessity for an impactful Optane pathfinding
Institute a business process proactively managing pathfinding

## Slide 2: Phases of Ideation
Concept –
Success: Backed by first principle or trust-worthy empirical
Leverage external research institutes or consortia, eg. SRC, SRS, IMEC and etc
Early Research –
Success: Competitive advantage for landing zone demonstrated at first principle
Leverage other Intel organizations , eg. CR, SiP
Proof of Concept –
Success: Integrated scope validated by segment
Leverage RTD/MCD
Module Definition –
Success: Critical logistics and infrastructures tested for intercept
Exit Pathfinding –
Success: Specification defined with risks mitigated or mitigation plan deemed feasible
Ready to transfer to main TD.

## Slide 3: Optane Pathfinding Projects at a Glance
Array
3D NAND Like
Deck Select
Pillar Select
Periphery
WideBG Channel
Selector
WideBG Diode
“No Seasoning”
Low Drift α-Chal
Memory
iPCM
+
CUR/SRC
CRC/SRS
NMTRI, IMEC & etc.
TSLRP
P1241/ATF
Electrode
Set Speed
Bantu DV and Test
P1250/BWF
2Kx4Kx4D
Space Scaling
Cell Scaling
CMOS Scaling
IC scheme
Architecture
Bipolar Decoder
Periphery
HVT Augmentation
(FINFET, RCT)
Selector + Memory
MLC (inc. BiSM)
Architecture
Float deselect
3DIC
Tile Scaling
MBA
Array
Low ρ BL/WL
DSA
Selector
Oxide Selector
Memory
PM Speed & TD
+
CR, SiP collaboration
Ideation
Transfer to Main TD
Proof of Concept
Notes: Need definition for Ideation (paper, external research)
PoC (some level of internal results
Transfer: for stepping up

## Slide 4: TCAD/Modeling Dual Roles
Technology Capability
Design Latitude
TCAD & Modeling
DTCO
Scaling assessment
&
Window exploration
Technology Development
Product Development
TCAD & Modeling
Si-2-Sim
Yield Segmentation
&
Corner Validation
Pathfinding
Main Development
Si Based
Collateral
Si-2-Sim
Calibration
  Design-Technology Co-Optimization
Segmentation for root cause elimination

## Slide 5: The Essentials for an Impactful Optane Pathfinding
Happening now – ATF electrode, set speed (PM) and scribe mini-array are not ready for prime-time TD (yield ramp)
Critical capability to facilitate the basic needs for Optane Pathfinding RED for ATF, BLUE for P1250/BWF, Boldface-italic for “yet to happen”
  Process Modules: Cosputter (cell stack), ALD (liner/seal)
  L1E: MID flow (Moat Isolated Device, MID, for SD, PM, Electrode and other thin films)
  L2: SC flow
    SD only, including SD/Electrode-interface (to segment SD in the self-aligned cell stack)
    Need to revisiting x’tor isolated memory cell for PM, Electrode only (eg. IG88, C3P0)
We also need a sustained lab capability and thruput
  Electrical: WLC automation (inconsistent, need clear ownership)
  Physical: Most of L0 char (inconsistent thruput @ RTD; some missing capabilities)

## Slide 6: Proactively Managing Pathfinding
Ideas are a dime a dozen; execution is everything
Reference and learnings –
  Intel Lab Projects Approval and Gates: IL Workstream 2.0
  Project WP and PoP metric of SRS
  Gladius: An initiative transforming PLC with sustainable and disciplined innovation and execution at high velocity & uncompromised quality
  Intel LTD/CR workflow and external JDP SOW experiences (IM, EMD/Intermolecule)
Institute a business process (independent from the size of the projects); see embedded doc 
One Page Project Cover Sheet for succinct communication, including
  Problem statement, Objective, Key Results, Strategy, Duration and Competitive Analysis
  Chartering Group, Sponsorship, stakeholders and feedback plans for gate and ratification  Step up or down or Change
  Guardrail, Scope and Resource and Silicon plan for “effort assessment”
  Customers and Sunset Plan  Successful transfer is a pulling process but not pushing process
One section of Study Plan or Work Package to highlight critical tasks, paths and deliverables
One section of Gantt Chart and iMBO for project tracking and management

## Slide 7: Notes on Pathfinding Scope Discussion

## Slide 8: What are the key questions in that scope?
How able to establish the pathfinding activities to match the Optane 7-quarter PRQ cadence?
Key questions:
  What is the scalability capability of current Optane cell?
  Can we double the bandwidth/GB at the desired cadence? What is the desired performance requirement cadence? (2x per 7Q, 2x per 10Q, etc.)
  How would the tick-tock strategy apply to Optane? Does it?
    What are the tick(s) and the tock(s)?
  Let’s write down as many generations as we think we can with certain boundary conditions (cost, performance?)
    Pitch, cell, array, partition, product; cost
  What triggers a change in architecture?
  What are the key physics questions we need to answer?
    Phase change observed down to ~3-8nm; no phase change occurs <3nm
    Threshold switching/selector à smaller actually works better, but not sure what limit is, what the variation is
    Challenge we don’t understand much is how to activate the PM/SD as device shrinks
  What are the criteria that define a fork in the scaling/architecture path?
    How far ahead do we need to plan to have key understanding of the different paths?
    Need to assess extendibility of the new path
  What is the scaling strategy for Optane?
    # of decks
    Array pitch scaling
    CMOS scaling
    Dis-aggregation

## Slide 9: How to deliver Pathfinding scope
Core team: Max, Derchang, Cathy, Derran
  Own and drive analysis & recommendations
  Own communication to stakeholders
Extended team:
  CMOS: Erv
  Leverage TD team, example: SORT/e-test methodologies: ??
    Ad-hoc pull of individuals in certain areas
Learning vehicles
  Class #1: L0D, blankets
  Class #2: minimally integrated, single-level mask structural work unique to PF (example: pre-BWFs L/S grating mask)
  Class #3: experiments on N-1 vehicle, low/med deviation from N-1 POR (example: ATF41 à BWF33.5)
  Class #4: experiments on N-1 vehicle, high deviation from N-1 POR (example: single chal ATF)
  Class #5: integrated test site specifically for PF (example: MID)
Simulation/modeling capability & development
  Device (Synopsis TCAD, Ansys, Finite Element)
  Integration (3D diagrams (Coventor), Ansys)
  Process (Synopsis, etc.)
Trajectory definition
  T-SLRP (5-10 yrs, refresh 1/yr)
  5Gen (5-8 yrs, refresh 2/yr)
  LRP (3-5 yrs, refresh 2/yr)
  IMBOs (1 year, quarterly)
Resources
  Internal vs. external project allocation
    IMEC, universities, etc.
  Si allocation
  People fraction
  Lab allocation
  Tools available for PF Si