## Slide 1: ATF Scribe Area Reduction
Christopher Chen
April 24, 2020

## Slide 2: Agenda
Goal: to fit all of our ATF scribe modules into a single vertical and single horizontal scribe width
  Problem: need to fit 50 modules into equivalent space of 18 Keithley modules
The topics we’ll discussed are a subset of Shafqat’s list:
Create a list of must-have and good-to-have structures – Priyanka
  So far, have ~35~40 must-haves; possibilities for further reductions (array?)
  Will meet today to finalize CMOS and ESD
Routing Arch for inline and EOL e-test for CMOS and interconnect and array – Khaled, Priyanka, Tuhin
  How many structures can we put into an interleaved module?
  Would interleaving enable to us to fit all the must-have structures?
Prober and probe card capability – alignment, etc. -- Chris
Array Testing needs and how is that comprehended in pad design – Matt, Daniel
RTD & HVM considerations – Matt, Daniel

## Slide 3: Scenarios to Evaluate
 | Scenario | Pad Height (um) | Pad Width (um) | Pad Pitch (um) | Space Between Pads (um) | Space Between Interleaved Pads (um) | # Vertical Modules | # Horizontal Modules | # K modules
1 | Keithley 1x16 | 65 | 49 | 114.3 | 65.3 | - | 12 K+20 P | 6 K+24 P | 18K
2 | Pyramid 1x17 | 32 | 40 | 50 | 10 | - | 74P | 50P | 
3 | Keithley 1x16, interleaved | 65 | 49 | 114.3 | 16.3 | 8.15 | 24K+20P | 12K+24P | 36K
4 | TMG 1x16 | 52(48) | 40.8 (37) | 55.7 | 15 | - | 26TMG+14P | 12TMG+24P | 38TMG
4a | TMG 1X16 | 32 | 42 | 56 | 14 |  | 12TMGa |  | 
5 | TMG 1x16, interleaved | 52 | 42 | 100 | 56 | 8 | 28 TMG+20P | 12TMG+24P | 40TMG
6 | TMG 1x24 | 52 | 42 | 56 | 14 | - | 18TMG+20P | 7TMG+24P | 26TMG
7 | Altera Benchmark 1x16 | 32 (30.4) | 32(30.4) | 70 | 40->38 | - | 58ALT (using Altera pad pitch) | 38P (using pyramid pad pitch) | 
Need to evaluate the scenarios below to see which ones enable us to fit all must-have modules
H1=10612um2 V1 & V4 =8767um2 | H2=11492um2 V2= 13770um2 | H3=10612um2 V3=10720um2
Module Area
624 pads
640 pads

## Slide 4: From Vendor
The Pad Size is Pad Opening size.

## Slide 5: E-test Options Table (work in progress – please treat these table as Rev0)
 | Pitch | Pad dimensions | Space between pads | Upside | Downside
POR Keithley | 2286 dum 114.3 um | 1300 x 980 dum 65 x 49 um | 1306 dum 65.3 um |  | 
POR Pyramid | 1000 dum 50 um | 650 x 800 32.5 x 40 um |  | 3-4x in space of one | Inline test need to move to M4. More metal for assembly to dice. Throughput
Altera Benchmark | 1400 dum 70 um | 30 x 30 um |  | Has been tested in volume at foundry | Never tested in Intel Throughput
TMG | 1120 dum 56 um | 1020 x 840 dum 51 x 42 um |  | ~2x fitting | 
Pad height Reduction | 2286 dum 114.3 um | 650 x 980 32.5 x 49 um |  | 2 rows in space of one with same routing capability | Never volume tested the pyramid
Keithley Pad Density Doubling | 2286 dum 114.3 um | 1300 x 980 65 x 49 um |  | 2 modules in space of one | Inline test need to be moved to M3 More metal for assembly to dice Design complexity

## Slide 7: Accretech UF3000EX Prober Specifications
Prober will not be limiting factor for alignment
  X/Y alignment tolerance: +/- 0.5um across wafer
  Overdrive tolerance: +/- 2um
  Theta tolerance: ~0.072um error at wafer edge
Probe card will be limiting factor for alignment

## Slide 8: Probe Card Alignment
Alignment limited by probe card, not prober
Use Case | Probe Card Vendor (Model) | Cost per Card | Pad Config | Tip Diameter (um) | X/Y tolerance (um) | Z tolerance (um) | Pad Pitch (um) | Pad Height (um) | Pad Width (um) | Space Between Pads (um) | Comments
Keithley | JEM (A16C45SZ) | $4.6k | 1x16 | 25 +/- 5um | +/- 5 | +/- 5 | 130 | 65 | 49 | 65 | 
Pyramid | Celadon VersaCore (VC20E-17.1) | $2.7k (core), $3k (board) | 1x17 | 8 | +/- 4 | +/- 4 | 50 | 32 | 40 | 10 | 
TMG 40x1 | FormFactor (S40F47) | $1.9k $3.3k high temp (2016) | 1x40 | 10 +/- 2.5um | +/- 5 | +/- 5 | 55.7 | 52 | 40.8 | 15 | Passivation opening 48um (height) x 36.8um (width)
Altera Benchmark | STAr VIRGO-PRO II-HT-SP 22 | $5.9k (2012) | 1x22 | 10 | +/- 5 | < 5 | 70 | 30 | 30 | 40 | 

## Slide 9: Keithley Probe Card Specs
Tip diameter ~26um, +/-5um alignment, +/-5um planarity
These number increase with usage

## Slide 10: Pyramid Card Specs
Celadon VC20E-17.1
Alignment tolerances:

## Slide 11: TMG 40x1 Probe Card Spec (S40FA7x)
Tip size: 10 +/-2.5um
Alignment: +/- 5um
Planarity: +/- 5um
Passivation opening: 48um (height) x 36.8um (width)
Metal pad size: 52um (height) x 40.8 (width)
Information Courtesy of Robert A Miller

## Slide 12: Altera Benchmark Probe Card Specs
STAr VIRGO-PRO-HT-SP
Note: high temp card for probing up to 150C

## Slide 13: Parametric Probing in 1x40 Pad Configuration
40 pads arranged in 1 row x 40 columns
  Pads run horizontal
  Pad width and pitch are slightly larger for even pads compared to odd pads
Dimension | X (um) | Y (um)
Pad size (odd pads) | 42 | 51.408
Pad size (even pads) | 42.076 | 51.408
Space from pad-to-pad | 13.612 | N/A
………
Pad 1 (odd)
Pad 2 (even)
Pad 3 (odd)
Pad 40 (even)
1 2 3 4 …
40

## Slide 14: Action item and Notes from Discussion (Monday) 19.1
Take TMG Pad-> use them for 40 modules. And take version of same pad with reduced height (32) and do 5 more modules (not needed to be tested much, noisy data) with same TMG pad pitch.
  Risk: Noisy data from 5 modules.
    Action item: Chris will check with Probe Card Vendor for Option 4a.
Take Altera Pad-> Make same Pad Size to Pyramid. Pad pitch is 70 and space between Pad as 28

## Slide 15: Action item and Notes from Discussion (Friday) 19.5
Go with Altera Pad (32x32) –All Pyramid in Horizontal, all critical in Vertical
  Testing layers MT2/MT4/TM2
  50 Vertical & 46 Pyramid (Action item : Divesh will close with Yun & Kala)
Evaluate TM2 Pad Mask & Altera Pad (5K)
  Evaluate in TC03?
  Order both Cantilever & {Vertical(50 pitch)- test 4 or 5 masks}
  Timeline for Probe Card: Cantilever- 1 month & Vertical 1 ½ month
-> If we see something wrong here.. Backup plan?
  Vertical is going to be Back up.