## Slide 1: Disaggregated Cache Memory Solutions for Performing Client Compute
Team FTE Pathfinding, Jan/27/23
Electric Pond: A 2MB one channel cacheline access test chip and scalability in pJ/b, τacc vs. capacity
Disaggregated SRAM and Package aggregation choices
Benchmark – SRAM and advanced Fanout Package
Foundry Engineering Group Content Expertise

## Slide 2: Electric Pond - Summary
Top Die
(Controller)
Power & test signals to bottom die
Embedded Die
(SRAM)
Controller
SRAM
RDL layer
Substrate
Power & test signals to top die
Drivers
Drivers
SRAM
MUX
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
Bank groups
Test Chip KPI | Test Chip | 32x Scaling | Notes
Memory capacity | 1 channel x 2MB | 8 channels x 8MB | 32x capacity
Bank Groups | 2 | 2 | 
Memory banks | 4 | 16 | 4x banks
Memory density | 2.25 MB/mm2 | 2.25 MB/mm2 | 
IO drivers (die-to-die) | 1,272 | 10,176 | IO drivers scaling w/ # channels
RD Bandwidth WR Bandwidth | 102 GB/s 102 GB/s | 816 GB/s 816 GB/s | 8x higher bandwidth
RD Latency WR Latency | 4.375 ns 2.5 ns | 4.375 ns 2.5 ns | Using same pipeline
RD energy per bit* WR energy per bit* | 0.22 pJ/bit 0.20 pJ/bit | 0.30 pJ/bit 0.28 pJ/bit | Datapath energy scaling: 0.08 pJ/bit  0.16pJ/bit (SRAM, IO drivers not scaling)
(*) preliminary
Electric Pond Testchip
  Technology: TSMC N6
  Memory density: 2.25 MB/mm2
  Die-to-die link (data, cmd, red) : 1272 pads @ 1.6GT/s
Package Assembly
  Technology: SPIL FO-EB (Fan-Out, embedded bridge)
  Face-to-Face integration between top die and embedded die
  Microbump pitch: 25um
  Microbump density: >1.7k/mm2
  RDL layer: 1 layer for routing test signals & power

## Slide 3: Disaggregated SRAM & Back End 3D Packaging Aggregation
  Cost
Top | I18A, N3E/N2, SF2P | I18A, N3E/N2, SF2P | I3, N4P/N6, SF4/SF5
Base | N4P/N6(DTC/MiM), SF4/SF5(ISC) | ADM(MiM), N4P/N6 (DTC/MiM), SF4/SF5 (ISC) | I18A?, N3E/N2, SF2P?
Package | SPIL/ASE/Amkor/JCET, TSMC | Intel/TSMC/SF, SPIL/ ASE/Amkor/PTI/JCET | TSMC/SF/Intel
Substrate
RAM + TSV w/ Opt. IPD (MiM/DTC etc.)
CPU
(FE-3D Chiplets)
GPU
(FE-3D Chiplets)
CPU
(FE-3D Chiplets)
GPU
(FE-3D Chiplets)
Substrate
Adv. monolithic Logic tech (CPU, GPU) with TSV or Tyche
SRAM
(single layer or Cube)
DTC
SRAM+TSV
Substrate
Top 
Base 
Advanced logic technologies; chiplets including single layer and heterogeneously stacked (HBI)
Mainstream matured technologies; active chiplets, bridge, and/or passives with TSV
Mainstream matured technologies; chiplets with TSV, cubing using hybrid bond integration

## Slide 4
Chart: ’24 Adv. Fanout Packaging by Suppliers
| µB Pitch [µm] | TMV Pitch [µm] | C4 Bump Pitch [µm] | RDL Pitch [µm] | Number of RDL layers | Number of Embedded Die | Module Sizes [x reticle] | Package Sizes [mm] square
SPIL | 4 | 1.8301 | 2 | 1.6781 | 2.5 | 3 | 4 | 4
ASE | 3.1926 | 1.8301 | 1.5406 | 0.67807 | 2 | 1.3333 | 3 | 4
JCET | 3.415 | 1.8301 | 1.5406 | 4 | 3.5 | 1.3333 | 3 | 3
Amkor | 3.1926 | 1.8301 | 1.5406 | 0.67807 | 2 | 1.3333 | 3 | 4
TSMC'22 | 3.6781 | 1.8301 | 1.8301 | 3.8625 | 2 | 0.33333 | 1 | 2.7364
3
2
100
9
4
4
50
6
16
8
4
2
160
80
40
20
160
80
80
2
1
3
75
6
40
40
8
Chart: SRAM Benchmark by Mainstream Logic
| Cell Size [µm^2] | $/64MB | 2R1W Energy [pJ/b] | SRAM Fmax [GHz] | Static Leakage [nW/b] | Iso Power Speed [Normalized]
Intel 3 | 2.8 | 2.2632 | 1.6704 | 3.37 | 1.3552 | 3.6726
N6 | 1.792 | 3.6943 | 3.7048 | 3.0912 | 3.4395 | 2
N5 | 3.574 | 3.4667 | 3.9304 | 2.8289 | 3.4053 | 3.165
N4P | 3.9828 | 3.5829 | 3.9304 | 3.173 | 3.3248 | 3.835
SF5 | 2.14 | 4.0908 | 3.41 | 2.4867 | 0.86551 | 1.9157
SF4 | 3.1 | 3.6167 | 3.926 | 2.6178 | 1.708 | 3.2767
0.0200
0.0233
0.0267
0.0300
12
9
6
0.07
0.06
0.05
0.04
0.75
1.25
1.0
0.5
0.75
1
1.25
1.2
1.1
1.0

## Slide 5: Who are We
Foundry Technology & Engineering (FTE by Changhong Dai) is the engineering branch of Global External Manufacturing and Sourcing (GEMS by Hai Wang) under Stu Pann’s Corporate Planning Group (CPG)
FTE provides end to end engineering coverage and handshake to external suppliers from pathfinding to PRQ. Once PRQ’d, External Manufacturing & Production (EMP by Angelo Pinto, manufacturing branch of GEMS) will pickup the ownership for product delivery.
External technology contributors to disaggregated cache memories for CCG
  Pathfinding – DerChang Kau
  Platform – Mike Goldsmith
  Logic – Andy Wei
  Memory – Dany Ly-Gagnon
  Packaging – Jason Zhang
  Design – Ping Liu, Jiajing Wang

## Slide 6: Supporting Materials

## Slide 7: Energy & Latency
~600um
MUX
TX/RX
SRAM
 | Energy per bit [pJ/bit] |  | Notes
 | Read | Write | 
Driver | 0.075 (TX only) | 0.044 (RX only) | Best / Worst: 0.047 / 0.070 pJ/bit TT/0.75V/105C
Datapath | 0.080* | 0.080* | Estimate (scaled for full datapath) TT/0.75V/85C
SRAM (Macro) | 0.064 | 0.074 | Active power TT/0.75V/85C
Total | 0.219 | 0.198 | 
Latency | Cycles delay (@1.6GHz) |  | Latency (ns) | 
 | Read | Write | Read | Write
Latency (pad-to-pad) | 7 | 4 | 4.375 | 2.5
BK
TX
RX
ff
ff
IO driver
RX
TX
ff
ff
uB
Test engine / MBIST
GIO
SRAM
ff
~10gates + ~500um
(~370ps)
~540um (~200ps)
Q
uB
MUX
ff
MUX
ff
D
2 cyc
0.080 pJ/bit
1 cyc
0.075 pJ/bit
1 cyc
0.080 pJ/bit
1 cyc
0.044 pJ/bit
IO driver
CTRL
RD/WR latency
  RD latency is 4.375ns (7 cycles at 1.6GHz)
  WR latency is 2.5ns (4 cycles at 1.6GHz)
  SRAM using 800MHz clk (2 cycles per memory operation)
  2 Bank Groups alternating access
RD/WR energy per bit (prelim estimates)
  Projecting 0.22 pJ/bit
  SRAM macro energy is ~30-40%
2 cyc
RD: 0.064 pJ/bit
WR: 0.074 pJ/bit
SRAM

## Slide 8
Chart: SRAM Benchmark
| Intel 3 | N6 | N5 | N4P | SF5 | SF4
Cell Size | 0.87719 | 1 | 0.78289 | 0.73309 | 0.9576 | 0.84064
$/bit | 0.92105 | 1 | 1.0987 | 1.0483 | 0.82804 | 1.0337
Access Energy | 1.4736 | 1 | 0.94747 | 0.94747 | 1.0686 | 0.94849
SRAM Speed | 1.0902 | 1 | 0.91513 | 1.0265 | 0.80444 | 0.84686
Static Leakage | 1.814 | 1 | 1.0133 | 1.0448 | 2.0052 | 1.6762
Logic Performance | 1.1673 | 1 | 1.1165 | 1.1835 | 0.99157 | 1.1277
Chart: SRAM by Suppliers
| Cell Size | $/bit | Access Energy | SRAM Speed | Static Leakage | Logic Performance
Intel 3 | 0.87719 | 0.92105 | 1.4736 | 1.0902 | 1.814 | 1.1673
N6 | 1 | 1 | 1 | 1 | 1 | 1
N5 | 0.78289 | 1.0987 | 0.94747 | 0.91513 | 1.0133 | 1.1165
N4P | 0.73309 | 1.0483 | 0.94747 | 1.0265 | 1.0448 | 1.1835
SF5 | 0.9576 | 0.82804 | 1.0686 | 0.80444 | 2.0052 | 0.99157
SF4 | 0.84064 | 1.0337 | 0.94849 | 0.84686 | 1.6762 | 1.1277

## Slide 9: Disaggregated SRAM & Back End 3D Packaging Aggregation
Substrate
RAM + TSV w/ Opt. IPD (MiM/DTC etc.)
CPU
(FE-3D Chiplets)
GPU
(FE-3D Chiplets)
CPU
(FE-3D Chiplets)
GPU
(FE-3D Chiplets)
Substrate
Adv. monolithic Logic tech (CPU, GPU) with TSV or Tyche
SRAM
(single layer or Cube)
DTC
Cost
SRAM+TSV
Substrate
Top | I18A/I16A, N3E/N2, SF2P | I18A/I16A, N3E/N2, SF2P | I3, N4P/N6, SF4/SF5
Base | N4P/N6(DTC/MiM), SF4/SF5(ISC) | ADM(MiM), N4P/N6 (DTC/MiM), SF4/SF5 (ISC) | I18A/I16A, N3E/N2, SF2P
Package | SPIL/ASE/Amkor/JCET, TSMC | Intel/TSMC/SF, SPIL/ ASE/Amkor/PTI/JCET | TSMC/SF/Intel

## Slide 10: Cost Comparison
Active Foveros: Large base die size with low utilization of high cost embedded active functionality
N6 SRAM vs. ADM |  |  |  |  |  |  | 
Component | Technology | Cell Size [µm2] | Die Size [mm2] | $/Wafer | MB/mm2 | Yield | Die Cost
BMG G10 448eu/512MB Q3’23 | P1222.61 (LRP’22) | 0.01458 | 366 | $16.6K | 1.40 | 77.3% | $143
 | TSMC N6 | 0.02736 | 274 | $10.5K | 1.87 | 82.5% | $ 62
Substrate
36µm µB FOV + 16nm SoC + ADM + MiM
GPU
GPU
GPU
GPU
Substrate
TSMC 6nm SoC
1. N6 for 16nm SOC + ADM
2. ODI-like for Foveros

## Slide 11: Package Selection
Cost
IP Integration Scheme (connectivity, speed, energy)
Capability

## Slide 12: InFO-LSI Mockup Flow
N6 Memory
Bridge
GPU N3E
CPU 18A
SOC N6
A
A’
B
B’
A
A’
SOC N6
GPU N3E
DTC
DTC
Bridge
N6 SRAM
B
B’
SOC N6
CPU 18A
DTC
N6 SRAM
N6 SOC
DTC
N6 SOC
DTC
WoW
10 µm
HB
N3E GPU
DTC
N3E GPU
DTC
WoW
10 µm
HB
18A CPU
Carrier Prep
Die Reconst.
Em. Chiplets Attachment
N6 SRAM
Bridge
RDL, Cu Pillar Platting
Mold, RDL, Bumping
C4
1
2
3
4
5
6
25µm µB
80µm C4
25µm µB

## Slide 13: FO-EB-T/CoWoS-LSI Mockup Flow
N3E GPU
DTC
N3E GPU
DTC
18A CPU
Carrier Prep
Top Die Attachment
Em. Chiplets Attachment
N6 SRAM
N6 SOC
Mold, RDL
RDL, Cu Pillar
C4
1
4
5
2
3
SOC N6 12.9x4.1
N6 Memory
GPU N3E
CPU 18A
A
A’
B
B’
A
A’
GPU N3E
DTC
N6 SOC
N6 SRAM
B
B’
GPU N3E
CPU 18A
DTC
SOC N6
Micro Bumping
WoW
10 µm HB
25µm µB
80µm C4
Top Carrier Bond,
Back Carrier Debond.
Bumping

## Slide 14: DTC vs. ISC

## Slide 15: Estimated Cost of making: MiM, Trench Cap, Stacked Cap
Chart: Cost Adder vs Cap Density
| 22 | 44 | 42 | 140 | 350 | 700 | 1000
WOW-ISC | 750
Cap Density [nF/mm2]
Cost Adder [$/wfr]
BE-MIM
WoW DTC/ISC
On-Wafer ISC, Staircase MiM (idea stage)
TSMC DTC
HB: based on 3DNAND -- $30
Grinding: $ ~50
TSV: ~$100
High dope CZ wafer: ~$100
DTC: ~¢10 per nF/mm2
Market Intelligence:
Graphcore price low $1000
Samsung ISC :
ECTC20
OSAT
SPIL QTR roadmap ’24
Supplier Engagement needed
On-Wafer ISC from Tier-1 DRAM suppliers
Tier-2 DRAM : Nanya, PSMC, Winbond
Staircase MiM 3D AND suppliers
Tier-1 NAND : Solidigm (NSG)
Tier-2 NAND: Macronix

## Slide 17: From Graphic Memory (component) to Client Compute (system)
Mike & DerChang, WW16.2’22
Problem Statement – The flag and the hindsight
The Engagement – some good going but some not so successful
Dual Drive initiative – Client Compute
Call of Duty – Platform, Technology, Design & Packaging

## Slide 18: Update to GEMS-SOTU
P1222.61/P1222.7 dual-drive initiative: Alternative SOC + HD SRAM + 3DIC technology
  TSMC N6 with ODI-like packaging is pursued due to 3Cs’ superiority
  Evaluating Samsung 5LPP as a strategic maneuver
Kick-off sessions with product owners and memory architects from AxG and CCG.
  Gen 1 dual-drive is deemed too late to be cost-effective for 2023 PRQ intercept
  Both teams seem understanding foundry capability but SoA packaging ignorant Team PTL/NVL actively seek for dual-drive solutions for eRAM/packaging alternatives but do not have resources to commit to supporting dual drive initiative.
Expected to close go-nogo Task Force by mid Q2
  Feasibility deep dive, managing risks and developing dual-drive strategy for 2024+ intercept
This engagement leads a path to compute memory scaling and disaggregation strategy development for 3nm and beyond.

## Slide 20: Estimate Die layouts (per Brian 04/11 ’22)
P1222 Interposer
GPU N3E 8.1x7.7
CPU 18A 8.1x10.6
SOC N6 12.9x4.1
A
A’
B
B’
A
A’
GPU N3E
P1222 Interposer
B
B’
SOC N6
CPU 18A
P1222 Interposer
CPU 18A
PTL-M
~18.5
~12.4
P1222 Interposer
(PLT-M)
P1222 Interposer
P1222 Interposer
P1222 Interposer
Reticle
26mm
33mm
Full-Si Interposer has low LFU on p1222; PX+ exceeds reticle
P1222 Interposer
GPU N3E ~12.1x8.3
CPU 18A 8.1x24.9
SOC N6 17.2x4.1
PTL-PX/PX+
~33
~12.4
PX+: GPU N3E ~12.1x14.9

## Slide 21: Call of Duty – Dual Drive for CCG 2024~2025
Dual Drive Initiative 1: N6 SRAM for ADM
Dual Drive Initiative 2: ODI-like OSAT 3C for Foveros
Dual Drive Initiative 3: DTC (and beyond) for MiM

## Slide 22: InFO-LSI Mockup Flow
N6 Memory
Bridge
GPU N3E
CPU 18A
SOC N6
A
A’
B
B’
A
A’
SOC N6
GPU N3E
DTC
DTC
Bridge
N6 SRAM
B
B’
SOC N6
CPU 18A
DTC
N6 SRAM
N6 SOC
DTC
N6 SOC
DTC
WoW
10 µm
HB
N3E GPU
DTC
N3E GPU
DTC
WoW
10 µm
HB
18A CPU
Carrier Prep
Die Reconst.
Em. Chiplets Attachment
N6 SRAM
Bridge
RDL, Cu Pillar Platting
Mold, RDL, Bumping
C4
1
2
3
4
5
6
25µm µB
80µm C4
25µm µB

## Slide 23: FO-EB-T Mockup Flow
N3E GPU
DTC
N3E GPU
DTC
18A CPU
Carrier Prep
Top Die Attachment
Em. Chiplets Attachment
N6 SRAM
N6 SOC
Mold, RDL
RDL, Cu Pillar
C4
1
4
5
2
3
SOC N6 12.9x4.1
N6 Memory
GPU N3E
CPU 18A
A
A’
B
B’
A
A’
GPU N3E
DTC
N6 SOC
N6 SRAM
B
B’
GPU N3E
CPU 18A
DTC
SOC N6
Micro Bumping
WoW
10 µm HB
25µm µB
80µm C4
Top Carrier Bond,
Back Carrier Debond.
Bumping

## Slide 24: Packaging Flow Comparison
Carrier Prep
Die Reconst.
Em. Chiplets Attachment
RDL, Cu Pillar Platting
Mold, RDL, Bumping
C4
Carrier Prep
Top Die Attachment
Em. Chiplets Attachment
Mold, RDL
RDL,
Cu Pillar
C4
Micro Bumping
Top Carrier Bond,
Back Carrier Debond.
Bumping
Base wafer
TSV
Chiplets attachment
Interconnect,
µBump
Bumping
C4
Carrier bond, TSV Reveal
Passive Foveros: High cost process tools for TSV and Interconnect in Fab
Active Foveros: Large base die size with low utilization of high cost embedded active functionality
InFO-L: lowest cost of making but higher price judged due to SiFO vs. OSAT margin delta + chip first yield loss vulnerability
FO-EB-T: Cost of making slightly higher than InFO-L due to one additional wafer bonding and debonding processes.
Logic, SoC and/or ADM

## Slide 25: De-cap flow options
Fab-Out
Sort
ow-SC or sc-MiM
Pad
Fab-Out
DTC, MiM, SC
Stacking
Sort
Wafer Start
DTC in FEOL
BEOL
Fab-Out
Wafer Start
FEOL
MiM in BEOL
Fab-Out
Substrate
Inteconnect + MiM or SC
Substrate +DTC
Inteconnect
Substrate
Inteconnect
Substrate + DTC
Inteconnect + MiM or SC