## Slide 1: Disaggregated Cache Memory Solutions for Performing Client Compute
Dany Ly-Gagnon, Jason Zhang & DerChang Kau
Team FTE Pathfinding, Jan/27/23
Electric Pond: A 2MB one channel cacheline access test chip and scalability in pJ/b, τacc vs. capacity
Disaggregated SRAM and Packaging aggregation choices
Benchmark – SRAM and Advanced Fanout Package
Foundry Engineering Group Content Expertise

## Slide 2: Electric Pond - Summary
Top Die
(Controller)
Power & test signals to bottom die
Embedded Die
(SRAM)
Controller
SRAM
RDL layer
Substrate
Power & test signals to top die
Drivers
Drivers
SRAM
MUX
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
SRAM
(*) preliminary
Electric Pond Testchip
  Technology: TSMC N6
  Memory density: 2.25 MB/mm2
  Databus width: 64B cache line
  Die-to-die link (data, cmd, red): 1272 pads @ 1.6GT/s
Package Assembly
  Technology: SPIL FO-EB (Fan-Out, Embedded Bridge)
  Face-to-Face integration between top die and embedded die
  Micro-bump pitch @ 25µm, 1.78K bumps per mm2 in HCP
  RDL layer: 1 layer for routing test signals & power
Test Chip KPI | Test Chip | 32x Scaling | Notes
Memory capacity | 2MB (1 channel x 2MB) | 64MB (8 channels x 8MB) | 32x increase: 8x independent channels 4x more memory per channel
Channel capacity | 2MB | 8MB | 
Memory density | 2.25 MB/mm2 | 2.25 MB/mm2 | 
IO drivers (die-to-die) | 1,272 | 10,176 | IO drivers scaling w/ # channels
RD Bandwidth WR Bandwidth | 102 GB/s 102 GB/s | 816 GB/s 816 GB/s | Scaling with # of channels
RD Latency WR Latency | 4.375 ns 2.5 ns | 4.375 ns 2.5 ns | Datapath propagation delay remains 1 clk up to ~8MB channel capacity
RD energy per bit* WR energy per bit* | 0.22 pJ/bit 0.20 pJ/bit | 0.30 pJ/bit 0.28 pJ/bit | Datapath energy scaling with channel capacity: [pJ/bit]
Test Chip KPI | Test Chip | 32x Scaling | Notes
Memory capacity | 2MB (1 channel x 2MB) | 64MB (8 channels x 8MB) | 32x increase: 8x independent channels 4x more memory per channel
Channel capacity | 2MB | 8MB | 
Memory density | 2.25 MB/mm2 | 2.25 MB/mm2 | 
IO drivers (die-to-die) | 1,272 | 10,176 | IO drivers scaling w/ # channels
RD Bandwidth WR Bandwidth | 102 GB/s 102 GB/s | 816 GB/s 816 GB/s | Scaling with # of channels
RD Latency WR Latency | 4.375 ns 2.5 ns | 4.375 ns 2.5 ns | Datapath propagation delay remains 1 clk up to ~8MB channel capacity
RD energy per bit* WR energy per bit* | 0.22 pJ/bit 0.20 pJ/bit | 0.30 pJ/bit 0.28 pJ/bit | 

## Slide 3: Disaggregated SRAM & Back End 3D Packaging Aggregation
  Cost
Top | I18A, N3E/N2, SF2P | I18A, N3E/N2, SF2P | I3, N4P/N6, SF4/SF5
Base | N4P/N6(DTC/MiM), SF4/SF5(ISC) | ADM(MiM), N4P/N6 (DTC/MiM), SF4/SF5 (ISC) | I18A?, N3E/N2, SF2P?
Package | SPIL/ASE/Amkor/JCET, TSMC | Intel/TSMC/SF, SPIL/ ASE/Amkor/PTI/JCET | TSMC/SF/Intel
Substrate
RAM + TSV w/ Opt. IPD (MiM/DTC etc.)
CPU
(FE-3D Chiplets)
GPU
(FE-3D Chiplets)
CPU
(FE-3D Chiplets)
GPU
(FE-3D Chiplets)
Substrate
Adv. monolithic Logic tech (CPU, GPU) with TSV or Tyche
SRAM
(single layer or Cube)
DTC
SRAM+TSV
Substrate
Top 
Base 
Advanced logic technologies; chiplets including single layer and heterogeneously stacked (HBI)
Mainstream matured technologies; active chiplets, bridge, and/or passives with TSV
Mainstream matured technologies; chiplets with TSV, cubing using hybrid bond integration

## Slide 4
Chart: ’24 Adv. Fanout Packaging by Suppliers
| µB Pitch [µm] | TMV Pitch [µm] | C4 Bump Pitch [µm] | RDL Pitch [µm] | Number of RDL layers | Number of Embedded Die | Module Sizes [x reticle] | Package Sizes [mm] square
SPIL | 4 | 1.8301 | 2 | 1.6781 | 2.5 | 3 | 4 | 4
ASE | 3.1926 | 1.8301 | 1.5406 | 0.67807 | 2 | 1.3333 | 3 | 4
JCET | 3.415 | 1.8301 | 1.5406 | 4 | 3.5 | 1.3333 | 3 | 3
Amkor | 3.1926 | 1.8301 | 1.5406 | 0.67807 | 2 | 1.3333 | 3 | 4
TSMC'22 | 3.6781 | 1.8301 | 1.8301 | 3.8625 | 2 | 0.33333 | 1 | 2.7364
3
2
100
9
4
4
50
6
16
8
4
2
160
80
40
20
160
80
80
2
1
3
75
6
40
40
8
Chart: SRAM Benchmark by Mainstream Logic
| Cell Size [µm^2] | $/64MB | 2R1W Energy [pJ/b] | SRAM Fmax [GHz] | Static Leakage [nW/b] | Iso Power Speed [Normalized]
Intel 3 | 2.8 | 2.2632 | 1.6704 | 3.37 | 1.3552 | 3.6726
N6 | 1.792 | 3.6943 | 3.7048 | 3.0912 | 3.4395 | 2
N5 | 3.574 | 3.4667 | 3.9304 | 2.8289 | 3.4053 | 3.165
N4P | 3.9828 | 3.5829 | 3.9304 | 3.173 | 3.3248 | 3.835
SF5 | 2.14 | 4.0908 | 3.41 | 2.4867 | 0.86551 | 1.9157
SF4 | 3.1 | 3.6167 | 3.926 | 2.6178 | 1.708 | 3.2767
0.0200
0.0233
0.0267
0.0300
12
9
6
0.07
0.06
0.05
0.04
0.75
1.25
1.0
0.5
0.75
1
1.25
1.2
1.1
1.0

## Slide 5: Who are We
Foundry Technology & Engineering (FTE by Changhong Dai) is the engineering branch of Global External Manufacturing and Sourcing (GEMS by Hai Wang) under Stu Pann’s Corporate Planning Group (CPG)
FTE provides end to end engineering coverage and handshake to external suppliers from pathfinding to PRQ. Once PRQ’d, External Manufacturing & Production (EMP by Angelo Pinto, manufacturing branch of GEMS) will pickup the ownership for product delivery.
External technology team on disaggregated cache memories
  Pathfinding – DerChang Kau
  Platform – Mike Goldsmith
  Logic – Andy Wei
  Memory – Dany Ly-Gagnon
  Packaging – Jason Zhang
  Design – Ping Liu, Jiajing Wang