## Slide 1: From Graphic Memory (component) to Client Compute (system)
Mike & DerChang, WW16.2’22
Problem Statement – The flag and the hindsight
The Engagement – some good going but some not so successful
Dual Drive initiative – Client Compute
Call of Duty – Platform, Technology, Design & Packaging

## Slide 2: What is not Working
How it starts – Insufficient ADM capacity addressed by CapEx; cost doubles
The hindsight problem is package Integration – (our visibility of problem statement)
  Active Foveros: Large base die size with low utilization of high cost embedded active functionality
N6 vs. ADM |  |  |  |  |  | 
Component | Technology | Cell Size [µm2] | Die Size [mm2] | $/Wafer | Yield | Die Cost
BMG G10 448eu/512MB Q3’23 | P1222.61 (LRP’21) | 0.01458 | 366 | $ 8.0K | 77.3% | $ 69
 | P1222.61 (LRP’22) | 0.01458 | 366 | $16.6K | 77.3% | $143
 | TSMC N6 | 0.02736 | 274 | $10.5K | 82.5% | $ 62
Substrate
36µm µB FOV + 16nm SoC + ADM + MiM
GPU
GPU
GPU
GPU
Substrate
TSMC 6nm SoC
1. N6 for 16nm SOC + ADM
2. ODI-like for Foveros
Foveros base die
ADM: 100mm2
SOC: 100mm2
+ Interposer: 100mm2
Active FOV: $123 on 300mm2
Processing cost:
ADM: ¢15/mm2
Logic/SRAM: ¢25/mm2
+ Interposer: ¢ 1/mm2
Active Foveros: ¢41/mm2
Fan Out mold with Embedded SRAM
SRAM: 100mm2
LOGIC: 100mm2
+ ___ Interposer: 100mm2
Fan Out mold : $51 on 300mm2
+ Emb. Chiplet

## Slide 3: Update to GEMS-SOTU
P1222.61/P1222.7 dual-drive initiative: Alternative SOC + HD SRAM + 3DIC technology
  TSMC N6 with ODI-like packaging is pursued due to 3Cs’ superiority
  Evaluating Samsung 5LPP as a strategic maneuver
Kick-off sessions with product owners and memory architects from AxG and CCG.
  Gen 1 dual-drive is deemed too late to be cost-effective for 2023 PRQ intercept
  Both teams seem understanding foundry capability but SoA packaging ignorant Team PTL/NVL actively seek for dual-drive solutions for eRAM/packaging alternatives but do not have resources to commit to supporting dual drive initiative.
Expected to close go-nogo Task Force by mid Q2
  Feasibility deep dive, managing risks and developing dual-drive strategy for 2024+ intercept
This engagement leads a path to compute memory scaling and disaggregation strategy development for 3nm and beyond.

## Slide 5: Estimate Die layouts (per Brian 04/11 ’22)
P1222 Interposer
GPU N3E 8.1x7.7
CPU 18A 8.1x10.6
SOC N6 12.9x4.1
A
A’
B
B’
A
A’
GPU N3E
P1222 Interposer
B
B’
SOC N6
CPU 18A
P1222 Interposer
CPU 18A
PTL-M
~18.5
~12.4
P1222 Interposer
(PLT-M)
P1222 Interposer
P1222 Interposer
P1222 Interposer
Reticle
26mm
33mm
Full-Si Interposer has low LFU on p1222; PX+ exceeds reticle
P1222 Interposer
GPU N3E ~12.1x8.3
CPU 18A 8.1x24.9
SOC N6 17.2x4.1
PTL-PX/PX+
~33
~12.4
PX+: GPU N3E ~12.1x14.9

## Slide 6: Call of Duty – Dual Drive for CCG 2024~2025
Dual Drive Initiative 1: N6 SRAM for ADM
Dual Drive Initiative 2: ODI-like OSAT 3C for Foveros
Dual Drive Initiative 3: DTC (and beyond) for MiM

## Slide 7: InFO-LSI Mockup Flow
N6 Memory
Bridge
GPU N3E
CPU 18A
SOC N6
A
A’
B
B’
A
A’
SOC N6
GPU N3E
DTC
DTC
Bridge
N6 SRAM
B
B’
SOC N6
CPU 18A
DTC
N6 SRAM
N6 SOC
DTC
N6 SOC
DTC
WoW
10 µm
HB
N3E GPU
DTC
N3E GPU
DTC
WoW
10 µm
HB
18A CPU
Carrier Prep
Die Reconst.
Em. Chiplets Attachment
N6 SRAM
Bridge
RDL, Cu Pillar Platting
Mold, RDL, Bumping
C4
1
2
3
4
5
6
25µm µB
80µm C4
25µm µB

## Slide 8: FO-EB-T Mockup Flow
N3E GPU
DTC
N3E GPU
DTC
18A CPU
Carrier Prep
Top Die Attachment
Em. Chiplets Attachment
N6 SRAM
N6 SOC
Mold, RDL
RDL, Cu Pillar
C4
1
4
5
2
3
SOC N6 12.9x4.1
N6 Memory
GPU N3E
CPU 18A
A
A’
B
B’
A
A’
GPU N3E
DTC
N6 SOC
N6 SRAM
B
B’
GPU N3E
CPU 18A
DTC
SOC N6
Micro Bumping
WoW
10 µm HB
25µm µB
80µm C4
Top Carrier Bond,
Back Carrier Debond.
Bumping

## Slide 9: Packaging Flow Comparison
Carrier Prep
Die Reconst.
Em. Chiplets Attachment
RDL, Cu Pillar Platting
Mold, RDL, Bumping
C4
Carrier Prep
Top Die Attachment
Em. Chiplets Attachment
Mold, RDL
RDL,
Cu Pillar
C4
Micro Bumping
Top Carrier Bond,
Back Carrier Debond.
Bumping
Base wafer
TSV
Chiplets attachment
Interconnect,
µBump
Bumping
C4
Carrier bond, TSV Reveal
Passive Foveros: High cost process tools for TSV and Interconnect in Fab
Active Foveros: Large base die size with low utilization of high cost embedded active functionality
InFO-L: lowest cost of making but higher price judged due to SiFO vs. OSAT margin delta + chip first yield loss vulnerability
FO-EB-T: Cost of making slightly higher than InFO-L due to one additional wafer bonding and debonding processes.
Logic, SoC and/or ADM

## Slide 10: DTC vs. ISC

## Slide 11: De-cap flow options
Fab-Out
Sort
ow-SC or sc-MiM
Pad
Fab-Out
DTC, MiM, SC
Stacking
Sort
Wafer Start
DTC in FEOL
BEOL
Fab-Out
Wafer Start
FEOL
MiM in BEOL
Fab-Out
Substrate
Inteconnect + MiM or SC
Substrate +DTC
Inteconnect
Substrate
Inteconnect
Substrate + DTC
Inteconnect + MiM or SC

## Slide 12: Estimated Cost of making: MiM, Trench Cap, Stacked Cap
TSMC DTC
HB: based on 3DNAND -- $30
Grinding: $ ~50
TSV: ~$100
High dope CZ wafer: ~$100
DTC: ~¢10 per nF/mm2
Market Intelligence:
Graphcore price low $1000
Samsung ISC :
ECTC20
OSAT
SPIL QTR roadmap ’24
Supplier Engagement needed
On-Wafer ISC from Tier-1 DRAM suppliers
Tier-2 DRAM : Nanya, PSMC, Winbond
Staircase MiM 3D AND suppliers
Tier-1 NAND : Solidigm (NSG)
Tier-2 NAND: Macronix
Chart: Cost Adder vs Cap Density
| 22 | 44 | 42 | 140 | 350 | 700 | 1000
WOW-ISC | 750
Cap Density [nF/mm2]
Cost Adder [$/wfr]
BE-MIM
WoW DTC/ISC
On-Wafer ISC, Staircase MiM (idea stage)