## Slide 1: Intel-Samsung LPW Follow-up Meeting
DerChang Kau, Aug. 5, 2024
Will be discussed today
  Why are we interested
  What are our possible intercepts
Pending Samsung’s feedback, we plan to discuss
  What is the project status within Intel.
  Project timeline and sample requirements.

## Slide 2: Intel’s Interests in High Bandwidth In-Package Memory
HBM plays a crucial role in enhancing AI accelerators
PRO
  GB/Module: 3D stacking
  GB/s: Data Width
  pJ/b: Shortened data path due to 3D stacking and in-package memory integration.
CON
  $/GB: Shared Through-Silicon Vias (TSVs) footprint blows up chip size and reduces array efficiency
  $/Stack: Low utilization of the oversized active Si interposer subject to package technology.
  Thermal: Highest power consumer with worst thermal resistance.
  Scaling: Pre-defined interconnection with built-in TSVs also limit flexibility and scalability.
Interests
  Array efficiency on-par with mainstream DRAM (MB/mm2)
  Wider data width scalable to improve bandwidth/die (WIO)
  Simplified Phy connecting with host at short distance (LPDDR)
  Modular memory for 2.xD and 3D in-package integration with SoC (µBump module with pitch ≤ 40µm)

## Slide 3: Data Center GP-GPUs, Domain Specific Accelerators & AI-PC
Metric |  | 1H'27 | 2H'27 | 1H'28
Stack | # of die | 4~16 | 4~24 | 4~32
 | Capacity [GB] (DC-GPU’s interests) | 8~64 | 8~96 | 12~160
 |  | 100 | 100~150 | 150~200
 | Bandwidth [TB/s] | 0.8~2.6 | 0.8~3.2 | 1.2~3.8
Die | Capacity [Gb] | 16~32 | 16~32 | 24~40
 | Transfer Rate [GT/s] | 8~10 | 9.6~12.8 | 11.2~15
 | # of Channel (x64) | 2 | 2 | 2
 | Bandwidth [GB/s] | 120~160 | 150~200 | 180~240
 | Density[MB/mm2] | 60 | 65 | 70

## Slide 4: Topics of Interests
LPW Current offering
Standardization
Roadmap
Document and features
a. Capacity, BW, energy pareto, DQ, GT/s
b. Organization: Ch/Pseudo Ch/Sub Ch/DQ, BG/bank
c. Other terminology such as stack, slice, quadrant
d. Operations: Open/Close Core-timing
e. Power/Signaling
f. MBIST/Repair scheme
g. Physical dimension and pad map
h. Core frequency
i. (Re)Configurability
j. Interface: DQ/DQS, Clocking scheme, termination, CA
k. Burst Length
l. pad order
2. JESD like Spec file?
a. How Samsung see market demand
b. Standardization: do Samsung plan to bring LPW to JEDEC?
3. Roadmap 2027 and beyond