## Slide 1: HBM3 Organization (JEDEC Spec R.95)
Each stack of HBM die includes (equivalent to 1 Rank of DDR DIMM)
Global command for the stack (52 µbumps)
Upto 16 channels / device (stack); upto 1K DQ
Double data rate @ 4.8~6.4GT/s (2.4~3.2GHz)
Max BW = 819.2GB/s/stack
I/O voltage 1.1 V, Tx driver voltage 0.4 V
DRAM core voltage 1.1 V
Unterminated data/add/cmd/clk interfaces
Unmatched data interfaces
2b encoded temp sensor
not prohibiting manufacturer specifics such as
an optional interface die in the stack
Signal redistribution and other functions
52
HBM3
Channel0
Channelm
…
…
120
52
Bank
  Channeli
Bank
….
Bank
….
Bank
Bank is the lowest independently operable unit
DRAM core 250~400MHz (not scalable)
tCCD (CAS2CAS delay, b2b same bank): 2.5~4ns
Hynix Spec: Open page latency (tAA) = 48ns Close page latency (tRCD+tAA) = 31ns
Bank Group is supported for fast tCCDF)
Number of rows (pages) is part of HBM3 spec
C/A
Memory Mat
SA
Page
RAS
DQ + Metadata
CAS
Bank
SWD
CSL
Channels are full independent to each other
2~32Gb channel capacity [231~35b];
16, 32 or 48 banks per channel
64 DQ + ECC, SEV per channel. BL = 8 I/O (~90µbump) & ADD/CMD (~30µbmp)
2KB physical page [214b] 1KB addressable [213b], C[6:0]
BW = 38.4~51.2GB/s/Channel, Max BW density = 205GB/s/GB
Bank grouping supported for short tCCD
2 Pseudo Channel (PC) per Channel; PCs share C/A RAS/CAS for finer granularity to lower cost to scheduler.

## Slide 2: TCM 2Gb Macro Organization (Sep/2021 Rev 2)
Each Macro includes
2Gb / Macro
8 channels / macro;
4K DQ
Double data rate @ 250MT/s (125MHz)
BW=128GB/s/macro,
Interface physical and electrical tbd
Hynix and Intel build based die separately with additional RDL
52
2Gb Macro
Channel0
Channel7
…
…
yyy
xx
Bank4
  Channeli
Bank0
….
Bank3
….
Bank7
Bank is the lowest independently operable unit
Bank Capacity 32Mb (228b); 8K WL; R[12:0]
DRAM core frequency 250MHz
tCCD (CAS to CAS delay, b2b same bank): 4ns
Open page latency (tAA) = 15ns
Close page latency (tRCD+tAA) = 19.8ns
C/A
Memory Mat
SA
Page
RAS
DQ + Metadata
CAS
Bank
SWD
CSL
Channels are full independent to each other
256Mb per channel capacity [228b]
8 banks per channel B[2:0]
DQ=512 [29b] (HB required?)
½KB physical/addressable page [212b] C[3:0]
BW = 16GB/s/Channel
BW density = 512GB/s/GB
Bank grouping ?
Pseudo Channel?

## Slide 3: High Level Spec Comparison
 |  |  | LPDDR5 | HBM3 |  | 2Gb Macro
 | Technology Node | nm | Hynix 1z | Hynix 1z | JEDEC R.95 | TCD 1z (512)
Die, including JEDEC device / stacked-die | Capacity | Gb | 16 | 16 | 2~512 | 2
 | Footprint | mm2 | 60.72 | 115.06 | n/a | 16.07
 | Density | Mb/mm2 | 270 | 142 | n/a | 127
 | # of DQ / die | pins | 16 | 256 (1K allocated) | uptp 1024 | 4096
 | # of Channel /Die | # | 1 | 4 | upto 16 | 8
 | Transfer Rate | GTpS | 6.40 | 6.40 | 4.8~6.4 | 0.25
 | Bandwidth Density | GB/s/GB | 6.4 | 102 | max. 205 | 512
 | Latency (Close page) | ns | 40.00 | 48.00 |  | 19.80
 | Latency (Open page) | ns | 25.00 | 31.00 |  | 15.00
 | access latency / tCCD | ns | 2.50 | 2.50 | 2.5~4.0 | 4.00
Channel | Channel Capacity | Mb/Channel | 16384 | 4096 | 2K~32K | 256
 | DQ / Channel | pins | 16 | 64 | 64 | 512
 | # of Bank / Channel | Bank/Channel | 16 | 16 | 16, 32, 48 | 8
 | BW/Channel | GB/s/Channel | 12.8 | 51.2 | 38.4~51.2 | 16
Bank, Partition | Bank Capacity | Mb/Bank | 1024 | 256 | see spec | 32
 | # of col of Mat/Tile (GBL) | n | 16 | 16 | n/s | 8
 | # of Row of Mat/Tile (GWL) | n | 64 | 32 | n/s | 16
 | Physical Page Size | bits | 16384 | 16384 | 16384 | 4096
Mat, Tile | Array Capacity | Mb/Array | 1.00 | 1.00 | n/s | 0.250
 | # of BL | Col | 1024 | 1024 | n/s | 512
 | # of WL | row | 1024 | 1024 | n/s | 512

## Slide 4: High Level Spec Comparison (2)
 |  |  | LPDDR5 |  | HBM2 | HBM3 |  | 2Gb Macro | AP HVM
 | Technology Node | nm | Hynix 1z | Apple M1 Pro | Hynix 1z | Hynix 1z | JEDEC R.95 | TCD 1z (512) | 2y
Die, including JEDEC device / stacked-die | Capacity | Gb | 16 | 64, 128 | 16 | 16 | 2~512 | 2 | 32
 | Footprint | mm2 | 60.72 |  | 104.17 | 115.06 | n/a | 16.07 | 220-320
 | Density | Mb/mm2 | 270 |  | 157 | 142 | n/a | 127 | 100~150
 | # of DQ / die | pins | 16 | 128 | 128 (1K/stack) | 256 (1K/stack) | uptp 1024 | 4096 | 10K
 | # of Channel /Die | # | 1 | 8 | 8 | 4 | upto 16 | 8 | 
 | Transfer Rate | GTpS | 6.40 | 6.4 | 03.20 | 6.40 | 4.8~6.4 | 0.25 | 3.20
 | Bandwidth Density | GB/s/GB | 6.4 | 12.8~6.4 | 51.2 | 102 | max. 205 | 512 | 1024
 | Latency (Close page) | ns | 40.00 |  |  | 48.00 |  | 19.80 | 
 | Latency (Open page) | ns | 25.00 |  |  | 31.00 |  | 15.00 | 
 | access latency / tCCD | ns | 2.50 |  |  | 2.50 | 2.5~4.0 | 4.00 | 
Channel | Channel Capacity | Mb/Channel | 16384 | 8192,16384 |  | 4096 | 2K~32K | 256 | 
 | DQ / Channel | pins | 16 | 16 |  | 64 | 64 | 512 | 
 | # of Bank / Channel | Bank/Channel | 16 |  |  | 16 | 16, 32, 48 | 8 | 
 | BW/Channel | GB/s/Channel | 12.8 |  |  | 51.2 | 38.4~51.2 | 16 | 
Bank, Partition | Bank Capacity | Mb/Bank | 1024 |  |  | 256 | see spec | 32 | 
 | # of col of Mat/Tile (GBL) | n | 16 |  |  | 16 | n/s | 8 | 
 | # of Row of Mat/Tile (GWL) | n | 64 |  |  | 32 | n/s | 16 | 
 | Physical Page Size | bits | 16384 |  |  | 16384 | 16384 | 4096 | 
Mat, Tile | Array Capacity | Mb/Array | 1.00 |  |  | 1.00 | n/s | 0.250 | 
 | # of BL | Col | 1024 |  |  | 1024 | n/s | 512 | 
 | # of WL | row | 1024 |  |  | 1024 | n/s | 512 | 

## Slide 5: High Level Spec Comparison (2)
 |  | LPDDR5 |  | HBM2 | HBM3 | 2Gb Macro | AP HVM
Technology Node | nm | Hynix 1z | Apple M1x | Hynix 1z | Hynix 1z | TCD 1z (512) | 2y
Pricing estimate | $/Gb | .50 | .50 | 2.00 | 2.00 |  | 
Component Unit |  | Die | Package | Package | Package | Macro | Macro
Capacity / Component | Gb | 16 | 64 | 64 | 64 | 2 | 32
Footprint | mm2 | 60.72 |  | 104.17 | 115.06 | 16.07 | 220-320
Density | Mb/mm2 | 270 |  | 157 | 142 | 127 | 100~150
# of DQ / component | pins | 16 | 128 | 1024 | 1024 | 4096 | 10K
# of Channel / component | # | 1 | 8 | 32 | 16 | 8 | 
Transfer Rate | GTpS | 6.40 | 6.4 | 3.2 | 6.40 | 0.25 | 3.20
Bandwidth | GB/s | 12.8 | 102.2 | 409.6 | 819.2 | 128 | 
Bandwidth Density | GB/s/GB | 6.4 | 12.8 | 51.2 | 102.4 | 512 | 1024
Normalized Bandwidth/$ | Ref. LPDDR5 | 1 | 2 | 2 | 4 |  | 
Channel Capacity | Gb/Channel | 16 | 8 | 2 | 4 | 1/4 | 
DQ / Channel | pins | 16 | 16 | 32 | 64 | 512 | 

## Slide 6: Compute Memory Disaggregation
Host
Memory Farm
Channel0
Channeln-1
…
…
Logic
Bank1
Channeli
Bank0
….
Bankm-2
….
Bankm-1
Logic
Mat
Decoder / Driver
SA / Data Latch
TFT channel planar / nonplanar XTOR
2T [independent read write] Option
Si channel planar / nonplanar XTOR
MRAM [STT/SOT]
Nanostructure change
High-k Capacitor
Ferro-capacitor
Access Device
Memory Element
Resistance Change ReRAM[1D, 2D], PCM [3D]
Ferroelectrics
Magnetic
[MRAM, STT(SOT)MRAM]
Volatile filament
Ovonic Threshold
Thermionic
[diode, MIEC, ..]
Metal-Insulator Transition
Access Device
Memory Element
Logic and Mix Signal
Mix Signal
Memory Specific
C/A
Memory Mat
SA
Page
RAS
DQ + Metadata
CAS
Bankj
SWD
CSL

## Slide 7: 3DXP Component Organization
Die size = 200mm2
Shaded area is global ~ 17mm2
4KTiles (64K Patches) occupy ~155mm2
Routing takes ~20mm2
Command /
Data
Interface
State Machine
(Instruction)
Data Buffer
Address Tag
Global MUX
Analog / control
Array
64Mb/tile
4X4 Patches/Tile
Patch footprint is ~[50µm]2
@ 41P node
Local MUX
Read / Write
1K/Patch
On Pitch Via
32/Patch
64/Patch
LVT
Mixed
HVT
64/Patch
HiZ Path
LoZ Path
1/Tile

## Slide 8: Memory and Array Core
Decoder/ Driver
Memory Mat
X, X-Y or X-Y-Z
Termination and Socket included
SA/Latch
Page Buffer
Control/decode
DQ
Mat
Decoder / Driver
SA / Data Latch
TFT channel planar / nonplanar XTOR
2T [independent read write] Option
Si channel planar / nonplanar XTOR
MRAM [STT/SOT]
Nanostructure change
High-k Capacitor
Ferro-capacitor
Access Device
Memory Element
Resistance Change ReRAM[1D, 2D], PCM [3D]
Ferroelectrics
Magnetic
[MRAM, STT(SOT)MRAM]
Volatile filament
Ovonic Threshold
Thermionic
[diode, MIEC, ..]
Metal-Insulator Transition
Access Device
Memory Element
Logic and Mix Signal
Mix Signal
Memory Specific

## Slide 9: Compute Memory Disaggregation
Host
Memory Farm
Channel
Channel
…
…
Logic
Bank
Channel
Bank
….
Bank
….
Bank
Logic
Bank
Mat
….
Mat
Mat
….
Mat
…
…
Logic and Mix Signal

## Slide 10
Mat

## Slide 11: 3DXP 3DIC Strategy
3DXP Team 3DIC
WW47.3

## Slide 12: P1240/ALF32 Decoder
NDIFF & PDIFF
One Tile of 3DXP
16k Sel. + 16k Desel. Per tile
4096 tiles/die.
130mm2 area for decoders

## Slide 15: Problem Statement and Solution Space Scope
Decoder Scaling becomes cost inhibitive or performance inhibitive
Solution Spaces
  Si Bulk CMOS augmentation – Trench, FinFET, SOI
  3D Integrated circuits – monolithic 3D, stacked 3D, wide EG FET
Key questions to guide 3DIC strategy development
  Which function block can be replaced by thin film transistor.
  What is circuit connectivity between bulk and thin-film devices.
  Seeking for modular strategy enabling density and performance scaling roadmap.

## Slide 16
NDIFF & PDIFF
AM1 & AM23
A_TILE

## Slide 17
NDIFF & PDIFF
LVID
A_TILE

## Slide 18: HVT Success Criteria
The goal is to meet or exceed ALF HVT device target spec
Electrical
  NMOS: Idsat ~500uA/um & Ioff ~10pA/um at L=350nm
  PMOS: Idsat ~ 300uA/um & Ioff ~ 1nA/um at L=350nm
Reliability (7-year AC lifetime)
  TDDB (5.3V stress): <100x increase in gate leakage at 5.57V
  BTI (5.3V stress): 10% Idsat degradation at Vd=Vg=5.1V
  CHC (WC stress): 10% Idsat degradation at Vd=Vg=5.1V

## Slide 20: Modularity
3DIC
  Monolithic √
  Stacked
Monolithic
  Gate oxide division
  Function block division
  HVT Type √

## Slide 21: Modularity for 3DIC
Replacement strategy – Which potion of HVT can be replaced by thin film transistor: all, Mux only, or local Mux only
Vertical placement – What is connectivity from circuit in substrate to circuit in thin film: below M1 or below M4 or other multilevel interconnect scheme.
Modularity for scaling such as wafer stacking feasibility
LV / HV MOS
M1
M2
M3
M4
Array
TM
LV
M1
M2
M3
M4
Array
TM
HVT
LV / HV
M1
M2
M?
M4
Array
TM
MUX
M?
Command /
Data
Interface
State Machine
(Instruction)
Data Buffer
Address Tag
Global MUX
Analog / control
Array
64Mb/tile
4X4 Patches/Tile
Patch footprint is ~[50µm]2
@ 41P node
Local MUX
Read / Write
1K/Patch
On Pitch Via
32/Patch
64/Patch
LVT
Mixed
HVT
64/Patch
HiZ Path
LoZ Path
1/Tile

## Slide 22: ATF HIGH LEVEL FLOOR PLAN
Intel Confidential
IO
PERIPHERY
PART 0
PART 31
Tile 0
Tile 127
LWLs/LWLd/PCL CTRL DRVRS
GWLS DRVR/TERM CAPS
Tile Circuits: Decoders, VDM source followers, current mirrors, sense amp, mask logic, ..
Partition Circuits: Address drivers, PCL, VDM_DAC, iREF_DAC
PERIPHERY CIRCUITS: PL, Fuses, redundancy matching, HV regulators,..
IO CIRCUITS: PADS, Tx, Rx, DLL,..
GBLS DRVR/TERM ANALOG
PCL/LBLS & LBLd DRVRS
Not all of this termination edge fits under the array

## Slide 23
NDIFF & PDIFF
LVID
A_TILE

## Slide 24: BLOCK DIAGRAM
IO (PADs, Tx, Rx, DLL,..)
Periphery Logic
( Command processor, SIPO, PISO,.. )
HV ( Fuses, redundancy matching, regulators )
Address Drivers
(GBL, LBL, GWL, LWL)
Partition Control Logic
(Read/Write algo u-controller)
Partition Analog
( VDM_DAC, iREF_DAC,…)
BL Tile Circuits
( BL Voltage mux, Mask Logic, Sense Amp)
WL Tile Circuits
( WL VDM, Mask Logic, Current Mirrors, Spike mit)
Global Column mux
Local Column mux
Local Row mux
Global Row mux
axn
hnreg
32 Global Selects
1 Global deselect
32 Local Selects
16 Local deselects
32 Local Selects
16 Local deselects
32 Global Selects
1 Global deselect
IO/Periphery
Tile x128 per partition
Partition x32
Global/Local mux’s x8 per tile
1024 LBL’s
1024 LWL’s
32 GBL’s
32 GWL’s
LV + HV
LV + HV
LV + HV
HV

## Slide 25: Monolithic thin film transistor topology
G
S
D
G
S
D
S
D
S
D
G
S
D
Front Gate
Back Gate
Hybrid
Flip Front Gate
Back Gate II

## Slide 26: Modularity
3DIC
  Monolithic √
  Stacked
Monolithic
  Gate oxide division
  Function block division
  HVT Type √

## Slide 27: Design Rules for SXP 3DIC
Follow design rules for ALF CMOS for lower and upper deck CMOS.
  Upper deck HV only.
  Lower Deck HV + LV.
Map metal design rules as shown in the figure.
Introduce new con2/v3 rules
  Con2 => same rules as CON, except interacts with upper deck CMOS ONLY. Connects upper decks Diffusion/poly to M4.
  Via3 connect M3 directly to M4.
    Via3 Size: 2x2, Space 3.0
    M3 overlap of V3 1.0.
    M4 coverage of V3: 0.50
    Via3 Space to upper deck Diff/Poly 2.0.

## Slide 28: Backup Materials

## Slide 29: Idle

## Slide 30: Read Algo SL SG SP
Does this work?