## Slide 1: TMC bests q2’24 goal: > 25% lower Cost
64GB TMC mockup (16x 32Gb stack) – 45% lower cost
30% lower $/bit
  No TSV in DRAM process (12% wafer cost saving)
  22% higher density
  Smaller die, higher yield
Base die eliminations (~$20, 10% saving)
Higher packaging cost (larger module size, more chips, $3~$12, 2~5% adder)
Better packaging yield (~8% saving)
PAT | GB | Size [mm2] | Cost | GB/s | $/GB | ¢/(GB/s) | Node | Density [Gb] | # Pile | Stack Height | # Die
3DS HBM4+ | 64 | 14.5x11.0 | $280.95 | 3276.8 | $4.39 | ¢8.57 | 1c | 32 | 1 | 17 | 17
TMC LPW6 | 64 | 14.9x10.5 | $156.35 | 3276.8 | $2.44 | ¢4.77 | 1c | 32 | 1 | 16 | 16
TMC LPW6 | 64 | 12.1x21.0 | $137.02 | 3276.8 | $2.14 | ¢4.18 | 1c | 32 | 2 | 8 | 16
TMC LPW6 | 64 | 12.5x22.0 | $123.30 | 6553.6 | $1.93 | ¢1.88 | 1c | 16 | 4 | 8 | 32
All mockups are superior to HBM4+
With yield loss reduction at ½ stack height and ½ of die density, 16GB component (8x 16Gb stack) is the most optimal built on density and cost
> 50% lower cost

## Slide 2: Terraced Memory Cube (TMC) Focus Team – Phase II
1. Ideation 2. Vetting 3. PoC 4. Definition 5. Change Control
7/11/2024
Rev 1.0
July’24 to September’24
On-Board memory modules such as xDIMM and LPx are reaching scaling limit. In-package memory (IPM) enables bandwidth improvement while boosting capacity growth. SoA IPMs include LPx-MoP and HBM as well as custom eDRAM from Intel, APM, PSMC, SEC and SKH as well as many proprietary memory technology R&D.
The Objective of this project is to define and to deliver IPM solutions for ’27 product and roadmap intercept to displace HBMx by exploiting mainstream DRAM technology and collaborating with tier-1 OSAT to deliver a low-cost low-power high-availability 3D packaged memory subsystem with bandwidth on par with HBMx.
Charter Group: FTE and MIO
Sponsors: Changhong Dai and Dimi Ziakas
Stakeholders: Percy Soto, Victor Cho, Mimi Ocampo, Prashant Damle, Long Wang & Srini Rajagopalan
Customer: (to be finalized) Accelerator: Rajat Agarwal Cloud: Jim Mccall, Muntaquim Chowdhury Client: Konika Ganguly, Chris Mozak
Suppliers: (wip) OSAT: Debendra Mallik (ATTD), 'Cool Creek' (ASE) LPW: Saemi Song (SEC), (SKH), (MU)
“Technology-driven disruption” to displace incumbent
“Market creation disruption” as a potential compute memory hierarchy redefinition as in AI (Client to Cloud)
Scope and Plan | 
Problem Statement | HBM’s low silicon utilization on all layers of DRAM chips due to shared TSV and low-density logic circuits in base die as a high-cost interposer. MoP formfactor constraint due to WB footprint scalability and # DQ as well as long trace length and variability impose data transfer limit in BW and power.
Key Results | TCC package MTS, DTS and thermal characteristics for Rev 1 package PDK R0.1 TMC-LPW Package Reference Design Rev 1.0 for TM-TV and IC-TV PoC validation
Team and Expertise | Team members’ disicipline covers MT, design enabling, DRAM & system. FT sizes of 4~8 persons at Idea vetting stage
Strategy | Critical Path and fast fail: package mechanical/thermal/electrical characteristics on par or better than HBM4+ as a scalable solutions to co-define and to deliver HBMi datasheet for product plan'27 and beyond
Logistics and Funding needs | Force team technical repository share point: TMC Weekly meeting: Thursday 8-9am cal time zone.
Decision Process | Consensus within FT before Sponsors’ final ratification.
Feedback Plan Communication | Weekly FT mission-oriented meeting for technical feedback and alignment. Monthly Ops review to solicitate from and to align with Customers and stakeholders Ad hoc process-oriented meeting with sponsors for status update the ratification.
Guard Rail | These are constraints or expected conditions that should be met in project execution. Calling out assumptions and boundary conditions explicitly to prevent scope creep.
Sunset Clause & Sunset Plan | When graduate, (passing gate level, meeting success criteria), team will move on to PoC package design to validate technology scaling capability and technology line of sight limitation as well as and seek for the BU endorsement for LRP @ 2027. Or else, revisit landing and project direction for sunset postmortem..

## Slide 3: Terraced Memory Cube (TMC) for xDIMM/xCAMM/HBM displacement
Assumptions:
Node: Micron D1ß
LPW Array Efficiency based on SEC D1a LPW
DDR
10mm or less of DQ trace length between TMC module and compute chiplet  0.5pJ/bit
Pact [nm] | PWL [nm] | PBL [nm] | Cell Size [nm2]
24 | 34 | 39 | 1330
Type | capacity [Gb] | die size [mm2] | pJ/b | DQ | GT/s
HBM3E | 24 | 100 | 3.70 | 128 | 9.2
TMC-LPW | 24 | 66 | 0.5 | 128 | 7.6
LP5 | 16 | 37 | 5 | 16 | 8.4
TMC-LP5 | 16 | 37 | 0.5 | 16 | 9.2

## Slide 4: Critical Path (Fast Fail)
2024: Ideation/Vetting concluded, meeting manufacturing 3Cs with DRAM/OSAT collaborator id’d
TMC Rev 1 flow and costing completed
  Line of sight technology feasibility with ¾ cost @ iso performance
TMC process flow and capability meeting performance and scalability success criteria
  HBM CoW package is the baseline
  OSAT short lists
  Cubing module OSAT supplier selected for TM-TV Tapeout
Package Module Electrical, Mechanical and Thermal assessed, defined to support 'HBM’ datasheet
  Memory Supplier engagement starts
2025: TM-TV and IC-TV Tapeout, PoC validated
TM-TV assessment meet success criteria
  Memory cubing module supplier selected for IC-TV Tapeout
Technology performance and reliability assessed using IC-TV
'27 Product PrePOR success criteria established for HBM4E replacement
  Test Chip planned starts (C-Spec, T-Spec, do we need MAS equivalent?)
‘TMC-LPW6’ spec & roadmap aligned; secure pre-POR position
2026: TMC at HBM4+ class demonstrated
Product intercept decision made
 | Q2'24 | Q3'24 | Q4'24~Q1'25
Objectives | TMC Process flow develop, cost | MTS and DTS covering Process, Electrical and Thermal characteristics, PDK Rev0.1 | TM-TV Tapeout
Tech Gate | Technology feasible Cost Lower than HBM | Mockup datasheet on par with HBM | MTS committed by OSAT

## Slide 5: Team TMC Chair: DerChang Kau
Technology and Design Enablement
CC Kuo, TMC-TSV Architect
  Module Target Spec, Design Rule and OSAT Engagement
Xiang Li, TMC-MWI Architect
  Process Flow Exploration
Po Yao Lin, 3D Physical and Thermal Model
  Thermal Spec
Po Yao Ke, PDK
  Device Target Spec, PI/SI
Product Architecture & Definition
Xiang Li, memory product alignment
  TMC package definition
  Product alignment and planning
DerChang Kau, DRAM supplier engagement
  acting
  work with Percy Soto and Mimi Ocampo
  Prepare SEC/SKH/MU LPW alignment for LP6
Accelerator: (Xiang to connect)
Cloud: (Xiang to connect)
Client: (Xiang to connect)

## Slide 6: Supporting Material

## Slide 7
Scope and Plan | 
Problem Statement | Defines the problem/opportunity the project is addressing.
Key Results | Measure what matters; necessary and sufficient quantifiable metric; Stretched yet realistic time-bounded measurables (S.M.A.R.T)
Team and Expertise | Chair, Coach, team members and coverage Team category: TF: 4~6. FT: 8~10 WG: 12~15, JET: <20
Strategy | High level Planning to achieve objectives
Logistics and Funding needs | Including meeting schedule, share point and other expenses to project execution, such as hardware, software, IP, license, tests, EFA/PFA, labs, tapeout, silicon.
Decision Process | The process used within the team to make decisions. This can be either: consensus, consultative, voting, or authoritative.
Feedback Plan Communication | To communicate to the ecosystem, with the team’s activities to ensure continual buy-in or forking to appropriate direction.
Guard Rail | These are constraints or expected conditions that should be met in project execution. Calling out assumptions and boundary conditions explicitly to prevent scope creep.
Sunset Clause & Sunset Plan | The completion point such as date and goal achieved to end the project Upon the completion and objectives met, describes what, when, where, and how to step up, down, change direction or terminate.

## Slide 9
Objective: Actionable, Significant, Inspirational, Concete |  |  | Key Results: Specific, Measurable, Attainable, Relevant, Time-bound |  |  |  | 
# | Objective | Eco System | # | Milestone | # | As Measured by | ECD
1 |  | – Chartering Group: team accountable for results – Sponsor: Typically the leader of chartering team – Customer: Recipients of the project outcome – Stakeholders: affect or affected by the projects. – Other dependency/support for execution | 1 |  | 1 |  | 
 |  |  |  |  | 2 |  | 
 |  |  | 2 |  | 1 |  | 
 |  |  | 3 |  | 1 |  | 
2 |  |  | 1 |  | 1 |  | 
 |  |  |  |  | 2 |  | 

## Slide 10: TMC bests q2’24 goal: > 25% lower Cost
64GB TMC mockup (16x 32Gb stack) – 45% lower cost
30% lower $/bit
  No TSV in DRAM process (12% wafer cost saving)
  22% higher density
  Smaller die, higher yield
Base die eliminations (~$20, 10% saving)
Higher packaging cost (larger module size, more chips, $3~$12, 2~5% adder)
Better packaging yield (~8% saving)
PAT | GB | Size [mm2] | Cost | GB/s | $/GB | ¢/(GB/s) | Node | Density [Gb] | # Pile | Stack Height | # Die | Aggregate Si Cost | PAT Cost | Assembly Yield | Density [MB/mm2] | BW Density [(GB/s)/mm2]
3DS HBM4+ | 64 | 14.5x11.0 | $280.95 | 3276.8 | $4.39 | ¢8.57 | 1c | 32 | 1 | 17 | 17 | $174.13 | $25.16 | 70.9% | 39.8 | 20.54
TMC LPW6 | 64 | 14.9x10.5 | $156.35 | 3276.8 | $2.44 | ¢4.77 | 1c | 32 | 1 | 16 | 16 | $92.41 | $27.67 | 76.8% | 55.4 | 20.89
TMC LPW6 | 64 | 12.1x21.0 | $137.02 | 3276.8 | $2.14 | ¢4.18 | 1c | 32 | 2 | 8 | 16 | $92.41 | $27.67 | 87.6% | 55.4 | 12.94
TMC LPW6 | 64 | 12.5x22.0 | $123.30 | 6553.6 | $1.93 | ¢1.88 | 1c | 16 | 4 | 8 | 32 | $89.05 | $27.67 | 94.7% | 52.5 | 23.91
TMC LPW6 | 32 | 12.1x10.5 | $68.51 | 1638.4 | $2.14 | ¢4.18 | 1c | 32 | 1 | 8 | 8 | $46.20 | $13.84 | 87.6% | 55.4 | 12.94
TMC LPW6 | 32 | 12.5x11.0 | $61.65 | 3276.8 | $1.93 | ¢1.88 | 1c | 16 | 2 | 8 | 16 | $44.52 | $13.84 | 94.7% | 52.5 | 23.91
TMC LPW6 | 16 | 12.5x5.5 | $30.82 | 1638.4 | $1.93 | ¢1.88 | 1c | 16 | 1 | 8 | 8 | $22.26 | $6.92 | 94.7% | 52.5 | 23.91
All mockups are superior to HBM4+
With yield loss reduction at ½ stack height and ½ of die density, 16GB component (8x 16Gb stack) is the most optimal built on density and cost