## Slide 1: Predictive (Pre-PDK) DTCO / STCO
Angada Sachid
Contributions from and Discussions with:
Jeff Watt, Derchang Kau, Prashant Majhi, Klaus Schruefer, Per Sverdrup, Mike Goldsmith, Wenjie Jiang, Sarita Thakar, Chung-Ching Peng, Sourav Chakravarti

## Slide 2: Predictive DTCO for N2/N3E
Opportunities at N3E / N2
  Achieve better PPA via fine-tuning technology/architecture choices (eg. metal RC, standard cell architecture)
  Considering TSMC PDK release schedule, need to focus on key areas
Wider impact for future nodes (N+2 and beyond) by early engagement with external foundries
  Opportunity to define the technology considering monolithic and 3DIC landscape
    Logic and memory heterogeneity; New device architectures like NSFET / CFET
  ~24 months before V0.1 PDK release date

## Slide 3: N2 Engagement
Deliver a mini-standard cell library for early pathfinding
Capable of generating L1 FOM (small-circuit PPA)
Timeline: Before N2 V0.1 PDK is released (22/Q1)
Milestone | Contributors | Start | Due By | Difficulty | Dependency | Status
Design and Technology Rules | Klaus, Angada | 02/07 | 02/18 | Low |  | Ongoing
Compact Model | Atul | 02/14 | 03/18 | Medium |  | 
ITF, nxtgrd and TLUplus | Angada | 02/14 | 03/11 | High | Design Rules | 
SLiC Evaluation | Eva, Angada | 02/28 | 03/31 | Low | Engagement docs | 
Standard Cell Layouts | Eva, Angada | 03/01 | 03/25 | Medium | SLiC Eval | 
Standard Cell Characterization | Wenjie’s Team | 03/14 | 04/01 | High | Layouts; ITF, nxtgrd… | 
Calibration against Field Solver | Angada | 04/04 | 05/30 | V. High |  | 
Very aggressive schedule
Overlaps with capability building
Requires meticulous planning and flawless execution to complete
Discussions: Derchang, Srini, Sourav, Jeff

## Slide 4: Foundry Engagement Workflow
Nodes (N, N-1, N-2 …)
Analyze Trends
FEOL, BEOL etc
Build Parallel PDK
Match w/ Foundry PDK
Extrapolate to N+1, N+2 ...
Analyze different tech options
Generate PPAC Metrics
Foundry N+1 V0.1 PDK
Foundry N+1 V0.01 PDK
FTiP-Foundry Engagement
Generate PPAC Metrics
Continuous Engagement with FTiD
Tech choices; Design Rules; Std. Cell Layouts; Architecture; Methodologies …
Engagement with Intel Product Teams
Product PPAC requirements
GAA, BS-PDN, BPR, 3DIC, Std. Cell Arch…
Build Parallel PDK
Benchmark circuits / designs
Validates the methodology

## Slide 5: Predictive DTCO: High-Level View
Design Rules
Compact Models
Ab-initio Simulations
Material Parameters
TCAD Models
Device Performance
Lithography Simulation
OPC Models
Process Integration
Small Circuit PPA
Std Cell Layouts
PDK Generation
Synthesis
PnR
RC Extraction
STA
DRC, LVS
IR Drop, ECO
Block-Level PPA
L0 FoM
L1 FoM
L2 FoM
CM can be extrapolated from previous models
N3E/N2 Engagement
N+2 Engagement

## Slide 6: Predictive DTCO Methodology : Detailed View
Building 4 separate flows
Gives insights into relative performance and area changes due to changes in standard cells
High risk
Process Models
Calibrated Process Models
Process Conditions
Process Simulation
Device Simulation
Measured Device Data
Electrical Calibration
Measured Process Data
Compact Model
Ab-initio Models
Technology File (.tf)
Synthesis
Floorplan
PnR, CTS
RC Extraction
STA
DRC, LVS
IR Drop, ECO
Block-Level PPA
Block-Level RTL
PDK
Process Emulation
Lithography Simulations
Design Rule Manual
Std Cells, Layouts
Characterize Std Cells (.lib)
Process Emulation
Parasitic RC Extraction
Small Circuit PPA
Process Emulation; RC Extraction
Gen itf, nxtgrd, tluplus
Doping, Etch Profile
Material properties etc
I-V, C-V etc
BSIM, PSP
.tdr
.tdr
.tbson
.csv, .xlsx
.gds
..xlsx, .pptx
.tbson
.tdr, . spi
.csv
.tbson
.tdr, . spi
.v, .vhdl
SProcess
SDevice
ICCAP, Mystic
MDLx
SLiC
SiliconSmart, StarRC, Hspice
SLitho
SPX, Coventor
SPX, Coventor
Raphael FX
Hspice
SPX, Raphael FX
StarRC
DC, ICC2, PT, PP, StarRC
VASP, Quantum ATK
SProcess Advanced Calibration
SProcess
L0 FoM
L1 FoM
L2 FoM
Critical Path

## Slide 7: Objectives and Key Results for 2022
Objective | Key Result | Dependency | Quarter
Build Predictive DTCO Flow for CMOS Logic | 1. Assess small-circuit PPA due to material and process changes in MOL and BEOL materials and processes (L1 PPA) | Set up license infrastructure | Q2
 | 2. Assess small-circuit PPA due to circuit-level changes (eg. Standard cell architecture / layout / circuit, fan out, Vdd, interconnect length etc) (L1 PPA) | SLiC evaluation complete by Q1 Hire 2 TCAD engineers by Q2.1 | Q2
 | 3. Capable of generating PDK collateral | Hire 1 Phy Des Engg by Q1.3 | Q3
 | 4. Assess block-level PPA due to material, process, circuit-level changes (L2 PPA) |  | Q3
 | 5. Assess device-level (transistor) due to material and process changes (L0 PPA) |  | Q3
 | 6. Provide 3 methods to improve PPA 5% |  | Q4
Build Predictive DTCO Flow for SRAM | 1. Assess bit-cell level PPA due to material and process changes in MOL and BEOL materials | Hire 2 TCAD engineers by Q2.3 | Q3
 | 2. Assess array-level PPA due to material and process changes in MOL and BEOL materials |  | Q3
 | 3. Assess bit-cell and array-level PPA due to material and process changes in FEOL changes |  | Q4
 | 4. Assess bit-cell and array-level PPA due to layout changes |  | Q4
 | 5. Provide 3 PPA optimization options considering logic and memory heterogeniety |  | Q4

## Slide 9: Cycle Time
Topic | Description | Phase 1 Target | Phase 2 Target
L2 FOM: Block-Level PPA | Complete RTL2GDS runs to generate block-level PPA metrics (assumes all collateral is present) Phase 1: POR APR methodology Phase 2: AI/ML-enabled APR | Few weeks | TBD
L2 PDK Collateral | ITF, TLUplus, TF, DRC / LVS decks, lib/db (assumes standard cell layouts are present) | 2 weeks | 1 week (enabled through automation)
L1 FOM: Small circuit PPA | Involves generating layouts, 3D structures, parasitic RC extraction and SPICE simulations Phase 2 & 3: Possible enablement through fast RC extraction | 4 hours / run (depends on the circuit) 1 week / per DOE set (25 experiments) | Phase 2: 2 hours / run Phase 3: 1 hour / run (by reducing run time for RC extraction)
Collateral: Standard Cells Layout | Type 1 1: <10 layouts (manual) Type 2: 100-300 standard cell layouts | 3 days (Type 1) | 3–5 days (Type 2) – enabled by automated layout tools
Collateral: Compact Model Generation | Compact model generation from simulation or experimental data | 2 weeks + initial setup time (for N&P – single VTH) | 2 weeks + initial setup time (for N & P for 4 VTH types – enabled by automation)
L0 FOM: Device-Level PPA | TCAD based device PPA exploration | 2 weeks for DOE + initial setup time | ---