## Slide 1: 3D XPoint™ Technology Competitive Landscape
Al Fazio
April 2020

## Slide 2: Executive Summary
Past conversations with Execs/BOD Members…
  Q: How much of a lead do you think you have?
  A: 18-36 Months … 18 Month = window which customers tell us being sampled by other suppliers; 36 Months = Competitor should be able to copy – e.g. our logic lead was never >3 year
Today: 5 yr post Tech intro; 3 yr post 1st commercial available systems…We should expect competition.
  MU (access to same technology) in early sampling phase of 1st SSD (FPGA based)
  @ end of JDP (2018), MU favored self select memory (BiSM) due to potentially simpler manufacturing, at other potential negative attributes.
    Internal Path-finding option; we could accelerate if competitively pressured
Korea Inc:
  Hynix publishes most on 3D XPoint copy technology; publications closest to Intel capability
  Samsung is silent publicly – Rumor from ~2016 was they were funding 3DXP program at level they would fund DRAM node. They should be capable of having something by ~now.
  Lots of poaching attempts for “3DXP consultants” in 2016/2017 for “Korea based” customer
Alternative technologies in research phase (long lead time) and/or deemed low probability of success
  With that said, Yole (market research) claim: “Sony plans to release low-latency drives with TB-capacity, and eventually direct-access-memory modules that could make use of new interfaces / protocols.”

## Slide 3: Many Industry Players Pursuing 3D XP Options (Select Examples of OTS+PCM & RRAM Based…furthest along)
* Perception based on understanding of memory switching mechanism and published data
Company | Memory Type | Memory Mechanism | Pros | Cons* | R&D Effort | Overall Assessment
Hynix | 1S1R | OTS + PCM | 3D stackable; Engineering composition for RW | TBD | Internal R&D; Array demo | Most aggressive publications; Publications closest to Intel capability
IBM / Macronix | 1T1R => 1S1R | OTS+PCM | 3D stackable; Engineering composition for thermal stability | Limited operating window (Variability?) | Internal R&D; Small array demo | Research Level
IMEC/ CEA-LETI | 1S1R 3DXP | OTS+PCM | 3D stackable; Binary alloys based OTS Selectors | Limited operating window (Variability?) | Internal R&D; device level | Research Level
Multiple Univ | 3DXP | OTS + PCM | Materials engineering for Scalability, Reliability, Extendibility | No array data | Device Level | Research Level
OTS + PCM
Company | Memory Type | Memory Mechanism | Pros | Cons* | R&D Effort | Overall Assessment
Sandisk/WD/Unity/Rambus/4DS | 1R (filament / interfacial) | (Non) linear RRAM | Stackable 4f2; 3D RRAM (Selector-less) | Variability(stochastic); High R at scale | University Collab, internal R&D; Limited Array Demo | Dropped
Hynix/HP | 1S1R | SiOx(S)/ ox-RRAM NbOx Selector | 3D RRAM; Scaled (filament) | Variability(stochastic); RRAM compatibility | Internal R&D; Array demo | Dropped
Crossbar/SMIC | 1T-nR; 1S1R | Oxide (S) | Stackable 4f2; High NL; FAAST selector | Disturb; Variability; Integration Compatibility | Internal R&D; Array demo | Deemed Low Probability of Success for 1S1R
Sony (Previously in JDP w/Micron) | 1T1R => 1S1R | OTS(s) + CBRAM | Stackable 4f2; High NL | Complex integration for Cu; Disturb; Variability; | Internal R&D; Array Level | Internal: Low Prop of Success; External: (Yole) Sony plans low-latency drives TB-capacity in 2020
Nantero | 1T-1R; 1R | CNT based RRAM | Selector-less 4F2; High Speed; | Low NL; Inhibit / Disturb; Variability; | Univ and Internal R&D; Limited Array Demo | Internal: Low Prob. of Success; External: Dell venture backed
RRAM

## Slide 4: Many Industry Players Pursuing 3D XP Options (Examples of Non-RRAM Memories – largely @ research level)
Company | Memory Type | Memory Mechanism | Pros | Cons* | R&D Effort
Avalanche | 1S-1MRAM | MRAM with Threshold Selector | Stackable 4f2 ; High NL; Lo Ioff; | Disturb; Operating Window (Variability); | Internal R&D; limited array demo
Namlab/Global Foundries | FeFET | HfO2 based FerroFET | High Speed + Low voltage; CMOS compatible | Variability; Endurance; | Univ and Internal R&D; device level
IMEC 3D FeFET | 3D FeFET | HfO2 based FerroFET | High Density 3D NAND like; BE ALD process; | Variability; High Op Voltage; Endurance | Internal R&D; device level
Toshiba | 1FTJ | HfO2 based Ferro tunnel junction | Selector-less; 3D Stackable | Low NL; Variability | Internal R&D; device level
Kilopass / TC Labs | Thyristor (3D) | Vertical thyristor | 3D stackable; high speed; | Epi for abrupt junctions; | Internal R&D; mostly simulations
Sunrise | 3D NOR | NOR | Known Material Base (Silicon) | Large block, Slow Erase (not memory friendly?) | 
Micron/Intel | 1X | Self Select Memory | --- | --- | Internal R&D
MRAM Based
Ferroelectric Based
T-RAM
* Perception based on understanding of memory switching mechanism and published data
INTEL CONFIDENTIAL
NOR

## Slide 5: Reference Material (syncplicity links available for those wanting to spelunk)
“Emerging Memory: Competitive Landscape”
  Q3’19 Presentation to cross Intel Memory Architecture Technologies Steering Committee (Carolyn Duran forum)
  Authors: DerChang Kau, Prashant Majhi, Al Fazio
“Build-in Selector Memory (BiSM)”
  July 2019 Whitepaper (written at Rob’s request), provided to Bob, Navin, Mike Mayberry
  Authors: Al Fazio, Erik Hammer
“Emerging Non-Volatile Memory 2020 Market and Technology Report 2020”
  Authors: Yole Développement (3rd party market-technology research)
Note: Above reference material (and summary in these slides) are based on our own research, published journal materials, notes, etc, from customers, start-up company engagements (Icap), and other industry engagements.