## Slide 1: Emerging Memory Competitive Landscape A snapshot in June/2020
Prashant Majhi & DerChang Kau

## Slide 2: Emerging Memories for Persistent Memory in 3D Cross Point Architectures
Key Challenge: Matching Memory & Selector
Intel Gen 1 3D XPoint™
Resistance Change ReRAM[1D, 2D], PCM [3D]
Ferroelectrics
Magnetic
[MRAM, STT(SOT)MRAM]
Volatile filament
Ovonic Threshold
Thermionic
[diode, MIEC, ..]
Metal-Insulator Transition
INTEL CONFIDENTIAL

## Slide 3: Top Tier 3DXP options for high density PM
Company | Selector | Memory | Memory | Maturity | Assessment | Density [Gb/mm2] | R/W BW [GB/s/GB] | R/W Latency [ns] | BER | Endurance
Intel | OTS | PCM | PCM | production | · 3rd Gen 3DXP, P1241/ATF, PRQ 2022, 4th Gen P1242/Bow Falls in LRP | 1.91 | .1/.034~.05 | 100/465 | 2E-04 | 4M
Micron | OTS | PCM | PCM | production | · 1st Gen, sample 2019, 2nd Gen passed storage qual, yet to be announced. | 0.62 | .1/.034 | 100/465 | 5E-04 | 130K
Intel | OTS |  |  | exiting PF | · Build-in Selector Memory, a.k.a. BiSM · Mb array @41nm pitch demo'd in 2018 · Silicon based scalability pending (as P1242 Bow-Falls candidates) | 2.93 | .075/.05 | 100/<320 | < 2E-4 | ~10M
Micron | OTS |  |  | exiting PF | · Self Select Memory (BiSM), IM JDP · Mb array @41nm pitch demo'd in 2018 · at the end of JDP (July/2018), MU favored due to simpler manufacturing |  |  |  |  | 
Hynix | OTS |  | PCM | exiting PF | · Internal R&D, 2z nm array demo'd (2018 publication) · die map, array organization, cell construct closely follow Intel S15 | ~0.6 |  | 100/300 |  | 
Sony | OTS |  | CBRAM | exiting PF | · Internal R&D, 20nm Array demo'd; · sample @ 2020 (Jan/2019 PM summit announcement) · high drift, read induced over set problems; delay expected. · Other challenges: disturb, Cu integration, set/reset sigma · deemed low probability to success due to snapback read disturb | ~0.6 [128Gb/ 200mm2] | .2/.075 [3.2/1.2 GB/s] | 400/2000 |  | 1M
Nantero/ Fujitsu | NRAM |  |  | exiting PF | · Internal R&D, multiple venture backed, seeking M&A · indicating sample in 2020 with Fujitsu 40nm Logic process · Cell size [145nm]2, 8Gb 4 deck, 80mm2, 56% array efficiency. · Low NL; no build-in selector evidence; self-select capability is unclear. · deemed low probability to success without high NL or selector | 0.1 [8Gb/ 80mm2] | 1.33/1.33 [2.7GTps on 16Gb die] | 25/25 |  | 10B
IBM/ Macronix | OTS |  | PCM | Research | · Internal research on material and Cell construct @ ~100nm · small array demo'd |  |  |  |  | 
Avalanche | OTS? |  | MRAM | Research | · internal R&D, limited array demo · high NL, good for high density · disturb due to threshold switching |  |  |  |  | 
Ranked by technical maturity for productization

## Slide 4: Other notable emerging memory cross point technologies for high density PM
Company | Selector | Memory | Maturity | Assessment
IMEC | OTS | PCM | Research | · early research on material exploration and single device char
CEA-LETI | OTS | PCM | Research | · early research on material exploration and single device char
Intel | ADM Schottky | iPCM | Research | · early research on material exploration and array definition
Micro | OTS | iPCM | Research | · early research on material exploration (EU Pastry project)
Crossbar/ SMIC | FAAST | VO+ RRAM | Research | · Internal R&D @ Array level · high NL (don't know how it works and what are the material) · filament RRAM, high sigma, disturb, & read snapback over-set issue · deems low probability to success.
HP/Hynix | NbOx | VO+ | Dropped | · Filamentary, variability, endurance are showstopper (Sandisk/WD included)
Kioxia | FTJ |  | Research | · Internal research on Cell char · low NL can be a problem; bipolar selector may be required
Kioxia | CBRAM |  | Research | · Toshiba published cell level research work on Ag based CBRAM [variability still issue] · No press about products; Kioxia still has reference to Toshiba research on their website
Unity | Interface |  | Dropped | · CMOx (acquired by Rambus), variability, slow (mass transport)
Intel | FeFET |  | concept | · High density 3D array construct (3D NAND like) in concept stage · Silicon channel and ADM channel under evaluation;
Namlab/ GF | FeFET |  | Research | · 2D array of scaled FeFET; challenging to reach high density; significant variability (no window) · FMC (spin-off of Namlab) is seeking TSMC JDP
IMEC | FeFET |  | Research | · High density 3D array construct (NAND like) in research stage [cell level r&d]; · significant variability (no window @ 3s)
Micron | FeFET |  | ? | · 3D NAND architecture
Kilopass / TC Lab | T-RAM |  | Research | · Mostly simulations of cell level; volatile memory · significant risk on 3D construct - require high quality epi in high AR structures
Sunrise | NOR |  | Research | · In stealth mode; recently recruited FeFET expert Cal Prof Salahuddin of Cal (~1yr sabbatical)

## Slide 5: Emerging Memories for In Package Memory candidates
Key Challenge: BW, Granularity
INTEL CONFIDENTIAL
Write Driver and Sense Amp
X –decoder and Multiplexer
Output driver and I/O
Y decoder
BL
SL
BL
SL
WL
WL
WL
Intel Gen 1 eDRAM [1T1C]
1T- 1X Array Architecture
TFT channel planar / nonplanar XTOR
2T [independent read write] Option
Si channel planar / nonplanar XTOR
MRAM [STT/SOT]
Nano-structure change
High-k Capacitor
Ferro-capacitor
Access Transistor
Memory Element

## Slide 6: Capacitive storage with access X’tor options for high BW memory
Company | X’tor | Memory | Maturity | Assessment | Density [Gb/mm2] | R/W BW [GB/s/GB] | R/W Latency [ns] | BER | Endurance
Intel | finfet | hiK | Production | · IPM with 22nm logic technology, PRQ 2013 | 0.013 | 800 | 12 | 1E-07 | 1E+14
Intel | ADM | hiK | exiting PF | · back gated, Gen 1 2022, Gen 2 2023 (metric quoted: Gen 2, 2-deck) · roadmap also include Gen 3 &4 each year @ density ~1.5X per generation | 0.060 | 6000 | 5 | 1E-06 | 1E+13
Intel | ADM | hiK | Pathfinding | · Finfet, 6F2, 2025 + (metric quoted based on dual deck (50nm)2 cell | > 0.27 | 6000 | 5 | 1E-06 | 1E+13
Samsung | 1T | 1C | Research | · Some indications of ADM like technology interest, but no public disclosure · Many DRAM flavors [DBM, HBM, DDR]; expect ~2023 (IGZO or or Si LT) |  |  |  |  | 
Hynix | 1T | 1C | Research | · Some indications of ADM like technology interest, but no public disclosure |  |  |  |  | 
Micron | 1T | 1C | Research | · Some indications of ADM like technology interest, but no public disclosure |  |  |  |  | 
Intel | ADM | n·FeCap | Research | · x'tor and FeCap electrical validated · 1T1FeC cell structure / array architecture and process integration in PF · 1TnFeC cell/array/integration is on drawing board | > 0.4 |  | 20/15 (destructive read) |  | 1E+12
Namlab/ DRAM | 1T | 1FeCap | Research | · Possibly JDP with all tier-1 DRAM manufacturer (Samsung and Hynix) |  |  |  |  | 
Micron | 1T | 1FeCap | Research | · Triangulation from supply chain interaction |  |  |  |  | 
TI | 1T | 1FeCap | Research | · TI work on HfO2 based FeCAP in collaboration with univ ; · TI has 1T1F embedded NVM product (PZT) |  |  |  |  | 

## Slide 7: Resistive storage with access X’tor options for high BW memory
Company | X’tor | Memory | Maturity | Assessment | Density [Gb/mm2] | R/W BW [GB/s/GB] | R/W Latency [ns] | BER | Endurance
Intel | finfet | STTM | Production | · Embedded or standalone, 22nm logic base, PRQ 2019 | 0.006 | 1000/10 | 10 | 1E-05 | 1E+07
Everspin/GF | 1T | STTM | Production | · Standalone; GF 22FDX based MRAM technology PRQ - no products yet |  | 16.5 | 35 |  | 
Samsung | 1T | STTM | Production | · embedded; 22nm FDSOI based product |  |  |  |  | 
TDK/ TSMC | 1T | STTM | Production | · embedded; TSMC technology PRQ @ 22nm [2019]. no product in HVM yet |  |  |  |  | 
Avalanche | 1T | STTM | Production | · embedded and standalone multiple products 4M to 64MB |  |  |  |  | 
Hynix | 1T | STTM | Pathfinding | · Array demo'd; 4Gb @ IEDM 2016; no press announcements of products |  |  |  |  | 
Kioxia | 1T | STTM | Pathfinding | · Toshiba was pursuing STTRAM for DRAM replacement (jointly w/ Hynix); |  |  |  |  | 
Micron/IBM | 1T | STTM | Dropped |  |  |  |  |  | 
Intel | 2T | SOT | Research | · CR assessment => SOTMRAM cell can scale ~0.01 um2 |  |  |  |  | 
TSMC | 2T | SOT | Research | · TSMC SOT MRAM in collab with univ [Stanford, NTU, ITRI]; · unclear about internal R&D status |  |  |  |  | 
IBM/Samsung | 2T | SOT | Research |  |  |  |  |  | 
IMEC | 2T | SOT | Research | · IMEC SOT MRAM positioning for SRAM replacement; cell level R&D |  |  |  |  | 
Adesto | 1T | CBRAM | Production | · Adesto 4 generation of cell CBRAM materials change, · no scaled memory beyond 40nm logic node [microcontroller space] |  |  |  |  | 
Sony/Micron | 1T | CBRAM | Dropped |  |  |  |  |  | 
Nantero | 1T | NRAM | Pathfinding | · Internal R&D, multiple venture backed, seeking M&A · deemed feasible for 1T-array; unclear about variability for high density |  |  |  |  | 
(Many) | 1T | 1VO+ | Dropped | · Showstopper: Variability at scaled dimensions and low operating currents |  |  |  |  |