## Slide 1: Abstract
Selector, an access device, isolates memory cells in an array. It improves signal to noise ratio as well as memory access disturbance immunity. A selector of a cross-point memory cell is a two-terminal switch serially connected to a matching storage element. An effective selector technology is realized with a low thermal budget process integrated at the cross point of a pair metal straps, a.k.a. wordlines and bitlines. This backend memory process is compatible with mainstream semiconductor technology featuring CMOS under array with deck stacking for low cost memory products. In this review, prospective two-terminal switches exhibiting nonlinear I-V characteristics in a cross point memory array will be discussed. The phenomenology and switching speed with the underline mechanism as well as the compatibility to memory access will be benchmarked.
Selector, an essential device in a memory cell of cross point memory technologies
DerChang Kau
an Intel Fellow and the director of 3D XPoint Technology at Intel. He leads the team responsible for the pathfinding of nonvolatile memory architecture and the strategic direction of atomistic memory devices and switches. He is a veteran in semiconductor industry, involved in various pathfinding and scaling deployments of mainstream memory, logic, mixed signal and radio technologies.

## Slide 2: Selector, an essential device in a memory cell of cross point memory technologies
DerChang Kau
Intel Fellow
Director, 3D XPoint Memory Technologies
SRC Workshop on New Trajectories for Memory and Storage Technologies, Oct/27~29/2020

## Slide 3: Cross Point Memory Array – ½ voltage biased scheme
The selected bit (•) is at the cross point of the selected bitline (BL) and wordline (WL)
Functionality –
A fully networked x-y resistive array  Sneak paths thru all de-selected cells (•) connect the selected BL/WL
Reliability –
All bits on selected BL (•) and selected WL (•) are biased  Read/Write disturbance and retention
A selector isolates memory cells in an array, improves access accuracy and strengthens reliability.

## Slide 4: Selector of a cross-point memory cell is a diode
Diode: two terminals and exhibiting a nonlinear I-V, IEEE Standard Dictionary of Electrical and Electronics Terms, 1980
§ : Kowk K. Ng, Complete guide to semiconductor devices, 2nd ed., 2002 ¶ :https://www.digikey.com/en/articles/design-in-tvs-diode-protection-enhance-can-bus-reliability
Unidirectional
Asymmetric
Unipolar
Bidirectional
Symmetric Ambipolar

## Slide 5: Random Access of a Memory in Cross Point Array
Unidirectional L-Shape Selector
Bidirectional S-Shape Selector
A rectifying selector turns on one bit with forward bias and isolates others with reverse bias.
Selected BL/WL are toggled between 0V and V
All bits but selected WL/BL are reversed biasd
Subject to Vdrop at each cross points, the selected bit is triggered, and the unselected bits are blocked.
Selected BL/WL are toggled between 0V and ±V
All bits but selected WL/BL are 0 biased

## Slide 6: Thin Film Diode Candidates for Cross Point Memory
Y. Sasago, et. al.,
VLSI ’09. T2B-1
D. Kau, et. al.,
IEDM ’09. S27.1
K. Gopalakrishnan, et. al.,
VLSI ’10. TS19.41
B. ﻿Govoreanu, et.al.,
IEDM’13. S10.2
S. Yasuda, et.al.,
VLSI, 2017. T2-4
S.G. Kim, et. al.,
IEDM ’15. S10.3

## Slide 7: Threshold Switching Phenomenology & Mechanisms
Mechanism | Thermionic | Filamentation | Tunneling | MIEC | MIT | OTS
Construct. | P-N or M-S Jx | Ion (Ag+) in Ox | MIM | Cu+ in SE | NbO2 | Chalcogenide
Switching | Electronic | Atomistic | Electronic | Atomistic | Atomistic | Electronic
Polarity | Unidirectional | Bidirectional | Bidirectional | Bidirectional | Bidirectional | Bidirectional
tswitch | sub nsec | ns ~ 100s ns | ps or faster | ns ~ 100s ns | ns to 10s ns | sub ns
JMAX | < 10MA/cm2 | 1-10MA/cm2 | < 1MA/cm2 | ~10MA/cm2 | > 10MA/cm2 | > 10MA/cm2
JInhibit | <1A/cm2 | <1KA/cm2 | <1KA/cm2 | <1KA/cm2 | <1KA/cm2 | <1KA/cm2
VInhibit | < 3V | < 1V | <3V | < 1V | < 3V | < 3V
I-V |  |  |  |  |  | 
Reference | Y. Sasago, et. al., VLSI ’09 | J. Yang, et.al., Adv Func Mtls (2018) | B. ﻿Govoreanu, et.al., IEDM’13. P10.2 | K. Gopalakrishnan, et.al., VLSI Symposium ’10. | X. Liu et.al., EDL Oct.’14 | S. Yasuda, et.al., VLSI symposium, ‘17,

## Slide 8: Consideration of architecting a cross point memory technology
Desirable Attributes: Nonvolatile, Low Cost, High Performance
Simple scalable, 3D stackable construction; low D·T, BEOL compatible with mainstream IC manufacturing
Memory switching in atomistic state (bulk); superior scalability than electrostatic memory switching physics
Individual cell access, small granularity
Fast switching materials + local low resistance metal interconnect
Challenge: to “mate” selector and memory in achieving a non-linear I-V for array access
Potential Selector Options:
  Unidirectional
  Homo/Heterogenous P/N Jx
  Schottky Barrier
  Bidirectional
  Mixed ionic-electronic conduction
  Tunneling barrier
  Metal–insulator transitions
  Ovonic threshold switching
Potential Memory Options:
  Spin polarization
  Phase change/segregation
  Ferroelectric hysteresis
  Interfacial barrier modulation
  Oxygen vacancy relocation
  Ionic transport
  NRAM (?)
Wordlines