## Slide 1: Scaling in Electron Devices and Electronic Systems A decadal projection in memory technologies
DerChang Kau (高德昌)
Intel Fellow, Director of External Technology Pathfinding
Corporate Planning Group
A chat at Graduate School of Advanced Technology at National Taiwan University May/29/2023

## Slide 2: Abstract
Since 1897’s discovery of electron by Sir Joseph John Thomson (Nobel Laureate 1906), electron devices started the journey of the 2nd industrial evolution onward. Under the guidance of Moore’s Law and Dennard Scaling, electron devices’ density increase at cadence and electronic systems strive maintaining power density while improving performance. This talk invites participants first travel down the time tunnel of electron devices. We will jointly revisit researches in material synthesis and device exploration in atomistic switching physics to disrupt electrostatic switching mechanism. Memory technology will be used to project decadal electronic system advances in homogenous and heterogenous integration through VLSI fabrication and chiplet interconnect processes.
About DerChang Kau
An Intel Fellow and a Director of External Technology Pathfinding, exploring chip manufacturing and system integration technologies aligning with product roadmap. For more than 3 decades, DerChang has been involved in various technology pathfinding and scaling deployment, including logic, memory, flash, embedded memory, mixed-signal, radio and advanced packaging. He also led Intel’s efforts to define strategic direction for atomistic memory switching and threshold switching devices and drove the product initiatives of Optane Memory Technology. He holds MS degrees in Electrical Engineering from OSU.

## Slide 3: Outline
Travel down the time tunnel of electron devices –
  A Centennial Journey of Electrical Charges
State of Art of Memory Technologies –
  System hierarchy and incumbent deployment
  A holistic view of Memories: Cell, Array and Subsystem
Memories in next decade –
  Cache, Memory and Storage
  Near Memory and Storage Class Memory

## Slide 4: Travel down the time tunnel of electron devices
A Centennial Journey of Electrical Charges
A chat at Graduate School of Advanced Technology at National Taiwan University May/29/2023

## Slide 5: Discoveries of Electron
1897 Sir Joseph John Thomson (1856 - 1940) discovered and identified the electron, for which he received the Nobel Prize for physics in 1906. Thomson demonstrated that cathode rays were actually units of electrical current made up of negatively charged particles of subatomic size as an integral part of all matter and theorized the "plum pudding" model of atomic structure in which a quantity of negatively charged electrons was embedded in a sphere of positive electricity, the two charges neutralizing each other.
1895 Wilhelm Conrad Röntgen (1845 - 1923) discovered X rays, for which he received the first Nobel Prize for physics in 1901. The “hand” was taken in 1896 with cathode-ray discharge. He later demonstrated the metallurgical and medical use of X rays.
https://www.nobelprize.org/prizes/physics/1901/summary/
https://www.nobelprize.org/prizes/physics/1906/summary/

## Slide 6: Innovations of Vacuum Electron Devices
1907 Lee De Forest (1873 - 1961) added a grid electrode to
Flemings' valve and
created the triode tube,
later improved and
called the Audion.
He was a prolific inventor, and was
granted more than 300 patents in Electronics
1905 Sir John Ambrose Fleming (1849 - 1945) made
the first diode tube,
the Fleming valve.
The device had
three leads, two
for the heater and the
cathode and the other for the plate.
https://madeupinbritain.uk/Vacuum_Tube
https://www.britannica.com/biography/Lee-de-Forest

## Slide 7: Revolution of Electronics – From Vacuum Science to Solid State Physics
In 1948, John Bardeen (1908 - 1991), William Bradford Shockley (1910 - 1989), Walter Houser Brattain (1902 - 1987) invented the transistor for Bell labs, sharing the 1956 Nobel Physics prize for the invention.
Shockley’s insight of “minority carrier injection” became the bible of the new era
    [1] W. Shockley, “The Theory of P-N Junctions in Semiconductors and P-N Junction Transistors.” Nokia Bell Lab, July 1949
    [2] W. Shockley, “Electrons and Holes in Semiconductors: With Applications to Transistor Electronics”, Van Nostrand, Jan, 1050

## Slide 8: Thermionic emission (single-/dual-carrier) and beyond
Diode: two terminals and exhibiting a nonlinear I-V, IEEE Standard Dictionary of Electrical and Electronics Terms, 1980
§ : Kowk K. Ng, Complete guide to semiconductor devices, 2nd ed., 2002 ¶ :https://www.digikey.com/en/articles/design-in-tvs-diode-protection-enhance-can-bus-reliability
L-Shape
N-Shape
S-Shape
Unidirectional
Asymmetric
Unipolar
Bidirectional
Symmetric Ambipolar
¶
§
§
§
§
§

## Slide 9: Thin Film Diode Candidates for Cross Point Memory
Y. Sasago, et. al.,
VLSI ’09. T2B-1
OTS
D. Kau, et. al.,
IEDM ’09. S27.1
K. Gopalakrishnan, et. al.,
VLSI ’10. TS19.41
B. ﻿Govoreanu, et.al.,
IEDM’13. S10.2
S. Yasuda, et.al.,
VLSI, 2017. T2-4
S.G. Kim, et. al.,
IEDM ’15. S10.3

## Slide 10: Threshold Switching Phenomenology & Mechanisms
Mechanism | Thermionic | Filamentation | Tunneling | MIEC | MIT | OTS
Construct. | P-N or M-S Jx | Ion (Ag+) in Ox | MIM | Cu+ in SE | NbO2 | Chalcogenide
Switching | Electronic | Atomistic | Electronic | Atomistic | Atomistic | Electronic
Polarity | Unidirectional | Bidirectional | Bidirectional | Bidirectional | Bidirectional | Bidirectional
tswitch | sub nsec | ns ~ 100s ns | ps or faster | ns ~ 100s ns | ns to 10s ns | sub ns
JMAX | < 10MA/cm2 | 1-10MA/cm2 | < 1MA/cm2 | ~10MA/cm2 | > 10MA/cm2 | > 10MA/cm2
JInhibit | <1A/cm2 | <1KA/cm2 | <1KA/cm2 | <1KA/cm2 | <1KA/cm2 | <1KA/cm2
VInhibit | < 3V | < 1V | <3V | < 1V | < 3V | < 3V
I-V |  |  |  |  |  | 
Reference | Y. Sasago, et. al., VLSI ’09 | J. Yang, et.al., Adv Func Mtls (2018) | B. ﻿Govoreanu, et.al., IEDM’13. P10.2 | K. Gopalakrishnan, et.al., VLSI Symposium ’10. | X. Liu et.al., EDL Oct.’14 | S. Yasuda, et.al., VLSI symposium, ‘17,

## Slide 11: State of Art of Memory Technologies
System hierarchy and incumbent deployment
A holistic view of Memories: Cell, Array and Subsystem
A chat at Graduate School of Advanced Technology at National Taiwan University May/29/2023

## Slide 12: Every Day Data is EXPLODING
1.5 GB
Average Internet User
50 GB Autonomous DRIVING
3 TB Smart Hospital
40 TB
Airplane Data
1 PB
Smart Factory
50 PB
Public Safety
https://www.cisco.com/c/dam/m/en_us/service-provider/ciscoknowledgenetwork/files/547_11_10-15-DocumentsCisco_GCI_Deck_2014-2019_for_CKN__10NOV2015_.pdf
We are in a data-centric world
Data are
stored, processed, and analyzed

## Slide 13: Incumbent Technologies in Memory/Storage Hierarchy each of which has greater capacity than the preceding but which is less quickly accessible
“The Memory Organ – Ideally one would desire an indefinitely large memory capacity such that any particular … word would be immediately … available. … It does not seem possible physically to achieve such a capacity. …We are therefore forced to recognize the possibility of constructing a hierarchy of memories, each of which has greater capacity than the preceding but which is less quickly accessible.”
Preliminary Discussion of the Logical Design of an Electronic Computing Instrument
Arthur Burks, Herman Goldstine and John von Neumann, June/28/1946
SRAM
DRAM
HDD
SSD
Bandwidth, Cost
Capacity, Latency

## Slide 14: A memory cell consists one storage element and one or more access switch(es)
Storage Elements:
  Latch: Circuit based or Thyristor device
  Electrostatic memory switch: Two terminal capacitor, floating gate/plate, charge traps devices
  Atomistic memory switch: Phase change, Magneto Tunnel Junction, Ferroelectric, Oxy-Vacancy (Filamentation)
Access Devices:
  3 terminal Transistor:
    Pass logic (1T) is typical used for read/write access.
    Gated common-source amp (2T) is used for read only access
    Biased Source-follower (1T) is used for read only access
  Two-terminal diodes: Thermionic (PN junction, Schottky barrier, DIAC & etc) , MIT, OTS MIEC, volatile filamentation and etc.
S
A1
A2
•••
•••
Brain teaser: multiple memory storage elements share one access device

## Slide 15: Multi-ported SRAM Symmetry
1R1W
U
U
D
D
G
G
RG
RD
WW
WB
RW1
WB
RB1
2R1W
RB2
RW2
U
U
D
D
G
G
RG
RD
RD
RG
G
D
U
D
U
G
RG
RD
RG
RD
2RW
WW
WB
WB
RB
RW
1RW
U
U
D
D
G
G
R
W
B
B
D
U
D
U
G
G
W1
B1
B1
B2
B2
W2
U
U
D
D
G1
G1
Vcc
Vss
B1
B1
W1
W1
G2
B2
W2
G2
W2
B2

## Slide 16: Why “Multi-Port Memories”
﻿Multi-Port Memories have all the features of single-port memories
Used for multi-tasking
Parallel Processing – increase bandwidth without cycle time compressing
“Simultaneously” read and write data or read-while-write
Examples
  Dedicated Memory – In a branch-target-buffer memory to keep track branch prediction and decision
  Shared Memory – multiple requests for data from multi-cores or networked processors
Analysis and Synthesis
  Multi-port (MP) SRAM is a commonly used for cache design as it allows simultaneous R/W accesses.
  For CISC CPUs, such as the X86 architecture, MP cache such as mRnW configuration is used
  For RISC CPUs, such as the ARM architecture, SP cache such as 1RW with multi-bank (MB) configuration is used.
  Overall, the choice of cache memory organization and multiport SRAM configuration depends on the specific design goals, performance requirements, and trade-offs between cost, power consumption, and performance.

## Slide 17: Array Capacity: · bits with 1RW, 1R1W, 2R2W cells
Read/Write
6T cell
1RW
Write
8T cell
n·m·w b Bank
ROW DECODER - WWL
ROW DECODER - RWL
n
n
m
0
1
2
Wsize-1
0
1
2
Wsize-1
m
Read
8T cell
1R1W
12T cell
n·m·w b Bank
ROW DECODER – WWL-A
ROW DECODER – WWL-B
n
n
n
ROW DECODER – RWL-C
ROW DECODER – RWL-D
n
m
0
1
2
Wsize-1
m
0
1
2
Wsize-1
Write A
Write B
m
0
1
2
Wsize-1
m
0
1
2
Wsize-1
Read D
Read C
16T cell
2R2W
Bruce Jacob et.al, Memory System, p.265

## Slide 18: ··-bit array 4 RW ports vs. 2R2W ports
Read/Write
6T cell
1 RW port
1Bank
6T cell
4 RW ports
4 banks
12T cell
n·m·w b Bank
ROW DECODER – WWL-A
ROW DECODER – WWL-B
n
n
n
ROW DECODER – RWL-C
ROW DECODER – RWL-D
n
m
0
1
2
Wsize-1
m
0
1
2
Wsize-1
Write A
Write B
m
0
1
2
Wsize-1
m
0
1
2
Wsize-1
Read D
Read C
16T cell
2R2W ports
1Bank
Read/Write
ROW DEC
n/2
m/2
0
1
2
Wsize-1
6T Cell
¼·n·m·w b Bank
0
1
2
Wsize-1
0
1
2
Wsize-1
0
1
2
Wsize-1
Bank Logic: 4ports Cmd/Add + I/O
Bruce Jacob et.al, Memory System, p.265

## Slide 19: Memories in next decade
Cache, Memories and Storage
Near Memory and Storage Class Memory
A chat at Graduate School of Advanced Technology at National Taiwan University May/29/2023

## Slide 20: Gaps to fill between Caches, Main Memory & Storage beyond scaling
“It’s the Memory, Stupid! … Processor Speed Has Outstripped Memory … today’s chips are largely able to execute code faster than we can feed them with instructions and data. There are no longer performance bottlenecks in the floating- point ... The real design action is in memory subsystems—caches, buses, bandwidth, and latency…I expect that over the coming decade memory subsystem design will be the only important design issue for microprocessors.”
Architects Look to Processors of Future,
Microprocessor Report, V10, No. 10, Aug/5/1996
Dick Sites, Digital Equipment Corp

## Slide 21: Cache Memory in next decade
Scaling trajectory of mainstream logic technology yet optimized for SRAM
IP folding to increase Cache capacity : Core
  Enabling technology: TSV, back-side metallization, reconstructed wafer, wafer-wafer (hybrid) bonding,
Key Challenges: Power and Thermal

## Slide 22: Emerging Memories for In Package Memory candidates
Key Challenge: BW, Granularity
Write Driver and Sense Amp
X –decoder and Multiplexer
Output driver and I/O
Y decoder
BL
SL
BL
SL
WL
WL
WL
Intel Gen 1 eDRAM [1T1C]
1T- 1X Array Architecture
TFT channel planar / nonplanar XTOR
2T [independent read write] Option
Si channel planar / nonplanar XTOR
MRAM [STT/SOT]
Nano-structure change
High-k Capacitor
Ferro-capacitor
Access Transistor
Memory Element

## Slide 23: Compute Memory Disaggregation
Host
Memory Farm
Channel0
Channeln-1
…
…
Logic
Bank1
Channeli
Bank0
….
Bankm-2
….
Bankm-1
Logic
Mat
Decoder / Driver
SA / Data Latch
TFT channel planar / nonplanar XTOR
2T [independent read write] Option
Si channel planar / nonplanar XTOR
MRAM [STT/SOT]
Nanostructure change
High-k Capacitor
Ferro-capacitor
Access Device
Memory Element
Logic and Mix Signal
Mix Signal
Memory Specific
C/A
Memory Mat
SA
Page
RAS
DQ + Metadata
CAS
Bankj
SWD
CSL

## Slide 24: Chiplet stacking to improve packing density, Power and Bandwidth
HBM, H Jun, et.al., IMW’2017
A. Su, et.al., ECTC2019
M. O’connor, et.al., ACM/MICRO 2017
Bank
Bank
Bank
Bank
Fine-Grained DRAM Arch:
  Partition Bank into narrower pseudo-banks
  32 Dedicatedm Local 2 GB/s Channel
  Local, parallel I/O per bank at lower energy
Quad-Bandwidth HBM Channels:
  Four 16 GB/s Channels
  Shared inter-bank bus
  High datapath & array act. energy
Bank
Bank
Bank
Bank
Bank
Bank
Bank
Bank
HBM2 Channels:
  Shared 16 GB/s Channel
  16 banks per channel
  BW of idle banks is “wasted”

## Slide 25: DRAM’s Journey beyond Trench Capacitor
Kinam Kim, IEDM’21, Plenary Session 1.1

## Slide 26: Emerging Memories for Persistent Memory in 3D Cross Point Architectures
Key Challenge: Matching Memory & Selector
Intel Gen 1 3D XPoint™
INTEL CONFIDENTIAL
Resistance Change ReRAM[1D, 2D], PCM [3D]
Ferroelectrics
Magnetic
[MRAM, STT(SOT)MRAM]
Volatile filament
Ovonic Threshold
Thermionic
[diode, MIEC, ..]
Metal-Insulator Transition
Access Diode
Memory Element

## Slide 27: Consideration of architecting a cross point memory technology
Desirable Attributes: Nonvolatile, Low Cost, High Performance
Simple scalable, 3D stackable construction; low D·T, BEOL compatible with mainstream IC manufacturing
Memory switching in atomistic state (bulk); superior scalability than electrostatic memory switching physics
Individual cell access, small granularity
Fast switching materials + local low resistance metal interconnect
Challenge: to “mate” selector and memory in achieving a non-linear I-V for array access
Potential Selector Options:
  Unidirectional
  Homo/Heterogenous P/N Jx
  Schottky Barrier
  Bidirectional
  Mixed ionic-electronic conduction
  Tunneling barrier
  Metal–insulator transitions
  Ovonic threshold switching
Potential Memory Options:
  Spin polarization
  Phase change/segregation
  Ferroelectric hysteresis
  Interfacial barrier modulation
  Oxygen vacancy relocation
  Ionic transport
  NRAM (?)
Bitlines
Selector & Memory Devices
Wordlines
Wordlines

## Slide 28: In Pursuit of a Dream …
Conclusion
September 28
1970
December 8
2009
August 13
2020
A Half Century Endeavor
D. Kau, VLSI-TSA 2021

## Slide 29: Long gestation of Disruptive Memory Technologies
4Kb
200nm feature,
4-mask
Sublitho Heater
Damascene PM
Subtractive SD
1970
64Mb
180nm ½ Pitch
6-Mask Sublitho Heater
Damascene PM,
Subtractive SD
64Mb
100nm feature
2-Mask
Self-Aligned,
Subtractive Cell
64Mb
50nm ½ Pitch,
2-Mask
Dual Deck,
Self Aligned
Subtractive Cell
128Gb
41nm Pitch
Dual Deck
Self Aligned Subtractive Cell
256Gb
41nm Pitch
Quad Deck
Self Aligned
Subtractive Cell
Scaled
Line/Space
2003
2007
2010
2012
2013
2015
2019
1st Production Generation
2nd Production Generation
3rd Production Generation
Ideation
PoC: Electron Devices
PoC: Cell and Array
PoC: Process Architecture
Research Graduation

## Slide 30: 3D NAND in next decade will continue to drive $/bit on par with HDD
Tiering/Decking engineering + multi-level placement algorithm
Kinam Kim, IEDM’21, Plenary Session 1.1

## Slide 31: Takeaway of Advances of Memory Technologies
Universal memory
  Universal memory often sought, but hierarchy always existed and likely always will be
  FoM must be benchmarked with respect to the corresponding hierarchy of memories
Disrupt memory technology
  ﻿Typical long gestation of Disruptive Memory Technologies
  Mainstream memories hard to establish; hard to displace or to replace; DRAM replaced Core memory in 1960’s and SSD displacing spin drive in 2000’s
  Memory technology research to productization can take decades and once productized, achieving mainstream is still not guaranteed
Memory Subsystem
  Modular, Modular, Modular
  Power/Thermal conscious: Energy from I/O and from moving bits back/forth becoming limiting
  3D (monolithic, wafer-wafer) and packaging of multi-chip
    TTM and Cost driven
  Pair memory tech research with compute architecture/hierarchy research.
  Software (often ignored ) enabling to alleviate adoption barriers or to unlock value