## Slide 1: Fan-Out Si Bridge Enabling Project
FTE EPAE
Alois Nitsch / David O’Sullivan / Evelyn Chen / Andreas Dost / Hans-Gerd Jetten /
Thomas Huber
2021-Oct

## Slide 2: 2.xD Packaging Technology Milestone
2017
2012
Si interposer (2.5D)
tsmc CoWoS first product shipment
EMIB
Si bridge in substrate
2017 first product shipment
RDL interposer (2.3D)
SPIL FO-MCM production
2020
Fan-out Si bridge
SPIL FO-EB production
(1ASIC+4HBM)*2, AMD GPU
2021
2024
ODI
In development
Same Si bridge concept with EMIB/ODI:
Plug-and-play complementary solution for Intel?
Today
Notes: EMIB: embedded multi-die interconnect bridge
ODI, Omni Directional Interconnect

## Slide 3: Project Target:
Enable external fan-out Si bridge technology:
Provide a complementary solution for EMIB/ODI for any internal capacity issue.
Plug-and-play solution —no Silicon redesign, minimum design modification effort on RDL/substrate. Use Silicon/substrate of Emarald Rapids.
Better electrical performance in PDN expected compared to 2.3D
Potential cost down. Ex: opportunity to reduce substrate layers.
Potential option for IFS-Customers
Current Phase : Technology Capability

## Slide 4: OSAT capability evaluation
Product feature | Emerald Rapids | OSAT experience |  | 
 |  | SPIL LVM experience | ASE Qualified | AMKOR Engineering/Development
Top die qty​ | 2 ASIC | (1+1HBM) in LVM (1ASIC+4HBM)*2 in LVM 1+8HBM in qualification 3 ASIC in dev | (1ASIC+1HBM) qualified (1ASIC+4HBM)*2 in qualification – 2022Q1 | (1ASIC+2HBM) in engineering
Bridge die qty​ | 3 | 4 | 1 | 2
ASIC die size​ | 858 mm2 (26x33) | 725mm2 | 235mm2 (17.6x13.4)​ | 566mm2 (23.4X24.2)
Die to Die Distance | 100um | 140um Eng experience 118um | 70um | TBD
Si bridge size​ | 16.2mm2 (2.7x 6) 32.4mm2 (2.7 x12) | 37mm2 (~1:1 ratio) | 35mm2 (5.6x6.3)​ | 46mm2 (7.3x6.3)
Molding interposer size | NA | 1460mm2 2x reticle | 404mm2 (27.3x14.8)​ 1x reticle | 836(32.8x25.5) 1x reticle
Package size​ | 4640mm² (80mmx58mm) | 5600mm2 | 1271mm2 (41x31)​ | 4556mm2 (67.5x67.5)
top die bump pitch | 55/100/130um | 45um * No mixed bump experience | 55um *No mixed bump experience * core bump/ubump diameter ratio <2 | 50um * No mixed bump experience
Bump out pitch to substrate​ | Top die core bump 100/130um | Molding interposer min 150um 2024 roadmap 90um | Molding interposer min 150um | TBD
              SPIL has most development experience and product in production.
No gap
Gap

## Slide 5: Product Concept Study – Emerald Rapids
Top die: Intel Silicon
Tall Cu pillar in molding interposer
Bridge die embedded in molding interposer
EMIB
External
Si Bridge
Bridge die: Intel Silicon, embedded in substrate
ubump 55um pitch
core bump 100/130um pitch
Key to project success:
Retain form factor. Keep same pitch to substrate.

## Slide 6: Design Options— Redistribution Layer (RDL)
Topic | A. No RDL | B. Top RDL | C. Top RDL | D. Bottom RDL
Design feature | No RDL | Die to interposer Core bump: RDL ubump: stacking via | Die to interposer Core bump: RDL ubump: RDL | interposer to sub RDL
Min design effort | *** | ** | ** | **
Low REL concern | ** direct vertical connection | ** direct vertical connection | *** OSAT experience | ** direct vertical connection
Electrical performance | *** | ** | ** | **
Low cost | *** | ** | ** | **
SPIL lesson learnt: REL failure is observed at direct vertical connection between top die & molding interposer.
  Option A ranks highest – best choice in design, electrical performance, cost
  OSAT has experience of option C. Lowest concern in REL – relaxed design rule needed
  Plan to have option A/ option C go in parallel

## Slide 7: Next Steps
What has been done
OSAT capability evaluation
Defined Project target & scope
Work Packages
Design rule review and design option decision. [Ongoing, Dec]
OSAT selection [Ongoing, Dec]
Bond and communicate with BU. [Dec]
Establish detail plan. Resource needed from BU/FTE/OSAT. [Ongoing, Dec]