## Slide 1: Advanced Packaging for Heterogeneous Integration
Fellows Forum – October 29-30, 2018
Ravi Mahajan, Bob Sankman
Acknowledgments: Chris Baldwin, Luke Garner, Pat Stover, Ram Viswanath, Sriram Srinivasan, Eugene Scuteri, Raj Varada, Randy Osborne, Wilfred Gomes, Jeff Howard, Suresh Chittor, Shawna Liff, Jose Cardona, Rob Nickerson, Mitul Modi, Ken Brown, Sri Nimmagadda, Surhud Khare, Pilin Liu, Deepak Goyal

## Slide 2: Key Messages
Multi-Chip Packages (MCPs) have been used @ Intel for TTM and enhanced performance for many years
Increasing demand for on-package bandwidth has driven revolutionary changes in package architectures1 (e.g. EMIB, Foveros)
TTM, Heterogeneous IP Integration and Die Yield continue to drive on-package interconnect density for joining multiple chips in increasingly complex packaging architectures
Resources required to develop these advanced architectures are significant
  Early planning & Cross-organization collaboration need to select the optimal packaging strategy since Package Architecture Development is a highly Integrated Effort
1. Today’s Focus entirely on-package Interconnects. MCP technology envelopes needed to meet off-package signaling, power delivery and thermal needs not covered today

## Slide 3: Some Definitional Stage Setting………
Heterogeneous Integration1 (HI) refers to the integration of separately manufactured components into a higher level assembly (SiP) that, in the aggregate, provides enhanced functionality and improved operating characteristics
In this definition, components should be taken to mean any unit whether individual die, MEMS device, passive component and assembled package or sub-system that are integrated into a single package. The operating characteristics should also be taken in its broadest meaning including characteristics such as system level performance and cost of ownership
SiP or System-in-Package2 refers to package (such as a SO, QFP, BGA, CSP, LGA) that has multiple die (Si, GaAs, SiGe and/or SOI) plus optional passives integrated together
William Chen (ASE), Chair : IEEE Heterogeneous Integration Roadmap Leader
Prismark Partners LLC, - June 2018
The term “Multi-Chip Package (MCP)” is used in this presentation to cover all Multi-Component Packaging

## Slide 4: Intel has a long history of MCPs for TTM & Performance….
CPU
MC-DRAM
SRAM Integration
Core i7
eDRAM
Kaby Lake G
Knights Landing
I7 Iris Pro
(G)MCH Integration
DRAM Integration

## Slide 5: Dense MCPs to meet On-Package BW Demand
High BW Demand has Spurred Recent Interest in Dense MCPs2
Speculative Projections based on RAMBO (Random Access Memory Bandwidth Optimized) Memory Configuration (Ack: Wilfred Gomes)
Dense MCP demand also driven by need for parallel, power efficient interconnects (Power Efficiency not specifically covered today)
GB/s
Year
HBM drove EMIB adoption
RAMBO is driving investigations in SRAM Stacking & Foveros Design Rules
Year | 2007 | 2010 | 2013 | 2017 | 2020+ Discrete Graphics1
Product | Xeon | Core | 4th gen core | 8th gen core | TBD
I/O Bus | Front side bus (FSB) | QPI | OPIO | HBM | CPU-SRAM
# of signals (data) | 64 | 32 (differential) | 128 | 1024 | TBD
Signaling rate (Gb/s) | 1.333 | 6.4 | 6.4 | 1.6 | TBD
BW (GB/s) | 10.7 | 25.6 | 102.4 | 204.8 | 2TB/s
BW Demand Growth – 2X every 2 Years

## Slide 6: Dense MCPs are here to stay…..
For Die Yield Resiliency
SPR (Xeon-SP)
10nm Silicon
XCC: Quad-tile w/ 10 EMIB’s
77.5mm
56.5mm
20.6x21mm
GLC
NVidia Tesla P100
4 HBM + GPU
AMD Vega 10
2 HBM + GPU
Intel Stratix 10
6 Xcvr + FPGA
For TTM and Heterogeneous IP Integration

## Slide 7: Interconnects in Multi-Chip Packaging : Density Metrics
Key Package Interconnect Density Metrics:
IO1/mm/Layer (Escape Density)
IO/mm2 (Die Area)
IO refers to physical wires and bumps

## Slide 8
Today’s MCP Technology Landscape1
Standard MCP
IO/mm/lyr = 28-34
IO/mm2 = 83-123
Bump Pitch = 110-90µm
Organic FCXGA – Industry Workhorse
HDI Organic Interposer
IO/mm/lyr = 103-150
IO/mm2 = 331
Bump Pitch = 55µm
Nascent Technology : ATTD has an internal Pathfinding and Monitors Industry Pulse
3/3 L/S
Passive Si Interposer (CoWOS)
IO/mm/lyr ≥ 250
IO/mm2 ≥ 625
Bump Pitch ≤ 40µm
Industry Solution for Dense MCPs (NVidia Tesla, AMD Fury, Xilinx)
Broad Spectrum of Dense MCP Technologies in Development & Pathfinding Today
EmIB
IO/mm/lyr ≥ 250
IO/mm2 = 331
Bump Pitch = 55µm
Intel Unique Technology
Stratix – 10, Kaby-Lake G in production; more products in pipeline
POR for Lakefield
Gen 1 - Foveros
IO/mm/lyr = NA
IO/mm2 = 400
Bump Pitch =50µm
10nm Core
P1222 Base
1. Multi-Die Stack technologies not shown. Primarily used today in High Bandwidth Memory (HBM)
Gen 2 - (Foveros + EMIB)
IO/mm/lyr = NA
IO/mm2 = 772
Bump Pitch =36µm
GNR Working POR

## Slide 9: 2D Dense MCPs - Current and Planned Deployments

## Slide 10: EMIB Roadmap
H2’18
H1’19
H2’19
H1’20
H2’20
H1’21
10nm Wave 1 (Sequoia Acres, Falcon Mesa 3-8)
Maximum 6 bridges
Up to 55x70mm BGA
Sequoia Acres
FPGA + ASICS + XCVRs
Falcon Mesa
FPGA + XCVRs + HBM2/2E
Right side of box represents tech cert
Stars represent lead product power-on and PRQ
10nm EMIB Tiling (Sapphire Rapids, Arctic Sound)
Maximum 12 bridges
Up to 80mm BGA and 77.5x56.5mm LGA
Sapphire Rapids
CPU tiling
Arctic Sound
GPU tiling + HBM2/2E
TSMC 7nm on EMIB (Rivercrest, Knights Run)
External silicon qual, Maximum 15 bridges
Up to 80mm BGA
Rivercrest
Logic tiling + HBM2/2E
Knights Run
Hetero logic tiling + HBM2/2E
EMIB Development Focus : Package Size & Bridge Count Increases, Improved Signaling in Bridge

## Slide 11: Scaling MCP Bump Pitch at Intel
Intel Conventional FCXGA
Advanced Packaging
Mature Current Future
Minimum Bump Interconnect Pitch (um)
Bump Density - 5X Increase over 6 nodes
~7X Increase Over Conventional FCxGA
What Does it Hit these Targets?

## Slide 12
EMIB 30mm
Substrate
  Up to 14 bridges per substrate
  New OST @30mm pitch on substrate
  PID or LIV via: ~6mm dia; alignment TBD
Silicon Bridge
  7:1 aspect ratio
  Wafer level OST at 30mm pitch
Assembly
  TCB/Underfill : Significant effort (Invention?) Required
EMIB 55mm Today
Substrate
  Up to 10 bridges per substrate
  OST @ 55mm on substrate bumps
  Laser via: 23mm dia; ±9.5mm alignment
Silicon Bridge
  5:1 aspect ratio
  Wafer level OST @ 55mm
Assembly
  NGWP
  TCB/CUF
>98% Assy Yield Today!
EMIB 45mm
Substrate
  Up to 14 bridges per substrate
  New OST @ 45mm pitch on substrate
  New UV Laser via: 20mm dia; ±9.5mm alignment
  New Planarization Tools
Silicon Bridge
  7:1 aspect ratio
  Wafer level OST at 45mm pitch
Assembly
    NGWP
    TCB/CUF
EMIB Pitch Scaling
Pitch Scaling Requires Significant Resources & Building Block Development
OST – Open Short Testing
Via Scaling requires improved alignment, test capability, new materials & equipment in Package Manufacturing
55mm EMIB Interconnect Pitch

## Slide 13: 3D Stacking - Current and Planned Deployments

## Slide 14: Foveros Generation 1 : Lakefield
P1222 Base Die
10nm Core
50mm Die-Die Interconnect Pitch
Yields on-track to Forecast Roadmap (Assembly Certification EO’18). Lakefield Sample Shipping

## Slide 15: Generation 2 : (Foveros + EMIB) aka Co-EMIB
10nm Base Die or Passive Interposer
EMIB
EMIB
EMIB
36mm Die-Die Interconnect Pitch
Multiple Top Die Tiles
(7nm & 10nm)
Backside Metallization for Solder TIM
Companion Die
HBM
Generation 2 Envelope covers Multiple Core Tiles Stacked on (Passive or Active) Silicon Interposers with EMIB Connections between Stacks & Peripherals

## Slide 16: (Foveros + EMIB) – Product Configurations
P1222 vs 10FV-
G
P1222 vs 10FV-
HBM2e
EMIB
EMIB
Rambo
G
7nm –
Core Tile
10nm –
MCDDR
EMIB Substrate
Si: (7nm + 10nm) on 10FV
Base die: 600-700 mm2
# of Chiplets: 8-10
# of Base die: 2
EMIB Pitch : 55mm
EMIB Count: 4
Si: 10nm on Passive Si Interposer
Base die: 1000-1600 mm2
# of Chiplets: 3
# of Base die: 1
(Foveros + EMIB) @ 75mm Or Full Silicon Interposer
EMIB Count: 7
Si: (7nm + 10nm) on 10FV
Base die: 312-624 mm2
# of Chiplets: 6
# of Base die: 4
EMIB Pitch : 55mm
EMIB Count: 14
Granite Rapids
Falcon Mesa 11/ASIC
Ponte Vecchio
Complex Architectures with plenty of Yield, Assembly, Test and Reliability challenges. Technology Envelopes are being actively negotiated with Product Architects

## Slide 17
Existing EMIB Building Blocks
Fab: Mixed Pitch & Mixed CD Bump Plating
Assembly: Fine Pitch Chip Attach Process
Test: Fine Pitch Sort @ 110mm pitch
Substrate: Bridge Embedding & Substrate Test
Existing Foveros Building Blocks
Fab: TSV Process
Fab: > 36mm pitch bump plating
Assembly: TCB die stacking on wafer >36um pitch
Assembly: Wafer mold and Grinding
Assembly: TCB stacked die to substrate
Test: Fine Pitch Sort @ 72mm pitch
Fab or Assembly: Backside Metal Sputter to enable STIM (planned)
New Required (Foveros + EMIB) Building Blocks
Fab: Mixed Pitch & CD PSB Bumps on Stacked Die Wafer
Fab: Via Reveal on “thick” stacked die wafer
Assembly: NGWP process on stacked die wafer
Assembly: TCB stacked die to EMIB substrate at ≤ 55mm pitch
(Foveros + EMIB) : Flavor of the Key Technical Challenge Areas
Plan is to Leverage & Extend All Existing Building Blocks

## Slide 18: What is Being Explored?

## Slide 19: Omni-Directional Interconnect (ODI)
Significantly Reduced Parasitics + Dense Interconnect
(Foveros + EMIB)
ODI
Improved Thermals
No TSVs in IO Die
ODI is a Novel Architectural Concept Currently Under Exploration
Ack: Shawna Liff, Adel Elsherbini & Johanna Swan
500mm Pencil Core
Foveros Base Die Thickness
A4 Paper Sheet Thickness

## Slide 20
EMIB
Foveros + EMIB
ODI
Dense MCP Scaling Vectors
Bump Pitch
Bridge Count & Size
Active Bridge
Die-Die & Die-Package Bump Pitches
Tile Count
Die-Die & Die-Package Bump Pitches
Tile Count

## Slide 21: Dense MCP Scaling Directions……….
Scale EMIB?
Scale 3D Stacking?
Invest in New Technologies
ODI?
Si Interposer?
Glass?
Strategic, Cross-Organizational Approach Needed to Set Directions & Invest in Key Technologies

## Slide 22: Back-up

## Slide 23: Multi-Chip Packages will have to address other challenges
Technologies for high Bandwidth, Off-Package Electrical & Optical Signaling Needed
Introduction of FIVR with package inductors helps current demand
Improved Inductors Needed
Improved Thermal Interface Materials (TIMs) and Interface Control Needed for MCPs

## Slide 24
IO/mm = N/A
IO/mm2 ≥ 625
Bump Pitch ≤ 40µm
Multi-Die Stacking
3-D Stacking
Primarily used for Memory Stacking (HBM)
Multi-Die Stacking Primarily Used Today for Memory Stacking
Global Foundries Presentation from Stanford System X Workshop, May 2018

## Slide 25: Dense MCP : Competitive Analysis
 | AMD Fury R9X | Tesla P100 | AMD Vega 10 | Xilinx VU9P | HiSilicon 1610 FOCoS | Stratix 10 GX2800
Image |  |  |  | image cropped/IHS removed |  | 
Package Size | 55x55mm | 55x55mm | 47.5 x 47.5 | 47.5x47.5 or 52.5x52.5 | 42.5x42.5mm | 55x55mm
HBM Supplier | SKHynix HBM1 | Samsung HBM2 | Samsung HBM2 | n/a | n/a | n/a
HBM-Interposer mBump Pitch Min | 55mm | 55mm | 55mm | n/a | n/a | n/a
HBM Top Die Thickness | 200um | 400um | 363um | n/a | n/a | n/a
xPU-Interposer mBump Pitch Min | 45mm | 55mm | 45mm | 40mm | 40mm | 55mm (EMIB), 130mm (pkg)
xPU Die Thickness | 511mm | 700mm | 652mm | 489mm | 647mm | 750mm
xPU die XY | 26.25x22.25 | 22.5x27.5mm | 19x25.6mm | 25.66x11.44 (x3) | 16.2x6.2,15.7x8.6 | 20.3x28.3mm
Interposer Size XYZ | 32.9 x 26 x .01mm | 40 x 28.9 x .01 | 27 x 29 x 0.11mm | 35.61x27.19x.01mm | 17.7x16.6mm | 3.1x8.4mm EMIB
Interposer Top Metal Layers | 3 Cu | 1 Cu + 1 Al | 4 Cu | 3 Cu + 1 Al | 3 Cu RDL + Pad | 4 Cu + 1 Cu Pad
Interposer Routing Min L/S | 1 / 1mm | 1.1 / 1.6 mm | 1 / 0.5mm | 0. 5/ 0.3 mm | 2.5 / 3.5mm | 2.1 / 1.9 mm
Min FLI Pitch | 200mm | 180mm | 150mm | 180mm | 200mm | 130mm (non EMIB)
D2D Interconnect Process | OSAT CoS,CoC | TSMC CoWoS | OSAT CoC, CoW-L | TSMC CoWoS | ASE FOCoS | EMIB

## Slide 26
Package Technology Announcement | Technology Claims | Applications | Intel Interpretation and Competing Package Technology
TSMC’s InFO extensions < L/S < Bump Pitch < BGA Pitch NEW Backside RDL | TSMC claimed improvements vs conventional FCCSP: 0.8 x thickness 0.9x footprint 0.85x thermal resistance 1.1x performance Finer features extend InFO into medium-high density die-to-die interconnect applications. | MUST: InFO_PoP Modem + LPDDRx in InFO. 6mm x 5mmm footprint, 0.6mm Z-ht. 40um FLI. TSMC will package/stack consigned DRAM wafers (rumored for Apple). InFO_AIP: mmW RF FEM with and IPDs and antennas on backside RDL. 12x12, 0.9mm z-ht, 2 layer RDL InFO_oS/InFO_MS: Connecting 2 or more die in with fine pitch InFO in lieu of silicon interposer then attached to organic substrate up to 65x65mm size. 830mm2 reticle, 2um L/S RDL, 40um bump pitch Customers claimed: AMD, Broadcom, eSilicon, GUC, HP Enterprise, Mediatek, Xilinx, NVIDIA Mediatek/Nephos network storage product (Q3’18) | Intel Pathfinding has Modem solution with RDL LPDDR die flip-chip connected to substrate standoffs & achieves similar Z-height and footprint. Intel is currently pursuing mmW packages with conventional materials and processes that we believe will meet product performance requirements more cost effectively. Intel’s EMIB technology offers similar interconnect capabilities to InFO_oS and InFO_MS, with slightly larger bump pitch. InFO_OS is analogous to ASE’s FoCoS now in production for HiSilicon 1610 networking product.
Wafer to Wafer Stacking w/Hybrid Bonding | GF: F2B Hybrid Bonding of multi-high stacked wafers @ 7.5um pitch, 2-5um TSVs, qualed on 14nm. TSMC WoW: Wafer on Wafer bonding: F2F, F2F2B @ 10um pitch w/TSVs | GF: 3D SRAM cube with >15Tb/s bandwidth for fast access. TSMC WoW: No product alignment stated. Rumored for GPU stacking. | Intel Foveros technology will compete with 2-die stack; Client/DC applications do not demand the tighter bump although bump pitch is ~4X higher in the initial 7nm version. Intel Components Research demonstrated functioning SRAMs with wafer to wafer stacking at 3-5um pitch; work was halted due to lack of a product application. Requires very high D/W Debug difficult on 3 die stack Thermal issues.
Die to Wafer Stacking | GF: Micropillar Mass Reflow TSMC SoIC - System on Integrated Chip  3D stacking with <10um CoW bonding process, TSVs and Thru-Dielectric Vias | GF: 2 3D-SRAM L4 Cache cubes stacked on top of ASIC >20Tbps Bandwidth, 32GB Capacity (test vehicle) for Machine Learning applications. TSMC SoIC: “Simplest bond structure & minimum parasitic for better performance. Compatible with many package types for various applications.” | SoIC architecture is similar to Foveros w/ODI. Intel Foveros technology will compete with but bump pitch is ~4X higher in the initial 7nm version. Design for Sort at ultra fine bump pitch

## Slide 27
Advertised Derivatives of Base Technologies
Copper Pillar Through Mold Interconnect
Die Embedded in Epoxy Mold Reconstituted Wafer
RDL Layers
Silicon Interposer
Die to Wafer Flipchip Attach
Epoxy Molded Stacked Die Wafer with Planarized Surface
INFO - POP
CoWoS/2.5D
MUST
Added
Topside RDL
Smaller Form Factor Stacked Package
RF coils & Patch Antennas in RDL
InFO_AIP
Eliminate Silicon Interposer
Incorporate HBM-like Die Stacks
Transition from 40um pitch solder interconnect to 10um pitch Cu-Cu direct bond, and active-to-active face to face die bonding
SoIC (Silicon on Integrated Chip)
Add Topside RDL
Finer L/S
Tighter Via Pitch
Active Interposer
Tighter Bump Pitch
Hybrid Bond
WoW (Wafer on Wafer)
InFO_oS / InFO_MS

## Slide 28: Die-to-Die Interconnect Comparison
Nvidia Tesla P100
1 Routing Layer 1um L/2um Sp
AMD Vega 10
4 Layer, 1um L/0.5um Sp
AMD Fury R9X
3 Layer 1um L/S
Intel EMIB
4 Layer, 2um L/S
29x40mm Interposer/55x55mm pkg
27x29mm Interposer/47.5x47.5mm pkg
2L redundant routing w/ guard trace + 2 Shield Layers
Min: 0.95um L, 0.5um S, T=1.15um, 45um Die Via Pitch
Up to 55x55mm package
RDL X-section images are approximately to scale
6um 2 signals
6um 2 signals
6um 2 signals
2L routing w/ guard trace + Shield Layer
Min: 1um L, 1um S, T=1.1um, 48um Die Via Pitch
1L routing w/ no guard trace +Al RDL/Shield Layer
Min: 1um L, 2um S, T=1.6um, 55um Die Via Pitch
23x36mm Interposer/55mm pkg
6.9um 2 signals
2L routing w/ guard trace + 2 Shield Layers
21 Ω/mm
16 Ω/mm
10 Ω/mm
6.5 Ω/mm
UniMicron Silicon Interposer
TSMC CoWoS Silicon Interposer
Al RDL
6um ~9 signals
60 Ω/mm
Xylinx VU9P
3 Routing Layer 0.5um L/0.3um Sp
35.6x27.2mm Interposer/47.5x47.5mm pkg
3L routing w/guard traces +Al Bump Pad
Min 0.49um L, 0.3um S, T=0.85um, 40um Die Via Pitch
L1 & L3 routing w/ no guard trace, L2=power/ground
Min: ~3um L, ~3um S, T=4-5.5um, 40um Die Via Pitch
ASE FOCoS
HiSilicon 1610
3L Fan Out ~3um L/Sp
16.6x17.7mm Pseudo Die 42.5x42.5mm pkg
6um 2 signals
1.5 Ω/mm
Signal Ground

## Slide 29

P100

V100

VU
TSMC CoWoS Today:
1.75x Reticle, 40um uPGA, 0.8um RDL pitch, >98% Yield
> 2Mu/Qtr output, Adding Capacity
Growing # of Tape outs
CoWoS Future:
Deep Trench Capacitor
Embedded Inductor
Beyond CoWoS: