## Slide 1: Co-Optimization Pipeline Quarterly Update
3DIC Reference Design & Test Chip Roadmap
HBI-C for Memory Stacking
Ramune Nagisetty, Randy Osborne, Fatih Hamzaoglu, Vivek Rajan, Nick Kuhlman, Lalitha Immaneni, Adel Elsherbini, Shawna Liff, Sonia Leon, Debendra Mallik, Wilfred Gomes, Ben Sell, Srinivas Chennupaty
tdbu
July 21, 2020

## Slide 2: Evolution over last 12 months  STCO
Power Delivery:
FIVR chiplets, GaN
Tightly Coupled In-Package Memory:
ADM Roadmap & Requirements
3DIC Reference Design and Testchip Proposal: HBI-A and HBI-B
Coop Kickoff & Scope:
3-5 year pre-roadmap horizon
6/2019
9/2019
12/2019
3/2020
3DIC Reference Design and Testchip Roadmap:
HBI-C for memory stacking
Today
STCO = System Technology Co-Optimization
Notes: July 2019: Kickoff and scope
  3-5 year pre-roadmap horizon
Sept 2019: Power Delivery, FIVR Chiplets, GaN
Dec 2019: Tightly Coupled In Package Memory
Mar 2020: 3DIC Reference Design & Test Chip Proposal
  2020 1H: HBI-A (Foveros style)
  2021 1H: HBI-B (ODI style)
Today: 3DIC Reference Design & Test Chip Roadmap
  2021 2H: HBI-C ADM memory stack with power delivery solution

## Slide 3: Outline
Proposal
Finding the Optimum Solution
Ingredients
Intel Differentiating Opportunity
IDM Advantage through Tightly Coupled Logic/Memory
In-Package Memory
Memory/Logic Integration
System-Technology Co-Optimization
Accurate/Agile Pathfinding
3DIC Reference Design
IDM Advantage through Tightly Coupled Logic/Memory
Memory
Requirements/Technologies
Memory/Logic/Power/Packaging
Integration Challenges
Accurate/Agile Pathfinding
3DIC Reference Design
Technology Development/Validation
3DIC Test Chip

## Slide 4: Tightly coupled IPM plays to IDM advantage
An IDM can co-optimize across memory and logic technologies, packaging architectures, power delivery & thermals, test, chiplet partitioning and design
Benefit  System-Technology Co-optimization, Flexibility, Cost vs Price
 | IDM/ Intel | Fabless/ Foundry | Memory Vendor
In Package Memory Technology (eg 1222 ADM) |  | ? | ?
Advanced Packaging Technologies (eg, EMIB, Foveros, ODI, HBI at Intel; SOIC at TSMC, HBI at memory vendor) |  |  | 
Logic Technologies (eg 1274, 1276, 1278) |  |  | 
Power Delivery Technologies (eg 1222 FIVR, GaN) |  |  | 
Thermal Solution |  |  | 
Test for known good die (SDX) |  | ? | 
Chiplet partitioning and design |  |  | 
System-Technology Co-optimization |  |  | 
Flexibility |  |  | 
Cost vs Price to Intel |  |  | 
Lakefield
Foveros
TSMC hybrid bonding memory + logic
Notes: Die on wafer is the first intercept for memory stacking.

## Slide 5: STCO: Areas for Improvement for IPM
Co-optimization parameters include chiplet partitioning, packaging architectures (ODI, HBI), TSV-RDL-metal stack, MIM, memory array architecture, power delivery, thermal solutions, sort test requirements
Memory capacity erosion due to
Top die power delivery TSVs
Die-to-die interconnect
Top die IO feedthroughs
4.5MB/mm2 => 2MB/mm2
Codependence between
Top & bottom die
Die & package
Hard IPs
Result
Brittle floor plans
Lower base die utilization
Reduced ROI
MTL base die floor plan
IO feedthroughs
Die to die interconnect microbump fields
DLVR TSVs
IPM = In Package Memory
Notes: Note: If any of these chiplets had std interfaces would they be reusable beyond MTL? Probably not.

## Slide 6: Memory Solutions & Workload Mapping
Memory BW, capacity, cost data 7/20: Percy Soto, Kuljit Bains
Chart: 
| 0.1 | 0.15 | 1 | 3 | 12 | 36 | 2 | 4 | 8 | 16 | 0.5 | 0.6 | 1 | 1.2 | 3.6 | 5.4 | 8 | 24 | 32 | 96 | 48 | 144 | 16 | 64 | 32 | 128 | 16 | 64
LPDDR5 | 134 | 134 | 268 | 268
DDR6 DIMM | 102 | 102 | 204 | 204
SRAM | 4000 | 4000
GDDR6 | 96 | 96 | 1152 | 1152
ADM Gen1 | 300 | 300
ADM Gen2 | 1024 | 1024
4-6 Stacked ADM, 90% efficiency | 4096 | 6144
HBM3 | 614 | 614 | 2456 | 2456 | 3684 | 3684
HBM3
1, 4, 6 stacks
SRAM
New hierarchy for high BW/W
ADM Gen1
ADM Gen2
Bandwidth (GB/s) vs Capacity (GB)
ADM
Gen2
4 hi stack
GDDR6
1, 12 channels
DDR and LPDDR
Challenges:
HBM
huge capacity
cost ~$6.5/GB, price ~$13/GB
minimum price ~$100
power < 4 pJ/bit
GDDR
large PHY & board footprint
cost ~$2/GB, price ~$4/GB
power ~14 pJ/bit
ADM
custom BW and capacity
can scale above 6 TB/s
cost $10-12/GB (Gen2)
power < 2 pJ/bit
SRAM
high cost
high leakage power
DL inferencing
HPC
WORKLOADS
3D Graphics
Client 2LM
DL training
DL training
Notes: Fatih: assume 6TB/s/GB is the slope for ADM
3D graphics: integrated need 1GB, 500GB/s; discrete need 1-2GB, 4TB/s
DL training: need 20-30GB, 4-8X HBM
Client 2LM: need 4-8GB, 300GB/s
The BW for the WLs spans a large range. I think it is better to show it as a rectangle up to 4TB/s for HPC, up to 1TB/s for 3D dgfx. For DL, the BW is actually very high for small capacity and then reduces for larger capacity – but still need HBM BW at large capacity
Slide 6:
All these solution rectangles can extend down to .1GB i.e. anything of less than 1GB also fits in a 1GB memory
Slice 7:
The stacked ADM needs to overlap with DL training and HPC rectangles… otherwise it falls in valley of death where it is not solving a problem. This will be easier to show if slide 5 shows a BW vs capacity rectangle that goes from .1GB to whatever, .1GB to 100GB in case of HPC and DL training

## Slide 7: Different Options Pros/Cons
HBM: high cost, overprovisioned capacity for GFX and client 2LM
GDDR: high power
SRAM: high cost, very low capacity
High BW fine-grained DRAM
- not available, no information
ADM: need more capacity, 4 to 6 GB for Client 2LM & datacenter accelerators
+ customize capacity with stacking
+ System Technology Co-Optimization favors Intel’s strength
 Recommend pursuing HBI-C stacked ADM reference design and testchip
Notes: 3 columns, external, in package, tightly coupled

## Slide 8: Outline
Proposal
Finding the Optimum Solution
Ingredients
Intel Differentiating Opportunity
IDM Advantage through Tightly Coupled Logic/Memory
In-Package Memory
Memory/Logic Integration
System-Technology Co-Optimization
Accurate/Agile Pathfinding
3DIC Reference Design
IDM Advantage through Tightly Coupled Logic/Memory
Memory
Requirements/Technologies
Memory/Logic/Power/Packaging Integration Challenges
Accurate/Agile Pathfinding
3DIC Reference Design
Technology Development/Validation
3DIC Test Chip

## Slide 9: 3DIC Solution Space for STCO Exploration
Problem or requirements | Possible solution
Power delivery and HSIO feedthroughs | ODI with copper pillars (similar to SOIC TDVs) FIVR chiplets where applicable
Routing flexibility, MIM | Middle interposer
Memory capacity | ADM scaling roadmap and multi-die HBI stacks
Thermals | Cold spray (Research)
Sort test, debug | Sacrificial RDL (Research)
Standardized die-to-die interfaces | Synthesis and compilers
Middle interposer
Notes: For super thin layers, wafer to wafer bonding would be better. Temp limits have to be managed.
What would we have exercised for MTL for a reference design that would have surfaced. If this Testchip would have been built, we would have saved x, y, z, etc. Deliberately degrade and measure some of these parameters. What is the actual impact of crappy power delivery.
Propose topside power delivery as a research direction.

## Slide 10: 3DIC Sandbox, Reference Design & Flow, Testchip Deliverables
Sandbox of key ingredients for STCO
Technologies and experimental PDKs
3DIC: Packaging architectures (Foveros, ODI, HBI), TSVs, RDL
Silicon technologies (Logic, memory, interposer)
IPs
3DIC die2die: FDI, DSI
Compute: Atom, ARM cores
Memory HIP
Power delivery: DLVR, FIVR
HSIO: PCIe, DDR
Test Chip
Full technology and TFM validation
Reference Design & Flow
Tools, flows, methods
  3DIC Project Moore Cockpit
Evaluate overall subsystem/system performance & interactions
Rapid exploration and learning
ROI:
Iron out inter-dependencies
Path clearing for PDK and tools, flows, methods (TFM)
Proven reference design (scripts, collateral, docs) to bootstrap projects
De-risk execution
Shift towards capabilities in support of product and technology portfolio
STCO: select/adjust technologies based on reference flow feedback
Down-selection to a specific implementation
Notes: Convert MTL to a shell only reference design
    path clearing PDK/TFM/etc.?
    prototyping 3DIC configurations (like fine-pitch ubumps, 3 levels of stacking, …)
    provide a “sandbox” of IPs for 3DIC system technology cooptimization studies
    provide design test-case to bring-up new capabilities in (design, tools, packaging, sign-off methods, …)
For the cross-org structure and roles and responsibilities, can you, together with Sonia and Nick put this together? We should put it together and review it with a different set of managers (Gary Patton, Daaman?, Ahmad?, etc).
Thanks,
Ramune
From: Rajan, Vivek K <vivek.k.rajan@intel.com> Sent: Friday, July 17, 2020 9:31 AM To: Nagisetty, Ramune <ramune.nagisetty@intel.com> Cc: Kuhlman, Nick <nick.kuhlman@intel.com>; Elsherbini, Adel A <adel.a.elsherbini@intel.com> Subject: RE: TDBU Coop slide review
Hi Ramune –
Thanks for driving 3DIC Reference Design and TC TDBU Proposal.
Few suggestions for the proposal:
It would be good to include 1-2 slides on following:
  What key aspects of “design enablement” will reference design and TC (each) focus on
  What exactly does design enablement mean in this context?
    Example: is it path clearing PDK/TFM/etc.?
    Example: is it prototyping 3DIC configurations (like fine-pitch ubumps, 3 levels of stacking, …)
    Example: is it going to provide a “sandbox” to IPs to validate their 3DIC Integration readiness
    Example: is it going to provide design test-case to bring-up new capabilities in (design, tools, packaging, sign-off methods, …)
    ….
Also, it would be good to propose a structure to make this successful
  What kind of structural support do we need to make this jump-start and successful with BU teams
  Such a capability (3DIC reference design and TC, being integration vehicles) are essential from a portfolio aspects
  What support and structures do we need for portfolio level of engagement
  For example: at Intel PDK is successful because of its Portfolio role. Earlier every BU had its own Library development, funding, etc., and now there is a well-organized structure to make PDK successful at Intel on numerous processes
  Similarly, it would be good to propose a structure for 3DIC Reference Design and TC, including R&R
A slide or two, that pictorially shows all the building blocks for this this proposal
  What already exists (green-color), what capabilities can be integrated quickly (orange-color), what would need new development/enabling, etc ..
  Something that should a development cadence and structural process

## Slide 11: 3DIC Test Chip Roadmap
1H’20: HBI-A Foveros style 1222/10 nm SRAM stacks
  Already taped out
1H’21: HBI-B ODI with 1276+ HSIO on passive interposer
  Slated to be Panther Creek derivative in Q4’20
    Far backend DRs aren’t ready, slip to Q1’21, Wolverton Creek
2H’21: HBI-C ADM memory stack
  Die on wafer (for > 2 um pitch, > 30 mm2 die)
  Wafer on wafer (for < 2 um pitch, < 30 mm2 die)
  Memory stacking, scalable solution
  System technology co-optimization with power delivery, thermal solution, test
Notes: 1H’20: HBI-A Stacked SRAM 10 nm on 1222, already taped out.
1H’21: HBI-B with ODI, was slated to be Panther Creek derivative in Q4’20, but since design rules aren’t ready it will slip to Q1’21
2H’21: HBI-C ADM stacking using die to wafer HBI. The primary goal is to do a strawman design that includes STCO.
Pitches less than 2 um would be wafer to wafer. And then have to do something with yield loss.
Talk to sriram.srinivasan@intel.com about DRM ADM stacks.

## Slide 12: Next Steps
Build the 3DIC reference design STCO sandbox
  Utilize MTL architecture as starting point
  Utilize IPs from shuttles (power delivery, HSIO, Die2Die IO)
Establish cross-org roles and responsibilities
  TD: DE, LTD, ATTD, CR
  IPSG: PESG, IP Testchips
Resources for Plan 2021
  + DE allocating 5 HC
  - Need resource allocation for IPSG 3DIC testchip swimlane
Notes: Need a Testchip roadmap that defines the technology path, rather than a product roadmap that defines just in time testchips.

## Slide 13: Backup

## Slide 14: IDM Advantage
Information sharing, simpler business processes
Access to internal and external silicon
Silicon, packaging, test, design under one roof
Control everything up to the package boundary
Can optimize for power delivery and thermals
Ability to do System Technology Co-Optimization

## Slide 15: Key direction: New memory focused on high BW
Chart: BW vs Capacity for various Memory Devices
| 2
DDR4 | 3.2
LPDDR5 x16 | 10
GDDR6 8Gb 18GT/s | 72
GDDR6 16Gb 18GT/s | 72
HBM2e 4hi | 358.4
HBM2e 8hi | 358.4
HBM3 8hi 4GT/s | 512
HBM3 8hi 6.4GT/s | 819.2
HBM2e 4hi, EOL
LP5
GDDR6 8Gb, EOL
GDDR6 16Gb, EOL
GDDR7 8Gb, EOL (optimistic)
HBM3 8hi, EOL
ULTRA HIGH BW
NEW BW FOCUSED MEMORY
TRADITIONAL CAPACITY FOCUSED DRAM
SRAM
New form of memory solution for 10s of TB/s, 10s of GB
ADM
Slope is BW/capacity ratio

## Slide 16: Memory Solutions
Chart: 
| 0.1 | 0.15 | 1 | 3 | 12 | 36 | 2 | 4 | 8 | 16 | 0.5 | 0.6 | 1 | 1.2 | 3.6 | 5.4 | 8 | 24 | 32 | 96 | 48 | 144 | 16 | 64 | 32 | 128 | 16 | 64
LPDDR5 | 134 | 134 | 268 | 268
DDR6 DIMM | 102 | 102 | 204 | 204
SRAM | 4000 | 4000
GDDR6 | 96 | 96 | 1152 | 1152
ADM Gen1 | 300 | 300
ADM Gen2 | 1024 | 1024
4-6 Stacked ADM, 90% efficiency | 4096 | 6144
HBM3 | 614 | 614 | 2456 | 2456 | 3684 | 3684
Memory BW, capacity, cost data 7/20: Percy Soto, Kuljit Bains
HBM3
1, 4, 6 stacks
SRAM
New hierarchy for high BW/W
ADM Gen1
ADM Gen2
Bandwidth (GB/s) vs Capacity (GB)
ADM
Gen2
4 hi stack
GDDR6
1, 12 channels
DDR and LPDDR
Challenges:
HBM
huge capacity
cost ~$6.5/GB, price ~$13/GB
minimum price ~$100
power < 4 pJ/bit
GDDR
large PHY & board footprint
cost ~$2/GB, price ~$4/GB
power ~14 pJ/bit
ADM
custom BW and capacity
can scale above 6 TB/s
cost $10-12/GB (Gen2)
power < 2 pJ/bit
SRAM
high cost
high leakage power
DL inferencing
HPC
WORKLOADS
3D Graphics
Client 2LM
DL training
DL training
$7
ADM Gen1
~.0.5 GB
$24-48
GDDR
6 to 12 GB
$100
HBM3
8 GB
$44
ADM Gen2
4 stack
~4 GB
Notes: Fatih: assume 6TB/s/GB is the slope for ADM
3D graphics: integrated need 1GB, 500GB/s; discrete need 1-2GB, 4TB/s
DL training: need 20-30GB, 4-8X HBM
Client 2LM: need 4-8GB, 300GB/s
The BW for the WLs spans a large range. I think it is better to show it as a rectangle up to 4TB/s for HPC, up to 1TB/s for 3D dgfx. For DL, the BW is actually very high for small capacity and then reduces for larger capacity – but still need HBM BW at large capacity
Slide 6:
All these solution rectangles can extend down to .1GB i.e. anything of less than 1GB also fits in a 1GB memory
Slice 7:
The stacked ADM needs to overlap with DL training and HPC rectangles… otherwise it falls in valley of death where it is not solving a problem. This will be easier to show if slide 5 shows a BW vs capacity rectangle that goes from .1GB to whatever, .1GB to 100GB in case of HPC and DL training

## Slide 17: Memory Requirements
Input from DL memory WG
Chart: Peak Bandwidth (GB/s) vs Capacity (GB)
| 0.1 | 0.15 | 0.3 | 1 | 2 | 3 | 2 | 4 | 1 | 1.2 | 4 | 6 | 8 | 20 | 24 | 30 | 64 | 100 | 192
DL Inference | 500 | 500 | 500
3D integrated GFX | 500
3D discrete GFX | 1000 | 1000
Client 2LM | 300 | 300 | 300
DL training | 4000 | 4000 | 4000
HPC/DL recommendation | 1500 | 1500
Client 2LM
DL inference
3D int GFX
3D discrete GFX
HPC
DL training
DL training
BW
capacity
Capacity is function of
compute assumption
Need to fill machine

## Slide 18: Physics and Technology Trends
Slowing scaling trend for logic and memory
Rise of accelerators
Range of DL architectures and workloads
  Inference, training, HPC/DL
Range of memory requirements
Range of memory solutions