## Slide 1: Beyond P1241
Option-1: 4 Deck Cross Point Array Stack / PQ, F=10.25nm – Feff = 5.125nm
Option-2: 3D Tier w/o TFT – Feff = 14.5nm  not scalable, (= dual deck cross point array)
Option-3: 3D Tier with Pillar Select X’tor, 2 bits per pillar per tier – Feff = 10.25nm /  This work
Option-4: 3D Tier with Pillar Select X’tor, 1 bits per pillar per tier

## Slide 2: 3DXP stacking: From Deck to Tier
DerChang, Prashant, Max, Khaled, Mase 11/27/2018
3D Tier Features
Design Rules
Tile Size
Process Flow
TFT
Product Physical attributes
Scaling
4 decks
S26

## Slide 3: 8X8X9 example: 9 Tiers, 4X8 Pillars, 2b/(pillar X tier)

## Slide 4
WL Comb: 2 WL Decoders per Tier
Pillar Select Transistor (PST)

## Slide 5: Design Rules
Cell Width = PST Space + 2 (Gate Thickness + Tox) + Pillar Width
Cell Length = ½ (WL Width + Pillar Length) + Memory Length
To achieve effect cell size equal or better than 4-Deck SXP cell, # of tiers Cell width Cell Length / 2
Memory width = 20.5nm (1F), Effective F = 10.25nm for one deck
Cell Width
Cell Length
Pillar Width
Pillar Length
Mem Width
Mem Length
½ WL Width
PST Width
Gate Thickness
Tox
PST Space
Design Rules | nm | 130 ref
Cell Width | 164 | 164
PST Space | 62 | 
Gate Thickness | 20 | 
Tox | 10 | 
Pillar Width | 63 | 67 (ch)
Memory width | 20.5 | 
Memory Space | 120 | 
Pillar Space | 101 | 
Cell Length | 164 | 148
WL Width | 42 | 
Memory Length | 110 | 
Pillar Length | 64 | 67 (ch)
PST Width | 270 | 
Effective F (SLC) | 10.25 | 6.49
Tier Height
Tier Space
3D Construct |  | 130 ref
F | 20.5nm | 
Cell footprint | 64F2 | 58F2
# of Tier: | 64 | 48x3
Tier Height | 20nm | 35nm
Tier Space | 30nm | 20nm
Pillar Metal AR | 50 | 45

## Slide 6: Strategy to Construct Multi-Tier Array
Goal: Equal or better than 4D 3DXP in BW/(GB/$)
  ≤ 1F2/bit, CUA & ≤ 13 immersion layer to increase GB/$
  Build smaller tile (parallelism, lower CV2) to increase BW
≤ 1F2/bit: Multi-tier
  NTier ≥ lengthcell ∙ widthcell / F2
2 bits per pillar per tier
  Tile Capacity = 2 ∙ NPillar ∙ NBL ∙ NTier
CUA: Decoders and Tile control/logic 100% under Array
  ∵ footprintarray ≥ footprintCMOS ∴ min number of BL and Pillar can be estimated
Optimize Tile size vs. WL capacitance
  To lower WL (tier-to-tier) cap, orient WL the same as BL geometrically & chop the stack evenly into npile
WL:
Tier Bias
BL:
Pillar Bias
PS: Pillar Select
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
NBL
NPS
NBL
NPS
Npile
1

## Slide 7: Product Physical Architecture
Technology | P1240 | P1240.T1 | P1241 | P1241 PF | P1241.T2 | P1242.T3 | P1243.T4
Product | ALF32 |  | ATF-64 | ATF-64 |  |  | 
Effective F [nm] | 10.25 | 10.25 | 7 | 7 | 7.25 | 5.92 | 5.125
Die Capacity [GB/die] | 32 | 32 | 64 | 64 | 64 | 96 | 128
Array overhead [%] | 16 | 22.5 | 16 | 16 | 22.5 | 22.5 | 22.5
# of Partition | 32 | 72 | 64 | 64 | 72 | 72 | 72
# of tile / Partition | 128 | 128 | 128 | 128 | 128 | 128 | 128
Tile Capacity [Mb/Tile] | 64 (75) | 28 (32) | 64 (75) | 64 (75) | 57 (64) | 86 (96) | 114 (128)
Tile Footprint [𝜇m2/Tile] | 181 X 181 | 88 X 175 | 124 X 124 | 124 X 124 | 88 X 175 | 88 X 175 | 88 X 175
# Deck | 4 | 1 | 4 | 4 | 2 | 3 | 4
# of Tier / Deck | N/A | 64 | N/A | N/A | 64 | 64 | 64
# of Pile / Tile | N/A | 28 | N/A | N/A | 14 | 9 | 7
# of WL Driver / Tile | 8K | 1*2*64*28 | 8K | 8K | 2*2*64*14 | 3*2*64*9 | 4*2*64*7
# of BL Driver / Tile | 8K | 512 | 8K | 8K | 512 | 512 | 512
# of PS Driver / Tile | N/A | 512 | N/A | N/A | 512 | 512 | 512
WL Resistance [KΩ] | 23.8 | 21.3 | 29.7 | 29.7 | 21.3 | 21.3 | 21.3
BL Resistance [KΩ] | 10.4 | 4.26 | 13 | 13 | 4.26 | 4.26 | 4.26
Pillar Resistance [KΩ] | N/A | 0.16 | N/A | N/A | 0.32 | 0.48 | 0.72
PST on-resistance [KΩ] | N/A | 3 | N/A | N/A | 3 | 3 | 3
WL Cap [fF] | 92 | 143 | 92 | 92 | 287 | 446 | 573
BL Cap [fF] | 92 | 2.61 | 92 | 92 | 2.61 | 2.61 | 2.61
PS cap [fF] | N/A | 28 | N/A | N/A | 28 | 28 | 28
Net Array [mm2] | 141 | 143 | 141 | 141 | 143 | 143 | 143
Net CMOS [mm2] | 143 | 144 | 143 | 143 | 144 | 143 | 144
Assumption:
P1240 Cell char used
𝜌metal = 203 Ω∙nm (WL, BL, P)
𝜖dielectric = 8𝜖0 (for isolation)
PST (LG=75nm, 5Volts, 110uA) ON-resistance 3KΩ Off leakage 10nA (VG=0V)
Non-decoder area: 9500 𝜇m2/Tile (vs. 11750 𝜇m2/Tile of ALF32)
Decoder size:
1.331 𝜇m2/driver Use P1240 driver Same size for WL, BL, PS
Array overhead: sockets, spares, redundancy & dummies: 22.5 % of net array size (vs. 16% of ALF overhead)
WL:
Tier Bias
BL:
Pillar Bias
PS: Pillar Select

## Slide 8: Product Roadmap Discussion
Technology |  | P1240 | P1240.T1 | P1241 | P1241 PF | P1241.T2 | P1242.T3 | P1243.T4
Product |  | ALF32 |  | ATF-64 | ATF-64 |  |  | 
Platform PRQ |  | Eo’20 |  | Eo’21 | TBD | Eo22 | Eo23 | Eo24
Capacity [GB/die] |  | 32 | 32 | 64 | 64 | 64 | 96 | 128
Read BW [MB/s] |  | 3200 | 7200 | 4800 | 48-5400 | 7200 | 7200 | 7200
Write BW [MB/s] |  | 1100 | 2400 | 2200 | 2200 | 2400 | 2400 | 2400
Read E [pJ/b] |  | 39 | 21 | 28 | 25-21 | 21 | 21 | 21
Write E [pJ/b] |  | 100 | 66 | 77 | 72-66 | 66 | 66 | 66
Power [W] |  | 1 | 1.27 | 1.15 | 1.15-1.39 | 1.27 | 1.27 | 1.27
I/O Interface |  | DDR5/LPDDR5 | LPDDR5+ | LPDDR5+ | LPDD5+ | LPDDR5+ | LPDDR5+ | LPDDR5+
DDR Rate [MT/s] |  | 3200 | 3600 | 4800 | 4800-5400 | 3600 | 3600 | 3600
DQ |  | X8 | X16 | X8 | X8 | X16 | X16 | X16
Chop | Capacity [GB/die] | 16 (2D or 16P) | 16 (36P) | 32 (2D or 32P) | 32 (2D or 32P) | 32 (36P) | 48 (36P) | 64 (36P)
 | Read BW [MB/s] | 3200 | 4800 | 4800 | 48-5400 | 4800 | 4800 | 4800
 | Write BW [MB/s] | 1100 or 550 | 1200 | 2200 or 1100 | 2200 or 1100 | 1200 | 1200 | 1200

## Slide 9: Enablers – PST
Pillar Select Transistor
  5V, 110uA GAA transistor (H75nm , W270nm , T42nm , S62nm), On-Resistance 3KΩ
  PST capacitance is 28fF  Can we ½ dielectric constant (𝜖ox = 4𝜖0)?  Cps = 14fF, or sub ½ pJ to select a pillar.
  One immersion layer need
  Need to consider TFT formation flow, will channel dimension variation impact sigma of the select device? What is contact approach for control gate and does it impact design rule or landing pad area?
  Low temperature gate ox for pillar select – any reliability concerns?
  Contact to BL whether W BL or Cu w/ W plug, must form reliably at low temperature
  Contact resistance and Pillar-TFT interface needs to be capable within Cu thermal budget(~400’C) and interface clean must be selective to the tier isolation layer and 2nd cut isolation between pillars.
  Can add plug above and/or below for extra cost but require good contact formation at low temperature in all cases.

## Slide 10: Enablers – Array
Tier Array Process
  Two immersion layers for high AR cuts –
  1st cut is similar to 3D-NAND’s, depending on WL sac layer or WL conductor layer in the stack.
  ALD Chal, Carbon & W lamina – maintain composition uniformity at high aspect ratio for chal films
  Recess process control: thickness control impacts - sigma in Vt, delta Vt, Iprogram (heaters) ~ endurance/WD
  2nd cut pattern generation (pillar wider than bit is required) OPC risk do we require two pass print + resist trim?
  2nd cut etch capable of W lamina removal over entire height of bit (vertical lamina) without chal damage
    PM and SD by definition exposed to full etch, GX style ALD dep protection possibly required. Reduce tier height (non-square area of bit).
  Replacement Pillar Metals, liner with good good contact to TE carbon and pillar select source/drain and barrier properties for W dep.
  Replacement or subtractive tier metal (Ruthenium Tier metal?)
    Flow does not have a clear replacement option currently. Need to either formulate replacement flow or enable tier stack “sac” layer as WL conductor.

## Slide 11: Enablers – Design
Design Technology
  Non-decoding circuit and/or CMOS 20% area scaling
Read/Write Energy matches “P1241PF” BKM energy. (1.27W/die required)
  Additional 5 to 10% of Write Energy reduction (IRESET = 110uA vs. 70uA in P1241 DTS)
Process Costs
  High Density Routing: two to four immersion layers are estimated
  TFT Technology: one immersion layer needed
  Two immersion layers for high AR cuts
  Invention of Etch/ALD
  vs.
  4D SXP reference – 13 immersion layers including
    8 PD or PQ + 5 OPV layers
    4 times “Rinse & Repeat” of 1st and 2nd partial cuts

## Slide 12: Replacement Tier/Pillar Process Flow
Array Key Processes: 2 immersion layers, 2 high AR cuts, ALD Chal & Carbon Replacement Tier & Pillar Metals

## Slide 13: Memory Tier Stack – 4 Tiers in the exhibit
Silicon Pillar
BL Poly
Memory Tier
Cell 1st Cut
Cell 2nd Cut
WL Poly
Alternate stacking sacrificial layer and dielectric layer to build memory tiers.
Sacrificial material, eg. silicon
Dielectric, eg, oxide

## Slide 14: Tier Stair Formation – an 8-tier exhibit
Mask
Tier Stair Etch
Mask
Mask
Mask

## Slide 15: 1st Cut: Opening for Cell Stack Materials
Silicon Pillar
BL Poly
Memory Tier
Cell 1st Cut
Cell 2nd Cut
WL Poly
A
A’
A
A’
Tier Stair not shown
64nm

## Slide 16: Tier Sacrificial Layer Recess Etch
A
A’
A
A’

## Slide 17: 1st Electrode
First Electrode Conformal Dep
First Electrode Recess Etch
A
A’
A
A’

## Slide 18: SD
SD Conformal Dep
SD Recess Etch
A
A’
A
A’

## Slide 19: 2nd Electrode & PM
PM Etch
2nd Electrode dep/etch, PM Conformal Dep
PM Etch
A
A’
A
A’

## Slide 20: 3rd Electrode & Fill: Replacement for Pillar
2nd Electrode Dep/Etch
Sacrificial Pillar Nitride Dep Etch/CMP
A
A’
A
A’

## Slide 21: End of 1st Cut module
A
A’
A
A’
Tier Dielectric, eg. Oxide
Sacrificial material for Tier metal (WordLine), eg. amorphous Silicon
Sacrificial material for Pillar metal (BitLine), eg. Nitride
1st, 2nd, 3rd Electrode, eg. Carbon
Selector, eg. SAG
Memory,
eg. GST

## Slide 22: 2nd Cut definition
Silicon Pillar
BL Poly
Memory Tier
Cell 1st Cut
Cell 2nd Cut
WL Poly

## Slide 23: 2nd Cut
Top Dielectric Removed

## Slide 24: Tier Metal Replacement
Isotropic sacrificial tier material (eg. amorphous silicon) etch then conformal Metal dep (eg. ALD W) fill the gap,
followed by anisotropic
metal etch removing
metal in the 2nd cut
opening region then gap
filled with oxide(not shown)
With
top dielectric
removed, Array with
Tier Stair (termination)

## Slide 25: Pillar Metal Replacement
Isotropic sacrificial pillar material (eg. nitride) removed then Metal (eg. W) fill the gap
gap filled oxide and top tier dielectric are not shown
(not shown)

## Slide 26: Backup Material

## Slide 27: Strategy to Construct Multi-Tier Array
Goal: Equal or better than 4D 3DXP in BW/(GB/$)
  1F2/bit, CUA & ≤ 13 immersion layer to increase GB/$
  Build smaller tile (parallelism, lower CV2) to increase BW
Assumptions
  Number of BL = Number of Pillar = n
1𝝀2/bit: Multi-tier
  ntier = lengthcellwidthcell/F2
CUA: Decoders and Tile control/logic 100% under Array
  footprintarray = 2∙lencellwidcell∙n2
  footprintCMOS = 2∙(npile∙ntier+n)∙fpdec+fpcntl
  ∵ footprintarray ≥ footprintCMOS ∴
Optimize Tile size vs. WL capacitance for BW
  To lower WL (tier-to-tier) cap, orient WL the same as BL geometrically & break the stack evenly into npile ∴
WL:
Tier Bias
BL:
Pillar Bias
PS: Pillar Select
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
nBL
Y
nBL
nPS
npile
1
2∙lencellwidcell∙n2
2∙(npile∙ntier+n)∙fpdec+fpcntl

## Slide 28: Partition Control/Logic/Referencing impact to Tile Attributes

## Slide 29: Array Architecture
SXP Tile Reference: 64Mb/tile of 4𝝀2 cell in 4Kx4KX4D – Floor space = 4K∙4K∙4𝝀2, # of decoders = 2∙(4K+4K)  decoder footprint (fD)= 4K𝝀2  decoder footprint assumption for all WL/BL Length for Lumped capacitance = 2𝝀∙8K = 16K𝝀
Tier architecture: 96 WL (48 tiers of comb pair), X BL & Y PS, PS length = 2 ∙ 6.93𝝀 ∙ X, BL Length = 6.93𝝀 ∙ Y, WL Length= PS Length ∙ Y / 2
To ensure 100% decoders 100% under the tile (96 + X + Y) ∙ 4K𝝀2 ≤ X ∙ Y ∙ 2 ∙ 48𝝀2
If X = Y  A Tile will be 96 WLs, 120 BL/PS or 1.318Mb/tile BL length = 1.623K𝝀, PS Length= 0.812K𝝀, WL Length= 48.7K𝝀
WL:
Tier Bias
BL:
Pillar Bias
PS: Pillar Select
N Piles of 48-Tier array: N ∙ 96 WL BL length = 6.93𝝀∙Y, PS Length= 6.93𝝀∙X, WL Length= PS Length∙Y/(2∙N )
To ensure 100% decoders 100% under the tile (N ∙ 96 + X + Y) ∙ 4K𝝀2 ≤ X ∙ Y ∙ 2 ∙ 48𝝀2
If N=128, X = Y  12K WLs, 768 BL/PS or 54Mib/tile BL length = 10.4K𝝀, PS Length= 5.2K𝝀, WL Length= 16K𝝀
If N=16, X = Y/N  1.5K WLs, 91 BL, 1.4KPS or 47Mb/tile BL length = 20K𝝀, PS Length= 630𝝀, WL Length= 28K𝝀
To reduce WL Cap, breaking down one tile into multiple piles of of 48-tiers of WL
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
∙
X
Y
X
Y
N
1

## Slide 30: Tile Size and First order WL/BL capacitance estimate (𝝀 = 20.5nm)
4 decks of 4K BLs x 4K WLs
1𝝀2/b, 64Mb/Tile, 64M𝝀2/Tile
Tile size: 168𝝁m X 168𝝁m
LBL = LWL = 2𝝀 ∙ 4K = 8K𝝀
HBL = HWL = 100nm ≈ 5𝝀
SBL = SWL = 20.5nm = 1𝝀
CBL + CWL = 2 ∙ 𝝐 ∙ L ∙ H / S = 80K𝝀𝜺
8 Piles of 48 Tiers in 229 pillars x 229 BLs
1𝝀2/b, 4.8Mb/Tile, 4.8M𝝀2/Tile
Tile size 33𝝁m X 65𝝁m (1 : 13.3)
LBL = 2 ∙ LPS = 2 ∙ 6.93𝝀 ∙ 229 = 3K𝝀
LWL = LPS∙NumPS/(2∙8) = 22K𝝀
CBL = 𝝐∙LBL∙HBL(40nm)/SBL(180nm) = 0.689K𝝀𝝐
CWL = 𝝐∙LWL∙WWL(40nm)/SWL(40m) = 22.2K𝝀𝝐
CPS = 𝝐∙LPS∙HPS(300nm)/SPS(40m) = 14.2K𝝀𝝐
CBL + CWL + CPS = 37.1K𝝀𝝐

## Slide 31: 130 Design Rule

## Slide 32: Tile Density & Dimension Estimate
Cell size = (164nm)2, Tier count = 64
To ensure 100% decoders 100% under the tile, NPS = NBL = Ndec is calculated for effective F = 10.25nm (2 ∙ 64 ∙ Npile + 2 ∙ Ndec) ∙ FPdec + FPcntl ≤ 2 ∙ Ndec2 ∙ (164nm)2
  Assumption:
  FPcntl – 30% of a P1240 tile floorspace is used by control
  FPdec -- 70% of a P1240 tile floorspace is taken by 16K decoders
Benchmark reference tile: ATF32 64Mb/tile (4Kx4KX4D, Effective F = 10.25nm) –
Iso memory density: 1𝝀2/bit
Tile size reduces to 32Mb/tile @ Npile=16
Bandwidth
  Operable bit density increase 2X  Latency constraint BW doubled
  Displacement energy of a tile reduces 2X  Power constraint BW doubled
Reliability
  BL capacitance reduces ~50X  Snapback impact alleviated
Ratio to ALF32 Tile Attributes

## Slide 33: Scaling Options for Strategy Development Multi-Deck: Stack of 64-Tier deck – Effective F (SLC) =
ALF32 Reference
#WL = #BL = 4K DensityTile=64Mb/tile RWL = 23.9K𝛀 RBL = 9.8K𝛀 CWL = 47fF CBL = 82fF
Moving 100fF 0V↔3V consumes ~1pJ.
Opt 1:
Constant Npile = 16
Opt 2:
Constant Tile Size
Opt 3:
Constant CWL

## Slide 34: 3D XPoint™ Roadmap
Technology |  | 10s | 20s | P1240 | P1241 | P1241.PF
Product |  | S15 | S26 | ALF32 | ATF-64 | ATF-64
Platform PRQ |  | Eo’18 | Eo’19 | Eo’20 | Eo’21 | TBD
Capacity [GB/die] |  | 16 | 32 | 32 | 64 | 64
Read BW [MB/s] |  | 1600 | 1600 | 3200 | 4800 | 48-5400
Write BW [MB/s] |  | 550 | 800 | 1100 | 2200 | 2200
Read E [pJ/b] |  | 71 | 52 | 39 | 28 | 25-21
Write E [pJ/b] |  | 170 | 118 | 92 | 77 | 72-66
Power [W] |  | 0.9 | 0.75 | 1 | 1.15 | 1.15-1.39
X8 I/O Interface |  | DDR4 | DDR4 | DDR5/LPDDR5 | LPDDR5+ | LPDD5+
DDR Rate [MT/s] |  | 1600 | 1600 | 3200 | 4800 | 4800-5400
Chop | Capacity [GB/die] |  |  | 16 (2D or 16P) | 32 (2D or 32P) | 32 (2D or 32P)
 | Read BW [MB/s] |  |  | 3200 | 4800 | 48-5400
 | Write BW [MB/s] |  |  | 1100 or 550 | 2200 or 1100 | 2200 or 1100