## Slide 1: Deck Select
DerChang Kau, Prashant Majhi, Max Hineman,
NSG-CR Meeting, 2/4/2019 @ Santa Clara, CA
Deck Select Value Prop
3DXP Array with Deck Select Scheme
Deck Select Architecture

## Slide 2: Snap-On Cross Point Memory Array Value Proposition
Deck Isolation – 20% die size reduction enabled by Deck Select TFT
MDP replacement – Enabled by Deck Isolation, 40% die cost reduction for each additional die in package with multi-wafer stacking by sharing CMOS decoder/data path and I/O

## Slide 3: Deck Select TFTs enable decoder sharing cross decks
Reference Technology P1240
  ALF32 is 256Gb components in 200mm2
  4K tiles of 4 decks in 4K BL x 4K WL cross point array  16K WL and 16K BL decoders per tile
Deck Select enables decoder sharing among decks.
  Estimated 45mm2 die size reduction due to ½ of decoders reduction with deck-select

## Slide 4: Single-Deck Cross Point Memory Array
WL
Local BL Decoder
Global BL Decoder
Read/Write circuit
VPP
Local WL
Decoder
Global WL
Decoder
Data Path
Address Mux
VRR
Bit Lines
b0
b1
bm
bm-1
wn
wn+1
wn+2
W
VNN
1 Deck
1 set of WL drivers,
1 set of BL drivers
Memory
BL
WL
A
A’
B’
B
1 set WL Sockets
Isolation
1 set BL Sockets
Isolation
A
A’
B
B’
4K WL
4K BL

## Slide 5: Dual-Deck Cross Point Memory Array
WL
Local BL Decoder
Global BL Decoder
Read/Write circuit
VPP
Local WL
Decoder
Global WL
Decoder
Data Path
Address Mux
VRR
Bit Lines
b0
b1
bm
bm-1
wn
wn+1
wn+2
W
VNN
2 Deck
2 set of WL drivers,
1 set of BL drivers
Memory
BL
WL
A
A’
B’
B
2 sets WL
Sockets
Isolation
1 set BL Sockets
Isolation
A
A’
B
B’
4K WL
4K BL
4K WL
+

## Slide 6: Dual Deck Cross Point Memory Array with Deck Select
WL
Local BL Decoder
Global BL Decoder
Read/Write circuit
VPP
Local WL
Decoder
Global WL
Decoder
Data Path
Address Mux
VRR
Bit Lines
b0
b1
bm
bm-1
wn
wn+1
wn+2
W
VNN
Deck Sel
2 Deck
1 set of WL drivers,
1 set of BL drivers
Memory
BL
WL
A
A’
B’
B
1 set WL
Sockets
Isolation
1 set BL Sockets
Isolation
A
A’
B
B’
Deck Sel Mux
4K WL
4K BL
2

## Slide 7: Quad-Deck Comparison
POR
2 set of WL drivers,
2 set of BL drivers
Memory
BL
WL
A
A’
B’
B
2 set WL
Sockets
Isolation
A
A’
2set BL Sockets
Isolation
B
B’
1 set WL
Sockets
Isolation
A
A’
Deck Sel Mux
1set BL Sockets
Isolation
B
B’
Deck Sel Mux
Deck Select
1 set of WL drivers,
1 set of BL drivers
4 levels of Deck Select mux
For a 20nm Quad Deck 256Gb product, POR implementation (P1240/ALF32) is 200mm2.
The invention enabled by Deck Select TFT can reduce die size by 45mm2 (> 20% of die size reduction)
4K BL
+
4K BL
2
4K WL
+
4K WL
4K WL
4K BL
2

## Slide 8: 3DXP Deck Select Architecture
Deck Select Transistors integrated with Cross Point Array Technology
3 Deck Select TFT ideas – Ω, Fin, Saddle
Saddle TFT embodiment
Fin TFT embodiment

## Slide 9: ½ Kb Array: 8 decks of 8x8 cross point

## Slide 10: 3 ideas
Saddle-TFT
FIN-TFT
Ω-TFT

## Slide 11: Saddle TFT Process Flow
First Cut Gap Fill
70~110nm height
Deck Select TFT Placeholder:
200~400nm stripe opening,
Selective etch, 4nm/side W CD reduction
21nm tW+ 20nm dielectric recess
Channel Length Definition (50~100nm)
Oxidize W
Saddling up TFT Fin Channel Material
(fin height 41nm)
Array First Cut
14nm ½ pitch
Assumed: all done with chop mask array protect layer over array cells.
All depositions low temp (<300’C)
Recess less challenged, no need of selectivity to lowk CDO
W trim dry will impact array protect layer, wet may be preferred, grain structure impacts?
Need protect layer for area beyond channel which can be removed selective to everything including WOx
How will grain structure of W impact oxidation of the film? Volume expansion on oxidation – will lines buckle?

## Slide 12: Saddle TFT Process Flow (cont.)
Saddle Isolation (Spacer Etch)
Saddle TFT Oxide conforming Dep
Saddle TFT Gate Dep
etch back
tGate = 20~25nm
Saddle TFT
W CMP SOO or SON (array protect) then Nit CMP stop on C and W. Prior to or following via process will determine CMP interactions.
How to protect from next cut W etch by l/s pattern and chop or provide sufficient budget of W thick on top of structure.

## Slide 13: FinTFT Process Flow
Array First Cut
First Cut Gap Fill
Deck Select TFT Placeholder:
200~400nm stripe opening,
Selective stack material removal
Optional Spacer to define TFT FinFET width
TFT Fin Channel Material Dep
TFT Fin Height definition

## Slide 14: Fin TFT Process Flow (cont.)
TFT FinFET Oxide Dep
TFT FinFET Gate Dep
FinFET S/D Placeholder
TFT FinFET S/D Dep