## Slide 1: BiSM Occupancy
Balaji, Mase & DerChang, WW36.4/2019
3DXP vs. BiSM
BiSM Gap to goal and ideas for bridging
Topics for symmetric memory

## Slide 2: Read
3DXP Read Occupancy = 100ns
BiSM Read. Occupancy = 70ns
Read Pulse incl. Ramp
(37.5ns)
Sense Amp Latch
(12.5ns)
BL 1st Termination (20ns)
Start
Read Pulse incl. Ramp
(37.5ns)
Sense Amp &
Latch
(12.5ns)
SET Pulse 3 (25ns)
BL 1st Termination (20ns)
Set? (5ns)
Yes
No
Start

## Slide 3: Set a reset cell
3DXP Set Occupancy = 394ns (additional 55ns cycle time required for on chip pre-read)
BiSM Set Occupancy = 311ns (vs. 185ns required, 126ns gap)
WL/BL Ramp
(211ns)
Incl.
Spike Miti (71ns)
Snap Detect (45ns)
C-cell (95ns)
Ilow (P1)
(30ns)
Ihigh (P3)
(103ns)
P4
(30ns)
Start
BL1st
(20ns)
WL/BL Ramp
(211ns)
Incl.
Spike Miti (71ns)
Snap Detect (45ns)
C-cell (95ns)
Ihigh (P3)
(50ns)
Start
P4
(30ns)
BL1st
(20ns)
Reset state (done with pos write previously)  need negative write (need to select a high Vt)

## Slide 4: Reset a set cell
3DXP Reset Occupancy = 70ns
BiSM Reset Occupancy = 311ns(vs. 185ns required, 126ns gap)
Set state (done with neg write previously)  need positive write (need to select a high Vt)
WL/BL Ramp
(37.5ns)
Sense
(12.5ns)
Reset Pulse (15ns)
Set? (5ns)
Yes
No
Start
WL/BL Ramp
(211ns)
Incl.
Spike Miti (71ns)
Snap Detect(45ns)
C-cell (95ns)
Ihigh (P3)
(50ns)
Start
P4
(30ns)
BL1st
(20ns)

## Slide 5: BiSM Occupancy Gap to Goal
Set/Reset occupancy gap: 126ns
Ideas for bridging the gap
Selection
  C-cell bias consumes 140ns
  Ramp reduction to match “Read” (33.5ns)
Pulse Termination
  P4 (30ns)

## Slide 6: BiSM Write Spec – 240ns including preRead
Gap closure: c-cell eliminated + “Read” Ramp + Set P4 elimination ( – 203.5ns)
Match preRead polarity to write – no polarity switching
 Gain 203.5ns  77.5ns margin to Spec
Set Occupancy = 162.5ns including pre-read
Yes
Negative Read inc. Ramp
(37.5ns)
Sense Amp &
Latch
(12.5ns)
threshold (5ns)
No
Start
WL/BL Ramp
37.5ns
Including SpkMiti
Ihigh (P3)
(50ns)
BL1st
(20ns)
Reset Occupancy = 162.5ns including pre-read
Yes
Positive Read inc. Ramp
(37.5ns)
Sense Amp &
Latch
(12.5ns)
threshold (5ns)
No
Start
WL/BL Ramp
37.5ns
Including SpkMiti
Ihigh (P3)
(50ns)
BL1st
(20ns)

## Slide 7: Ideas for symmetric memory Match cycle time of WRITE to READ’s
WRITE: need 92.5ns reduction
  Memory organization to “hide” preRead (55ns) (common mode to 3DXP)
  P3 width reduction (~35ns?)
Yes
Write-Polarity Read + Ramp
(37.5ns)
Sense Amp &
Latch
(12.5ns)
Reset Occupancy = 162.5ns including pre-read
threshold (5ns)
No
Start
WL/BL Ramp
37.5ns
Including SpkMiti
Ihigh (P3)
(50ns)
BL1st
(20ns)
BiSM Read. Occupancy = 70ns
Read Pulse
inc. Ramp
(37.5ns)
Sense Amp Latch
(12.5ns)
BL 1st (20ns)
Start

## Slide 8: BiSM features and IP ideas
Built-in low energy write: Bipolar normal write
C-cell elimination: bipolar read refresh
Program Verification without disturb
Page buffer for symmetric memory

## Slide 9: Scratch Pad