## Slide 1: Quilt vs External comparison (01-20-11)
Conclusion:
For same budget requirements, same litho node, same transistor technology
Quilt offers smaller die size, cheaper metallization.
2K x 1K footprint (4Mbit tile)
2K WL drivers, 2K BL drivers
Shared BL, 2 deck
2K x 1K footprint (4Mbit tile)
2K WL drivers, 2K BL drivers
Shared BL, 2 deck
Tapping at mid-point of electrodes, reduces IR due to WL’s and BL’s significantly. This array IR advantage trades off against the reduced area available for the drivers.
Other areas to analyze:
Design complexity
Defectivity
Socket complexity
scalability
 | Ext driver | Quilt option 0
Glue layers | 2@4F | 1@4F
Die size – comparison only. | 202mm^2 | 157mm^2
WL leakage | 2K cells | 2K cells
IR drop in array | 2560r+driver | 1216r+driver
Area per WL/BL driver available | 1.72/1.12 um^2 | 1.04/0.68 um^2
Area per WL/BL driver required | 1.72/1.12 um^2 | 0.83/0.55 um^2
1.12um^2/Bldriver
1.72um^2/WLdriver

## Slide 2: Socket Complexity
Socket has been analyzed by litho team in Agrate.
The only obvious differences that come to my mind, comparing our preferred solutions for External and for Quilt are:
Quilt is more demanding on chop masks, because of the “sliding bundles” approach;
Quilt is more demanding on PV3 alignment requirements, due to the “traffic” of PM1 lines going from one tile to the other.

## Slide 3
Socket concept
(WL drivers for 2 decks example)
Even Pair
or even bundle
Odd Pair or odd bundle
One driver connected to only one word-line layer
Word-lines
Bit-lines
Word-line drivers
Bundle up electrodes and drive from opposite sides to create space for upper deck feed-through
Deck 1 WL
Deck 2 WL
Cross-section view
Top view

## Slide 4
Same socket approaches work for External and Quilt tile architectures
Connections to 2nd WL layer driver
Connections to 2nd WL layer driver
Connections to 2nd WL layer driver
QUILT
OPTION
EXTERNAL
DRIVER
OPTION
Simplest case
First Deck WL example

## Slide 5: Compatible with SADP – various options evaluated
Core Mask
Spacer pattern
Specifics of sockets to be discussed by Fabio

## Slide 6
Single Deck word-line sockets depicted as example
Same array litho node for two architectures
1 socket per tile in horizontal direction
4 sockets per tile in horizontal direction
Number of Sockets

## Slide 7
Ext: need 1 of these per tile
Socket Dimensions
(Assuming 10F pitch between geometries in orthogonal direction to array plus 10F on each side for array termination dummies. No vias under array)
110F
190F
One layer
Two layers
70F
110F
Quilt: need 4 of these per tile
One layer
Two layers
50F
70F
70F
110F
Bundle of 8
Bundle of 4

## Slide 8
Bundle of 8

## Slide 9: Defectivity handling
There are no isolated tiles in a quilt architecture
3D Cross-point memories can repair WL-BL shorts
  This has been the primary reason to repair entire tiles in planar technologies.
  Defects in the memory layers do not affect CMOS supply lines.
CMOS defect rates are low compared to array defect rates.
  PCM yield group estimates no significant yield loss due to this restriction

## Slide 10
BL-WL shorts
Intersecting ‘super-BL’ and ‘super-WL’ must be mapped out
Current during ABC biasing will be limited by resistance of deselection path.
Small current compared to leakage in 2T driver implementations.
AB or V/2 are not an issue.

## Slide 11
7v
0v
4v
3v
~3.5v
~3.5v
3v
4v
BL-WL shorts
Sort/First Fire
  BL-WL shorts are detected at sort and mapped out (or repaired)
  Cells on this BL or this WL do not First-Fire  therefore the thresholds for these cells are very large.
  If cells do FF and are able to SET, then it should be able to be RESET.
  If cells do FF and end up SET but cannot RESET, then allow them to drift.
AB biasing: Read, RESET, low Vth SET
  Since type C cells are shorted, there is no impact to other cells in the array
  No additional power dissipation
ABC biasing: high Vth SET
  Low resistance short may bring the affected BL/WL to intermediate value between DESWL and DESBL, which creates larger biasing for affected BL/WL.
  Additional bias on these cells do not impact de-biasing of high threshold cells (need to quantify limits)
  Short current is limited by deselected BL driver in series with deselected WL driver – estimated ~50uA. This is small compared to total leakage current in large arrays during ABC biasing.
Example during ABC biasing with BL-WL short
0.5v bias
3.5v bias of high Vth cell
0.5v bias
3.5v bias of high Vth cell
Short current
Cross-point biasing allows for BL-WL repairs even when BL and WL are shorted
Option: if likely-hood of high Vth SET is low, can allow ECC to correct for this?

## Slide 12: Replacing Bad Clusters
Smallest array unit to repair is a cluster.
Cluster size can be adjusted against cluster overhead to allow for process maturity
A 128Gb device has 512 clusters
  1K x 2K x 2d tiles
  64 quilt-tiles per cluster (8x8 tiles per cluster)

## Slide 13: Budget IR drop, Leakage, CMOS
Midpoint taps reduces IR drop and voltage requirement
  This reduced IR drop means the transistor requirements can also be reduced.
  Area required is also reduced
Additional resistance reduction because of quilting offset effect
  The farthest bit on the word-line, never aligns with the farthest bit on a bit-line. Offset is 25% for one or the other electrode.
The benefit can be traded off against
  Window budget
  CMOS process complexity
  Voltage requirement

## Slide 14
Driver Vds versus electrode IR trade-off
Z/L
Z”/L
384 r/2
128 r/2
512 r/2
1024r
1024r
1024 r/2
2048r
dVE ~ 0.5(2048ileak *2048r)
dVQ ~ 0.5(1024ileak *1024r) = ¼ dVE
2048ileak
(1024+1024)ileak
Z/L
E
Q
Transistor size limited by leakage requirements during selection of reset cells.
Same terminal voltage at Vx (and Vy).
Ignore leakage variation along WL or BL.
Ignore offset component due to voltage variation in array and drivers.
Ignore additional length of WL or BL due to socket differences.
Vx
Vy
Z’/L
Vx
Vy
(512+512)ileak

## Slide 15
Bias Budget
CENTER BIAS
LLSB
LLSA
ULR
Word-line direction
Bit-line direction
CENTER BIAS
LLSB
LLSA
ULR
Balanced BIAS requirement:
ULR=LLSA+IRA+LLSB+IRB
IRB
IRB
Vx = IR_e + VDS
Vx = IR_e + VDS
Selection of ULR in 2Kx1K x2 tile with static biasing
LLSA set by total leakage < 50uA
LLSB set by acceptable rate of parasitic snap-back of B cells
Vx = combined voltage of driver + electrode at point of selection.
For constant Vx, and constant Center Bias (ULR), leakage current is lower in Quilt than External. (LLSA under-utilized).
For Vx, the rate of failure is lower in Quilt than External (LLSB also under-utilized).
LLSA

## Slide 16
Bias Budget
Break up ULR into two components:
ULR = ULRA + ULRB
Condition for constant ULR:
ULR_A=LLSA_e + IRA_e = LLSA_q + IRA_q
LLSA_q = LLSA_e – deltaIRA
Same applies to ULRB
Selection of ULR in 2Kx1K x2 tile with static biasing
246mV VDS advantage
Assume total Vx = 600mV
VDSe = 600-282mV = 318mV
VDSq = 318+246mV = 564mV
Ratio to Q current to E current = 0.814
Zq/Ze = 0.814 * 318/564 = 0.459

## Slide 17: Metallization
Quilt architecture allows placement of the sockets centered over the driver area
  Done for both BL sockets and WL sockets.
This reduces the routing pitch requirement for the socket connection by ½ compared to placement at the edges of the arrays.
This reduced pitch requirement can be traded off against number of interconnect layers.

## Slide 18
Motivation/Feature 2
Quilt architecture requires simpler metallization than external driver architecture
Example of 2K x 1K x2
512 lines at 4F (2nd deck WL)
512 lines at 4F (first deck WL)
1024 lines at 4F (BL)
512 lines at 4F (BL connection)
512 lines at 8F (WL connection)
External 2 Deck | Quilt 2 Deck
G1 at 4F with orthogonal capability | G1 at 4F in one direction (8F in orthogonal direction)
G2 at 4F in one direction | 

## Slide 19: Why?
Possible because sockets can be placed at midpoint of driver groups
Sockets are key
M3
G1
G2
WL
BL
WL
M2
M1
M3
G1
WL
BL
WL
M2
M1
4F in one direction
4F in one direction
4F in orthogonal directions

## Slide 20
1Deck Quilt
2Deck Quilt
3Deck Quilt
4Deck Quilt
G1: 8F
M2: 10.6F
M1: 10.6F
G1: 4F/8F
M2: 10.6F
M1: 10.6F
G1: 4F
M2: 10.6F
M1: 10.6F
G1: 4F
M2: 10.6F
M1: 10.6F
SADP - immersion
4F - immersion
8F-12F - dry
2+1 quilt options @F=20.5nm
No direct-self-aligned vias required.
‘PCMS-via’ not used
 | F=20.5nm Quilt |  |  | 
 | 1D | 2D | 3D | 4D
SADP | 2 | 3 | 4 | 5
immersion | 0 | 4 | 6 | 7
8F-12F dry | 7 | 4 | 3 | 3
Cu metallization assumed for M1, M2, G1.

## Slide 21: Die Size
Quilt ideal 4F  ~5F effective cell size because of the socket and cluster termination overhead (conservative)
Depends on number of decks.

## Slide 22
Socket overhead (2 deck, shared BL):
4 sockets per tile, horizontal and vertical
30 pitches in WL direction (guess)
20 pitches in BL direction (guess)
tile footprint: 2kBL x 4kWL
(2K+4*30)*(4K+4*20)/16Kcells = 0.54F^2
Overhead Calculation
Combined:
Cluster cell size: ddd
4 WL sockets per tile
4 BL sockets per tile
Cluster overhead (8x8T/CL):
In WL direction: 3 WL drivers.
In BL direction: 1.5 BL drivers for two edges
BL driver ~ 256 pitches
WL driver ~ 256 pitches
(2K*8+3*256)*(2K*8+1.5*256)/2^28 = 1.0714
Driver area: (4F^2) (2Kbl x 4Kwl)/(2x4K+2K)
= 800’pitch’^2/drv = 1.38um^2 /drv
Overhead per cluster:
¾ of BL drivers within 1 tile,
¾ of WL drivers within 1 tile
Applies to 1,2,3,4 decks.

## Slide 23
Single Deck word-line sockets depicted as example
Same array litho node for two architectures
1 socket per tile in horizontal direction
4 sockets per tile in horizontal direction
Number of Sockets

## Slide 24
Ext: need 1 of these per tile
Socket Dimensions
(Assuming 10F pitch between geometries in orthogonal direction to array plus 10F on each side for array termination dummies. No vias under array)
110F
190F
One layer
Two layers
70F
110F
Quilt: need 4 of these per tile
One layer
Two layers
50F
70F
70F
110F
Bundle of 8
Bundle of 4

## Slide 25
Required CMOS for isolated clusters
Sockets for 1 tile
CMOS for 1 tile
WL drivers
BL drivers
1.5X the WL drivers in one patch per side of cluster.
Estimate for XP20: 1.2X of one regular patch width.
1.5X the BL drivers in one patch per side of cluster.
Estimate for XP20: 0.6X of one regular patch height.
07-01-11

## Slide 26
Motivation/Feature 1
Quilt architecture re-arranges drivers and sockets so that all drivers are under array
Reduces litho requirement of array for same CMOS driver capability
2K x 1K x 2
@20.5nm
2K x 1K x 2
@~25nm

## Slide 27
20.5nm
2048+4 + 2*41p
87.5um
1024+4+ 2*318p
68.19um
25.6nm
1024+4+41
54.6um
2048 + 4 + 2*41p
109.1um
Example of 202mm^2 128Gb estimate
 | External | Quilt
Die size | 202mm2 | 202mm2 ***
metallization | 3+2 | 3+1
Array pitch | 2x20.5nm | 2x25.2nm
WC IR in RESET | 2560 cells * | 1248 cells **
WL leakage | 2K cells | 2K cells
Required WL Decoder Area/cell | 1.364um2 | 1.364um2
** assumes double BL electrodes ** 256*0.875 + 1K for quilt *** ~7% area overhead for cluster termination at 8x8 clusters |  | 
Uses Intel analysis for NAND competitive lead product
From DK document 06-08-10
Option1: Keep same cell size, increase line spaces
  Lower parasitic capacitance
  Same Reset current requirement
  Higher R per cell but lower electrode resistance
Option2: larger cell size
  Larger reset current
  Reduced cell and electrode resistance compensates for constant driver size

## Slide 28
20.5nm
2048+4+2*41p
87.5um
1024+4+4*318p
94.3um
30.1nm
1024+4+41p
64.3um
2048+4+ 2*41p
128.3um
Why should it be limited to driver circuits?
Estimated ‘other’ area = Area of BL drivers
Include: Global drivers, repeaters, write circuits, sensing, data interface, etc.

## Slide 29
20.5nm
2048+4 + 2*41p
87.5um
1024+4+ 2*318p
68.19um
20.5nm
1024+4+41
43.8um
2048 + 4 + 2*41p
87.5um
If drivers could be drawn smaller
(new rules, new tricks, etc.)
~50% area improvement
1.364um^2/WL  0.63um^2/WL

## Slide 30: Design Complexity
There is no clean array boundary compared
Decoding at the edges of the array requires extra decoders, sensing and other circuits. These must be switched in depending on address pattern.

## Slide 31
PY0
PY1
PY2
PY3
PY0
PY1
PY0
PY1
PY2
PY3
PY0
PY1
PY2
PY3
PY2
PY3
PY0
PY1
PY2
PY3
T0
T1
T2
T3
TTR
TTL
WL driver / SA group |  | BL driver location (L2Y high order bits) | SA data valid
(L3X bit) | RX value |  | 
Top half of patch L3X=0 | P0 | P0, P1, P2 | No shift
 |  | P3 | Shift Right
 | P1 | P0, P1, P2 | No shift
 |  | P3 | Shift Right
 | P2 | P1, P2, P3 | No shift
 |  | P0 | Shift Left
 | P3 | P1, P2, P3 | No shift
 |  | P0 | Shift Left
Bottom half of patch L3X=1 | P0 | P0, P1 | No shift
 |  | P2, P3 | Shift Right
 | P1 | P2, P3, P0, P1 | No shift
 | P2 | P2, P3, P0, P1 | No shift
 | P3 | P0, P1 | Shift Left
 |  | P2, P3 | No shift
Depending on X and Y address range, valid SA-group data shifts location.
Shifting at tile level done in this design. Optionally, the shifting can be done at cluster or chip level.
Cluster termination mapping
06-29-11
Example of 4-tile-wide cluster
TTR
TTL
T0
T1
T2
T3
SA
Valid data
Shift left
No shift
Shift right
PX0
PX1
PX2
PX3
SA / WL driver group locations
L3X0
L3X1
L3X1
L3X0
L3X0
L3X1
L3X1
L3X0

## Slide 32
One Tile:
Repeating unit for Socket
Decoding must wrap-around the edges of the CLUSTER.
In this example, 16 unique bits can be selected. Only one Bit per WL or BL driver.
Decoding on a toroidal surface
4 word-line segments
4 bit-line segments
Cluster example: 4 tiles x 4 tiles

## Slide 33
Cluster Termination
Provides drivers for the extra electrode segments required to support the active array
One tile
07-01-11

## Slide 34
Edges of cluster are not clean. Ideally, the last set of bit-lines (or word-lines) should mesh with the first set of bit-lines (or word-lines).
To correctly terminate the cluster array in a planar surface, requires an extra set of drivers at each end. These are located at the termination tiles.
The array termination and termination drivers create address dependent ‘fanthom’ array regions. Data bits may be generated at the cluster edges that must be mixed with the rest of the data away from the cluster edge.
Decoding on a Toroidal surface

## Slide 35: other

## Slide 36: Design path choices
External
  1T drivers
    floating electrodes
      Large line to line coupling
      Complex timing
      Budget impact
Positive/Negative voltage drivers
    More complex CMOS requirements
    Potential for latchup or snap-back of CMOS
Combination
    No room for multiple limit circuits
      High WL capacitance  snapback disturb sensitivity
      More timing complexity, slower access, higher power
Because of limited CMOS area.
Proposed XP20 uses ‘junky’ deselect transistors.
Not necessarily due to tile arch choice. XP20 uses all positive voltages.
XP20 has 64 limiters per tile.

## Slide 37
Goal of present analysis: 4k x 4k x 2 @ 20.5nm
Area available per driver under the tile
This is the area to be used for 1T, 2T, 3T drivers etc.
BL and WL drivers may occupy different areas.
Chart: 
| LBL driver selection | LBL driver deselection | GBL driver selection | GBL driver deselection | LBL sel repeater | GBL sel repeater | LWL driver selection | LWL driver deselection | GWL driver selection | GWL driver deselection | current mirror+bypass | sense circuits + data drivers
area per tile (um^2) | 7241.728 | 3833.856 | 2129.92 | 425.984 | 11075.584 | 8093.696 | 1533.5424 | 340.7872 | 1533.5424 | 2288
Example area allocation for circuits under a tile for an evaluation done at F=52nm

## Slide 38
Patch
Tile
Goal of present analysis: 4k x 4k x 2 @ 20.5nm
174um
173um
Layout is still under way
Local drivers fit within allocated area

## Slide 39
Local BL driver selector
Local WL driver selector
Local WL driver selector
Local BL driver de-selector
Global WL driver
Local WL driver de-selector
Global BL driver
~75% of area per tile (or patch) is allocated to driving the word-lines and bit-lines.
This includes selection and de-selection devices.

## Slide 40: Tile with patch / tile level LV
Tile with no LV
Red boxes available for cluster level circuits (256 tiles per cluster).
07-20-11