## Slide 1: SSM IM JDP SOW
Version 0.1
October 20th, 2017

## Slide 2: Signature Page
This SxP Joint Development Program Statement of Work Rev 0.1 (“SSM SOW”), having been approved by the JDP Committee is hereby approved by Intel and Micron respectively effective as of October 20, 2017, and shall terminate upon the earliest to occur of (i) completion of the purpose, objectives and/or milestones defined herein, or (ii) December 31, 2019 (or aligned Qual date reference in this SOW) unless extended by mutual agreement of the Parties, as signified by the signature of each company’s authorized representative below. It is understood and agreed that this JDP SOW may be amended in due course in accordance with the procedures set forth in the Joint Development Program Agreement.
MICRON TECHNOLOGY, INC. INTEL CORPORATION
By: By:
Name: Name:
Date: Date:

## Slide 3: Revision Page
Approval Date | REV | Pages Affected | Was | Is | Comments
10-20-2017 | 0.1 | ALL |  | SSM SOW | 
Notes: 3

## Slide 4: SOW Contacts
Name | Function | Company
Russ Meyer | JDP co-manager | Micron
Al Fazio | JDP co-manager | Intel
Mark Helm | Design | Micron
Sandeep Guliani | Design | Intel
Kiran Pangal | Array Development, including Product/Test | Intel
Fabio Pellizzer | Technology Development | Micron
DerChang Kau | Technology Development | Intel

## Slide 5: SOW Contents
0.0 SOW purpose
1.0 Strategy
  1.1 Strategy overview – Alpha Product
  1.2 Strategy overview – Further Nodes
  1.2 Development vehicles
  1.2 SSM Development strategy – Alpha Product
  1.5 SSM Development strategy – Further Nodes
2.0 High Level Milestones
3.0 Cost analysis
4.0 SSM Target Specs (DTS)
  4.1 SSM DTS
  4.2 SSM DTS Rev0 - performance
  4.3 SSM DTS Rev0 – reliability
  4.4 Key risks for SSM
5.0 SSM TD deliverables
6.0 Process Arch Challenges
  6.1 SSM 4-Deck strategy
  6.2 Process architecture overview
  6.3 Key Risks and Development Vehicles
7.0 Design Strategy
  7.1 SSM design requirements
  7.2 Key Specifications / Features
  7.3 Design Milestones
8.0 Development Budget

## Slide 6: 0.0 SOW Purpose
To define the development strategy for SSM to determine viability and enable a multimode roadmap
To enable the initial product utilizing the SSM technology. The goal is to tape-out in 2018, targeting product qualification within 5 quarters.
To define project deliverables
To define milestones and performance metrics to track the progress towards the deliverables
To define the resource allocation and budget to achieve the targeted deliverables

## Slide 7: 1.0 Strategy

## Slide 8: Strategy Overview – Alpha Product
The goal is to minimize the need for any cell development work beyond SSM pathfinding by adhering to same cell and deck configuration whenever possible.
The SSM flow developed on S26 A1 mask set will be exploited to develop a multi-deck SSM process with array structural yield demonstration prior product TO.
The dual polarity programming with negative reading on 4-deck architecture will require the development of a dedicated decoding strategy that differs from SxP.
Minimal dedicated CMOS process development is planned. HV CMOS devices may be adjusted in case it is strictly required by the new decoding scheme.
No change in the 4-deck quilt tile architecture and in the BEOL. Tile size may be revised if strictly required.
Cell development needs will be accommodated by SR71B and structural yield enhancement will be based on S26 main array, both based on S26A A1 mask set with multi-deck SSM process flow.

## Slide 9: Strategy Overview – Further Nodes
The goal is to exploit the S36X design for pitch reduction, from 41nm to 28nm.
Synergic process development, with SD-only pitch-quad (PQ) as a stepping stone for Full-Stack 3DXP PQ.
Fast validation of scaling assumptions, in terms of:
  Intrinsic performance (median window, Vt sigma, program time/current)
  Reliability (Vt Drift, Vt Shift, Reset Read Disturb)

## Slide 10: Development vehicles
Cell development (device performance and reliability) will be done on SR71B in A1 mask set, for both first and second deck
  2k x 2k physical tile, with 512x512 sparse active bits
  Max visibility for each tile is 4ppm (256kb), 2 tiles/chip
  Full testing capabilities already in place for limited silicon volume (max 1 lot/wk)
  Changes on SR71B are required for second deck testing
Structural yield on wafer will be evaluated and improved on S26A main array
  2 decks structural yield, may be extended to 4 decks if required
  Probe platforms available
S36X may be exploited for a fast transition from 20.5nm h.p. to 14nm h.p.

## Slide 11: SSM Development strategy – Alpha Product
SSM Goals:
1. Fast time to market exploiting S26 A1 mask set for cell development and structural yield enhancement
2. Focus on 4 decks with 3DXP Memory specs
3. Minimal additional effort in CMOS and BEOL if not strictly required by decoder (or other) design constraints
4. Half-size and Quarter-size derivatives planned
SSM / SR71B
Pitch: 41nm pitch
Decks: 1
Test chip with full bipolar capability, 2 cores
Density: 2x256kb
SSM / Alpha Product
Pitch: 41nm pitch
Decks: 4
Density: 256Gb
2 Decks
Learning
SSM / S26
Pitch: 41nm pitch
Decks: 1
Density: 64Gb
SSM cell development
SSM structural array yield
SSM / SR71B
Pitch: 41nm pitch
Decks: 2
Test chip with full bipolar capability, 1 core dedicated to each deck
Density: 2x256kb
SSM / S26
Pitch: 41nm pitch
Decks: 2/4
Density: 128/256Gb
2 or 4 Decks
Learning
S26 A1 mask set
SSM / Half-size
Pitch: 41nm pitch
Decks: 4
Density: 128Gb
SSM / Quarter-size
Pitch: 41nm pitch
Decks: 2
Density: 64Gb

## Slide 12: SSM Development strategy – Further Nodes
SSM Goals:
1. Fast time of transition to 14nm half-pitch exploiting S36X A1 mask set for cell development and structural yield enhancement
2. Focus on demonstration of further scaling viability
SSM / SR71B
Pitch: 28nm pitch
Decks: 1
Test chip with full bipolar capability, 2 cores
Density: 2x256kb
2 Decks
Learning
SSM / S36X
Pitch: 28nm pitch
Decks: 1
Density: 64Gb
SSM cell development
SSM structural array yield
SSM / SR71B
Pitch: 28nm pitch
Decks: 2
Test chip with full bipolar capability, 1 core dedicated to each deck
Density: 2x256kb
SSM / S36X
Pitch: 28nm pitch
Decks: 2
Density: 128/256Gb
2 Decks
Learning
S36X A1 mask set

## Slide 13
2.0 High Level Milestones
# | Milestone | Date
1 | DTS rev1, TD roadmap and CMOS models release | November 30th, ‘17
2 | Mid-term DTS check-point | May 15th, ’18
3 | 2-deck SR71/S26 process capable | April, ’18
4 | Product TO | December, ’18
5 | Ship Release | September, ‘19
6 | Qual | December, ‘19

## Slide 14: 3.0 Cost analysis - SSM vs. 20s 3DxP -
Used April, ‘17 MOR
 | CoT ($M/1k) | Delta ($M/1k) | CPW | Delta
10s -> 20s MOR | 144.9 |  | $2,274.00 | 
10s -> 4 Deck SSM | 114.8 | -30.1 | $2,040.00 | ($234.00)
10s -> 20s 2 Deck MOR | 26.1 |  | $1,559.29 | 
10s -> 2 Deck SSM | 25 | -1.1 | $1,438.25 | ($121.04)
SSM Die size projected to be the same of S26A
  Key assumption is the capability to place the bipolar-capable decoders under the SSM array, keeping the same tile size
Preliminary green-field analysis has been performed for cost-of-transition and cost-per-wafer
  Based on simple assumptions for the technology  The team will update the committee over next quarters as MOR is better defined

## Slide 15: 4.0 SSM Target Specs (DTS)

## Slide 16: SSM DTS
Key advantages of SSM are the performance and reliability specs able to match or even exceed PG1T1 requirements
DTS rev0 is intended to provide a first set of specs useful to finalize the design targets
DTS rev1 will be finalize by the end of November providing target specs for design
A consistent TD roadmap will be provided to meet DTS rev1 specifications (cell performance and array yield) prior product TO

## Slide 17: SSM DTS rev0 – Performance
 | SSM | 3DXP PG1T1 | 3DXP PG1T2
FF 100% bits [V] | 7.5-8.5 | 9.1 | 9.1
Set Vth [V] | 4.2-4.7 | 4.65 | 4.65
Set Vth sigma [mV] | 100-120 | 105 | 110
Reset Vth [V] | 5.2-6.0 | 5.95 | 5.95
Reset Vth sigma [mV] | 100-110 | 90 | 100
Vth window [V] | 1.0-1.4 | 1.3 | 1.3
True window @ 3.54s [mV] | 150-400 | 610 | 560
Max Vth customer [V] | 6.5-7.0 | 7.7 | 7.7
Time 0 BER | 2e-4/5e-5 | 5e-5 | 2e-4
Set pulse total duration [ns] | 20-40 | 245 | 245
Set current [uA] | 25-30 | 25-60uA (shaped) | 25-60uA (shaped)
Reset pulse total duration [ns] | 20-40 | 5-10 | 5-10
Reset current [uA] | 25-30 | <125 | <125
Min Prog-to-read delay [ns] | 100-1000 | 1000 | 1000
Read method | SSR/FFR | SSR | SSR
Tsense [ns] | 30 | 30 | 40

## Slide 18: SSM DTS rev0 – Reliability
 | SSM | 3DXP PG1T1 | 3DXP PG1T2
Set read disturb | Negligible | 256k reads | 50k reads
Reset read disturb | 5k reads with 250mV of margin (256k reads with +100mV additional margin) | 256k reads | 50k reads
Write disturb | 512k cycles | 2048 NW | 768 NW
Write endurance | 10Mcycles | 4M NW | 1M NW
Vth shift @ max cycles [mV] | +200 | -150 | -150
Read endurance | 400Mreads | 400Mreads (with 1 FW every 5kreads) | 3-100Mreads (with 1 FW every 5kreads)
Retention | 3day 0C-85C + 7yrs@40C | 2day 0C-85C + 7yrs@40C | 2yr total @40C with <2days @ 85C
Vth shift @ max retention [mV] | +600 | +650 | +650

## Slide 19: Key risks for SSM
Limited true window (set and reset distribution separation @3.54s) for accomodating reliability margins is the main risk for SSM technology
Mechanism | Impact | EOL value | Mitigation by process | Mitigation by design
Vth evolution over cycling | Vth shift to higher value | +200mV | True window increase SD stabilization | Vdm tracking Multiple Vdm
Vth drift | Vth shift to higher value | +600mV | True window increase SD stabilization | Multiple Vdm
Reset read disturb | Margin between Vread and Reset distribution | +250mV | Vth window increase | Limitation on number of consecutive reads

## Slide 20: 5.0 SSM TD deliverables
DTS rev1 and TD roadmap  Nov/17
Continued characterization of physical mechanisms explaining the electrical behavior of the cell
True window increasing through process optimization
  Single deck process matching DTS Rev1  Jun/18
  Dual deck process matching DTS Rev1  Oct/18
Structural yield enhancement
  Single deck process matching DTS rev1 RBER at Time0 with 30% array yield  Jun/18
  Multi deck process matching DTS rev1 RBER at Time0 with 30% array yield  Oct/18

## Slide 21: 6.0 Process Arch Challenges

## Slide 22: SSM 4-Deck strategy - same as 20s 3DxP -
WL
BL
2 BL Sockets
2 WL Sockets
PM
SD
PM
SD
PM
SD
PM
SD
PM
SD
PM
SD
PM
SD
PM
SD
PM
SD
PM
SD
PM
SD
PM
SD
S26 WL First, 4-Decks 2 sets of WL drivers, 2 sets of BL drivers
Isolation
SSM S26 WL First, 4-Decks 2 sets of WL drivers, 2 sets of BL drivers
2 BL Sockets
2 WL Sockets
SD
SD
SD
SD
SD
SD
SD
SD
SD
SD
SD
SD
Isolation
No change for the 4-Deck management strategy between 3DxP and SSM

## Slide 23: Process architecture overview
 | SSM 4kx4k 4-deck
CMOS | 17-18 mask levels Dual gate CMOS (23A/110A) HV CMOS width scaling from 10s (comprehended in Si based model)
M1-M4 (Cu) | All 193-dry levels, apart V3 and M4 that go 193i (+2) M1 and M4 single damascene Cu M2-M3 remains dual-damascene Cu
Array levels | 4 decks  8 PD levels 5 OPV levels 13 193i levels for array
Top Metal / Passivation | Thick Al SiO2+SiON Passivation Polyimide
Comments | Total of 15 193i level 1st- and 4th-deck WL strapping requires OPV landing on bottom-most WL Read disturb and Set-ability are key risks due to 4x higher WL Cap.

## Slide 24: Key Risks and Development Vehicles
Notes:
No additional test-chip TO is expected ahead of the alpha product
Dual deck capability on SR71B will require mask and design edits
Name | Purpose | Description | Key risks
SR71B | Cell performance/reliability evaluation on 2 decks | Capable of full bipolar program/read operation Single deck, dual deck capability will be developed on the second core | Tile size is 2k x 2k No 4 decks capability No simultaneous testing for both decks
S26 main array | Structural yield on 2 or 4 decks | Target quilt tile 4k x 4k FF and Set operation feasible | No cell performance evaluation on target tile

## Slide 25: 7.0 Design Strategy

## Slide 26: SSM design requirements
Circuitry under the array with dual polarity program capabilities
Negative reading (cell bottom electrode is positive biased) for all decks
SSM S26 WL First, 4-Decks 2 sets of WL drivers, 2 sets of BL drivers
2 BL Sockets
2 WL Sockets
SD
SD
SD
SD
SD
SD
SD
SD
SD
SD
SD
SD
Isolation
Vread

## Slide 27
Key Specifications / Features
Design target: DDR4-1600 specs
Same density (256 Gb) and die size (200mm2) as S26
Read Latency to match S26 (80-95ns)
Write Latency to improve S26 (< 475ns)
Write and Read energy to match or improve S26

## Slide 28: Design Milestones
Targeting end of Q4’18 for earliest availability of Alpha Product mask set.
Design team is to come back to the JDP with TO timelines, resourcing, and execution strategies for the Alpha Product.

## Slide 29: 8.0 Development Budget
This SOW project scope and activities for 2018 needs to be comprehended in the 2018 JDP budget.
Budgets for subsequent years of this development will be adopted on a yearly basis, as part of the overall JDP budget.