## Slide 1: SSM “Step Up” Strategy
DerChang and SSM cross functional team, WW08.4/18
The strategy for ‘fast fail or succeed’ is built on 3-phase stepping-up as the interim milestone achieved.
Dual deck SR71 RWB fundamental established (intrinsic cell symmetry, scaling, empirical and physics)
Bipolar decoder architecture pathfinding and collateral development for alpha product intercept, including
  Build high density dual deck vehicle or spider to validate for structure/MTS/DTS/RWB, and
  Develop bipolar arch and collateral for energy/die size on par or better than SXP counterpart.
Alpha product full qual to validate SSM product worthiness as a roadmap technology
The 20nm and 14nm Alpha product strategy and comparison in this report are a collective judgement by Matt, Balaji (design), Max, Kolya, Steve (PI) and Fabio. Will continue getting feedback from Shafqat (Collateral), Kiran(Array) and Agostino (device) in next few days.

## Slide 2
SSM 20nm Alpha Product
Alternative Alpha Product – 14nm
Risk in schedule

## Slide 3: Roadmap Expectation
 | S26A | S37A | S26S | S37S | S48S
Density/Die Size | 256Gb / 197mm2 | 256Gb / 195mm2 | 256Gb / 197mm2 | 512Gb / 195mm2 | 1Tb /<200mm2
Architecture | SXP, Quilt, QD | SXP, Quilt, QD | SSM, Quilt, QD | SSM, Quilt, QD | SSM, Quilt, QD
Feature | Unipolar NW | Unipolar NW | Bipolar NW | Bipolar NW-FW | Bipolar FW
half pitch | 20.5nm | 14nm | 20.5nm | 14nm | 10.25nm
Read/Write Time | 95/475ns | 80/475ns | 95/240 ns | 80/120~240 ns | 80/80~120 ns
Read/Write Energy | 52/118 pJ/b | 26/59 pJ/b | 52/118 pJ/b | 26/59 pJ/b | 13/30 pJ/b
Read/Write Thruput | 1600/800 MB/s | 3200/1100 MB/s | 1600/800 MB/s | 3200/1600 MB/s | 6400/3200 MB/s
I/O and Transfer Rate | DDR4 1600MT/s | DDR5 3200MT/s | DDR4 1600MT/s | DDR5 3200MT/s | DDR5 6400MT/s
PG1/T1 PRQ | Q4/2018 | Q2/2020 | Q2/2020 | Q1/2021 | Q2/2022

## Slide 4: Assumption and Critical Path for 14nm Alpha Product
SR71 Development: Demonstrate piecewise RWB for 14nm technology roadmap
  Dual-Deck @ 20.5nm; material class and stack defined; RWB gap manageable.
  SR71 on PQ is working (need to be validated)  S36X SD only flow and SR71 testable; 14nm scaling on single deck; RWB consistent with 20.5nm learning
  PQ SR71’s critical path are resources in silicon allocation and module development, minimum leverage from 20’s and 30’s projects; additional funding / scope need to be assessed.
  14nm scaling expectation – 40% program current scaling no Vt changes by Q3/2018
S34X DBR: 14nm dual-deck spider based on option-1 decoder
  Based layout is S36X + Option-1 CMOS decoder (no new DR);
  Reduced addressable space (near ½ of S36X)
  Similar Read/Write energy of S34S (higher read/write delays) in probe
  14nm array design collateral feedback/correction 2 quarters prior to S37S DBR (2 quarters of learning)
14nm Bipolar Architecture
  14nm die size and energy assessment being consistent with 20nm assessment
14nm SSM collateral release
  Preliminary release including 14nm cell DTS, TGnMOST model and Design Rules
  Revision are based on additional learning on TGnMOST, S37A periphery yield and S34X learning
  Schedule risk: upto 1 quarter push to the best case.

## Slide 5
To build alpha product
  SR71 – SSM basics, including geometric scaling, deck symmetry both empirical and underline physics
  S24S – SSM cell/array, WLR, Burn
  Build alpha product
    Pick a node so CMOS, Array, BEOL all work.
    Decoder fitted
    Energy matched
    CMOS and DR requirements