## Slide 1: SSM Alpha Product analysis to build SOW
DerChang WW08.2/18
Feedback to S26S qual by Q4/2019 –
Time to flesh out alpha product after DBR is too short  likely qual date Q2/2020
6 quarters after SXP counterpart qual is not competitive.
Explicitly calling out bipolar decoder architecture pathfinding.
  including the corresponding design collateral to support energy and die size required
The SOW should in 3 pieces built with continuity
Dual deck SR71 RWB fundamental established.
14nm pathfinding, including
  high density “product” test chip DBR/dual deck validation and
  Bipolar architecture/collateral for energy and die size on par or better than SXP counterpart.
14nm Alpha product intercept to reduce time to market delay (ie. S37S vs. S37A)
The 14nm Alpha product strategy in this report are a collective judgement by Matt (design), Max, Kolya (PI). Will continue getting feedback from Shafqat (Collateral), Balaji, Kiran(Array) and Ago and Fabio (device) in next few days.

## Slide 2
SSM 20nm Alpha Product
Alternative Alpha Product – 14nm
Risk in schedule

## Slide 3: Assumption and Critical Path for 14nm Alpha Product
SR71 Development: Demonstrate piecewise RWB for 14nm technology roadmap
  Dual-Deck @ 20.5nm; material class and stack defined; RWB gap manageable.
  SR71 on PQ is working (need to be validated)  S36X SD only flow and SR71 testable; 14nm scaling on single deck; RWB consistent with 20.5nm learning
  PQ SR71’s critical path are resources in silicon allocation and module development, minimum leverage from 20’s and 30’s projects; additional funding / scope need to be assessed.
  14nm scaling expectation – 40% program current scaling no Vt changes by Q3/2018
S34X DBR: 14nm dual-deck spider based on option-1 decoder
  Based layout is S36X + Option-1 CMOS decoder (no new DR);
  Reduced addressable space (near ½ of S36X)
  Similar Read/Write energy of S34S (higher read/write delays) in probe
  14nm array design collateral feedback/correction 2 quarters prior to S37S DBR (2 quarters of learning)
14nm Bipolar Architecture
  14nm die size and energy assessment being consistent with 20nm assessment
14nm SSM collateral release
  Preliminary release including 14nm cell DTS, TGnMOST model and Design Rules
  Revision are based on additional learning on TGnMOST, S37A periphery yield and S34X learning
  Schedule risk: upto 1 quarter push to the best case.