## Slide 1: Self-Select Memory Research IM JDP SOW
Version 1.0
January 20, 2016

## Slide 2: Signature Page
This SxP Joint Development Program Statement of Work Rev 1.0 (“Self-Select Memory SOW”), having been approved by the JDP Committee is hereby approved by Intel and Micron respectively effective as of Jan 20, 2016, as signified by the signature of each company’s authorized representative below. It is understood and agreed that this JDP SOW may be amended in due course in accordance with the procedures set forth in the Joint Development Program Agreement.
MICRON TECHNOLOGY, INC |  |  | INTEL CORPORATION | 
By: |  |  | By: | 
Name: |  |  | Name: | 
Date: |  |  | Date: | 

## Slide 3: Revision Page
Approval Date | REV | Pages Affected | Was | Is | Comments
Jan-20-2016 | 1.0 | ALL |  | Initial Self-Select Memory SOW | 
Notes: 3

## Slide 4: SOW Contacts
Name | Function | Company
Russ Meyer | JDP co-manager | Micron
Al Fazio | JDP co-manager | Intel
Hernan Castro | Design | Micron
Sandeep Guliani | Design | Intel
Kiran Pangal | Array Development | Intel
Fabio Pellizzer | Technology Development | Micron
DerChang Kau | Technology Development | Intel

## Slide 5: SOW Contents
0.0 Purpose
1.0 Background
2.0 Scope
3.0 Strategy
4.0 Milestones
5.0 Design
6.0 Process
7.0 Test
8.0 Budget & Assumptions
Backup (success criterial placeholder)

## Slide 6: 0.0 Purpose

## Slide 7: Purpose of SOW Rev 1.0
To introduce self-select memory
To define the research strategy for 3DXP technology capability expansion
To define project deliverables through calendar year 2016
To define performance metrics to track the progress towards the milestones for decision making
To define the resource and the budget to achieve the targeted deliverables

## Slide 8: 1.0 Background
Introduction to self-select memory and the novelty

## Slide 9: Self-Select Memory (SSM) concept
A Vth window has been observed by applying programming pulses to the SD device with opposite polarity
The mechanism underlying this effect is unknown (atomic species electromigration is the leading candidate model), but the effect has been experimentally observed on several vehicles (PTX SD-only, S15 SD-only, S15 FS) and for various SD compositions (SD1 and several version of SDd)
Positive programming pulse
Negative Vth detection  Vth=5.6V  VTHigh
Negative programming pulse
Negative Vth detection  Vth=4.7V  VTLow
VTH
VTL
S15B SD-only, lot 8792062, 18nm SDd ver 4

## Slide 10: Key features
Simpler process integration, with lower aspect ratio and no cross-contamination
Flat VT-I with programming currents as low as Ihold (25uA)
Fast program (20ns easily achieved) and short delay between program and read (100ns demonstrated)
Vth window depends on SD thinckness (70mV/nm sensitivity on SDd)
W WL
Carbon
SD
Carbon
W BL
W WL
Carbon
SD
Carbon
PM
Carbon
W BL
Self-selector
SxP
Pulse width [s]
Vth [V]
SD thickness
Vth window [mV]
VTH
VTL

## Slide 11: SD polarity effect exploitation
SD polarity effect may be exploited for
Stand-alone self-selecting memory device with
  Simpler process integration
  Lower programming current
  Faster program speed
  Less reliability issues
Enabling eMLC capability in the SxP configuration, with 3 and 4 level intrinsic feasibility demonstrated
Widening the Vt window in the SxP configuration

## Slide 12: 2.0 Scope

## Slide 13: Scope
Self-select memory (SSM) cell
  Evaluate operating scheme in seeking for fundamental understanding, supported with ±3 sigma statistics for Read/Write and retention.
  Develop basic cell architecture including electrode, interface and it’s interaction with self-select memory.
Application of SSM in 3DXP architecture
  Read/Write scheme and retention fundamentals to support cross point memory array
  Window expansion of 3DXP SLC
  MLC enablement and performance assessment

## Slide 14: 3.0 Strategy

## Slide 15: Research Strategy
Algorithm and physics development of Self-Select Memory at 1st principle
  Design SSM single cell and mini array in S26A scribe with opt-in metal jumper avoiding the incurred risk to S26A development
  Develop S26A SD-only process flow and physical and electric performance metrics
  Test and Characterize bi-direction Read/Write algorithm for NVM
Assess SSM for NVM limitation and tread-off
  Including program transfer mechanisms, distribution, disturb and retention
  Performance metrics subject to cell stack and architecture impact
Evaluate applicability of SSM basics for Comparable Technology Product such as
  Stand along SSM using SD only stack
  SLC window expansion or MLC in S26A full stack

## Slide 16: 4.0 Milestones

## Slide 17: Milestones & Check points
# | Objectives | ECD
1 | Test structures design validated, including Opt-in metal jumper in QTT | Feb/16
2 | SD-only flow portable to S26A | May/16
3 | Design validated, including bi-direction operation for ead/write | June/16
4 | Validate SSM window & distribution for NVM retention and endurance | July/16
5 | Risk assessment of SSM architecture and capability for the decisions on Comparable Technology Product direction | July/16
6 | Define the next phase of research scope and success criteria for research exit if #5 passes. The success criteria are tangible for process architecture, device performance, scalability projection and product architecture. | 
i | S26A SD only flow improvement for stand alone SSM | Q3/16
ii | Algorithm development and validation for S26A window expansion | Q4/16
iii | Algorithm development and validation for 3DXP full stack MLC | Q4/16

## Slide 18: 5.0 Design

## Slide 19: Test structures on S26A
On S15C the reverse polarity measurement capability is established with the 2xCMOS test structure. 2xCMOS structure can provide intrinsic information, but no statistics (ramdom) and no info on ED variation (sysmatic) impact.
In addition to 2XCMOS strcture, reverse polarity capability with larger cell count will be added to S26A scribe in order to support both the investigation on single deck wafer of the second deck behavior, and the reverse polarity effects.
  IG88– Addressable single cell test structure: This is based on S26A-IG88. Opt-in metal jumper for metal mask optional TO to enable bidirectional operation schematics.
  QTT– A electrically bi-directional operable mini array test structure: This is based on S26A-QTT. A subset cells in QTT array are designed with opt-in metal jumper for bi-directional operable circuit scheme .
  SR71 – A brand new bi-directional operable 4Mb array: Array characterization using Magnum tester is required.

## Slide 20: 6.0 Process

## Slide 21: Masks and Process Flow
Enable Opt-in metal jumper for bidirectional operation in parallel with S26A POR TO
Process Flow #1: for SSM Integration:
  SD-only process flow based on S26A
Process Flow #2: for Window expansion and MLC
  Identical to S26A Full loop process flow

## Slide 22: 7.0 Test

## Slide 23: Characterization and Algorithm
Key tasks include
  test structure design validation
  Device and Array Characterization
  Algorithm development
Test instruments include
Test Structures | Tester
2XCMOS | WLC platform
IG88 | WLC platform
QTT | WLC platform
SR71 | Magnum Tester

## Slide 24: 8.0 Budget

## Slide 25: Budget and Assumptions
This SOW project scope activities for 2016 are consistent with the 2016 SXP JDP budget.
  Resources and logistics are part of S26A development work
Budgets for subsequent years of this SOW will be adopted on a yearly basis, as part of the overall SXP JDP budget.

## Slide 26: Back-up slides

## Slide 27: Intrinsic Performance
Comparable leakage (same SD material).
More flexible Read algo (no spurious reset of Set bit).
Similar Set Vt, but much faster (~20ns demonstrated) and simple (no pulse shaping needed) and lower current Set operation.
Similar DVt, but much lower reset current (~1/3 of actual SxP current).
Negative polarity needed for reset operation (added decoder complexity/area).
A thicker SD is preferable (better Vth window, leakage and drift), so higher voltages may be needed.

## Slide 28: Reliability
Comparable Drift for Set (same SD material) and better Drift for Reset (no additional Drift of reset PM).
No Read Disturb on Set
Read Disturb on Reset represents the only failure mode specifically related to the proposed approach  > 104 reads feasible up to 125C
No Proximity Thermal Disturb (very low current and temperatures).
Similar Write and Read Endurance.
Good retention up to 125C, but activation energy still to be quantified (wip).
> 1E4 reads