## Slide 1: Hybrid bonding of 1 vs. 4 dies
Problem statement:
  SRAM should be scalable to multiple dies to add extra capacity, leading to multiple possible configs, such as single SRAM-on-Logic, or 4x-SRAM-on-Logic.
  In a shared-bus architecture, the I/O needs to handle all possible configurations
  Proposal: characterize the impact of those different configurations on hybrid bonding process, and how far they deviate from simulation models.
Base die (logic)
SRAM die
SRAM die
SRAM die
SRAM die
TSV
Base die (logic)
SRAM die
SRAM
SRAM
SRAM
Core
Core
TSV
Config A: 1xSRAM-on-Logic
Config B: 4xSRAM-on-Logic
Base die (logic)
SRAM die
SRAM die
SRAM die
SRAM die
TSV
SRAM
SRAM
Core
Config C: 4xSRAM-on-Logic

## Slide 2
Base die (logic)
SRAM die
SRAM die
SRAM die
SRAM die
TSV
Config B: 4xSRAM-on-Logic
Base die (logic)
SRAM die
SRAM die
SRAM die
SRAM die
TSV
Config C: 4xSRAM-on-Logic
Base die (logic)
SRAM die
SRAM die
TSV
SRAM die
SRAM die
Config D: 4xSRAM-on-Logic
Base die (logic)
SRAM die
SRAM die
SRAM die
SRAM die
Config E: 4xSRAM-on-Logic
SRAM Face Up, No TSV
Base die (logic)
SRAM die
F2F
Config A: 1xSRAM-on-Logic

## Slide 3
TSV/
TDV
Active
Active
TSV/
TDV