## Slide 1: Memory Organ
“The Memory Organ – Ideally one would desire an indefinitely large memory capacity such that any particular … word would be immediately … available. … It does not seem possible physically to achieve such a capacity. …We are therefore forced to recognize the possibility of constructing a hierarchy of memories, each of which has greater capacity than the preceding but which is less quickly accessible.”
Arthur Burks, Herman Goldstine and John von Neumann, Preliminary Discussion of the Logical Design of an Electronic Computing Instrument, Jun. 28,1946.
“TPC-C...were spent waiting for memory . . . . MPEG… limited by memory accesses . . . . Processor speed has seriously outstripped memory speed. . . . The real design action is in the memory subsystems — caches, buses, bandwidth and latency.”
Dick Sites, It’s the Memory, Stupid! Microprocessor Report, 10(10):2–3, Aug. 5 1996.

## Slide 2: SoA Memory Organization
Host
Memory Farm
Channel0
Channeln-1
…
…
Channel
Bank Group0
….
Bank Groupg-1
Bank1
Bank Group
Bank0
….
Bankb-2
….
Bankb-1
Macro1
Bank
Macro0
….
Macrob-2
….
Macrob-1
C/A
Array a.k.a. Mat or Tile
SA
Mux / Word
Row Dec
DQ + Metadata
Col Dec
Macro
CSL
Array/Mat/Tile
WL Decoder / Driver
BL Mux / SA / Data Latch
Cell
BL
WL
BL
WL

## Slide 3: Cell Types
WL
BL
6T-SRAM
1T1C-DRAM
2T-DRAM
Cross Point Array

## Slide 4: HBM3 Organization (JEDEC Spec R.95)
Each stack of HBM die includes (equivalent to 1 Rank of DDR DIMM)
Global command for the stack (52 µbumps)
Upto 16 channels / device (stack); upto 1K DQ
Double data rate @ 4.8~6.4GT/s (2.4~3.2GHz)
Max BW = 819.2GB/s/stack
I/O voltage 1.1 V, Tx driver voltage 0.4 V
DRAM core voltage 1.1 V
Unterminated data/add/cmd/clk interfaces
Unmatched data interfaces
2b encoded temp sensor
not prohibiting manufacturer specifics such as
an optional interface die in the stack
Signal redistribution and other functions
52
HBM3
Channel0
Channelm
…
…
120
52
Bank
  Channeli
Bank
….
Bank
….
Bank
Bank is the lowest independently operable unit
DRAM core 250~400MHz (not scalable)
tCCD (CAS2CAS delay, b2b same bank): 2.5~4ns
Hynix Spec: Open page latency (tAA) = 48ns Close page latency (tRCD+tAA) = 31ns
Bank Group is supported for fast tCCDF)
Number of rows (pages) is part of HBM3 spec
C/A
Memory Mat
SA
Page
RAS
DQ + Metadata
CAS
Bank
SWD
CSL
Channels are full independent to each other
2~32Gb channel capacity [231~35b];
16, 32 or 48 banks per channel
64 DQ + ECC, SEV per channel. BL = 8 I/O (~90µbump) & ADD/CMD (~30µbmp)
2KB physical page [214b] 1KB addressable [213b], C[6:0]
BW = 38.4~51.2GB/s/Channel, Max BW density = 205GB/s/GB
Bank grouping supported for short tCCD
2 Pseudo Channel (PC) per Channel; PCs share C/A RAS/CAS for finer granularity to lower cost to scheduler.

## Slide 5
Channel 0
Channel 2
Channel 3
Channel 4
Channel 5
Channel 6
Channel 7
Channel 1
Component (64MB)
64B per channel
6.4 GT/s per lane
Bank group: 4 Banks (1MB)
macro
256
256
Bank0
macro
Bank1
Bank2
Bank3
4:1
512
8:1
800 MT/s per lane
512
512
512
512
512
Channel: 8 Bank groups (8MB)
Bank Group Mux
64MB SRAM Cache Density 2MB/mm2
Latency ns
BW 1000(GB/s)/MB
Energy 0.1pJ/b
1GBx8 HBM3
Density 20MB/mm2
Latency 30s ns
BW 300(GB/s)/GB
Energy 4.5pJ/b
32GB Optane
Density 350MB/mm2
Latency 300s ns
BW 1(GB/s)/GB
Energy 50pJ/b
IO
PERIPHERY
Bank 0
Bank 31
Tile 0
Tile 127
LWLs/LWLd/PCL CTRL DRVRS
GWLS DRVR/TERM CAPS
GBLS DRVR/TERM ANALOG
PCL/LBLS & LBLd DRVRS
CUA
1/4th Tile (1K x 1K)

## Slide 6: Disaggregation: An access energy consideration
Developing Disaggregation Strategy
System level PPA
Build PPA Pareto by module
Monolithic Design as baseline/reference
Fine-grained DRAM: energy-efficient DRAM for extreme bandwidth systems
Mike O'Conner et.al, Nvidia
ACM Symposium on Microarchitecture, 2017
HBM3
HBI
ADM Gen 1
ADM HBI

## Slide 7: High Bandwidth Memories
 |  |  | DRAM |  |  |  | SRAM | 
 |  |  | HBM3 | HBM4 | LLC | ADM Gen 2 | D-Cache | V-Cache
Component | Component Capacity | Gb | 16 | 16 | 8 | 2 | 0.5 | 0.5
 | die stacking | # | 6.4 | 8 | 1 | 1 | 1 | 1
 | Density | MB/mm2 | 22.6 | 21.6 | 12.0 | 6.7 | 2.2 | 1.56
 | R+W Max Bandwidth | TB/s | 0.65536 | 2.048 | 1.024 | 3.2768 | 6.5536 | 2.048
 | R/W Energy | pJ/bit | 4.5 | 3.6 | 2.7 | 0.800 | 0.1 | 0.1
 | Latency (Open) (tRP+tCCDS) | ns | 21 | 21 | 15 | 9 | <3 | 6
 | Latency (Close) (tRC+tCCDS) | ns | 55 | 55 | 33 | 14 | <3 | 6
 | R+W Max BW/GB | (TB/s)/GB | 0.32768 | 1.024 | 1.024 | 13.107 | 104.858 | 32.768
 | R+W Max BW/W | (TB/s)/W | 0.028 | 0.035 | 0.054 | 0.955 | 1.250 | 1.250
Channel | # of Channel / Component | # | 2 | 4 | 32 | 8 | 8 | 8
 | DQ per Channel | # of Lanes | 64 | 64 | 32 | 512 | 512 | 256
 | R+W Max Bandwidth | GB/s | 51.2 | 64 | 32 | 409.6 | 819.2 | 256
Bank | # Bank Group / Channel | # | 8 | 8 | 2 | 1 | 8 | 
 | # Bank / Bank Group | # | 4 | 4 | 4 | 32 | 4 | 
 | # Bank / Channel | # | 32 | 32 | 8 | 32 | 32 | 
 | # Bank / Component | # | 64 | 128 | 256 | 256 | 256 | 
 | # Bank / Cube | # | 409.6 | 1024 | 256 | 256 | 256 | 

## Slide 8: High Level Spec Comparison
 |  |  | LPDDR5 | HBM3 |  | 2Gb Macro
 | Technology Node | nm | Hynix 1z | Hynix 1z | JEDEC R.95 | TCD 1z (512)
Die, including JEDEC device / stacked-die | Capacity | Gb | 16 | 16 | 2~512 | 2
 | Footprint | mm2 | 60.72 | 115.06 | n/a | 16.07
 | Density | Mb/mm2 | 270 | 142 | n/a | 127
 | # of DQ / die | pins | 16 | 256 (1K allocated) | uptp 1024 | 4096
 | # of Channel /Die | # | 1 | 4 | upto 16 | 8
 | Transfer Rate | GTpS | 6.40 | 6.40 | 4.8~6.4 | 0.25
 | Bandwidth Density | GB/s/GB | 6.4 | 102 | max. 205 | 512
 | Latency (Close page) | ns | 40.00 | 48.00 |  | 19.80
 | Latency (Open page) | ns | 25.00 | 31.00 |  | 15.00
 | access latency / tCCD | ns | 2.50 | 2.50 | 2.5~4.0 | 4.00
Channel | Channel Capacity | Mb/Channel | 16384 | 4096 | 2K~32K | 256
 | DQ / Channel | pins | 16 | 64 | 64 | 512
 | # of Bank / Channel | Bank/Channel | 16 | 16 | 16, 32, 48 | 8
 | BW/Channel | GB/s/Channel | 12.8 | 51.2 | 38.4~51.2 | 16
Bank, Partition | Bank Capacity | Mb/Bank | 1024 | 256 | see spec | 32
 | # of col of Mat/Tile (GBL) | n | 16 | 16 | n/s | 8
 | # of Row of Mat/Tile (GWL) | n | 64 | 32 | n/s | 16
 | Physical Page Size | bits | 16384 | 16384 | 16384 | 4096
Mat, Tile | Array Capacity | Mb/Array | 1.00 | 1.00 | n/s | 0.250
 | # of BL | Col | 1024 | 1024 | n/s | 512
 | # of WL | row | 1024 | 1024 | n/s | 512

## Slide 9: High Level Spec Comparison (2)
 |  |  | LPDDR5 |  | HBM2 | HBM3 |  | 2Gb Macro | AP HVM
 | Technology Node | nm | Hynix 1z | Apple M1 Pro | Hynix 1z | Hynix 1z | JEDEC R.95 | TCD 1z (512) | 2y
Die, including JEDEC device / stacked-die | Capacity | Gb | 16 | 64, 128 | 16 | 16 | 2~512 | 2 | 32
 | Footprint | mm2 | 60.72 |  | 104.17 | 115.06 | n/a | 16.07 | 220-320
 | Density | Mb/mm2 | 270 |  | 157 | 142 | n/a | 127 | 100~150
 | # of DQ / die | pins | 16 | 128 | 128 (1K/stack) | 256 (1K/stack) | uptp 1024 | 4096 | 10K
 | # of Channel /Die | # | 1 | 8 | 8 | 4 | upto 16 | 8 | 
 | Transfer Rate | GTpS | 6.40 | 6.4 | 03.20 | 6.40 | 4.8~6.4 | 0.25 | 3.20
 | Bandwidth Density | GB/s/GB | 6.4 | 12.8~6.4 | 51.2 | 102 | max. 205 | 512 | 1024
 | Latency (Close page) | ns | 40.00 |  |  | 48.00 |  | 19.80 | 
 | Latency (Open page) | ns | 25.00 |  |  | 31.00 |  | 15.00 | 
 | access latency / tCCD | ns | 2.50 |  |  | 2.50 | 2.5~4.0 | 4.00 | 
Channel | Channel Capacity | Mb/Channel | 16384 | 8192,16384 |  | 4096 | 2K~32K | 256 | 
 | DQ / Channel | pins | 16 | 16 |  | 64 | 64 | 512 | 
 | # of Bank / Channel | Bank/Channel | 16 |  |  | 16 | 16, 32, 48 | 8 | 
 | BW/Channel | GB/s/Channel | 12.8 |  |  | 51.2 | 38.4~51.2 | 16 | 
Bank, Partition | Bank Capacity | Mb/Bank | 1024 |  |  | 256 | see spec | 32 | 
 | # of col of Mat/Tile (GBL) | n | 16 |  |  | 16 | n/s | 8 | 
 | # of Row of Mat/Tile (GWL) | n | 64 |  |  | 32 | n/s | 16 | 
 | Physical Page Size | bits | 16384 |  |  | 16384 | 16384 | 4096 | 
Mat, Tile | Array Capacity | Mb/Array | 1.00 |  |  | 1.00 | n/s | 0.250 | 
 | # of BL | Col | 1024 |  |  | 1024 | n/s | 512 | 
 | # of WL | row | 1024 |  |  | 1024 | n/s | 512 | 

## Slide 10: High Level Spec Comparison (2)
 |  | LPDDR5 |  | HBM2 | HBM3 | 2Gb Macro | AP HVM
Technology Node | nm | Hynix 1z | Apple M1x | Hynix 1z | Hynix 1z | TCD 1z (512) | 2y
Pricing estimate | $/Gb | .50 | .50 | 2.00 | 2.00 |  | 
Component Unit |  | Die | Package | Package | Package | Macro | Macro
Capacity / Component | Gb | 16 | 64 | 64 | 64 | 2 | 32
Footprint | mm2 | 60.72 |  | 104.17 | 115.06 | 16.07 | 220-320
Density | Mb/mm2 | 270 |  | 157 | 142 | 127 | 100~150
# of DQ / component | pins | 16 | 128 | 1024 | 1024 | 4096 | 10K
# of Channel / component | # | 1 | 8 | 32 | 16 | 8 | 
Transfer Rate | GTpS | 6.40 | 6.4 | 3.2 | 6.40 | 0.25 | 3.20
Bandwidth | GB/s | 12.8 | 102.2 | 409.6 | 819.2 | 128 | 
Bandwidth Density | GB/s/GB | 6.4 | 12.8 | 51.2 | 102.4 | 512 | 1024
Normalized Bandwidth/$ | Ref. LPDDR5 | 1 | 2 | 2 | 4 |  | 
Channel Capacity | Gb/Channel | 16 | 8 | 2 | 4 | 1/4 | 
DQ / Channel | pins | 16 | 16 | 32 | 64 | 512 | 

## Slide 11: BLOCK DIAGRAM
IO (PADs, Tx, Rx, DLL,..)
Periphery Logic
( Command processor, SIPO, PISO,.. )
HV ( Fuses, redundancy matching, regulators )
Address Drivers
(GBL, LBL, GWL, LWL)
Partition Control Logic
(Read/Write algo u-controller)
Partition Analog
( VDM_DAC, iREF_DAC,…)
BL Tile Circuits
( BL Voltage mux, Mask Logic, Sense Amp)
WL Tile Circuits
( WL VDM, Mask Logic, Current Mirrors, Spike mit)
Global Column mux
Local Column mux
Local Row mux
Global Row mux
axn
hnreg
32 Global Selects
1 Global deselect
32 Local Selects
16 Local deselects
32 Local Selects
16 Local deselects
32 Global Selects
1 Global deselect
IO/Periphery
Tile x128 per partition
Partition x32
Global/Local mux’s x8 per tile
1024 LBL’s
1024 LWL’s
32 GBL’s
32 GWL’s
LV + HV
LV + HV
LV + HV
HV

## Slide 12: 3DXP Component Organization
Die size = 200mm2
Shaded area is global ~ 17mm2
4KTiles (64K Patches) occupy ~155mm2
Routing takes ~20mm2
Command /
Data
Interface
State Machine
(Instruction)
Data Buffer
Address Tag
Global MUX
Analog / control
Array
64Mb/tile
4X4 Patches/Tile
Patch footprint is ~[50µm]2
@ 41P node
Local MUX
Read / Write
1K/Patch
On Pitch Via
32/Patch
64/Patch
LVT
Mixed
HVT
64/Patch
HiZ Path
LoZ Path
1/Tile

## Slide 13: Modularity for 3DIC
Replacement strategy – Which potion of HVT can be replaced by thin film transistor: all, Mux only, or local Mux only
Vertical placement – What is connectivity from circuit in substrate to circuit in thin film: below M1 or below M4 or other multilevel interconnect scheme.
Modularity for scaling such as wafer stacking feasibility
LV / HV MOS
M1
M2
M3
M4
Array
TM
LV
M1
M2
M3
M4
Array
TM
HVT
LV / HV
M1
M2
M?
M4
Array
TM
MUX
M?
Command /
Data
Interface
State Machine
(Instruction)
Data Buffer
Address Tag
Global MUX
Analog / control
Array
64Mb/tile
4X4 Patches/Tile
Patch footprint is ~[50µm]2
@ 41P node
Local MUX
Read / Write
1K/Patch
On Pitch Via
32/Patch
64/Patch
LVT
Mixed
HVT
64/Patch
HiZ Path
LoZ Path
1/Tile

## Slide 14: Memlet
SRAM Chiplet
Capacity 64, 256MB (30, 100mm2)
Phi:
  Channel: 8 and 32
  Channel Capacity: 8MB, 32MB
  Lanes: 512
  DQ: Duplex (x2), Simplex (x1), Simultaneous(x1)
  Address pins: 20, 22
  Pins per chip: 5K~20K
Max Bump Density:
  Shore: 1~2.5µm pitch
  Stacking: (70µm)2/pad
Memory subsystem construct
Max # of chiplet: 4
Memory construct
  Chips or cube
Sea of Bits:
  MCP
  2.3D: embedded chips with controller on the top
  2.3D: embedded controller with chips on the top
  3D-2.3D: embedded cube with controller on the top
  3D-2.3D: embedded controller with cub one the top
Dual-edges
2.5K on 5x6 mm2
10K on 10x10 mm2

## Slide 15
·········
·········