## Slide 1: TMC: LPW Exploration and Beyond
Intel-Samsung Meeting, Oct/3/24
Objective: 2027 DC/AI Product Intercept
Enabling Technology
KPI & Benchmark
Cost of Making & Cost Model
Business Proposition

## Slide 2: Circa 2027 DC/AI Product Intercept
DC - GPU
TMC
TMC
TMC
TMC
TMC
TMC
TMC
TMC
A
A’
TMC
A
A’
DC-GPU
Embedded Bridge / Active
Cross Sectional View
Shared with Samsung under NDA

## Slide 3: Introduction to Terraced Memory Cube
Objective: high bandwidth memory with significantly better costs & extend HBM scaling trajectory
Key Enablers:
  TSV-less + LPDDR PHY on mainstream DRAM: on par with or better than HBM in MB/mm2, GB/s & pJ/b
    Density improvement: no TSV, smaller die size
    High BW & Low Energy: Low-Power Wide-IO mainstream DRAM
    Eliminate low utilization CMOS base die in Chip-on-Wafer advanced packaging
µBumped Memory module
  Readily available with wide options of adv. packaging integration solutions, including EMIB/ODI/Foveros (IF), FO-3D (SPIL/ASE), iCube family (SF) and CoWoS family (TSMC)
TMC – terraced stacking of memory chips interconnected vertically using low cost TSV chips to widen data width in a Terraced Chiplet Cubing (TCC) construction.
A TMC example for 3DS of Low-Power wide-IO, LPW, DRAM chips
16 tiers of 32Gb LPW
64GB TMC 2K DQs
Shared with Samsung under NDA

## Slide 4: Intel-Samsung Meeting (Feb'24, Aug’24)
Samsung LPW Revision Aug. 5, 2024 |  | Mock-1 | Mock-2
 |  | Add DODT | 1c,2xCap/DQ
Technology | D1b | ⟸ | D1c
Capacity [Gb] | 16 | ⟸ | 32
# DQ | 64 | ⟸ | 128
# of Ch | 1 | ⟸ | 2
# of pCh or subCh / Ch | 2 | ⟸ | ⟸
Burst Length | 8, 16, 32 | ⟸ | ⟸
Data Rate [GT/s] | 3.2 | 10.7~14.4 | ⟸
[GB/s] | 25.6 | 85.6~115 | 171~230
#DQ/diffDQS | 32 | ⟸ | ⟸
tRC [ns] | 60 | ⟸ | ⟸
pJ/bit | 1.9 | 2.3 | 1.5
Shared with Samsung under NDA

## Slide 5: 64GB TMC-LPW module Mockups and Benchmark
64GB Module | Package-IF | Node | Gb/Die | Module Size [mm2] | Cost | GB/s | pJ/b | BW/mm | # Module | Height
HBM4E | 3DS-HBM | 1c | 32 | 14.2x11.0 | $281 | 3276.8 | 2.8 | 298 | 1 | 17
TMC Mock-1 | TMC-LPW | 1b | 16 | 14.9x14.0 | $156 | 3276.8 | 2.3 | 234 | 2 | 16
TMC Mock-2 | TMC-LPW | 1c | 32 | 14.9x10.5 | $176 | 3276.8 | 1.5 | 312 | 1 | 16
TMC Mock-1
Shared with Samsung under NDA

## Slide 6: Mockups of Terraced Memory Cube and Cost Breakdown
Input Information |  |  | 1c-process w/ 4GB-die |  |  |  | 1b-process w/ 2GB-die |  |  |  |  |  |  | 
 |  |  | HBM4P –16Hi 64GB |  | TMC –16Hi 64GB |  | TMC – 4Hi 8GB |  | TMC – 8Hi 16GB |  | TMC – 12Hi 24GB |  | TMC – 16Hi 32GB | 
Memory | Memory component |  | 3DS-1c-32Gb/die |  | LPWIO-1c-32Gb/die |  | LPWIO-1b-2GB/die |  |  |  |  |  |  | 
 | Size |  | 11.5 x 9 mm2 |  | 6 x 14 mm2 |  | 7 x 7 mm2 |  |  |  |  |  |  | 
 | Gross die/wafer |  | 595 |  | 721 |  | 1301 |  |  |  |  |  |  | 
 | Yield |  | 76.5% |  | 79.7% |  | 85.7% |  |  |  |  |  |  | 
 | Incoming wafer $$ |  | $ 4463 |  | $ 3979 |  | $ 3586 |  |  |  |  |  |  | 
 | $$ / die |  | $ 9.8 |  | $ 6.9 |  | $3.2 |  |  |  |  |  |  | 
Controller | Size |  | 12.6 x 9.2 mm2 |  | -- |  | -- |  |  |  |  |  |  | 
 | Gross die/wafer |  | 525 |  | -- |  | -- |  |  |  |  |  |  | 
 | Yield |  | 80% |  | -- |  | -- |  |  |  |  |  |  | 
 | $$ / die |  | $ 18.3 |  | -- |  | -- |  |  |  |  |  |  | 
TSV die | Scheme |  | -- |  | 0P1M + TSV |  | 0P1M + TSV |  |  |  |  |  |  | 
 | Size |  | -- |  | 2 x 5.2 mm2 5.3 x 5.2 mm2 |  | 2.05 x 5.2 mm2 |  | 2.4 x 5.2 mm2 |  | 3.83 x 5.2 mm2 2.04 x 5.2 mm2 |  | 5.26 x 5.2 mm2 2.4 x 5.2 mm2 | 
 | Gross die/wafer |  | -- |  | 3033 |  | 5867 |  | 5023 |  | 3161 5867 |  | 2313 5023 | 
 | Incoming wafer $$ |  | -- |  | $ 450 |  | $ 450 |  |  |  |  |  |  | 
 | $$ / die |  | -- |  | $ 0.149 |  | $ 0.077 |  | $ 0.090 |  | $ 0.143 (need 6ea) $ 0.077 (need 5ea) |  | $ 0.195 (need 8ea) $ 0.090 (need 7ea) | 
Assembly | Stack Height |  | 1 + 16Hi |  | 0 + 16Hi |  | 0 + 4 Hi |  | 0 + 8 Hi |  | 0 + 12 Hi |  | 0 + 16 Hi | 
 | Size |  | 14 .5 x 11 mm2 |  | 13.6 x 14 mm2 |  | 9.9 x 7 mm2 |  | 11.7 x 7 mm2 |  | 12.8 x 7 mm2 |  | 14.9 x 7 mm2 | 
 | Gross die/wafer |  | 367 |  | 303 |  | 871 |  | 725 |  | 663 |  | 569 | 
 | Process cost/wafer |  | $ 9460.2 |  | $ 6919.6 |  | $ 2776.5 |  | $ 4393.3 |  | $ 6057.0 |  | $ 7367.9 | 
 | Process cost/unit |  | $ 25.16 |  | $ 22.8 |  | $ 3.27 |  | $ 6.45 |  | $ 10.13 |  | $ 15.22 | 
 | Yield |  | 70.9% |  | 76.8% |  | 97.6% |  | 94.0% |  | 90.2% |  | 85.1% | 
Memory Cube Module Cost |  |  | $ 281.0 |  | $ 176.3 |  | $ 16.6 |  | $ 34.4 |  | $ 54.1 |  | $ 78.0 | 
64GB Build Cost |  | # of modules | $ 281 | 1 | $ 176 | 1 | $ 133 | 8 | $ 138 | 4 | $ 163 | 3 (72GB) | $ 156 | 2
Shared with Samsung under NDA

## Slide 7: Business Proposition
Key Asks
  Increase Data Transfer Rate on-par with LPDDR6
  Package development of Terraced Memory Cube Module
Collaborate on developing the solution with the aim of being first to market.
Lead industry adoption and open up to gain wide adoption and economies of scale
Potentially expanding TMC collaboration to wide range of DRAM
  PHY-less, TSV-less HBMx
  Small Outline LPDDRx
Shared with Samsung under NDA