## Slide 1: ADM Scaling Value Proposition
Abhishek A. Sharma, Sarah Atanasov, Noriyuki Sato, Van Le

## Slide 2: Need for in-package Memory
Intel’s current ADM thrust
 Enabled with IPM/custom design
No current TD thrust
Real need for high bandwidth AND high capacity in-package memory
Defines 2 clear distinctions in requirements
Huawei, Hot Chips ‘19
TSMC, Hot Chips ‘19

## Slide 3: DRAM Design and Application Space
Parameter | eDRAM (ADM) | DRAM (from datasheet)
Transistor type | Fin/BG | RCAT/Fin
Density (Gb/mm2) | 0.04 | 0.241 (1y)
Bandwidth Density (GB/s/mm2) | 42.667 | 2.107
Cell size (μm2) | 0.01458 | 0.002244
Cell dim (nm x nm) | 108 x 135 | 44 x 51 (1y)
Latency @ array edge (ns) | 2-5 | 12-15
Product Latency (ns) | 15-20 ns | 20-35 ns
tRC (ns) – row cycle time | 7-15ns | 50-55 ns
eDRAM is geared towards low latency and High Random Bandwidth applications
Scaled DRAM is >6x smaller cell size than eDRAM  geared towards high capacity segment
P1222 ADM base die
PCH
CPU
GFX
Meteor Lake PRQ ‘22

## Slide 4: DRAM Design and Application Space
Parameter | eDRAM | DRAM
Transistor type | Fin/BG | RCAT/Fin
WL slew (ns) | 1.5ns (low R) | 3ns (low C)
Access Transistor Resistance (Ω) | 10k-30k | 30k-50k
Storage Capacitance (fF) | 8-15 fF | 15-20 fF
Cov (aF/cell) | 25 ( fewer bits/BL) | 6
DRAM achieves similar read latency performance by optimizing WL capacitance (low C) despite high R
DRAM bottleneck is in the write through the array transistor when writing 1 onto 0 (high Vds condition)

## Slide 5: ADM Provides ~ION @ >10x lower IOFF
DRAM
ADM
ADM is scaled in Lg and has better contact resistance to achieve high drive currents
Because of being wide bandgap, there is no junction/tunneling leakage – <50mW idle power target @100C; peak BW power ~2-3 W; 3 pJ/bit @subarray; SRAM @~100-300fJ/bit
Hynix 2006
DRAM uses long channel devices with pulled-back tips to achieve RCAT configuration with low Ioff
Suffers from low drive current due to poor Rc and long Lg; HBM @ 5pJ/bit @ mem
Z ~100/70 nm

## Slide 8: Timing Analysis of eDRAM
Chart: 
VSN
VWL
VBL
VSAEN
tRC
WL ON, BL development, bit write-back (WB), WL OFF, BL PCH
tRCD
WL slew, BL development, R/W completion; WL driver, BL/COB cap dependent
tWB
Transistor drive strength, COB size
Voltage (V)
time (s)
VSN post retention depends on leakage;
Disturbs associated with unintentional body biasing
SA
SA
SA
WL driver
CBL-WL
CWL-WL
CBL-BL
RWLD, CWLD
COV
RSA, CSA
tBL depends on SA strength, BL RC including COV
Notes: 1. Complete array schematics and all 6 algo
2. Detailing one algo with all DTS numbers and analytical function
3. calibrating the DTS calculator by comparing P1271.3 and P1222.6
Read 0, Read 1; Write 0 to 0; Write 0 to 1; Write 1 to 0; Write 1 to 1

## Slide 9: WL and BL design
Worst-case bitcell
WL is loaded by Cgg (gate cap) and WL-WL coupling
Worst-case bitcell
BL is loaded by Cov (Cgs/Cgd) and BL-BL coupling
WL0
active
SA
WL Loading
BL Loading
Ratio of CBL to Cstorage determines sensing margin
CBL scales with #bits
More #bits/BL preferred due to lower transition area
Longer WL important for high BW/vector math, but comes at cost of wire RC
WL C further increases noise  detrimental for high random BW
Very important to control WL delay (mostly C) by limiting gate capacitance
Transistor Cov helps in improving sensing margin (indirectly area), and helps reduce the need for large storage cap
WL1
OFF
WL
driver
SA
“1” pattern
“0” pattern

## Slide 10: Timing Analysis of eDRAM
WR 0 onto 1
WR 1 onto 1
WR 1 onto 0
WR 0 onto 0
RD 0

## Slide 11: Timing Analysis of eDRAM
Three key sections of DRAM timing
Access transistor is the limiter for all BL operations
WL RS is the limiter in the WL operations
WL rise
BL dev
Writeback

## Slide 12: Timing Analysis of eDRAM
SA
SA
SA
WL driver
CBL-WL
CWL-WL
CBL-BL
RWLD, CWLD
COV

## Slide 13: Timing Analysis of eDRAM: WL Rise/Fall
1222.6
τWL = RWL_dr*(CWL_dr + CWL*(n-1) + CWL*(1))
+ RWL*(n-1)*(CWL*(n-1) + CWL*(1)) + RWL*CWL
τWL = 500*(4f +250f) + 4k*(250f) + 4*0.24f = 1.127ns
Worst-case bitcell
WL is loaded by Cgg (gate cap) and WL-WL coupling
WL0
active
WL Rise and Fall
WL1
OFF
WL
Driver
RWL_dr, CWL_dr
Word-line delay has the following components:
WL driver resistance and capacitance
WL wire resistance and WL wire capacitance  consists of WL-WL coupling (CWL-WL) and WL-active coupling (Cgg); minor components are WL-BL metal coupling and WL coupling to layers underneath
Load capacitance is the farthest bit with Cgg+CWL-WL of one bit as the load
CWL-WL
Cgg
Mostly WL RC dominated
1271.3:
τWL = RWL_dr*(CWL_dr + CWL*(n-1) + CWL*(1))
+ RWL*(n-1)*(CWL*(n-1) + CWL*(1)) + RWL*CWL
τWL = 400*(4f +130f) + 4k*(130f) + 4*0.24f = 0.573ns

## Slide 14: Timing Analysis of eDRAM: BL development
Worst-case bitcell
BL is loaded by Cov (Cgs/Cgd) and BL-BL coupling
SA
BL development
SA
“1” pattern
“0” pattern
1222.6
τWL = RADM*(CBL*(1)+ CBL*(n-1) + CSA)
+ RBL*(n-1)*(CBL*(n-1) + CSA) + RBL*(1)*CSA
τWL = 1e5*(12f +5f) + 500*(12f + 5f) + 5*5f = 1.7ns
CBL-BL
Cov
Bitline delay has the following components:
Access transistor is the driver; driver resistance and capacitance
BL wire resistance and BL wire capacitance  consists of BL-BL coupling (CBL-BL) and Cov capacitance; minor components are WL-BL metal coupling
Load capacitance is the SA CSA
RSA, CSA
Mostly AT resistance dominated
1271.3
τWL = RADM*(CBL*(1)+ CBL*(n-1) + CSA)
+ RBL*(n-1)*(CBL*(n-1) + CSA) + RBL*(1)*CSA
τWL = 6e4*(10f +5f) + 500*(10f + 5f) + 5*5f = 0.907ns

## Slide 15: Timing Analysis of eDRAM: BL/SN Writeback
Worst-case bitcell
BL is loaded by Cov (Cgs/Cgd) and BL-BL coupling
SA
BL and storage node write-back
SA
“1” pattern
“0” pattern
1222.6
τWL = RSA*(CSA + CBL*(1)+ CBL*(n-1) + CSN)
+ RBL*(n)*(CBL*(n) + CSN) + RADM*(1)*CSN
τWL = 1000*(5f + 12f +8f) + 500*(12f + 8f) + 1e5*8f = 0.83ns
CBL-BL
Cov
Bitline delay has the following components:
SA is the driver; driver resistance and capacitance
BL wire resistance and BL wire capacitance  consists of BL-BL coupling (CBL-BL) and Cov capacitance; minor components are WL-BL metal coupling
Load transistor is access transistor and load capacitance is the CCOB
RSA, CSA
Mostly AT resistance dominated
AT resistance is a key enabler that needs to be maintained across generations
1222.6
τWL = RSA*(CSA + CBL*(1)+ CBL*(n-1) + CSN)
+ RBL*(n)*(CBL*(n) + CSN) + RADM*(1)*CSN
τWL = 1200*(5f + 10f +13f) + 500*(10f + 13f) + 6e4*13f = 0.825ns

## Slide 16: DRAM Saddle-type FinFET/ RCAT
Si
W-MG
SiN
SiGe80
SiGe80
S
D

## Slide 17: DRAM Saddle-type FinFET/ RCAT: Gate Loop, WL
Uses FinFET technology with special gate recess technology followed by high quality thermal oxidation
Uses partial 111 surface post etch for high quality GOX formation using up 3.2nm Si (i.e. initial trench = 28nm + thermal oxidation to give 17nm space for W)  most likely @950C
Followed up with W recess and CVD-SiN fill
toxe = 7nm
Gate line resistance = 10-20kΩ
WL capacitance = 21 fF with 85-90% contrib from Cgg (no signs of strapping); 0.021 fF /cell
WL WL noise inhibited due to angled fin
WL slew = 5-10ns
Parameter | DRAM (1x) | Gen1 eDRAM | ADM
toxe (A) | 70 | 14 | 11
WL Resistance (Ω) | 10k-20k | 4k | 1.3k
WL capacitance (fF) | 21 | 130 | 300
WL slew (ns) | 5/10 | <1 | 1.5/2.5

## Slide 18: RCAT: Contact Loop, BL, n0
Resistance:
Two sources of leakage:
  Junction leakage
  GIDL (mostly dominant) (0.1 fA – 100’s fA for tail bits)
Contact resistivity ~ 1e-8 Ω-cm2 across 17*26 nm2 area
Total contact resistance = Rc = 2.2 kΩ (x2 for 2 CON)
Doping @SiGe80,top = 1e20 /cm3 (peak)
BL resistance = 840 cells * 35 uohm-cm*50nm/(16*40nm2) = 4.6 kΩ
Capacitance:
BL-n0 cap = C_metal-metal + C_SiGe-SiGe
BL-n0 cap = 5.7 aF + 5.5 aF (/cell)
BL-WL cap = 5.79 aF (/cell)  ~half of Cgg
Total BL loading cap = 15 aF/cell
Net BL parasitics = 12.6 fF
Column IO ~ 2-5 fF
Net BL loading = 19 fF
Net RC, Sensing:
BL charge/disch = 2ns
Sense margin = 120 mV approx
0 25 50
10-14
10-16
GIDL (A)/bit vs Lov (nm)
DRAM target
DRAM loads >840 cells on the BL to get array efficiency

## Slide 19: RCAT: Channel, Overall transistor performance
Transistor parameters:
Lg = 20nm fin-type + 40*2 nm gated planar
Z = 20nm + 90nm
toxe = 7nm
Idsat = 217 uA/um @ Vds = 1V; Vgs-Vt = 3V
Ioff,GIDL = 1e-13 to 1e-15 A/um @ Vgs = -0.3V
Refresh parameters:
Refresh time = 32/16ms @100C
Refresh power ~ 5fF * 1 * 1 * 5e8 Hz = 2.5e-6
DRAM has matched drive current for the same charge (i. e. (VGS-Vt) ) compared to ADM
Long channel
Poor Rext
Thick EOT/toxe
ADM main advantage is fundamentally low leakage at better drive current

## Slide 20: DRAM Unique Aspects
Benefit in Ioff due to high curvature channel
High Vt device with BODY BIAS to improve leakage
Air-gaps between BLs
GIJL issues @tip

## Slide 21: Parameters I
Parameter | DRAM (1x) | Gen1 eDRAM | ADM
Cell size (nm x nm) | 48 x 54 | 108 x 270 | 108 x 135
Lg (nm) | 100 | 40 | 40
Z (nm) | 210 | 60 | 73
Cov capacitance (aF) | 6 | 38 | 25
BL Resistance (Ω) | 3k-4k | 0.5k | 1k-2k
Idsat (uA/um) @ Vds = 1V | 217 (Vov = 3V) | 315 (Vov = 0.65V) | 300 (Vov = 1.2V)
Ioff (pA/um) @ Vds = 1V | <0.01 | 0.1 | 0.1 to 0.0001
V_WL (V) | -0.4 to 3.5 | -0.4 to 1.8 | -1 to 1.8
tref (ms) | 16 @45C/ 8 @100C | 0.5 @ 100C | >8 @100C
RC + Rext (kΩ-um) | 2.2 | 0.8 | ~0.5
Fundamental transistor matches or surpasses eDRAM/ADM in leakage  but can ADM’s lower leakage matter for tref >16ms @100C/120C?

## Slide 22: Parameters II
Parameter | DRAM (1x) | Gen1 eDRAM | ADM
WL capacitance (fF) | 21 | 130 | 300
WL slew (ns) | 3-5 | 1.2 | 1.5
BL Resistance (Ω) | 3k-4k | 0.5k | 1k-2k
WL Resistance (Ω) | 10k-20k | 4k | 1.3k
WL capacitance (fF) | 21 | 60 | 80-100
WL slew (ns) | 5/10 | 1.2 | 1.5/2.5
BL Resistance (Ω) | 3k-4k | 1.1k | 1k-2k
BL capacitance (fF) | 19 | 21 | 16
Storage capacitance (fF) | 11-16 | 13-16 | 7
Sense time (ns) | 3 | 1.1 | 1.3
Latency (ns) | 30-70 | 5 | <8.5
Power @ BW (W/GBps) | 50/100 | ? | ?
ADM uses thin EOT devices
ADM uses Cu lines
ADM uses Cu lines
Notes: Optimistic next gen
PLANAR

## Slide 23: Gen5 Scaling Options
FinFET topo:
Offers advantage if COB and BL on opposite sides
Shared S/D and reduces Cov
Choice between RCAT and true fin
Lots inline; ECD 11/20
Vertical topo:
Offers advantage as COB may be completed before ADM processing
Gated contacts like backgate
Large Z despite scaling
Lot debug ongoing
1T-nF:
Bitcell scaling without change in transistor dimensions
Leakage needs alleviated
Capacitor can be vertically integrated like NAND
Susceptible to noise
Gated by Ferroelectric technology + disturb
1T Memory:
Leakage needs alleviated
Needs precise Vt targeting to maintain sense margin across lifetime
Assists vertical AR in stacking
Gated by Ferroelectric technology + disturb
BG topo:
Offers advantage if COB and BL on opposite sides
Shared S/D and reduces Cov
Choice between RCAT and true fin
Lots inline; ECD 11/20
Recess Channel Topology
How do we define the success criteria for each of these technologies?
How do we differentiate between results on large CR vehicle vs scaled implementations?

## Slide 25: DRAM vs eDRAM Timings: Rate Limiting Metrics
tRC = 45ns to 48ns
tRAS = 35ns
0 10ns 20ns 30ns 40ns 50ns 60ns 70ns
eDRAM tRC is lower than DRAM/HBM due to the following:
1.2-1.5x Slow Transistor in DRAM vs eDRAM/ADM and 2x worse COB (50%)
WL/BL rise/fall is 1.5x lower in eDRAM due to Cu lines (30%)
Major difference is also SA speeds causing another 2x difference (20%)
Short write-back
i.e. low transistor resistance
Long write-back
i.e. high transistor resistance
tRC = 2ns to 5ns
Related to scaling bitcell
Most different comes from array transistor resistance @cost of IOFF

## Slide 26: X22M Block Timing (Write)
Umut Arslan, AD

## Slide 29: X22M Block Timing (Read)
Umut Arslan, AD

## Slide 30
  Retention – Median Bit - 25C
Intel Top Secret
Assume 250 mV lost in storage node voltage  Another 250 mV used for sensing margin
COB = 5 fF, parasitic capacitances = 20 fF
 | Store 0 |  | Store 1 | 
Self-refresh |  |  |  | 
 | Target (5σ bit + 110C) | ~ ms | Target (5σ bit + 110C) | ~ ms
 | Median Bit – Current UPF | 11 s | Median Bit – Current UPF | >> 100 s
Active Bitline |  |  |  | 
 | Target (5σ bit + 110C) | ~ 200-300 µs | Target (5σ bit + 110C) | ~ 200-300 µs
 | Median Bit – Current UPF | 1.6 s | Median Bit – Current UPF | 29 ms
0.5V
-0.4V
0V
0.5V
-0.4V
1V
1V
-0.4V
0V
0V
-0.4V
1V
AD team

## Slide 31
  Retention – Median Bit - 110C
Intel Top Secret
Assume 250 mV lost in storage node voltage  Another 250 mV used for sensing margin
COB = 5 fF, parasitic capacitances = 20 fF
 | Store 0 |  | Store 1 | 
Self-refresh |  |  |  | 
 | Target (5σ bit + 110C) | ~ ms | Target (5σ bit + 110C) | ~ ms
 | Median Bit – Current UPF | 340 ms | Median Bit – Current UPF | 200 s
Active Bitline |  |  |  | 
 | Target (5σ bit + 110C) | ~ 200-300 µs | Target (5σ bit + 110C) | ~ 200-300 µs
 | Median Bit – Current UPF | 75 ms | Median Bit – Current UPF | 3.8 ms
0.5V
-0.4V
0V
0.5V
-0.4V
1V
1V
-0.4V
0V
0V
-0.4V
1V
AD team

## Slide 32
  Read and Write – Median Bit - 25C
Intel Top Secret
Read: Includes WL slope, measured time until equalization (10 mV difference)
Write: 99% charge or discharge, median bit does not reach WL slope turning off
 | ‘0’ |  | ‘1’ | 
Read |  |  |  | 
 | Target (5σ bit) | 2.5 ns (including WL slope) | Target (5σ bit) | 2.5 ns (including WL slope)
 | Median Bit – Current UPF | 1.2 ns | Median Bit – Current UPF | 1.5 ns
Write |  |  |  | 
 | Target (5σ bit) | 2.5 ns + WL slope | Target (5σ bit) | 2.5 ns + WL slope
 | Median Bit – Current UPF | 1.2 ns | Median Bit – Current UPF | 1.8 ns
0.5V
1.7V
0V
0.5V
1.7V
1V
0V
1.7V
1V  0V
1V
1.7V
0V  1V
AD team

## Slide 33
  Read and Write – Median Bit - 110C
Intel Top Secret
Read: Includes WL slope, measured time until equalization (10 mV difference)
Write: 99% charge or discharge, median bit does not reach WL slope turning off
 | ‘0’ |  | ‘1’ | 
Read |  |  |  | 
 | Target (5σ bit) | 2.5 ns (including WL slope) | Target (5σ bit) | 2.5 ns (including WL slope)
 | Median Bit – Current UPF | 1.4 ns | Median Bit – Current UPF | 1.9 ns
Write |  |  |  | 
 | Target (5σ bit) | 2.5 ns + WL slope | Target (5σ bit) | 2.5 ns + WL slope
 | Median Bit – Current UPF | 1.5 ns | Median Bit – Current UPF | 2.4 ns
0.5V
1.7V
0V
0.5V
1.7V
1V
0V
1.7V
1V  0V
1V
1.7V
0V  1V
AD team

## Slide 34: FinFET: Z, L Design Strategy
Fin height for on-state resistance to optimize tsense
Recess Fin to increase Chanel length to reduce leakage for retention time
L1
Z1,H
Z1,W
RCh1 = (qµCoxVon)-1 · L/W
RCh1-1 = qµCoxVon· (2·Z1,H+ Z1,W)/LG1
RCh2 = (qµCoxVon)-1 · L2/[ ½ ·(Z1+Z2)]
RCh2-1 = qµCoxVon· [Z1,H+ Z2,H+ ½(Z1,w+Z2,w)]/L2
L1 + 2 · L2 ≈ Lmin ;
Z2,H = Z1,H + L2 ;
Z2,W = Z1,W + 2 · L2 ;
RCh1-1 = qµCoxVon · (2 · Z2,H + Z2,W – 4 · L2) / L1 ;
RCh2-1 = qµCoxVon · (2 · Z2,H + Z2,w – 2 · L2) / L2 ;
where
Von = VP – VT ;
RCh = RCh1 + 2· RCh2 ;
Active Design Rule (2 Cells)
Cell Active Pitch = Z2W+ SZ ;
Cell Active Pitch = 3 · LSD + 2 · L1 + SL
L2
Z2,H
Z2,W
LSD
SL
SZ

## Slide 35: Layout for Shared Contact FinFET
BL
BL
WL1
WL2
WL0
Shared S/D
Shared S/D
Shared S/D
COB via
COB via
COB via
COB via
COB via
COB via
COB via
WL1
WL2
Shared BL
COB via
Cut along active

## Slide 36
WL1
WL2
Shared BL
COB via
Cut along active

## Slide 37: FinFET: WL and BL design
Key bottleneck is BL parasitics to COB-via and WL
Worst-case bitcell
BL is loaded by Cov (Cgs/Cgd) and BL-BL coupling
SA
BL Loading
SA
“1” pattern
“0” pattern
Worst-case bitcell
WL is loaded by Cgg (gate cap) and WL-WL coupling
WL0
active
WL Loading
WL1
OFF
WL
driver
WL1
OFF
WL2
ON
Shared BL
COB via
Cut along active
Cov
Cgg
CWL-WL
CBL-CV
CBL-WL

## Slide 38: Channel WA: Z, L Design Strategy
Cylinder circumference for on-state resistance to optimize tsense
Cylinder height to increase Chanel length to reduce leakage for retention time
t_ADM + t_hik + Le,min ≈ Lg ;
Zch =  ·( Dcon,b – 2 · t_ADM) ≈  · Dcon,b ;
Dcon,b = 2 · (t_ADM + t_hik ) + t_MG
Rcon,b = con ·  · Dcon,b2/4 ;
Rcon,t = con ·  · Dcon,t · Lcon,t ;
RCh = (qµCoxVon)-1 · Lg / ( ·( Dcon,b – 2 · t_ADM)) ;
RCh = (qµCoxVon)-1 · Lg / ( ·( 2 · t_hik + t_MG)) ;
where
Von = VP – VT ;
Rtotal = RCh + Rcon,b + Rcon,t;
Active Design Rule
Cell Active Pitch = Dcon,b+ SWL + 2 · mWL ;
Cell Active Pitch = Dcon,b+ SBL
Lg
Le,min
Lcon,t
t_ADM
t_hik
Zch = pi*Dcon,t
Dcon,b
t_MG
SWL
SBL
mWL

## Slide 39: Layout of Channel Wrap-around Topology
Manhattan Geometry
Staggered Geometry
Manhattan Geometry
Staggered Geometry
WL0
WL2
WL4
WL2
WL1
WL3
WL5
WL0
WL1

## Slide 40: Channel wrap-around: WL and BL design
WL-WL coupling is high, unless WL height reduced
Worst-case bitcell
BL is loaded by Cov (Cgs/Cgd) and BL-BL coupling
SA
BL Loading
SA
“1” pattern
“0” pattern
Worst-case bitcell
WL is loaded by Cgg (gate cap) and WL-WL coupling
WL0
active
WL Loading
WL1
OFF
WL
driver
Cut along active
WL0
WL2
WL4
WL1
WL3
WL5
Cov
Cgg
CWL-WL
CBL-BL
CBL-WL
Shared BL
CBL-WL
WL OFF
Cgg
CBL-WL
WL ON

## Slide 41: Comparison between Fin and Vertical
Type | resitivity (uohm.cm) | BL CD (nm) | BL space (nm) | height of BL (nm) | resistance/bit (ohms) | Cov (F) | BL-BL coupling (F) | BL-WL Coupling | Total BL cap/bit (F) | BL driver resistance (ohms) | BL driver capcitance (F) | bits/BL (#) | WB delay (s) | BL delay (s)
FinFET | 350 | 30 | 20 | 30 | 273.99 | 5.56E-19 | 3.74E-18 | 5.782E-19 | 4.88E-18 | 1500 | 1.39025E-15 | 1024 | 5.01E-08 | 1.07E-09
Channel WA | 350 | 10 | 10 | 10 | 1168.46 | 3.77E-17 | 2.22E-18 | 4.779E-20 | 4.00E-17 | 1500 | 1.39025E-15 | 128 | 6.33E-09 | 5.99E-10
Type | resitivity (uohm.cm) | height of WL | resistance/bit (ohms) | Cgg (F) | WL-WL coupling (F) | BL-WL Coupling | Total WL cap/bit (F) | WL driver resistance (ohms) | WL driver capcitance (F) | bits/WL (#) | WL delay (s)
FinFET | 30 | 30 | 10.21 | 1.36E-17 | 7.84932E-17 | 2.36E-19 | 9.24E-17 | 1500 | 1.39025E-15 | 1024 | 1.32E-09
Channel WA | 30 | 30 | 4.94 | 1.84E-16 | 7.2321E-18 | 4.248E-20 | 1.92E-16 | 1500 | 1.39025E-15 | 1024 | 2.15E-09

## Slide 42
Fatih H.
Lg = 40nm
Lcon = 20nm
Z = 70nm
Lg = 35nm
Lcon = 17.5nm
Z = 60nm
Lg = 30nm
Lcon = 17.5nm
Z = 45nm
Final scaling with current doping with planar geometry
For planar, need to reduce doping
Raised S/D already assumed to increase Lg by ~7-10nm
Channel
TD Roadmap

## Slide 43: CR Research Direction
Figure out the limitations for BG scaling (TCAD + data)
Define smallest DR’s possible for each topo
Establish pit-stops to assess scaling
Need help to define mask-set for intermediate steps
Backgate
FinFET
Vertical
Alternate contact
Cell size (μm2)
X22M
90 x 60
Lateral scaling limits
BIG Question @Conclusion:
When should we jump from back-gate to a different topology?

## Slide 44: CR ADM WG Goals
Setup a clear parametric window for High Density Memory
  Architecture  latency, BW, specs
  Identify array-level pinch-points with scaling and disturb mechanisms
Determine BG topology challenges and scaling roadmap
  Work with TD to define layout and device techniques that scale eDRAM (integrity of BG)
  Work with TCAD to understand limits of scaling and potential solutions
Ascertain the scalable topology for eDRAM scaling
  Define DTS and MTS for each topology
  Identify break-points with scaling (Electrical + Integration)
  Define DRs based on critical parameters (CRs, performance etc)
Define a framework for final mask-set needed for ‘fast-fail’ eDRAM transistor screening

## Slide 45: CR Mask Timeline
Establish deliverables on existing CR masks & identify shortcomings
Create integration options + design space
Understand challenges of scaling BG flow
Define different topos and their features
Decide on DRs for different topos
Define test flow
Spider Flow with X22S/MA
Define immediate intercept for new CR mask-sets
PHASE I
PHASE II

## Slide 46: Timeline of Milestones
Vertical
Demonstrate paired configuration with TD – implants, ozone treatment
ALD IGZO/In2O3, Raised S/D
CDO+CDN on top
C and other contact metals
Demonstrate top gate on 1x35AA @ Lg <30nm
Scale GOX (<20A toxe), then stabilize cont/Rext (<2kohm-um)
Backend CDO/CDN stability
S/D regrowth, In2O3 channel
Follow TG:
FinFET on 1x35 @Lg<30nm; Z>100nm
GOX (<20A toxe), Rext (<2kohm-um)
Backend stability; S/D regrowth, In2O3 channel
Gain cell structures
Demo. Rext, ueff, Lg –ready device with vertical topology
Scale GOX, ALD MG, In2O3 channel
Impact of integration schemes and scaling limits
CON experiments
Q3’19
Q4’19
Q1’20
Q2’20
No progress here

## Slide 47: Timeline of Milestones
Vertical
Tentative cell size to Abhishek ww42.4
Establish DTS and process flow ww43 (rev1)
Finalize DTS and cell topo selection ww44
Discuss process flow with NSG stakeholders ww45
Peer review with TD+NSG ww46
Engage with Derchang ww41+
Engage with Elliot+Kim+Nikhil ww43+
Engage with Travis ww44+
Engage with NSG ww45+
Q3’19
Q4’19
Q1’20
Q2’20
Starting next week – we will start a meeting with Elliot+Kim+Nikhil and use it as a discussion forum

## Slide 48: CR New Mask Objectives
Must be easily transferable
Should learn at relevant pitches
Should answer fast-fail questions (what fundamentally fails upon scaling)
What is a Spider Flow?
Advantages of Spider Flow
CMOS + 3-4 metal layers (TD start)
New Product Flow (CR – RECL/FL)
CR builds upon existing TD infrastructure at scaled pitches – changes ONLY:
Array
Socket
Advantages: @pitch, fast transfer to TD, aggressive topology skew
Disadvantages: Slow to NPI/develop/implement? Slow to SORT, need design alignment
Old array
May not be able to test each row
Reuses X22 infra
Fast cycle time and sturdy vehicle
New array

## Slide 49: ADM eDRAM Array Design
ADM is back-gated transistor
Targeted cell:
108 x 135 nm2
2x cell area scaling wrt 22nm eDRAM
WL1
WL0
Lg = 40nm
2F
4F
CON = 27.5nm
BL
8F2 cell
COB
COB
COB

## Slide 50: Depletion Depth in TFT-ADM
TiN
HfO2
Doping ~6e17 /cm3
CR-Coupon
CB
EF
Doping ~6e18 /cm3
CR 300mm
Doping ~6e19 /cm3
TD 300mm (X22M)
Full Depletion
Limited Depletion
<1nm Depletion
Increased doping from contacts and channel prevents gate field from fully depleting ADM  SS/Vt degradation  Poor ILEAK
TiN
HfO2
CB
EF
TiN
HfO2
CB
EF
ADM
ADM
ADM

## Slide 51: Model parameters that were optimized
ADM CHANNEL
PASSIVATION FILM
HIGH-K DIELECTRIC
GATE METAL
SOURCE
DRAIN
RAISED CONTACT
RAISED CONTACT
Constant electron mobility
Contact resistivity
Metal work function
TCAD team

## Slide 52: Contact Improvement with RSD
DISTANCE FROM ADM TOP SURFACE (nm)
DISTANCE FROM ADM TOP SURFACE (nm)
CURRENT DENSITY
1T1C
M6
1T1C
M6
CHANNEL CUT LINE
CONTACT CUT LINE
VD=1.0
VD=1.0
Channel cut line
Contact cut line
Current crowds at bottom surface when device is on.
*ADM top surface references to ADM/passivation interface
TCAD team

## Slide 53: Off current (VG=-0.8V)
DISTANCE FROM ADM TOP SURFACE (nm)
DISTANCE FROM ADM TOP SURFACE (nm)
CURRENT DENSITY
CURRENT DENSITY
1T1C
M6
1T1C
M6
1T1C
M6
1T1C
M6
CHANNEL CUT LINE
CONTACT CUT LINE
VD=0.05
VD=1.0
VD=0.05
VD=1.0
Leakage current crowds at top surface
Channel cut line
Contact cut line
*ADM top surface references to ADM/passivation interface
TCAD team

## Slide 54: Device structure
Simulated geometry: InOx  ADM
PTD1930196 Summary
002 - W368(0,0) - 300C 5nm InOx RSD w/W/TaN BLD liner at M7
PASSIVATION
ADM
HIGH K DIELECTRIC
GATE
INOX
INOX
SOURCE
DRAIN

## Slide 55: Scaling skews and metrics
WL1
WL0
Lg
2F
4F
Drain
BL
8F2 cell
COB
COB
COB
COB
Z
LG
LCON
Doping skews:
0.1X, 0.5X, 1X (Fit = 1e19), 2X, 10X
Bias Conditions |  |  | 
 | VG | VS | VD
ION, CON | 1.7 | 0.5 | 0.7
 |  | 0 | 1
IOFF,COFF | -0.4 | 0 | 1
 | -0.8 | 0 | 1

## Slide 56: Calibration with non-RSD contact
Parameter | Value
Mobility | 15.9
Contact Resistivity | 1.097e-7
Bulk Doping (Ho) | 1e19
Bulk Vo | 1e16
Interface Vo | 1e13
Bulk No | 1e10
Interface No | 1e8
Gate Work Function | -0.256 eV
Parameters applied to RSD scaling study
PASSIVATION
ADM
HIGH K DIELECTRIC
GATE
SOURCE
DRAIN
Constant mobility
Vo, No as Dit at passivation interface
Uniform bulk doping (Ho) and traps (Vo, No)
Dit + Uniform bulk density model
Lot Z917R52
Ho = Hydrogen on Oxygen site
Vo = Vacancy on Ox
No = Nitrogen on Ox

## Slide 57: ID-VG vs doping (nominal roadmap)
IDLIN
IDSAT
LOWER DOPING
LOWER DOPING

## Slide 58: Impact of doping on ION and IOFF
IDSAT vs. NOMINAL IOFF
LOWER DOPING
POR in BOLD BLUE
Target space is GREEN BOX
LOWER DOPING
IDLIN vs. NOMINAL IOFF
*Corrected for VT shift

## Slide 59: Impact of doping on ION and IOFF
LOWER DOPING
IDLIN vs. UNDERDRIVE IOFF
IDSAT vs. UNDERDRIVE IOFF
LOWER DOPING
POR in BOLD BLUE
Target space is GREEN BOX
*Corrected for VT shift

## Slide 60
6F2 cell architecture - M5, VBG, New mask and ADM level
M5 WL at ½ of OGD pitch
Requires new mask to cut TiN before ADM HiK (use ADB?)
VBG needs:
  Enclosed by ADM and/or TiN
  Enough overlap to proper WL
  Enough separation to adjacent WL
Ideas and concerns:
  WL at different levels using deep via?
  Coupling of unselected WL to selected BL in the same ADM island?
PGD cut 1
PGD cut 2
PGD cut 2
PGD cut 1

## Slide 61
PGD cut 1
PGD cut 2
PGD cut 1
PGD cut 2
BLD pitch relaxed
BLD to VCB vs VCB to COB coverage trade-off
Ideas and concerns:
  BLD overlapping two xtors?
  BLD pitch division landing islands below VCB for shorting margin/ VCB centered on COB?
6F2 cell architecture - ACT, BLD and VCB level

## Slide 62
PGD cut 1
PGD cut 2
PGD cut 1
PGD cut 2
COB square
BLD to VCB vs VCB to COB coverage trade-off
Ideas and concerns:
  Double wall COB. Impact on layout?
  If BLD landing pads, then VCB could be centered
6F2 cell architecture - COB level

## Slide 63
PGD cut
PGD cut
WL
TiN
ES
VBG
VBG
HiK
ADM
ACT
ACT
ACT
ES
BLD
VCB
VCB
COB
COB

## Slide 64
PGD cut
PGD cut
WL
TiN
ES
VBG
VBG
HiK
ADM
ACT
ACT
ACT
ACT needs to be large enough that it does not walk off of TiN/ADM Island
Looks like Center ACT will always need to be bigger
Space needs to be large enough to limit CAP/crosstalk
Height must be short enough to reduce CAP
Lg still defined by ACT space, so L/R Lg always are the same
How will we define these cuts? Bottom cut not “necessary” but may make tessellating easier

## Slide 65: TCAD Request (2019/10/11)
ADM
“x”
ADM
BL
COB
COB
Questions (assuming doping skew between 0.5X POR to 5x POR; 120x90 cell component dimensions):
How much does Rext change vs Vg?
How much does Ioff change when ‘x’ is an underlap?
What is it’s impact on Cov and WL-WL coupling (vs TiN MG thickness 5, 10, 20 nm)?
Does an underlap in the COB side matter equally?
What is the sensitivity to misalignment (range +/- 20nm) given x = Lcon, 0.5*Lcon, 2*Lcon ?
What is the breakdown of RextBL, RextCOB, Rchannel?
“Lcon”
For ADM thickness 5nm, 6nm, 7nm
In2O3 contacts 3nm, 5nm

## Slide 66: Solutions for BG ADM Scaling
Recessed Channel for Lg increase
Raised S/D for Rc improvement
Z-scaling still fundamentally limited
What is the correct topo for scaling?
WL0
Lg = 30nm
CON = 15nm
BL
COB
WL1
COB
COB
Scaled cell:
60 x 90 nm2
Lg = 40nm; Lcon = 15nm; Z = 40nm
ADM
S
D
ADM
S
D
S
D
Recessed Channel
Raised S/D
What limits S/D spacing/Lg/AR of trench?
Max impact
Notes: Topos for Lg increase
Lcon increase
Z-scaling
Summarize into Lg, Lcon,

## Slide 67: Scaling Challenges/Paths
ADM Scaling
XTOR scaling
Ion + Ioff in voltage range
Contact length scaling
Parasitic capacitance scaling
Angled ADM?
COB scaling
Double-walled capacitor to reduce noise/increase cap
Ferroelectric to increase retention – decouple Ioff
Pillar type?
Parasitic Scaling
Introduce air-gaps BLn0
Reduce Cov with scaling or S/D regrowth
Angled ADM?

## Slide 68: Scaling Challenges/Paths
ADM Scaling
XTOR scaling
Ion + Ioff in voltage range
Contact length scaling
Lg scaling
New topologies
Vertical ADM
Demonstrate scaling limit of vertical ADM
Rc and Rext
Shared gating
FinFET ADM
Demonstrate scaling limit of FinFET ADM
RCAT
Rc and Rext
C_overlap
Planar ADM
Demonstrate scaling limit of planar ADM at high doping
Recess Channel/Z
S/D Regrowth
Materials
Scalable and tunable ADM to enable multi-Vt EOL
CON stability, EOL stability
MG WF engineering
GOX engineering
Implantation, treatments etc

## Slide 69: Topologies with TFTs
Channel
Bottom Gate Top Contact
Channel
Top Gate Top Contact
Channel
Top Gate Bottom Contact
Channel
Top Gate Alternate Contact
Key advantages:
Fin  better gate control, better subthreshold swing, better leakage, more Z  more current @Ion
Gate to contact overlap  better contact resistance while having low Cov @BL side for good SM
Cov at CUB-side is miller  does not affect active device
No need for angling
D
S
MG
CAA
S
D
GAA
Key advantages:
Better electrostatics
Lg independent of scaling cell
Large contact areas
Fewer masks
Key advantages:
Fin  better gate control, better subthreshold swing, better leakage, more Z  more current @Ion
Key advantages:
Ease of integration
8F2 – 6F2
6F2 – 5F2
4F2

## Slide 70: Changes with ADM Scaling
Back-gated device suffers from Lg scaling due to SCE @high doping
Lcon and Z scaling further reduces the performance
WL0
Lg = 30nm
CON = 15nm
BL
COB
WL1
COB
COB
Scaled cell:
60 x 90 nm2
WL_p = 50nm; BL_p = 90nm; Active_p = 50 x 90
Lg = 40nm; Lcon = 15nm; Z = 40nm
50 x 67.5 nm2
WL_p = 60nm; BL_p = 135nm; Active_p = 50 x 135
Lg = 30nm; Lcon = 15nm; Z = 35nm
WL0
COB
WL0
COB
COB
Scaled cell:
40 x 50 nm2
WL_p = 40nm; BL_p = 100nm; Active_p = 40 x 100
Lg = 20nm; Lcon = 15nm; Z = 100nm
Optimal angle = 76 deg for OGD = 40nm
Fin height  wide Z
Better gate control
Angled for 6F2
WL0
Lg = 30nm
CON = 15nm
BL
COB
WL1
COB
Scaled cell:
40 x 50 nm2
WL_p = 40nm; BL_p = 50nm; Active_p = 40 x 50
Lg = 20nm; Lcon = 35nm; Z = 100nm
GAA/2-sided  wide Z
Long Lg
Contact area = active pitch

## Slide 71: FinFET: Z, L Design Strategy
Fin height for on-state resistance to optimize tsense
Recess Fin to increase Chanel length to reduce leakage for retention time
L1
Z1,H
Z1,W
RCh1 = (qµCoxVon)-1 · L/W
RCh1-1 = qµCoxVon· (2·Z1,H+ Z1,W)/LG1
RCh2 = (qµCoxVon)-1 · L2/[ ½ ·(Z1+Z2)]
RCh2-1 = qµCoxVon· [Z1,H+ Z2,H+ ½(Z1,w+Z2,w)]/L2
L1 + 2 · L2 ≈ Lmin ;
Z2,H = Z1,H + L2 ;
Z2,W = Z1,W + 2 · L2 ;
RCh1-1 = qµCoxVon · (2 · Z2,H + Z2,W – 4 · L2) / L1 ;
RCh2-1 = qµCoxVon · (2 · Z2,H + Z2,w – 2 · L2) / L2 ;
where
Von = VP – VT ;
RCh = RCh1 + 2· RCh2 ;
Active Design Rule (2 Cells)
Cell Active Pitch = Z2W+ SZ ;
Cell Active Pitch = 3 · LSD + 2 · L1 + SL
L2
Z2,H
Z2,W
LSD
SL
SZ

## Slide 72: Layout for Shared Contact FinFET
BL
BL
WL1
WL2
WL0
Shared S/D
Shared S/D
Shared S/D
COB via
COB via
COB via
COB via
COB via
COB via
COB via
WL1
WL2
Shared BL
COB via
Cut along active

## Slide 73
WL1
WL2
Shared BL
COB via
Cut along active

## Slide 74: FinFET: WL and BL design
Key bottleneck is BL parasitics to COB-via and WL
Worst-case bitcell
BL is loaded by Cov (Cgs/Cgd) and BL-BL coupling
SA
BL Loading
SA
“1” pattern
“0” pattern
Worst-case bitcell
WL is loaded by Cgg (gate cap) and WL-WL coupling
WL0
active
WL Loading
WL1
OFF
WL
driver
WL1
OFF
WL2
ON
Shared BL
COB via
Cut along active
Cov
Cgg
CWL-WL
CBL-CV
CBL-WL

## Slide 75: Channel WA: Z, L Design Strategy
Cylinder circumference for on-state resistance to optimize tsense
Cylinder height to increase Chanel length to reduce leakage for retention time
t_ADM + t_hik + Le,min ≈ Lg ;
Zch =  ·( Dcon,b – 2 · t_ADM) ≈  · Dcon,b ;
Dcon,b = 2 · (t_ADM + t_hik ) + t_MG
Rcon,b = con ·  · Dcon,b2/4 ;
Rcon,t = con ·  · Dcon,t · Lcon,t ;
RCh = (qµCoxVon)-1 · Lg / ( ·( Dcon,b – 2 · t_ADM)) ;
RCh = (qµCoxVon)-1 · Lg / ( ·( 2 · t_hik + t_MG)) ;
where
Von = VP – VT ;
Rtotal = RCh + Rcon,b + Rcon,t;
Active Design Rule
Cell Active Pitch = Dcon,b+ SWL + 2 · mWL ;
Cell Active Pitch = Dcon,b+ SBL
Lg
Le,min
Lcon,t
t_ADM
t_hik
Zch = pi*Dcon,t
Dcon,b
t_MG
SWL
SBL
mWL

## Slide 76: Layout of Channel Wrap-around Topology
Manhattan Geometry
Staggered Geometry
Manhattan Geometry
Staggered Geometry
WL0
WL2
WL4
WL2
WL1
WL3
WL5
WL0
WL1

## Slide 77: Channel wrap-around: WL and BL design
WL-WL coupling is high, unless WL height reduced
Worst-case bitcell
BL is loaded by Cov (Cgs/Cgd) and BL-BL coupling
SA
BL Loading
SA
“1” pattern
“0” pattern
Worst-case bitcell
WL is loaded by Cgg (gate cap) and WL-WL coupling
WL0
active
WL Loading
WL1
OFF
WL
driver
Cut along active
WL0
WL2
WL4
WL1
WL3
WL5
Cov
Cgg
CWL-WL
CBL-BL
CBL-WL
Shared BL
CBL-WL
WL OFF
Cgg
CBL-WL
WL ON

## Slide 80: Gate WA: Z, L Design Strategy
Cylinder circumference for on-state resistance to optimize tsense
Cylinder height to increase Chanel length to reduce leakage for retention time
2 · LgCONUL + Le,min ≈ Lg ;
Zch =  · Dcon ;
Rcon = con ·  · Dcon2/4 + RLgCONUL ;
RCh = (qµCoxVon)-1 · Lg / ( · Dcon) ;
where
Von = VP – VT ;
Rtotal = RCh + 2 · Rcon;
Active Design Rule
Cell Active Pitch = 2 · t_hik + Dcon + SWL + 2 · mWL ;
Cell Active Pitch = 2 · t_hik + Dcon + SBL
Lg
Le,min
t_ADM
t_hik
Zch = pi*Dcon
Dcon
SWL
SBL
mWL
Dcon
LgCONUL

## Slide 81: Changes with ADM Scaling
Back-gated device suffers from Lg scaling due to SCE @high doping
Lcon and Z scaling further reduces the performance
Today’s cell:
108 x 135 nm2
WL_p = 108nm; BL_p = 135nm; Active_p = 108 x 135
Lg = 40nm; Lcon = 27.5nm; Z = 73nm
WL1
WL0
Lg = 40nm
2F
4F
CON = 27.5nm
BL
COB
COB
COB
WL0
Lg = 30nm
CON = 15nm
BL
COB
WL1
COB
COB
Scaled cell:
60 x 90 nm2
WL_p = 60nm; BL_p = 90nm; Active_p = 60 x 90
Lg = 30nm; Lcon = 15nm; Z = 45nm

## Slide 82: Accumulation-mode Band Diagram in ADM
SiO2
SiO2
ADM
HfO2 10 nm
TiN 100 nm
CNT
Passivation
CNT
Passivation
ADM gate modulates both Rchannel and Rcontact  together they result in low IOFF

## Slide 83
Short Channel Effects Improve with Adamantine Body Scaling of Doping Reduction
TCAD Simulations predicts that thin body will enable SS target
High doping results in Poor Gate Control
Intel Top Secret
TCAD: Sean Ma
Experimental Data
ADM Scaling
1e20 /cm3
1e18 /cm3
1e19 /cm3
SiO2
SiO2
ADM
HfO2 6 nm
TiN 100 nm
CNT
Passivation
CNT
Passivation
Notes: ION Ioff vs Lg min Z possible

## Slide 84: CR Memory Research Density vs. Latency Benchmark
Intel Confidential
Chart: Cell Latency (s)
| 2.5000000000000002E-10 | 2.5000000000000002E-10 | 2.5000000000000002E-10 | 2.5000000000000002E-10 | 5.0000000000000001E-9 | 2.9999999999999997E-8 | 2.9999999999999997E-8 | 2.9999999999999997E-8 | 9.9999999999999995E-8 | 9.9999999999999995E-8 | 1.0000000000000001E-5 | 1.0000000000000001E-5 | 1.0000000000000001E-5
Array Bit Density (Mb/mm2) | 23.6 | 25 | 13.7 | 7.5 | 17.5 | 75 | 120 | 200 | 500 | 1000 | 2200 | 4400 | 6600
Array Bit Density (Mb/mm2) | 23.6 | 25 | 13.7 | 7.5 | 17.5 | 75 | 120 | 200 | 500 | 1000 | 2200 | 4400 | 6600 | 45 | 86 | 125 | 173
1271.3
e-DRAM
HBM
DRAM
OPTANE
X-Point
Intel
NAND
e-NVM
MRAM
RRAM
SRAM
1274
CR Research
ADM
Vertical ADM or FeFET
ORION + ADM x 2
ORION or ADM x 2
PTD – 1222 Dev’t
In Production (Intel, Samsung)
NAND 1T-1C or NAND FerroFET with Word Access
Notes: Add another column showing Q2/Q3 progress

## Slide 85: Topology Assumed for simulations
TiN 5nm
ADM 5nm
HfO2 5nm
S
D
S
D
20nm
Leff = 40nm
10nm
15nm
11nm
20nm
5nm
S
D
S
D
20nm
50nm tall
15nm
11nm
20nm
TiN 5nm
Leff = 30 + 20 + 30
D
S
MG
Wrap-around Channel
5nm ADM; 5nm HfO2; 10nm space; 20nm MG
S
D
GAA
5nm ADM; 5nm HfO2; 10nm space; 20nm ADM

## Slide 86: Topology Assumed for simulations
ADM 5nm
HfO2 5nm
D
S
TiN 5nm
S
D
40+nm
15nm
11nm
20nm
5nm
S
D
S
D
20nm
50nm tall
15nm
11nm
20nm
TiN 5nm
Leff = 20 + 20 + 20
D
S
MG
Wrap-around Channel
5nm ADM; 5nm HfO2; 10nm space; 20nm MG
S
D
GAA
5nm ADM; 5nm HfO2; 10nm space; 20nm ADM
2nm
ADM 5nm
orig
HfO2 5nm
redep
S
TiN 5nm
D
x
D
180C
250C

## Slide 87: Changes with ADM Scaling
Back-gated device suffers from Lg scaling due to SCE @high doping
Lcon and Z scaling further reduces the performance
WL0
Lg = 30nm
CON = 15nm
BL
COB
WL1
COB
COB
Scaled cell:
50 x 90 nm2
WL_p = 50nm; BL_p = 90nm; Active_p = 50 x 90
Lg = 30nm; Lcon = 15nm; Z = 35nm
50 x 67.5 nm2
WL_p = 60nm; BL_p = 135nm; Active_p = 50 x 135
Lg = 30nm; Lcon = 15nm; Z = 35nm
WL0
COB
WL0
COB
COB
Scaled cell:
40 x 50 nm2
WL_p = 40nm; BL_p = 100nm; Active_p = 40 x 100
Lg = 20nm; Lcon = 15nm; Z = 100nm
Optimal angle = 76 deg for OGD = 40nm
Fin height  wide Z
Better gate control
Angled for 6F2
WL0
Lg = 30nm
CON = 15nm
BL
COB
WL1
COB
Scaled cell:
40 x 50 nm2
WL_p = 40nm; BL_p = 50nm; Active_p = 40 x 50
Lg = 20nm; Lcon = 35nm; Z = 100nm
GAA/2-sided  wide Z
Long Lg
Contact area = active pitch

## Slide 89
Gate
Monolithic Stacking
Gate
Gate
Gate
ADM eDRAM offers stackable arrays
Caveats with vertical stacking:
Beyond 2 layers, peripherals will exceed array every additional layer @7-10% /layer Xdec for every layer
Unless ADM Xdec used  latency +1.5ns
If ADM high performance, it can be used as row Xdec too
Row decoder area grows by 2.2x every stack

## Slide 90: CR New Mask Objectives
Demonstrate scaling limits (Lg, Lcon) of ADM topologies
Array + etest vehicles using ADM only and ADM+Si_nmos demonstrations
Etestable at fast speeds including charge pumping
<10 masks
3 masks < 70nm pitch
What is a Spider Flow?
New Target Definition
CMOS + 3-4 metal layers (TD start)
New Product Flow (CR – RECL/FL)
CR builds upon existing TD infrastructure at scaled pitches – changes ONLY:
Array
Socket
CR build NEW VEHICLE:
Array
Socket
Advantages: @pitch, fast transfer to TD, aggressive topology skew
Disadvantages: Slow to NPI/develop/implement? Slow to SORT, need design alignment
New Product Flow (CR – RECL etest)
Advantages: @pitch fast prototyping, aggressive topology skew and flexibility, device fundamentals
Disadvantages: slow transfer to TD, ltd in transferability due to change in tools, pitches, array size etc

## Slide 91: 1T-1X vs 1T vs 1S-1X
Semiconductor
Source
Drain
HfO2 4 nm
Gate
BL
Storage element
Semiconductor
Source
Drain
Storage element
Gate
SL
BL
Modes: 1T-1C, 1T-1F, 1T-1M
Advantages:
Known physics for 1T-1C, 1T-1M
Word access – high BW; unselected bits consume 0 power
2-5 pJ/bit R/W energy
Low latency 1T-1C; ~4-9ns R/W
Disadvantages:
8F2 to 6F2 orientation when planar; 4F2 vertical
Best scaling EOL roadmap ~45x45 nm2 (DRAM)
More mask steps w/o self-alignment
Modes: 1T ferroelectric
Advantages:
Fewer mask steps, no need for tall COB or complicated MTJ etch
Similar BW and latency (~20% lower)
2-10 pJ/bit R/W energy
Disadvantages:
Ferroelectric physics new; endurance <1e9 cycles; research work in progress
8F2 to 6F2 orientation when planar; 4F2 vertical
Best scaling EOL roadmap ~45x45 nm2 (DRAM)
Modes: 1S-1PCM, 1S-1M
Advantages:
Ultra dense; EOL roadmap 10x10nm (>15x better than DRAM)
MRAM + selector may be better performance than PCM
Disadvantages:
Bitwise R/W  lower BW
Best case latency limited by parasitics @~200ns
Unselected bits burn half-select power
50 pJ RD and 0.5-2 nJ/bit WR energy (parasitics)
Endurance < 1e9 cycles (selector limited)

## Slide 92: ADM eDRAM Array Design
WL in different plane than COB and BL
 No angled fins needed
Targeted cell:
108 x 135 nm2
2x cell area scaling wrt 22nm eDRAM
WL1
WL0
Lg = 40nm
2F
4F
CON = 27.5nm
BL
8F2 cell
COB
COB
COB

## Slide 93: Tyche – II eDRAM Array (Teleios)
Optional WL strap
>1µm
COB
Power for hvcc, PLL etc (optional – can be Tyche)
BL routing to SA
WL driver
SA, PLL, HVCC gen
WL1
Lg = 14nm?
2F
6F/2cells
BL
6F2 cell
COB
COB
COB
COB
WL0
PGD
OGD
COB in different plane than WL and BL
 No angled fins needed
WL 
BL

## Slide 94: Topologies with TFTs
Channel
Bottom Gate Top Contact
Channel
Top Gate Top Contact
Channel
Top Gate Bottom Contact
Channel
Top Gate Alternate Contact
Key advantages:
Fin  better gate control, better subthreshold swing, better leakage, more Z  more current @Ion
Gate to contact overlap  better contact resistance while having low Cov @BL side for good SM
Cov at CUB-side is miller  does not affect active device
No need for angling

## Slide 95: Alternate Contact 1T-1C
SiN ES
1T – 1C
Channel
Channel
Key advantages:
Fin  better gate control, better subthreshold swing, better leakage, more Z  more current @Ion
Gate to contact overlap  better contact resistance while having low Cov @BL side for good SM
No need for angling

## Slide 96
Chart: 
| 2 | 1.9 | 1.7999999999999998 | 1.6999999999999997 | 1.5999999999999996 | 1.4999999999999996 | 1.3999999999999995 | 1.2999999999999994 | 1.1999999999999993 | 1.0999999999999992 | 0.99999999999999922 | 0.89999999999999925 | 0.79999999999999927 | 0.69999999999999929 | 0.59999999999999931 | 0.49999999999999933 | 0.39999999999999936 | 0.29999999999999938 | 0.19999999999999937 | 9.9999999999999367E-2 | -6.3837823915946501E-16 | -0.10000000000000064 | -0.20000000000000065 | -0.30000000000000066 | -0.40000000000000069 | -0.50000000000000067 | -0.60000000000000064 | -0.70000000000000062 | -0.8000000000000006 | -0.90000000000000058 | -1.0000000000000007 | -1.1000000000000008 | -1.2000000000000008 | -1.3000000000000009 | -1.400000000000001 | -1.5000000000000011 | -1.6000000000000012 | -1.7000000000000013 | -1.8000000000000014 | -1.9000000000000015 | -2.0000000000000013
 | 8.0106e-06 | 7.2506e-06 | 6.651e-06 | 6.0476e-06 | 5.4468e-06 | 4.8518e-06 | 4.2376e-06 | 3.5686e-06 | 2.954e-06 | 2.3214e-06 | 1.7101e-06 | 1.1558e-06 | 6.9688e-07 | 3.4414e-07 | 1.2483e-07 | 2.686e-08 | 3.4082e-09 | 3.098e-10 | 2.66e-11 | 6.8e-12 | 3.4e-12 | 4.2e-12 | 3.8e-12 | 7.4e-12 | 6.2e-12 | 4.6e-12 | 5e-12 | 6e-12 | 5.4e-12 | 6.4e-12 | 5.6e-12 | 5.4e-12 | 8.2e-12 | 8.6e-12 | 7e-12 | 7.8e-12 | 9.4e-12 | 9.8e-12 | 9.4e-12 | 1.02e-11 | 1.18e-11
 | 0.00010431 | 8.6534e-05 | 7.266e-05 | 5.9392e-05 | 4.8122e-05 | 3.8352e-05 | 2.9576e-05 | 2.2098e-05 | 1.605e-05 | 1.11e-05 | 7.209e-06 | 4.3586e-06 | 2.398e-06 | 1.0934e-06 | 4.1608e-07 | 1.1047e-07 | 1.7065e-08 | 2.0342e-09 | 2.372e-10 | 2.7e-11 | 5.6e-12 | 4.6e-12 | 3.8e-12 | 4.8e-12 | 6.4e-12 | 5.8e-12 | 6.6e-12 | 6.2e-12 | 8.4e-12 | 1.08e-11 | 8.8e-12 | 7.8e-12 | 1.08e-11 | 1.24e-11 | 1.12e-11 | 1.26e-11 | 1.4e-11 | 1.7e-11 | 1.9e-11 | 1.72e-11 | 1.78e-11
 | 7.6614e-06 | 6.8266e-06 | 6.2302e-06 | 5.6728e-06 | 5.0824e-06 | 4.4958e-06 | 3.886e-06 | 3.2952e-06 | 2.6572e-06 | 2.0474e-06 | 1.4807e-06 | 9.5636e-07 | 5.4196e-07 | 2.3526e-07 | 7.1374e-08 | 1.4748e-08 | 1.5604e-09 | 1.118e-10 | 1.14e-11 | 7.6e-12 | 6.8e-12 | 7.2e-12 | 7e-12 | 7e-12 | 7.4e-12 | 7.8e-12 | 8.6e-12 | 7.8e-12 | 6e-12 | 7.6e-12 | 8.4e-12 | 9.6e-12 | 1e-11 | 8e-12 | 1.02e-11 | 1.18e-11 | 1.06e-11 | 1.02e-11 | 1.18e-11 | 1.22e-11 | 1.34e-11
 | 0.00011336 | 9.2764e-05 | 7.6478e-05 | 6.338e-05 | 5.1654e-05 | 4.104e-05 | 3.181e-05 | 2.3772e-05 | 1.6995e-05 | 1.1915e-05 | 7.6562e-06 | 4.5744e-06 | 2.351e-06 | 1.0273e-06 | 3.4752e-07 | 8.4902e-08 | 1.138e-08 | 9.348e-10 | 6.74e-11 | 9e-12 | 5.6e-12 | 6.8e-12 | 5.6e-12 | 6.6e-12 | 7.4e-12 | 8.4e-12 | 8.4e-12 | 8.4e-12 | 8.8e-12 | 1e-11 | 1.18e-11 | 1.14e-11 | 1.22e-11 | 1.4e-11 | 1.6e-11 | 1.62e-11 | 1.74e-11 | 1.82e-11 | 2.04e-11 | 2.22e-11 | 2.36e-11
 | 7.7433e-06 | 6.6718e-06 | 6.0152e-06 | 5.35e-06 | 4.7238e-06 | 4.0395e-06 | 3.388e-06 | 2.7437e-06 | 2.1342e-06 | 1.5521e-06 | 1.033e-06 | 6.198e-07 | 2.949e-07 | 1.1396e-07 | 3.0945e-08 | 5.1148e-09 | 4.11e-10 | 3.05e-11 | 1.375e-11 | 1.425e-11 | 1.25e-11 | 1.35e-11 | 1.225e-11 | 1.4e-11 | 1.55e-11 | 1.425e-11 | 1.3e-11 | 1.375e-11 | 1.425e-11 | 1.85e-11 | 1.65e-11 | 1.65e-11 | 1.75e-11 | 1.575e-11 | 1.625e-11 | 2e-11 | 1.975e-11 | 2e-11 | 1.925e-11 | 2.15e-11 | 2.35e-11
 | 9.4993e-05 | 7.604e-05 | 6.221e-05 | 5.0525e-05 | 3.9873e-05 | 3.099e-05 | 2.3177e-05 | 1.6783e-05 | 1.1708e-05 | 7.629e-06 | 4.6457e-06 | 2.5477e-06 | 1.2684e-06 | 4.9675e-07 | 1.5797e-07 | 3.521e-08 | 5.0795e-09 | 4.66e-10 | 4.225e-11 | 1.2e-11 | 1e-11 | 8.75e-12 | 1.225e-11 | 1.275e-11 | 1.275e-11 | 1.3e-11 | 1.3e-11 | 1.525e-11 | 1.675e-11 | 1.575e-11 | 1.725e-11 | 1.875e-11 | 2.225e-11 | 2.2e-11 | 2.2e-11 | 2.725e-11 | 2.825e-11 | 2.825e-11 | 3.075e-11 | 3.325e-11 | 3.6e-11
Top gate top contact
Bottom gate top contact
Bottom gate bottom contact
Current (A/um)
Simulated Id-Vg
Chart: 
| BGTC | TGTC | TGAC
Cov | 31 | 8.4 | 12

## Slide 97: Commodity DRAM Array
<Samsung DRAM>
WL0
WL1
WL2
WL3
BL0
BL1
BL2
BL3
(0, 0)
(0, 1)
(0, 2)
(0, 3)
(1, 0)
(1, 1)
(1, 2)
(1, 3)
(2, 0)
(2, 1)
(2, 2)
(2, 3)
(3, 0)
(3, 1)
(3, 2)
(3, 3)
(Row, Column)
TEM XS
(along the diffusion)
Bit lines
Bit lines
wordline
61nm
Samsung 3Xnm 2Gb DDR3 DRAM
COB, WL, BL in same plane
 Angled fins needed
Courtesy: Tomishima, Shigeki, IL

## Slide 98: Advantage of Angled Fins: ~25% area reduction
WL1
WL0
Lg
2F
4F
Drain
BL
8F2 cell
COB
COB
COB
COB
HCP Layout:
Manhattan Layout:
= 30
Because we share BL, we eliminate 1 isolation per 2 cells
This results in ~25% reduction in area going to angled fins
It also enables densest possible configuration of capacitors @hcp  assumes double-walled capacitor

## Slide 99: Timeline of Milestones
Vertical
Demonstrate paired configuration with TD – implants, ozone treatment
ALD IGZO/In2O3, Raised S/D
CDO+CDN on top
C and other contact metals
Demonstrate top gate on 1x35AA @ Lg <30nm
Scale GOX (<20A toxe), then stabilize cont/Rext (<2kohm-um)
Backend CDO/CDN stability
S/D regrowth, In2O3 channel
Follow TG:
FinFET on 1x35 @Lg<30nm; Z>100nm
GOX (<20A toxe), Rext (<2kohm-um)
Backend stability; S/D regrowth, In2O3 channel
Gain cell structures
Demo. Rext, ueff, Lg –ready device with vertical topology
Scale GOX, ALD MG, In2O3 channel
Impact of integration schemes and scaling limits
CON experiments
Q3’19
Q4’19
Q1’20
Q2’20
Add a slide for doping control  impact of flows etc

## Slide 100: Tools Used
Fundamental Studies:
  C-V dot – GOX scaling, ADM scaling, CON reactivity
  Long Lg Xtors – GOX, scaling, Channel Mobility, CON reactivity, Passivation
Integrated Studies:
  300mm 1x35
  X22M vehicle (<15 mask RECL)

## Slide 101: CR New Mask Objectives
Demonstrate scaling limits (Lg, Lcon) of ADM topologies
Array + etest vehicles using ADM only and ADM+Si_nmos demonstrations
Etestable at fast speeds including charge pumping
<10 masks
3 masks < 70nm pitch
What is a Spider Flow?
New Target Definition
CMOS + 3-4 metal layers (TD start)
New Product Flow (CR – RECL/FL)
CR builds upon existing TD infrastructure at scaled pitches – changes ONLY:
Array
Socket
CR build NEW VEHICLE:
Array
Socket
Advantages: @pitch, fast transfer to TD, aggressive topology skew
Disadvantages: Slow to NPI/develop/implement? Slow to SORT, need design alignment
New Product Flow (CR – RECL etest)
Advantages: @pitch fast prototyping, aggressive topology skew and flexibility, device fundamentals
Disadvantages: slow transfer to TD, ltd in transferability due to change in tools, pitches, array size etc

## Slide 102: CR Mask Timeline
Establish deliverables on existing mask-set & identify shortcomings
Create Flows for new topologies
Learn existing X22M flow
Get DRs from existing X22M flow and their purpose
Decide on DRs for new Product
Define full-flow scope, SORT, design needs
Spider Flow with X22S/MA
New Mask Definition
PHASE I
PHASE II

## Slide 105: Topology Assumed for simulations
TiN 5nm
ADM 5nm
HfO2 5nm
S
D
S
D
20nm
Leff = 40nm
10nm
15nm
11nm
20nm
5nm
S
D
S
D
20nm
50nm tall
15nm
11nm
20nm
TiN 5nm
Leff = 20 + 20 + 20
D
S
MG
Wrap-around Channel
5nm ADM; 5nm HfO2; 10nm space; 20nm MG
S
D
GAA
5nm ADM; 5nm HfO2; 10nm space; 20nm ADM

## Slide 106
Lgmin = 47nm
Lgnom = 70nm
Le,min = 40nm
Lg > t_ADM + t_hik + Le,min
t_ADM,min = 2nm
t_ADM,max = 5nm
t_hik,min = 5nm
cbcn_dia,min = 39nm
cbcn_dia = 2*t_ADM + 2*t_hik + t_MG,min
t_MG,min = 25nm
sp_ADM_BL,min = 10nm
BLcn_area,min = pi*cbcn_dia,min x h_BL
BLcn_area,min =
H_BL = Lcon_BL > 20nm
Min cell size = 49 (WL) x 53 (BL)
Z = pi*(cbcn_dia-t_ADM*2) = 109 nm

## Slide 107
Lgmin = 40nm
Lgnom = 70nm
h_WL <= Lgmin = 40nm
BLcn_dia,min = 15nm = t_ADM
BLcn_dia = doping electrostatics
t_hik,min = 5nm (leakage)
BLcn_area,min = pi*(BLcn_dia,min/2)^2 = 176 nm2
sp_ADM_WL,min = 10nm
Z = pi*BLcn_dia = 47nm
Min cell size = 35 (BL) x 39 (WL)

## Slide 108
T_con = 5nm
25nm
Zcon
t_hik = 5nm
t_ADM = 2nm
H_fin = 40nm
Lgv,min = Lgh,min = 7.5*2 + Lg,drw – 2*t_hik = 30nm
Z = (h_fin + t_hik)*2 + t_fin + 2*t_hik = 120nm
10nm
T_fin
25nm
Lgdrw
Min cell size = 49 (BL) x 55 (WL)

## Slide 110
ADM
Gox
Gate
Contact
Small SBH: ~0.4 eV
High doping:
Controlled doping ~5e18 /cm3
Gate induced electrostatic doping
SiO2
SiO2
ADM
HfO2 10 nm
TiN 100 nm
CNT
Passivation
CNT
Passivation
ADAMANTINE
Gox
Gate
Low doping:
Controlled doping <5e17 /cm3
Controls Lg scaling

## Slide 111: Subtractive BG CV dot flow
POR TiN
GOX Y; POR = 10, 5nm HfO2
ADM (10nm, 40nm)
Metal (0.5nm TiN/50nm Pd)
P++ Si
TiN
HfO2
ADM
Metal
Si
Blanket layer dep
PR + develop + F22 etch
Suggestions:
2 ADM thicknesses – 10, 40 nm
Different metal layer deps (C, TiN, ALD metal etc)

## Slide 112: Subtractive TG CV dot flow
POR TiN
5nm HfO2
ADM (10nm, 40nm)
Metal (0.5nm TiN/50nm Pd)
P++ Si
Metal X
GOX Y
ADM (10nm, 40nm)
TiN, W, InOx, ITO, IrOx etc
P++ Si
Blanket layer dep
PR + develop + F22 etch
Suggestions:
Metal X can be differently deposited metals (ALD PVD etc), and different materials (TiN, W, Co etc)
Gate oxide can be any material or temperature that we want to try (SiO2, HfO2, SIN, Al2O3 important)

## Slide 113: C-V Vehicle: Method + assumptions
Cdepl (F/cm2)
ADM thickness (nm)
1/e depletion layer width
35nm ADM
95nm ADM
195nm ADM
With thick ADM, depletion depth is less than ADM thickness, so ADM doping is calculated
Xdep=159nm
Doping = 2.5e16
TiN
HfO2
ADM
Metal
Doped layer X
C-V assumes effective box-type doping profile and gives us an interaction distance from contact metal
If Cdepl changes  contact doping
If additionally Vfb & dC/dV change  doping difference

## Slide 114: CR Mask Timeline
Establish deliverables on existing mask-set & identify shortcomings
Create Flows for new topologies
Learn existing X22M flow
Get DRs from existing X22M flow and their purpose
Decide on DRs for new Product
Define full-flow scope, SORT, design needs
Spider Flow with X22S/MA
New Mask Definition
PHASE I
PHASE II

## Slide 115: 1T-1X vs 1T vs 1S-1X
Semiconductor
Source
Drain
HfO2 4 nm
Gate
BL
Storage element
Semiconductor
Source
Drain
Storage element
Gate
SL
BL
Modes: 1T-1C, 1T-1F, 1T-1M
Advantages:
Known physics for 1T-1C, 1T-1M
Word access – high BW; unselected bits consume 0 power
2-5 pJ/bit R/W energy
Low latency 1T-1C; ~4-9ns R/W
Disadvantages:
8F2 to 6F2 orientation when planar; 4F2 vertical
Best scaling EOL roadmap ~45x45 nm2 (DRAM)
More mask steps w/o self-alignment
Modes: 1T ferroelectric
Advantages:
Fewer mask steps, no need for tall COB or complicated MTJ etch
Similar BW and latency (~20% lower)
2-10 pJ/bit R/W energy
Disadvantages:
Ferroelectric physics new; endurance <1e9 cycles; research work in progress
8F2 to 6F2 orientation when planar; 4F2 vertical
Best scaling EOL roadmap ~45x45 nm2 (DRAM)
Modes: 1S-1PCM, 1S-1M
Advantages:
Ultra dense; EOL roadmap 10x10nm (>15x better than DRAM)
MRAM + selector may be better performance than PCM
Disadvantages:
Bitwise R/W  lower BW
Best case latency limited by parasitics @~200ns
Unselected bits burn half-select power
50 pJ RD and 0.5-2 nJ/bit WR energy (parasitics)
Endurance < 1e9 cycles (selector limited)

## Slide 116: ADM eDRAM Array Design
WL in different plane than COB and BL
 No angled fins needed
Targeted cell:
108 x 135 nm2
2x cell area scaling wrt 22nm eDRAM
WL1
WL0
Lg = 40nm
2F
4F
CON = 27.5nm
BL
8F2 cell
COB
COB
COB

## Slide 117: Tyche – II eDRAM Array (Teleios)
Optional WL strap
>1µm
COB
Power for hvcc, PLL etc (optional – can be Tyche)
BL routing to SA
WL driver
SA, PLL, HVCC gen
WL1
Lg = 14nm?
2F
6F/2cells
BL
6F2 cell
COB
COB
COB
COB
WL0
PGD
OGD
COB in different plane than WL and BL
 No angled fins needed
WL 
BL

## Slide 118: Commodity DRAM Array
<Samsung DRAM>
WL0
WL1
WL2
WL3
BL0
BL1
BL2
BL3
(0, 0)
(0, 1)
(0, 2)
(0, 3)
(1, 0)
(1, 1)
(1, 2)
(1, 3)
(2, 0)
(2, 1)
(2, 2)
(2, 3)
(3, 0)
(3, 1)
(3, 2)
(3, 3)
(Row, Column)
TEM XS
(along the diffusion)
Bit lines
Bit lines
wordline
61nm
Samsung 3Xnm 2Gb DDR3 DRAM
COB, WL, BL in same plane
 Angled fins needed
Courtesy: Tomishima, Shigeki, IL

## Slide 119
Fatih H.
Lg = 40nm
Lcon = 20nm
Z = 70nm
Lg = 35nm
Lcon = 17.5nm
Z = 60nm
Lg = 30nm
Lcon = 17.5nm
Z = 45nm
Final scaling with current doping with planar geometry
For planar, need to reduce doping
Raised S/D already assumed to increase Lg by ~7-10nm
Channel

## Slide 120
Gate
Monolithic Stacking
Gate
Gate
Gate
ADM eDRAM offers stackable arrays
Beyond 2 layers, peripherals will exceed array every additional layer @7-10% /layer Xdec for every layer
Unless ADM Xdec used  latency +1.5ns
If ADM high performance, it can be used as row Xdec too
Row decoder area grows by 2.2x every stack

## Slide 121: Scaling Challenges/Paths
ADM Scaling
XTOR scaling
Ion + Ioff in voltage range
Contact length scaling
Parasitic capacitance scaling
Angled ADM?
COB scaling
Double-walled capacitor to reduce noise/increase cap
Ferroelectric to increase retention – decouple Ioff
Pillar type?
Parasitic Scaling
Introduce air-gaps BLn0
Reduce Cov with scaling or S/D regrowth
Angled ADM?

## Slide 122: Advantage of Angled Fins: ~50% area reduction
WL1
WL0
Lg
2F
4F
Drain
BL
8F2 cell
COB
COB
COB
COB
HCP Layout:
Manhattan Layout:
= 30
Because we share BL, we eliminate 1 isolation per 2 cells
This results in ~50% reduction in area going to angled fins
It also enables densest possible configuration of capacitors @hcp  assumes double-walled capacitor

## Slide 123: Gain Cell – 2T and 2T-1C configuration
Optional WL strap
>1µm
COB
BL routing to SA
WL driver
Read Xtor
Capacitor size (fF) | Random->Access latency (ns) | Read time (ns) | Refresh time (ms) | Write latency (ns)
5fF | 3ns | 200ps | 100ms | 8ns
3fF (limit) | 2.5ns | 200ps | 60ms | 8ns
Gain cell – with and without peripherals underneath

## Slide 124: POR eDRAM
Challenges in Current Art:
Long raw access/read time makes it unattractive for SRAM replacements
SRAM scaling is progressing @30% every generation
Read 0
Short write-back
i.e. low transistor resistance
tRCD/tRC = 3ns/9ns
tRCD/tRC = 1ns/9ns
Read 1
Gain-Cell eDRAM

## Slide 125: Nano Pillar Transistor with Shared Gate 1T-1X

## Slide 126: Data on ADM Double-Gate to demonstrate shared=gating
Id-Vg
Lg = 40nm
Z = 80nm
SiO2
SiO2
ADM 20 nm
HfO2 10 nm
TiN 100 nm
TaN
PVD
Cu
PVD
Cu
PVD
SiN
halide
TiN
~2V delta in Vt when both gates are ON vs one ON
SS is degraded with single gating due to charge sharing

## Slide 127: ADM cell architectures (up to opt 5)
 | Back-gate Planar | Vertical ALD ADM | Vertical NW ADM with GAA | Vertical NW with SPG
Min cell size (um2) | 90 x 60 w/ Agni/Orion | 50 x 50 | 50 x 50 | 50 x 50
Cell Aspect ratio | 6F2 | 4F2 | 4F2 | 4F2
Lg,typ (nm) | 35 | 50 | 50 | 50
Masks till VCB | 6 | 6 | 5 | 5/6
Contact area (um2) | 27.5 x 73 | 40 x 40 | 40 x 40 | 40 x 40
Advantages | X22M | Ultra-thin body Fully gated contact | Ultra-thin body DRAM roadmap No passivation needed Akin to BG | Gate self-aligned to channel
Disadvantages | ALD essential Lg scaling-SCE Contact scaling Passivation needed Sealants challenging | ALD essential Contact scaling Fewer sealant locations Contact below ADM | Ungated contacts Channel CD needs ctrl Need WL ADM alignment Contact below ADM | Etch on ADM surface Ungated contacts Channel CD needs ctrl Cov, Vbd Contact below ADM
Broadly – Surround Gate vs Surround Channel

## Slide 128: Details: TFT offers Versatile Device Topology
Channel
Metal gate
Gate oxide
Channel
Contacts
Channel
Bottom Gate Top Contact
Channel
Top Gate Top Contact
Channel
Top Gate Bottom Contact
Bottom Gate Bottom Contact
FinFET structures:
Fin-cut View
Gate Cut View
oxide
Planar structures:

## Slide 129: TFT offers Versatile Device Topology
Metal gate
Gate oxide
Channel
Contacts
D
MG
S
D
S
S
D
MG
ALD TFT enables Vertical Devices
ADM
S
D

## Slide 130
ADM Planar Scaling Challenges & Roadmap
SiO2
ILD
ADM
HfO2
TiN
Source
Drain
35nm
35nm
40nm
ILD
ADM
HfO2
TiN
Source
Drain
18nm
18nm
35nm
ILD
ADM
HfO2
TiN
S
D
10nm
10nm
20nm
Metrics | X22MR: ADM | ADM+ | ADM++ | Remarks
Cell dimension | 108 x 135 | 60 x 90 | 60 x 67.5 | 2x scaling every generation
SS (mV/dec) | 83 | 96 | >100 | Short-channel effects
Idsat (A/um) | 100 uA/um | 40 uA/um | <5 uA/um | SCE, Rc dominated
Ioff (A/um) | 0.01 pA/um | 0.01 pA/um | >1nA/um | SCE
COV (aF/cell) | 31 | 15 | 8 | SCE; will need to scale down to reduce power
Need an architectural change to enable ADM scaling only beyond 90 x 60 cell
Requires S/D doping

## Slide 131
TiN
HfO2
IGZO
Al S/D
HfO2
Pd
25nm Lg
Top metal gate does not reach bottom of gate trench, so gating is by back gate
SS of 77mV/dec with ~25mV/V DIBL achieved on a 25nm single gated device!!!!!
SS=77mV/dec DIBL=26mV/V
Metal to Metal Lg=25nm

## Slide 132: CR-QTM vs X22MR
ILD
ADM
HfO2
TiN 100 nm
Passivation
TaN
Cu
electrode
TaN
MIM Capacitor
Cu (wordline)
TaN
Metal Gate
Gate dielectric
Bitline
S/D Contact
ADM
Key transistor enablements in X22M are:
Short Lg, self-alignment, integrated BE learning vehicle
Enables capacitor, transistor and 1T-1C learning with focus on transistor performance under backend conditions
Structural
1T, 1C testable separately

## Slide 133
Parameter | Existing CR-QTM | New CR-QTM | X22M (ADM option masks) | Process learning/ Targets
Lg | 60+ | 40+ | 30+ | Short channel effects/ leakage
Small contacts | 100+ | 30+ | 30+ | Contact resistance
Self-aligned contacts | Yes* (topo-only) | Yes* (topo-only) | Yes | 
Hermeticity | Yes (loose pitch) | Yes (loose pitch) | Yes | O-vacancy formation
BE dT | Yes | Yes | Yes | ADM stability against BE temp
X22MR single PFT transistor enablement
Key transistor enablements in X22M are:
Short Lg
Hermeticity learning at tighter pitches
Option for self-aligned contacts

## Slide 134
Parameter | Existing CR-QTM | New CR-QTM | X22M (ADM option masks) | Process learning/ Targets
Transistor | Yes | Yes | Yes | Full stack
Capacitor learning | No | No | Yes | Cap leakage vs ADM Xtor
1T-1C cell | No | No | Yes | Retention, performance learning
Array learning | No | No | Yes | Sense margin/loading
X22MR eDRAM test-structure enablement
Key eDRAM enablements in X22M are:
Capacitor learning (can we limit leakage of capacitor vs low-leakage ADM)
1T-1C cell and array learning