## Slide 1: Comparison among high bandwidth DRAM options JEDEC vs. TCC-D
DerChang Kau, Sep/21/21
Reference Doc
  HBM3 JEDEC Proposal Rev 0.95 Feb/18/21
  Tightly Coupled Cache-DRAM Rev 2, Sep/13/21
  Discussion & feedback from Kuljit Bains, Abhishek Sharma and Prashant Majhi
Key take away
  2Gb TCC-D macro provides 2x bandwidth density and ½ access latency advantage over HBM3 specification.
  Manufacturing cost per GB likely ~10x of the commodity DRAM – Mat capacity reduction (1/4 of HBM’s) is deployed to achieve lower latency (~ ½). 8X DQ parallelism at 1/16 channel capacity is used to improved bandwidth density (2X of HBM3). TSV overhead not included in TCC-D report and hybrid bonding at sub 10µm pitch is yet to be incorporated. All are expected to take another density hit at higher wafer processing cost.
  t-spec and state diagram are not available (to me?) at this time. These are ~80% of scope for memory spec.
  Robust engagement from Technology team (eg. memory & integration, OSAT, sort/class from GMES/FTE) for custom DRAM development and planning is strongly recommended to comprehend risk analysis and mitigation strategy development.
WIP
  Floor plan, macro size and wafer cost estimate – Abhishek Sharma and Prashant Majhi
  Electrical metric and benchmark for memory core & si technology – Abhishek Sharma
  Physical links (WB, µBump and HB) metric and benchmark– Prashant Majhi

## Slide 2: HBM3 Organization (JEDEC Spec R.95)
Each stack of HBM die includes (equivalent to 1 Rank of DDR DIMM)
Global command for the stack (52 µbumps)
Upto 16 channels / device (stack); upto 1K DQ
Double data rate @ 4.8~6.4GT/s (2.4~3.2GHz)
Max BW = 819.2GB/s/stack
I/O voltage 1.1 V, Tx driver voltage 0.4 V
DRAM core voltage 1.1 V
Unterminated data/add/cmd/clk interfaces
Unmatched data interfaces
2b encoded temp sensor
not prohibiting manufacturer specifics such as
an optional interface die in the stack
Signal redistribution and other functions
HBM3
Channel0
Channelm
…
…
120
52
Bank
  Channeli
Bank
….
Bank
….
Bank
Bank is the lowest independently operable unit
DRAM core 250~400MHz (not scalable)
tCCD (CAS2CAS delay, b2b same bank): 2.5~4ns
Hynix Spec: Open page latency (tAA) = 31ns Close page latency (tRCD+tAA) 48ns
Number of rows (pages) is part of HBM3 spec
C/A
Memory Mat
SA
Page
RAS
DQ + Metadata
CAS
Bank
SWD
CSL
Channels are full independent to each other
2~32Gb channel capacity [231~35b];
16, 32 or 48 banks per channel
64 DQ + ECC, SEV per channel. BL = 8 I/O (~90µbump) & ADD/CMD (~30µbmp)
2KB physical page [214b] 1KB addressable [213b], C[6:0]
BW = 38.4~51.2GB/s/Channel, Max BW density = 205GB/s/GB
Bank grouping supported for short tCCD
2 Pseudo Channel (PC) per Channel; PCs share C/A RAS/CAS for finer granularity to lower cost to scheduler.

## Slide 3: TCM 2Gb Macro Organization (Sep/2021 Rev 2)
Each Macro includes
2Gb / Macro
8 channels / macro;
4K DQ
Double data rate @ 250MT/s (125MHz)
BW=128GB/s/macro,
Interface physical and electrical tbd
Hynix and Intel build based die separately with additional RDL
52
2Gb Macro
Channel0
Channel7
…
…
yyy
xx
Bank4
  Channeli
Bank0
….
Bank3
….
Bank7
Bank is the lowest independently operable unit
Bank Capacity 32Mb (228b); 8K WL; R[12:0]
DRAM core frequency 250MHz
tCCD (CAS to CAS delay, b2b same bank): 4ns
Open page latency (tAA) = 15ns
Close page latency (tRCD+tAA) = 19.8ns
C/A
Memory Mat
SA
Page
RAS
DQ + Metadata
CAS
Bank
SWD
CSL
Channels are full independent to each other
256Mb per channel capacity [228b]
8 banks per channel B[2:0]
DQ=512 [29b] (HB required?)
½KB physical/addressable page [212b] C[3:0]
BW = 16GB/s/Channel
BW density = 512GB/s/GB
Bank grouping ?
Pseudo Channel?

## Slide 4: High Level Spec Comparison
 |  |  | LPDDR5 | HBM3 |  | 2Gb Macro
 | Technology Node | nm | Hynix 1z | Hynix 1z | JEDEC R.95 | TCC-D 1z proposal
Die JEDEC device specs is based on stacked-die configuration | Capacity | Gb | 16 | 16 | 2~512 | 2
 | Footprint | mm2 | 60.72 | 115.06 | n/a | 16.07*
 | Density | Mb/mm2 | 270 | 142 | n/a | 127
 | # of DQ / die | pins | 16 | 256 (1K allocated) | uptp 1024 | 4096
 | # of Channel /Die | # | 1 | 4 | upto 16 | 8
 | Transfer Rate | GTpS | 6.40 | 6.40 | 4.8~6.4 | 0.25
 | Bandwidth Density | GB/s/GB | 6.4 | 102 | max. 205 | 512
 | Latency (Close page) | ns | 40.00 | 48.00 |  | 19.80
 | Latency (Open page) | ns | 25.00 | 31.00 |  | 15.00
 | access latency (tCCD) | ns | 2.50 | 2.50 | 2.5~4.0 | 4.00
Channel | Channel Capacity | Mb/Channel | 16384 | 4096 | 2K~32K | 256
 | DQ / Channel | pins | 16 | 64 | 64 | 512
 | # of Bank / Channel | Bank/Channel | 16 | 16 | 16, 32, 48 | 8
 | BW/Channel | GB/s/Channel | 12.8 | 51.2 | 38.4~51.2 | 16
Bank, Partition | Bank Capacity | Mb/Bank | 1024 | 256 | see spec | 32
 | # of col of Mat/Tile (GBL) | n | 16 | 16 | n/s | 8
 | # of Row of Mat/Tile (GWL) | n | 64 | 16 | n/s | 16
 | Physical Page Size | bits | 16384 | 16384 | 16384 | 4096
Mat, Tile | Array Capacity | Mb/Array | 1.00 | 1.00 | n/s | 0.250
 | # of BL | Col | 1024 | 1024 | n/s | 512
 | # of WL | row | 1024 | 1024 | n/s | 512
*TSV overhead not included. No-SerDes circuit assumed
TCC-D data shared under CNDA 30991112 & CNDA 112784

## Slide 5
Mat:
  i/p: cell size, # of BL/WL, SWD eq, SA eq, SWD/SA eq, including dummy reduntent col/rol and array termination/socket connectivity
  o/p: mat x, y, footprint
Bank
  Ip: X and Y mat
  Also include Col Mux, Row dec, CLS (Mat dec), i/o buffer (page)
  o/p: Bank x, y and footprint
Channel
  i/p: number of bank, Bank decode/register logic/periphery area, physical i/o and cmd/add driver
  o/p: channel footprint
Die level of Channel level:
  Fuse, TSV and chip level I/O