## Slide 1
Saint-D - Bufferless HBM

## Slide 2
Motivation for Bufferless HBM
More number of HBMs, power/thermal problem should be matter in total system
Bufferless HBM can give
  1) Power can be reduced about 40% by excluding Buffer die
  2) Latency improvement through direct access C-die to Logic die
  3) Customer can flexibly configure Logic die regarding DRAM related IP
Power Improvement
Flexible Logic Configuration
Latency Improvement
Substrate
Interposer
Logic (MC/PHY)
B-die
2.5D IC
C-die
C-die
C-die
C-die
Substrate
Logic + Interposer
(B-die + MC/PHY)
C-die
C-die
C-die
C-die
3D IC
<HBM 2.5D IC>
<Bufferless 3D IC>
HBM Density & Power
Time
3X
2X
‘18
HBM2
8GB
14W
‘22
HBM3
24GB
25W
‘26
HBM4
48GB
50W
HBM
Capacity
HBM Power
15W
30W
Bufferless HBM Power
※ Customer can configure Logic die without the
unnecessary functions in Buffer die.
 | HBM 2.5D IC | Bufferless 3D IC
Latency (tRC) | 60ns | 55ns

## Slide 3
Saint-D Architecture - Bufferless HBM
Open for customer’s feedback: IPs in Saint-D
1) Discussion slot is open until the end of this year
 | 2022 | 2023 | 2024
Overall Schedule |  |  | 
4Q
2Q
1Q
3Q
2Q
1st Vehicle
Veri.
2nd Vehicle
Veri.
F/O
MTO
Dram Interface IP Transfer
HBM3
Interposer
HBM3 Core Die
Saint-D
HBM3 Core Die
(10.26mm x 9.875mm)
Saint-D(12.17mm x 10.39mm)
1st Vehicle Architecture
Saint-D + 4H HBM3 Core Die
uBump(TCB)
2nd Vehicle Architecture
3.5D : 1st Vehicle + HBM3
uBump(TCB)
Saint-D Information
Concept of Saint-D IP
HBM3
controller
DFI
DRAM interface IP
(0.75V)
TSV
C-DIE
(1.1V)
Saint-D
(bottom die)
DRAM
(top die)
TSV IO
HBM3PHY
PHY
C-DIE
B-die
HBM3
controller
HBM3
ASIC
TSV
DFI
JEDEC
TSV
IO
DRAM Interface IP in Logic Die
Feedback Discussion

## Slide 4
Bufferless HBM vs. HBM3(w Buffer die)
Main Diff. : # of DQ(x1024 → x4096), Operation speed(CA 3.2Gbps → 1.6Gbps, DQ 6.4Gbps → 1.6Gbps)
DBI, Jedec MRS and Test function(IEEE1500, DA, MBIST) are not supported
Category | Item | HBM3(w B-die) | Bufferless HBM(C-die) | Note
Mechanical | Die size | 11 x 11 (mm) | 10 x 10.4 (mm) | 16Gb die
 | Bump Pitch | 96 x 110 (um) | 28.5 x 27 (um) | C-die : TSV pitch
Core | Density | 16, 24, 32Gb | 16, 24, 32Gb | 
 | Stack height | 4, 8, 12, 16 | 4, 8, 12, 16 | 
 | # of channel / # of p-channel | 16 ch/ 32 p-CH | 16 ch/ 32 p-CH | 
 | # of Bank | 16 ~ 64 bank/p-CH | 16 ~ 64 bank/p-CH | 
 | Bank group | Support | Support | 
 | Burst length | BL8 | BL2 | 
 | # of DQ per 16 channel | x1024 | X4096 | DQ TSV Write Read common path
 | # of DQ per p-channel | x32 | x128 | DQ TSV per p-channel
 | Page size | 1KB / p-CH | 1KB / p-CH | 
 | Peak BW(Reference) | 819.2GBps(6.4Gbps) | 819.2GBps(6.4Gbps) | 
IO | VDD / VDDQ / VDDQL | 1.1 / 1.1 / 0.4V | 1.1 / 1.1 / 0.4V | 
 | CA / DQ data rate | DDR (3.2Gbps) / DDR (6.4Gbps) | DDR (1.6Gbps) / DDR (1.6Gbps) | CLK based operation
 | DQ / CA Tx | NMOS/NMOS un-term. (VDDQL swing) | CMOS/CMOS term. (VDD swing) | 
 | DQ Rx | DQ-DQS delay unmatched | DQ-CLK delay matched | 
 | DQS pair | 1 diff RDQS & WDQS per DWORD(32 DQ) | WCK & BRCK/CRCK per DWORD | BRCK : from B die to C die Read CLK CRCK : from C die to B die Read CLK
Function | Data masking | X | X | 
 | On-die ECC | O | O | 
 | External system ECC | X | X | 
 | DBI | O | X | 
 | MRS | O | X | Jedec
 | Test and Boundary Scan | O | X | IEEE1500, DA, MBIST

## Slide 5
10x Bandwidth Memory

## Slide 6
Ideation for 10x Bandwidth Memory
1. Buffer die design by using Logic process
→ Pin speed improvement
2. Direct access to DRAM Core with HCB
→ Increase # of IOs
3. Co-Packaged Optic Link HBM
→ Expand capacity, Bandwidth
HBM expectation
Ideation for BW
IO and Pin speed for 10TB/s
HBM Density & BW & Power
Time
3.3X
12H
16H
‘18
304GB/s
HBM2
8GB
14W
‘22
HBM3
1TB/s
24GB
25W
‘26
HBM4
2TB/s
48GB
50W
8H
‘30
HBM B/W
HBM
Capacity
HBM Power
2X
2X
Chart: 
 | 80 | 40 | 26.6667 | 20 | 16 | 13.3333 | 11.4286 | 10 | 8.8889 | 8 | 7.2727 | 6.6667 | 6.1538 | 5.7143 | 5.3333 | 5 | 4.7059 | 4.4444 | 4.2105 | 4
Pin Speed [Gbps]
Number of IOs [K ea]
※ Reasonable IO and Pin speed
→ 6K ~ 12K for IO
→ 6Gbps ~ 13Gbps for Pin speed
Logic
EPIC
EPIC
…
HBM
HBM
DRAM
CPU
Cu-Cu
HBM Doubles Bandwidth with 4 years cadence
New technology will be needed to achieve more memory Bandwidth 1) Current Memory Pin speed is expected to be limited about 10Gbps with DRAM process (Many IO products) 2) Difficult to increase number of IOs a lot due to constraints as chip size and IO power

## Slide 7
10x BW Memory Requirement for 10TB/s
Conventional DRAMs are difficult to achieve 10x Bandwidth. It is necessary to develop new technologies not only for memory but also for systems and packages
Case | IO | Pin SPEED (Gbps) | Bandwidth (TB/s) | How to | Requirements
1 | 1K | 80 | 10 | - | -. Memory Pin Speed limitation (up to 10Gbps with DRAM process)
2 | 2K | 40 | 10 |  | 
3 | 4K | 20 | 10 | Pin speed | -. Need to improve Pin speed by applying logic process Buffer die
4 | 8K | 10 | 10 | IO density | -. Staking solution : 8H SID or More (HBM, LLC DRAM and etc.)
5 | 12K | 6.7 | 10 |  | 
6 | 16K | 5 | 10 | New tech. | -. Need to find new solution such as CPO(pooled HBM), HCB(Direct access to core 3D)
7 | 20K | 4 | 10 |  | 

## Slide 9: Ideation for Bandwidth Increase
Samsung is considering and trying to improve memory performance. However, there will be a limit to Bandwidth increase only by Memory improvement
  Difficult to increase number of IOs a lot due to issues such as chip size and IO power
  Memory operation speed is expected to be limited to 9.6Gbps (Many IO products)
Industry should work together to find Bandwidth solutions in terms of Design/Package/System
Case1 : HBM based
Case3 : New DRAM Concept
Case2 : LLC DRAM based
1. Current HBM structure
→ No further improvements other than Speed Scaling
Logic
LLC
LLC
Interposer
Logic
Logic
Interposer
LLC
LLC
LLC
LLC
LLC
LLC
LLC
LLC
Logic
※ New DRAM using HCB
→ Direct access to DRAM Core (Increase # of IOs)
→ Separated WR/RD path for Full duplex
WR
RD
2. Twin tower HBM (2 Core die cubes on Buffer die)
→ 2x Density, Bandwidth compared to normal HBM
3. Pooled HBM Memory Module with CPO
→ Expand capacity, Bandwidth
※ Conventional DRAM
→ Common external WR/RD path
→ need serialize, de-serialize operation
Logic
Interposer
HBM
HBM
Logic
Twin Buffer
HBM
HBM
Logic
EPIC
EPIC
…
HBM
HBM
1. LLC DRAM structure
→ Same Bandwidth with current HBM3 products
→ Improve Latency, Power Efficiency
2. LLC DRAM stacking type
→ Expand Capacity, Bandwidth by stacking
WR
RD
DRAM
CPU
Cu-Cu

## Slide 10: Expected Bandwidth of each Idea
Conventional DRAMs are difficult to achieve 10x Bandwidth. It is necessary to develop new technologies not only for memory but also for systems and packages
Case | Product | Concept | Stack | Density | IO | Operation Speed | Bandwidth | 10x BW Possibility | Note
Case 1-0 | HBM3 | Current HBM | 4H | 8GB | 1K | 6.4Gbps | 0.8TB/s | Low | -. B-die & C-die Design change not required -. No further improvements other than Speed Scaling
 |  |  |  |  |  | 8.0Gbps | 1TB/s |  | 
 |  |  |  |  |  | 9.6Gbps | 1.2TB/s |  | 
 |  |  |  |  |  | 80Gbps | 10TB/s |  | 
Case 1-1 |  | Twin Tower (2 C-dies on B-die) | 4H x2 | 16GB | 2K | 6.4Gbps | 1.6TB/s | Low | -. B-die Design change required -. HBM Cube size increase (X-axis double)
 |  |  |  |  |  | 8.0Gbps | 2TB/s |  | 
 |  |  |  |  |  | 9.6Gbps | 2.4TB/s |  | 
 |  |  |  |  |  | 40Gbps | 10TB/s |  | 
Case 1-2 |  | Optical HBM3 MM (Memory Module) | 4H x12 | 96GB | 12K | 6.4Gbps | 9.6TB/s | Mid | -. Improve to manage Power/Thermal away from XPU -. CPO Tech. required and Expensive System cost
 |  |  |  |  |  | 8.0Gbps | 12TB/s |  | 
 |  |  |  |  |  | 9.6Gbps | 14.4TB/s |  | 
Case 2-0 | LLC DRAM | LLC | - | 1GB | 1K | 6.4Gbps | 0.8TB/s | Low | -. Advantage of Latency, Power efficiency compared to HBM -. Low Density
 |  |  |  |  |  | 8.0Gbps | 1TB/s |  | 
 |  |  |  |  |  | 9.6Gbps | 1.2TB/s |  | 
 |  |  |  |  |  | 80Gbps | 10TB/s |  | 
Case 2-1 |  | Stacking Product | 4H | 4GB | 4K | 6.4Gbps | 3.2TB/s | Low | -. Improve Density/Bandwidth of LLC DRAM using TSV
 |  |  |  |  |  | 8.0Gbps | 4TB/s |  | 
 |  |  |  |  |  | 9.6Gbps | 4.8TB/s |  | 
 |  |  |  |  |  | 20Gbps | 10TB/s |  | 
Case 3-0 | Chiplet DRAM (New Memory) | Direct access from Logic to IOSA | - | 1GB | RD : 16K, WR : 16K (RD/WR 0.5K per CH) | 1.6Gbps | 3.2TB/s | Mid | -. Limitation of Speed scaling due to DRAM Core cycle
 |  |  |  |  |  | 4.8Gbps | 9.6TB/s |  | 
Case 3-1 |  | Stacking Product | 4H | 4GB | RD : 64K, WR : 64K (RD/WR 0.5K per CH) | 0.8Gps | 6.4TB/s | Mid | -. Improve Density/Bandwidth of Chiplet DRAM using TSV
 |  |  |  |  |  | 1.2Gbps | 9.6TB/s |  |