## Slide 1: SRAM Array Hierarchy Definition
I/O
Cell size is defined by height x width in wl/bl orientation correspondingly.
Subarray is a matrix of cells enclosed by decoders and sense amplifier
Macro is an independent operable memory array, consists of a matrix of subarray, power rail, r/w control, address, and I/O.
Array is a matrix of macro with data path and control interface to compute unit

## Slide 2: AMD L3D SRAM Array (V-Cache)

## Slide 3: Die Size: 40.88 (6.51x6.28) mm2 2.77mm2 on the top is unknown 7% Base uses 38.11mm2 (L3 cache AE = 35.5%)
Array: 32MB/14.94(6.15x2.43)mm2 (x2) 78.4%
2.14MB/mm2 (Macro AE=48.5%)
8x32 128KB macro
Macro: 128KB/0.0416(0.16X0.26)mm2
3MB/mm2 (Subarray AE=68% with I/O amortized)
4X4X2 4K
4K Subarray: 32 col X128 row(?)
Cell Size
0.027µm2
4.42MB/mm2
Tag/LRU: 1.35(6.15x0.22) mm2 (x4) 14.1%
1088/4 * 6KB = 1632KB 1.18MB/mm2
I/O: 1.415 (6.15x0.23) mm2 (x2) 7.5%
256bFD/core x 8 core = 4K pads