## Slide 1
Matrix Multiply-Accumulate (MAC) or Multiply-Add (MAD) –
for i in xrange(4096):
for j in xrange(4096):
for k in xrange(4096):
C[i][j] += A[i][k] * B[k][j]
From “There’s plenty of room at the Top: What will drive computer performance after Moore’s law?”
Leiserson et.al. Science 368, eaam9744 (2020)
See also Dick Feynman’s “There’s plenty of room at the bottom” Eng. Sci.23,22–36 (1960)
Coding Efficiency 47x
Multi-Core 7.8x
2.7x
ISA Optimization
3.5x
Vector Processing
18.4x
Memory Hierarchy
18.4x
Memory Hierarchy
Upadhyay, et.al., Journal of Low Power Electronics, Volume 11, Number 1, March 2015, pp. 37-48(12)

## Slide 2
Publisher ‏ : ‎ Springer; 1st edition (June 19, 2009)
Language ‏ : ‎ English
Paperback ‏ : ‎ 77 pages
ISBN-10 ‏ : ‎ 3031005961
ISBN-13 ‏ : ‎ 978-3031005961

## Slide 4: In Package Memory Technology
DerChang Kau, Nov. 27, ’23 @ FTiP Review Meeting
Memory Technology Construct in System hierarchy
IPM Benchmark
Edited Nov. 28, ‘23

## Slide 5: Memory Technology Construct in System hierarchy
JEDEC Memory
Custom Memory

## Slide 6: DDR is Memory Module Socketed on PCB
Ki-Jun Sung et.al., EDTM’23 DOI: 10.1109/EDTM55494.2023.10102966

## Slide 7: LPDDR5 in Phone Wire-bonded Package surface mounted on a PCB

## Slide 8: LPDDR5 in Client Compute System
Wire-bonded package micro bumped to an organic substrate surface mounted on PCB

## Slide 9: HBM in Accelerator
2.3D µB/TSV CoW Memory (8+1) chip stack in a 2.3D FO EB Module

## Slide 10: Disaggregated SRAM – AMD Zen 3 CCD V-Cache 7nm SRAM CoW F2B 9µm HBI to Logic Base die

## Slide 11: Custom DRAM (i) – MCP for Client Compute ~60nm 1T1C DRAM (~7nm 6T SRAM eq.) + 14nm Logic
Haswell/Broadwell eDRAM – L4 Cache
Skylake eDRAM – Memory Side Cache

## Slide 12: Custom DRAM (ii) – Cryptographic Hashing
Mixed SiFO/OSAT | 
PSMC 30nm DRAM | Logic: SMIC 40nm
3DIC: XMC WoW HBI2.25µm | C4 A/T: ASE

## Slide 14: Beyond HBM3 – JEDEC In Package Memory

## Slide 15: Beyond HBM3 – Custom In Package Memory
AP Memory
High-Capacity Macro (128MB 1Ch)
21MB/mm2, 32GB/s/ch, 1.5pJ/b
High-Bandwidth Macro (16MB 1Ch)
16MB/mm2, 32GB/s/Ch, 1.5pJ/b
2GB, 4TB/s
128mm2)
Intel-Hynix TCC-D
1GB, 2TB/s
64mm2
1 GB, 256GB/s 50mm2
2 GB, 256GB/s 50mm2
Samsung LLW/LLC
a.k.a. DBM, SKH ULP

## Slide 16: IPM Benchmark
What is the metric
Benchmark

## Slide 17: Incumbent Technologies in Memory/Storage Hierarchy
“The Memory Organ – Ideally one would desire an indefinitely large memory capacity such that any particular … word would be immediately … available. … It does not seem possible physically to achieve such a capacity. …We are therefore forced to recognize the possibility of constructing a hierarchy of memories, each of which has greater capacity than the preceding but which is less quickly accessible.”
Preliminary Discussion of the Logical Design of an Electronic Computing Instrument
Arthur Burks, Herman Goldstine and John von Neumann, June/28/1946
SRAM
DRAM
HDD
SSD
Bandwidth, Cost
Capacity, Latency

## Slide 18: Memory Hierarchy
~100sMB, ~1ns
~1sGB, ~10ns
HC, HS SRAM: Cell size and capacity, architecture and ip folding
~10sGB, ~100ns
~100sGB, ~1µs
~1sTB, ~10µs
~10sTB, ~100µs
Disagg. HD SRAM or Custom HBW DRAM: Chiplet in 3DIC
JEDEC DRAM Cell Size, 3D Topo
3D XPoint Adoption tipping point, “Crossing the chasm”
3D NAND HAR, Layer Transfer
~10sMB, ~100ps
Main Memory

## Slide 19: Component (die) Attributes
 | JEDEC Memory |  |  |  | Custom In Package Memory |  |  |  |  |  | 
Tech Attributes | DDR5 | LPDDR5 | HBM3 | GDDR6 | P1271.3 | P1227.7 | Muddy Creek | APM VHM AI | APM VHM Blockchain | SKH TCCD | SEC LLW
Package Integration | FC | xDP WB | 2.xD | FC | MCP | 2.5D/3D | 2.xD/3D | 3D HBI | 3D HBI | 3D HBI | 3D HBI
Silicon Technology @ NPI | 1z | 1z | 1z | 1z | 22nm | 22nm | SF4X | 30nm | 30nm | 1z | 1z
Capacity (GB) | 4 | 2 | 2 | 2 | 0.125 | 1 | 0.25 | 0.59 | 4.39 | 4 | 1
Die Size (mm2) | 120 | 58 | 121 | 121 | 78 | 153 | 95 | 100 | 600 | 293 | 123
Protocol (Cmd/addr/DQ) | DDR | LPDDR | LP like | GDDR | F. Duplex | LP Like | F. Duplex | SDR | SDR | LP Like | LP Like
# of Channel per die | 1 | 2 | 4 | 16 | 128 | 32 | 32 | 300 | 1125 | 256 | 32
Max DQ width | 16 | 16 | 256 | 32 | 128 | 16384 | 16384 | 38400 | 72000 | 131072 | 4096
Max Data rate/pin (GT/s) | 8.4 | 6.4 | 8 | 24 | 6.4 | 1.6 | 1.6 | 0.5 | 0.5 | 0.25 | 2
Theoretical max BW (GB/s) | 16.8 | 12.8 | 256 | 96 | 102 | 3277 | 6554 | 2400 | 4500 | 4096 | 1024
DQ Density (DQ/mm2) | 0.1 | 0.3 | 8.5 | 0.3 | 1.6 | 107.2 | 344.9 | 384.0 | 120.0 | 448.0 | 33.3
Pin footprint (µm square/ pin) |  |  |  |  | .0108 | 68 | 44 | 36 | 65 | 33 | 122

## Slide 20: Normalized Performance
 | JEDEC Memory |  |  |  | Custom In Package Memory |  |  |  |  |  | 
 | DDR5 | LPDDR5 | HBM3 | GDDR6 | P1271.3 | P1227.7 | Muddy Creek | APM VHM AI | APM VHM Blockchain | SKH TCCD | SEC LLW
Density (MB/mm2) | 34.1 | 35.3 | 16.9 | 16.9 | 1.6 | 6.7 | 2.7 | 6.0 | 7.5 | 14 | 8.3
BW/Capacity (BW/GB) | 4.2 | 6.4 | 128 | 48 | 819 | 3277 | 26214 | 4096 | 1024 | 1024 | 1024
BW/ Density ([GB/s]/mm2) | 0.140 | 0.221 | 2.12 | 0.79 | 1.31 | 21.4 | 69.0 | 24.0 | 7.5 | 14.0 | 8.3
Random Access Latency (ns) | 33 | 36 | 34 | 30 | 13 | 15 | 3 | 15 | 15 | 15 | 32
Access Energy (pJ/b) | 16 | 5 | 3.7 | 16 | 10 | 0.8 | 0.23 | 0.5 | 0.7 | 0.96 | 1.5
Power Density (mW/mm2) | 17.9 | 8.8 | 250.5 | 101.6 | 105.0 | 137.2 | 126.9 | 96.0 | 42.0 | 107.5 | 100.0
Performance of a 100mm2 die
 | JEDEC Memory |  |  |  | Custom In Package Memory |  |  |  |  |  | 
 | DDR5 | LPDDR5 | HBM3 | GDDR6 | P1271.3 | P1227.7 | Muddy Creek | APM VHM AI | APM VHM Blockchain | SKH TCCD | SEC LLW
Capacity [GB] | 3.3 | 3.4 | 1.7 | 1.7 | 0.2 | 0.7 | 0.3 | 0.6 | 0.7 | 1.4 | 0.8
BW [TB/s] | 0.014 | 0.022 | 0.212 | 0.079 | 0.131 | 2.144 | 6.899 | 2.400 | 0.750 | 1.400 | 0.833
Power [W] | 1.8 | 0.9 | 25.0 | 10.2 | 10.5 | 13.7 | 12.7 | 9.6 | 4.2 | 10.8 | 10.0
Random Access Latency (ns) | 33 | 36 | 34 | 30 | 13 | 15 | 3 | 15 | 15 | 15 | 32
Access Energy (pJ/b) | 16 | 5 | 3.7 | 16 | 10 | 0.8 | 0.23 | 0.5 | 0.7 | 0.96 | 1.5

## Slide 21: Performance Benchmark of a 100mm2 die
 | JEDEC Memory |  |  |  | Custom In Package Memory |  |  |  |  |  | 
 | DDR5 | LPDDR5 | HBM3 (ref) | GDDR6 | P1271.3 | P1227.7 | Muddy Creek | APM VHM AI | APM VHM Blockchain | SKH TCCD | SEC LLW
Capacity [GB] | 3.3 | 3.4 | 1.7 | 1.7 | 0.2 | 0.7 | 0.3 | 0.6 | 0.7 | 1.4 | 0.8
(Large is better) | 2.02x | 2.09x |  | 1x | 0.1x | 0.4x | 0.16x | 0.35x | 0.44x | 0.83x | 0.49x
BW [TB/s] | 0.014 | 0.022 | 0.212 | 0.079 | 0.131 | 2.144 | 6.899 | 2.400 | 0.750 | 1.400 | 0.833
(Large is better) | 0.07x | 0.1x |  | 0.38x | 0.62x | 10.13x | 32.61x | 11.34x | 3.54x | 6.62x | 3.94x
Power [W] | 1.8 | 0.9 | 25.0 | 10.2 | 10.5 | 13.7 | 12.7 | 9.6 | 4.2 | 10.8 | 10.0
(Small is better) | 0.07x | 0.04x |  | 0.41x | 0.42x | 0.55x | 0.51x | 0.38x | 0.17x | 0.43x | 0.4x
Random Access Latency (ns) | 33 | 36 | 34 | 30 | 13 | 15 | 3 | 15 | 15 | 15 | 32
(Small is better) | 0.97x | 1.06x |  | 0.88x | 0.38x | 0.44x | 0.09x | 0.44x | 0.44x | 0.44x | 0.94x
Access Energy (pJ/b) | 16 | 5 | 3.7 | 16 | 10 | 0.8 | 0.23 | 0.5 | 0.7 | 0.96 | 1.5
(Small is better) | 4.32x | 1.35x |  | 4.32x | 2.7x | 0.22x | 0.06x | 0.14x | 0.19x | 0.26x | 0.41x

## Slide 22: IPM Selection
~100sMB, ~1ns
~1sGB, ~10ns
HC, HS SRAM: Cell size and capacity, architecture and ip folding
~10sGB, ~100ns
~100sGB, ~1µs
~1sTB, ~10µs
~10sTB, ~100µs
Disagg. HD SRAM or Custom HBW DRAM: Chiplet in 3DIC
JEDEC DRAM Cell Size, 3D Topo
3D XPoint Adoption tipping point, “Crossing the chasm”
3D NAND HAR, Layer Transfer
~10sMB, ~100ps
Main Memory
IPM Tech | Latency [ns] | BW [TB/s] | Capacity [GB] | Power [W]
MDC | 3 | 6.899 | 0.3 | 12.7
APM VHM | 15 | 2.400 | 0.6 | 9.6
P1227.7 | 15 | 2.144 | 0.7 | 13.7
SKH TCCD | 15 | 1.400 | 1.4 | 10.8
SEC LLW | 32 | 0.833 | 0.8 | 10.0
HBM3 | 34 | 0.212 | 1.7 | 25.0
LPDDR5 | 36 | 0.022 | 3.4 | 0.9

## Slide 23: Strategy for In Package Memory Exploration, Development and Deployment
Choosing Right Success Criteria – “pick on someone your own size”
  Universal memory often sought, but hierarchy always existed and likely always will be
  FoM must be benchmarked with respect to the corresponding hierarchy of memories of a computer architecture
In Package Memory Subsystem
  Power/Thermal conscious: Energy of moving bits back and forth becoming limiting
  Pair memory tech with compute architecture/hierarchy.
  Modular, Modular, Modular