## Slide 1: TC DRAM Intel SK Hynix Collaboration
TCD team
09/02/2021
Data shared under CNDA 30991112 & CNDA 112784

## Slide 2: Agenda
Data shared under CNDA 30991112 & CNDA 112784
TCD Overview
Product Value Proposition
  Data Center/AI/HPC
  Client/Mobile
  Graphics
TCD Macro details and perf/power/area summary
Proof –of-Concept & Test Chip Plans
Product Intercept Timeline
Manufacturing Details
Business Model
Next steps

## Slide 3: TCD Overview
Data shared under CNDA 30991112 & CNDA 112784
Topic of discussion today

## Slide 4: TCD Overview
Data shared under CNDA 30991112 & CNDA 112784
Tightly Coupled DRAM (TCD) concept
Standard
SK Hynix makes full DRAM metal stack
Silicon Substrate
SK Hynix Si Transistors + M1/M2/M3
SK Hynix Metal Stack
Custom
SK Hynix makes DRAM wafers up to M3
Intel completes top metal layers
TSV processing can by SK or Intel (TBD)
Silicon Substrate
SK Hynix Si Transistors + M1/M2/M3
Intel Top metal layers, MIM & TSV
Goal  Develop custom DRAM interposers to enable tighter integration with logic.
TCD Benefit  Ability to specialize memory solutions for the specific bandwidth, capacity and integration requirements across Intel portfolios by leveraging a common DRAM macro.

## Slide 5: TCD macro key metrics (High Bandwidth)
Data shared under CNDA 30991112 & CNDA 112784
Parameters \tech. | 2Gb Macro* (1znm) | 2Gb Macro* (1bnm) | 16Gb HBM2E (1ynm) | 16Gb HBM3 (1znm)
Density/mm2 | 16MB/mm2 | 21.12MB/mm2 | 19.66MB/mm2 | 17.8MB/mm2
# Channel | 8 |  | 8 | 16?
# pre-fetch/ch | 512b |  | 1024b | 
Page Size/ch | 0.5KB |  | 1KB | TBD
# Bank/ch | 8 |  | 32 | 
tCCD target | 4ns |  | 2.5ns | 1.25ns?
BW/ch | 16GB/s |  | 51.2GB/s | 102.4GB/s
Total BW (per 1GB) | 512GB/s |  | 51.2GB/s | 102.4GB/s
pj/bit 1 | ~1.5 |  | 5.2 | ~3-4?
LATENCY(Close) 2 | 19.8ns |  | 43.5ns | 48ns
LATENCY(Open) 3 | 15ns |  | 28ns | 31ns
tRCR/tRCW | 30ns |  | 60ns | 60ns
# DQ/Ch | 512b |  | 128b | 64b?
In DRAM ECC | O |  | X(Parity bit) | O(RS code)
BW/pin | 250Mbps |  | 3.2Gbps | 6.4Gbps
1 pj/bit: Watt/Bandwidth
2 Latency (Close page): tRCD + tAA (ACT~RD + RD~ DATA)
3 Latency (Open page): tAA ( RD~ DATA)
*TSV overhead not included. No-SerDes circuit assumed
**pJ/bit and latency numbers above are at macro level and do not account for base die/3D stack costs
High-Bandwidth Macro (2Gbit 8Ch)

## Slide 6: TCD macro key metrics (High Capacity)
Data shared under CNDA 30991112 & CNDA 112784
Parameters \tech. | 1Gb Macro* (1znm) | 1Gb Macro* (1bm) | 16Gb LPDDR5 (1zm)
Density/mm2 | 19.17MB/mm2 | 25.56MB/mm2 | 33.73MB/mm2
# Channel | 1 |  | 1
# pre-fetch/ch | 512b |  | 128b
Page Size/ch | 1KB |  | 2KB
# Bank/ch | 8 |  | 16
tCCD target | 4ns |  | 2.5ns
BW/ch | 16GB/s |  | 12.8GB/s
Total BW (per 1GB) | 128GB/s |  | 6.4GB/s
pj/bit 1 | ~1.5 |  | 3.5
LATENCY(Close) 2 | ~25ns |  | 40ns
LATENCY(Open) 3 | 15ns |  | 25ns
tRCR/tRCW | 30ns |  | 60ns
# DQ/Ch | 512b |  | 16b
IDD6(4GB, mA) | 4.13 |  | 1.28
In DRAM ECC | O |  | O
BW/pin | 250Mbps |  | 6.4Gbps
1 pj/bit: Watt/Bandwidth
2 Latency (Close page): tRCD + tAA (ACT~RD + RD~ DATA)
3 Latency (Open page): tAA ( RD~ DATA)
High-Capacity Macro (1Gbit 1Ch)
*TSV overhead not included. No-SerDes circuit assumed
**pJ/bit and latency numbers above are at macro level and do not account for base die/3D stack costs

## Slide 7: High Bandwidth Macro for Product - Cube
Cube like implementation of the proposed high BW macro
High-Bandwidth Macro (2Gbit 8Ch)
2 GB, 1 TB/s
(2stack of ~70mm2)
Data shared under CNDA 30991112 & CNDA 112784
4.745mm
3.72mm
Single 256MB Macro with TSV @ ~15.5MB/mm2
4 GB, 2 TB/s
(2stack of ~140mm2)
8 GB, 4 TB/s
(2stack of ~280mm2)

## Slide 8: High Bandwidth Macro for Product - Interposer
Interposer like implementation of the proposed high BW macro
High-Bandwidth Macro (2Gbit 8Ch)
2 GB, 1 TB/s
(2stack of ~140mm2)
Data shared under CNDA 30991112 & CNDA 112784
4.745mm
3.72mm
Single 256MB Macro with TSV @ ~15.5MB/mm2
4 GB, 2 TB/s
(2stack of ~280mm2)
8 GB, 4 TB/s
(2stack of ~560mm2)

## Slide 9: TSV and area overhead for Macros
Data shared under CNDA 30991112 & CNDA 112784
Sized for Data-Center/AI/HPC & Client/Mobile power delivery requirements.
High-Capacity macro sees ~11% area growth and the High-Bandwidth sees ~8% area growth.
TSV Assumptions
Chart: SOC Power TSV die over head
| Server | Client | Server | Client | Server | Client | 1z | 1a | 1b
Macro | 16.01 | 19.17 | 17.7064 | 21.35 | 21.1138 | 25.56
Macro+ SOC Power TSV | 14.8111 | 17.4447 | 16.4136 | 19.215 | 19.4594 | 23.004
High-BW
High-Capacity
High-BW
High-Capacity
High-BW
High-Capacity

## Slide 10: Power delivery and Die2die routing
Data shared under CNDA 30991112 & CNDA 112784
Given the routing constraints Intel team is proposing only 1Ch per Macro, but eventually needs to be 2Ch/Macro.
Even for 1ch high-capacity macro at least 1 -2 additional metal layers are needed.
At least 2 additional metal layers needed for larger high-bandwidth macros.

## Slide 11: Process Construction /Hybrid Manufacturing
Data shared under CNDA 30991112 & CNDA 112784
Top three metal routing layers are Cu with a pitch and patterning scheme that is compatible with Intel processing.
No technical show-stoppers for custom metal layer addition or 3D integration.
Standard
SK Hynix makes full DRAM metal stack
Silicon Substrate
SK Hynix Si Transistors + M1/M2/M3
SK Hynix Metal Stack
Custom
SK Hynix makes DRAM wafers up to M3
Intel completes top metal layers
TSV processing can by SK or Intel (TBD)
Silicon Substrate
SK Hynix Si Transistors + M1/M2/M3
Intel Top metal layers, MIM & TSV

## Slide 12: Yield and Recovery Model for large dies
Data shared under CNDA 30991112 & CNDA 112784
Memory Cube like Usage Model (Client, D-GFx & GP Server): Small DRAM dies
  SKH projects yield of 50-100mm2 DRAM die (like standard products) using existing modelling methodology (similar model as commodity HBM, with different die size)
DRAM as Interposer Usage Model (AI/HPC): Large DRAM dies
  SKH to extend yield model of 50-100mm2 DRAM die to incorporate additional repair and redundant banks (small additional area overhead or small capacity reduction for same area) and project the die yield.
  Intel then create a next-level model that puts together multiples 50-100 mm2 dies (that can defeature banks/channels) as a larger 700mm2 interposer.
  Potential usage scenarios:
  Interposer is just a larger dicing boundary – individual 50-100mm2 DRAM “dies” within the interposer are completely independent and defeatured, may need to support interconnect stitches crossing across scribe lines
  Interposer is a larger dicing boundary, but all individual dies need to function – total yield will be composite yield of individual dies

## Slide 13: Test Issues
Data shared under CNDA 30991112 & CNDA 112784
Array BIST at macro/die/stack level ownership and details of implementation
Need new test methodology between macro vs. full product
  IP sharing concerns from SK Hynix
  Need to build new controllers for cube or interposer options

## Slide 14: Summary table on DRAM Technology Node Choice
Data shared under CNDA 30991112 & CNDA 112784
TCD Metric |  | 1z |  | 1a |  | 1b |  | SRAM
 |  | High-Capacity | High-Bandwidth | High-Capacity | High-Bandwidth | High-Capacity | High-Bandwidth | 
Density | MB/mm2 | 19.2 | 16 | 21.4 | 17.71 | 25.6 | 21.12 | 3-4
BW/Ch | GB/s | 16 | 128 | 16 | 128 | 16 | 128 | 128
pJ/bit 1 |  | ~1.5 | ~1.5 | ~1.5 | ~1.5 | ~1.5 | ~1.5 | ~0.2
Latency 2 | ns | ~ 24 | ~19.8 | ~ 24 ns | ~19.8 | ~ 24 ns | ~19.8 | ~1-2
Need competitive density for a given capacity and BW target in 2025.
DRAM node 1a nm is considered optimal in terms of cost effectiveness and longevity in supply.
1 pj/bit: Watt/Bandwidth
2 Latency (Close page): tRCD + tAA (ACT~RD + RD~ DATA)
SRAM nos. based on 256Mb macro in N-1 or N node

## Slide 15: Proof-of-Concept Goals
Data shared under CNDA 30991112 & CNDA 112784
Build simple test vehicle to test out integration with base die either from SKH or Intel.
Focus on manufacturing and test plans
Enable test/validation of more than one construction option.
Risk/Challenge | Objective/Goal of PoC Vehicle
Wafer Handling (Scribe, EDM, Fiducials) | Integration details to handle wafers across SK & Intel (alignment/metrology/wafer-health monitors etc)
Power Delivery/Thermals | Qualifying thermal solutions, TIM, backside metals, Tj-limits
Assembly | Die-wafer/hybrid-bonding 3D integration solution validation
Yield (Sort/Class) | Showing path to low-DD for overall concept
Test | Enable M-BIST engines in base-die with the 3D integration scheme (programmable micro-controller option makes test easier but at cost of area and complexity)
Bandwidth/Latency/Power | Process tuning to match macro spec for BW, latency and power
Reliability/ECC/DPM | Establish DPM targets/ECC bits/Row-hammer solution

## Slide 16: POC plan – Achieving Technology & Volume Goals
Team advocating a 3-step plan
  Step1: Implement a PoC to prove out the basic concept and logistics
  Step2: Bring to life an MVP product using the high-bandwidth macro
  Step3: Scale out technology to high volume to enable a viable business model
Need to implement steps 2 and 3 in parallel and cannot be a serial implementation.

## Slide 17: Value of doing PoC TC as Step1
Manufacturing, assembly, wafer-handling, TSV processing, thermals and test are the critical elements of the TCD product architecture plan.
Need early test vehicle to gain confidence before implementing an actual product. SK Hynix also recommending this as first step.
Exact macro construction, product spec closure and construction options need more in-depth technical study to close.

## Slide 18: Step1 : Proof-of-Concept & Test Chip Plans – Option 1a & 1b
Data shared under CNDA 30991112 & CNDA 112784
Use existing HBM2e macro from SK
Two options for base die: SKH HBM or Intel.
SKH team advocating using HBM2e base die (TBD).
Intel team sees value in integrating HBM2e macro with Intel/modern base die due to architecture and power needs.
HBM2E core die, 2ch/16Gb
Option 1b: Use SKH HBM2e core die with Intel base die
Intel Process Base die
DRAM
.
.
.
1 - N
Option 1a: Use SKH HBM2e base die
DRAM
Existing HBM Base die
DRAM
.
.
.
1 - N
DRAM

## Slide 19: Step1 : Proof-of-Concept & Test Chip Plans – Option2
Team is advocating macro to build capacity of 2, 4, 8 GB ( High-Bandwidth Macro)
  Enable Cube and Interposer
High-Capacity Macro (1Gbit 1Ch)
High-Bandwidth Macro (2Gbit 8Ch)

## Slide 20: Joint Recommendation : Option1b for PoC
Data shared under CNDA 30991112 & CNDA 112784
Team recommending Option1b as lead candidate for this engagement.
PoC Goals | Option 1a (HBM2e Macro) | Option 1b (HBM2e Macro) | Option 2 ( High-BW Macro)
Wafer Handling |  |  | 
Power Delivery/Thermals | X |  | 
Assembly | X |  | 
Yield |  |  | 
Test |  |  | 
Bandwidth/Latency/Power | X |  | 
Reliability/ECC/DPM |  |  | 
Execution Time |  |  | XX
New IP Dev Effort |  |  | XX
Matched to Final Product | XX | X | 

## Slide 21: Step2 : Enable High Bandwidth Macro
Use step1 infrastructure for test and logistics
High-Bandwidth Macro (2Gbit 8Ch)
2 GB, 1 TB/s
(2stack of ~70mm2)
Data shared under CNDA 30991112 & CNDA 112784
4.745mm
3.72mm
Single 256MB Macro with TSV @ ~15.5MB/mm2
4 GB, 2 TB/s
(2stack of ~140mm2)
8 GB, 4 TB/s
(2stack of ~280mm2)

## Slide 22: Step3 : Scale out technology to high volume
Derive density optimized macros to cost optimized segments for high volume manufacturing
Derive density optimized macros
High-Capacity Macro (1Gbit 1Ch)
High-Bandwidth Macro (2Gbit 8Ch)
Data shared under CNDA 30991112 & CNDA 112784

## Slide 23: Product Intercept Timeline
Data shared under CNDA 30991112 & CNDA 112784
Earliest PoC TC has to be enabled by end of Q1 ‘22 for a 2H 24/1H 25 product intercept.
Use 2 Step plan to achieve technology and scale goals
PRQ
PRQ
PRQ
PoC
PC*
Data-Center/AI/HPC Product Macro intercept
PoC
EC**
GFx Product
Macro intercept
Client/Mobile Product Macro intercept
* Product Concept
** Execution Commit
Data-Center Product Def
Client/Mobile Product
PoC
TC
D-GFx Product Def
GFx Interposer based PoC/MVP

## Slide 24: Product Value Proposition
Data shared under CNDA 30991112 & CNDA 112784
Product | Use Case | Usage Type | Capacity | BW | Performance/Power
Data-Center/ AI/HPC | GP Perf | Memory Side L4 Cache | 6-12 GB | 3 TB/s | ~20% IPC
 | AI/HPC | Tightly Coupled HBM | 16 GB | 4 - 8 TB/s | ~20% IPC
Client/Mobile | GP Client | DDR Supplement | ~2-8 GB | 0.2-0.8 TB/s | ~10-20% Power
 | iGFx | Mid-Large MSC | < 1 GB | 0.6 TB/s | ~30-40% Perf
Graphics | Discrete GFx | Large MSC | 1-2 GB | 2-4 TB/s | ~10% Perf
 |  | NUMA memory w/ page migration | 4-8 GB | 2-4 TB/s | ~15% Perf
TC-DRAM delivers ~4-7x capacity at iso-area compared to SRAM for potentially lower cost.
Assuming necessary BW and capacity is achieved, there is significant performance upside for all product segment use cases.
~4-7x @ iso-area

## Slide 25: TCD application to Intel Data-Center/AI/HPC Architecture
Two use cases:
  Mainstream/General Purpose Performance
  AI/HPC Performance
~20% Server IPC Perf benefit with TCD
  •8-16% higher performance vs. SRAM L3 (iso-area)
Looking for 2025 product intercept
Construction Options:
Data shared under CNDA 30991112 & CNDA 112784
Compute
Compute
DRAM Interposer
Option 1: Interposer
Option 2: DRAM cube
With scalable height for capacity
Compute
DRAM
Logic Interposer
DRAM
Compute
Use Case | Usage Type | Capacity | BW | Priority1
GP Perf | Memory Side L4 Cache | 6GB - 12GB | 3 TB/s | Latency
AI/HPC | Tightly Coupled HBM | 16GB | 4 - 8 TB/s | Power

## Slide 26: TCD application to Intel Client/Mobile
Data shared under CNDA 30991112 & CNDA 112784
Option 1: Interposer with DRAM above/below
DRAM
Logic die + control
Option 2: DRAM on side with control above/below
DRAM
Logic die
Control
Use Case | Usage Type | Capacity | BW | Priority1
Client iGFx | Mid-Large MSC | 64MB – 1GB | 0.6 TB/s | Power
GP Client | DDR Supplement | ~ 2-8 GB | 0.2 – 0.8 TB/s | Power
Two use cases:
  DRAM as Cache (iGFx)
  DDR supplement
Looking for 2024 or early 2025 product intercept
Construction Options:

## Slide 27: TCD application to Intel GFx
Data shared under CNDA 30991112 & CNDA 112784
Use Case | Usage Type | Capacity | BW | Priority1
GFx | Large MSC | 1-2 GB | 2-4 TB/s | Performance
GFx | NUMA memory w/ page migration | 4-8 GB | 2-4 TB/s | Performance
Two use cases:
  DRAM as Cache
  NUMA memory – if it can achieve sufficient cost-effective capacity
Looking for 2025 product intercept
Construction Options:
Option 3: DRAM cube
With scalable height for capacity
Compute
DRAM
Logic Interposer
DRAM
Compute
Compute
Logic Interposer
Option 2a: small DRAM chiplets
DRAM
DRAM
Compute
Logic Interposer
Option 2b: small DRAM chiplets
DRAM
DRAM
Compute
Compute
DRAM Interposer
Option 1: Interposer

## Slide 28: Business Engagement Details
Data shared under CNDA 30991112 & CNDA 112784
Manufacturing Model using N-1 DRAM nodes
Joint partnership and JV possibilities and overall manufacturing strategy
Key partnerships in packaging, test, OSAT leveraging ……..
* Product Concept
** Execution Commit

## Slide 29: Cost vs. Volumes from SK Hynix
Data shared under CNDA 30991112 & CNDA 112784
Need estimates of cost/GB vs. volume to make it a viable business engagement for both sides.
* Product Concept
** Execution Commit

## Slide 30: Manufacturing Details – Intel/SK
Data shared under CNDA 30991112 & CNDA 112784

## Slide 31: Business Model - SK
Data shared under CNDA 30991112 & CNDA 112784

## Slide 32: Next Steps
Data shared under CNDA 30991112 & CNDA 112784

## Slide 33: Next Steps – Intel/SK Team Recommendation
…..
Data shared under CNDA 30991112 & CNDA 112784

## Slide 34: Backup
Data shared under CNDA 30991112 & CNDA 112784

## Slide 35: ROI Plots
Data shared under CNDA 30991112 & CNDA 112784

## Slide 36: Step1 : Proof-of-Concept & Test Chip Plans
Data shared under CNDA 30991112 & CNDA 112784
Two main options being proposed for the proof-of-concept vehicle plan.
Team recommending Option2 with a minimum viable product for initial POC
PoC Goals | Option 1a (HBM2e Macro) | Option 1b (HBM2e Macro) | Option 2 ( High-BW Macro)
Wafer Handling |  |  | 
Power Delivery/Thermals | X |  | 
Assembly | X |  | 
Yield |  |  | 
Test |  |  | 
Bandwidth/Latency/Power | X |  | 
Reliability/ECC/DPM |  |  | 
Execution Time |  |  | XX
New IP Dev Effort |  |  | XX
Matched to Final Product | XX | X | 
Intel Advocacy (MVP)
SK Advocacy (PoC TC )