## Slide 1: 14nm 3DXP Targets & Strategy for Definition Closure
TD-DE team, WW41/17
1st Principle Scaling Validation
Target Under Evaluation
Strategy / Lead

## Slide 2: Scaling Path 1st Principle Validation
3DXP product family envelop is power and die size; generally doubling density and bandwidth in scaling
Array scaling needs to maintains or lowers array voltage drop, including selection and read/write operation.
  Rparasitics * Iprogram + Von
  Selection/Inhibiting voltages and Window budge

## Slide 3: 14nm Targets under Evaluation
 | Energy BW |  | Density Die Size | 
 | Read | Write | Lead | Chop
S26 | 52 pJ/b 1600 MB/s | 118 pJ/b 800 MB/s | 256 Gb 12.7 X 15.6 mm2 | 128Gb 12.7 X 8.5 mm2
POR | 26 pJ/b 3200 MB/s | 59 pJ/b 1100 MB/s | 512 Gb 12.7 X 15.6 mm2 | 256 Gb 12.7 X 8.9 mm2
“DDR5” based target | 13 pJ/b 6400 MB/s | 45 pJ/b 2100 MB/s | 512 Gb 12.7 X 15.6 mm2 | 256Gb 12.7 X 8.5 mm2

## Slide 4: Strategy
Current Reduction
  50% cell reset current reduction with CD scaling
Voltage Reduction
  Parasitic resistance reduction with WSiN removal from Array Via
  Read Supply Voltage reduction with E2 drift/shift/evolution reduction
Capacitance Reduction
  Interconnect Cap reduction thru low K ILDs and thinner metals
Bandwidth Scaling
  LV CMOS for DDR5 transfer rate
Die Size reduction
  Pitch cell (HV CMOS) layout design rule for 100% under one tile
Other topics
  Low energy level shift architecture
  Bipolar for lower energy / wider window
  Supply, including Pumps, optimization

## Slide 5: Strategy and Lead Owners
item | Topics | CMOS | Design | Cell PI | PI
1 | 50% Ireset reduction |  | Jaydip | Andrea | Kolya
2 | RAV reduction |  | Jaydip | Andrea | Kolya
3 | VDM reduction |  | Sandeep | DerChang | Steve
4 | Cap reduction | Teja/Ron | Jaydip |  | 
5 | LV CMOS for DDR5 | Alan/Divesh | Matt |  | 
6 | “1x1” layout | Khaled/Tony | Balaji |  | 
7 | Low energy level shift |  | Jaydip |  | 
8 | Bipolar Operations | Shafqat | Sandeep | Fabio | 
9 | Supplies optimization |  | Sandeep |  |