## Slide 1: Scaling of PCMS Component
DerChang Kau
Feb/9/2011
Objective: making storage memory architectures that scale
This is a preliminary scaling analysis
Looking for feedback and vertical alignment to plan ahead

## Slide 2: Scaling Assumption
Sync point cadence: 18 months
Patterning: 70%/Gen linear shrink; 50% cell size shrink
ICELL: 60%/Gen shrink; voltage is non-scalable.
Logic scaling follows Moore’s law (power and die size)
Array CMOS Tox, LG are not scaling due to voltage and 60% width shrink subject to cell operating current.
Access latency, driven by cell performance and array CMOS, remains constant.
Socket and interconnect is assumed 70% linear shrink
Constant die size therefore cost neutral (~200mm2)

## Slide 3: Scaling of PCMS attributes
Technology Attributes | Unit | Multiplier (a=1.414) |  | PCMS80 | Gen+1 | Gen+2 | Gen+3 | Gen+4
½ Pitch | nm | K=1/a | 0.707 | 20.5 | 14.50 | 10.25 | 7.25 | 5.13
Cell Current | uA | 1/a1½ | 0.595 | 111 | 66 | 39 | 23 | 14
Tile Dimension |  |  |  |  |  |  |  | 
#bit/col | b/col | a½ | 1.189 | 1024 | 1024 | 2048 | 2048 | 2048
#bit/row | b/row | a½ | 1.189 | 2048 | 3072 | 2048 | 3072 | 4096
# of deck | # | 1 | 1.000 | 2 | 2 | 2 | 2 | 2
Density/Tile [#bits/Tile] | *Mib/Tile | a | 1.414 | 4 | 6 | 8 | 12 | 16
Tile Physical Area | um2 | 1/a | 0.707 | 3525 | 2644 | 1763 | 1322 | 881
Array Efficiency |  | 1 | 1.000 | 65% | 65% | 65% | 65% | 65%
Array Core |  |  |  |  |  |  |  | 
Sequencer Width | Tile/Slice | a½ | 1.189 | 2048 | 2560 | 3072 | 3584 | 4096
Slice Depth | Slice/core | a½ | 1.189 | 16 | 18 | 22 | 26 | 32
# tile / component | Tile/core | a | 1.414 | 32768 | 46080 | 67584 | 93184 | 131072
Component Density | *Gib/core | a2 | 2.000 | 128 | 270 | 528 | 1092 | 2048
Array Performance |  |  |  |  |  |  |  | 
READ Bandwidth | MB/s | a½ | 1.189 | 1600 | 2000 | 2400 | 2800 | 3200
WRITE Bandwidth | MB/s | a½ | 1.189 | 400 | 500 | 600 | 700 | 800
READ Power | mW | 1/a | 0.707 | 576 | 428 | 305 | 212 | 144
WRITE Power | mW | 1/a | 0.707 | 293 | 218 | 155 | 108 | 73
Normalized Performance Benchmark |  |  |  |  |  |  |  | 
READ Energy | pJ/b | 1/a1½ | 0.595 | 45.00 | 26.76 | 15.91 | 9.46 | 5.63
WRITE Energy | pJ/b | 1/a1½ | 0.595 | 91.49 | 54.40 | 32.35 | 19.23 | 11.44
READ BW/Density | [MB/s]/GiB | 1/a1½ | 0.595 | 100.0 | 59.3 | 36.4 | 20.5 | 12.5
WRITE BW/Density | [MB/s]/GiB | 1/a1½ | 0.595 | 25.00 | 14.81 | 9.09 | 5.13 | 3.13
READ BW/Power | [MB/s]/mW | a1½ | 1.682 | 2.78 | 4.67 | 7.86 | 13.21 | 22.22
WRITE BW/Power | [MB/s]/mW | a1½ | 1.682 | 1.37 | 2.30 | 3.86 | 6.50 | 10.93
* : http://physics.nist.gov/cuu/Units/binary.html

## Slide 4: Other factors impacting scalability
Fork in scaling roadmap, such as
  Dual Decks to 4 decks may result in a step function in scaling attributes – eg. Density of tile therefore slice width and concurrency
C-spec items scaling against this analysis, such as
  Granularity: partition and region width, page size and transfer size
  Address translation: full binary vs. partial binary addressing space and void
  Concurrency limitation: number of regions
Platform architecture elements to be independently built / scaled, such as
  NAND page size and block size: tends to go up every 1.5 generations
  DRAM page size: tends to go up every 2 generations
  Cache entry structure: data width & burst length are platform driven