## Slide 1: 30s ww10

## Slide 2: SXP Component Roadmap
2014
2015
2016
2017
2018
S15C 16GB
S26A 32GB
Storage
Qual
Memory
Qual
S15C
DBR
S26A
DBR
S37A 64GB
S37A
DBR
Q4’14 NVM Component Internal Roadmap
2012
2013
S15B
DBR
TODAY
S25A 16GB
S15A
DBR
S25A
DBR
Start Pathfinding
Milestones for 30s development (Need to discuss):
Paper Specs (Rev -1 DTS, MTS,??) - Q2 ’15
Preliminary silicon based on S35X (Rev0) – Q4’15 (When is S35X expected to TO?)
Updated Silicon based specs (Rev1) – Q2’16
Final specs for S37A Silicon (Rev2) – Q4’16
Co-ordination among different functions (What should we do different on 30 series compared to 10s and 20s )

## Slide 3: High Level Specs
Item | S1x | S2x | S3x | S4x
Capacity | 16GB | 32GB/16GB | 64GB/32GB | 128GB/64GB
Rd/Wr pj/bit | 71/157 | 52/118 | 36/79 | 26/55
Rd/Wr latency | 95ns/475ns | <95ns/475ns | <80ns/475ns | <80ns/475
Max Rd/Wr BW per SXP (GB/s) | 1.6/0.55 | 1.866/0.8 | 2.4/1.1 (+ Reset write or split write in 2 for lower latency ) | 3.2/1.6 (1.1 for chop)
Partitions | 16 | 16/32 | 32 | 32 to 64
RBER | 5E-5 | 5E-5 | 2E-4? | 4-8E-4?
Max Interface Speed controller/SXP (MT/s) | 1600 | 1866 | 2400 | 3200
Write Endurance | 1e7 | 1e7 | <=1e7 | <=1e7
DPM | 500 | 500 | >=500 | >=500

## Slide 4: 20s/30s Array Architecture
Isolation
PM
SD
PM
SD
PM
SD
PM
SD
PM
SD
PM
SD
1 BL Sockets
2 WL Sockets
35
35
35
35
35
35
35
65
Isolation
2 BL Sockets
2 WL Sockets
PM
SD
PM
SD
PM
SD
PM
SD
PM
SD
PM
SD
PM
SD
PM
SD
PM
SD
PM
SD
PM
SD
PM
SD
35
35
35
65
35
35
35
35
35
35
35
65
35
35
35
35
S15B
20s/30s WL First, 4-Decks
Thicknesses are for 20 series;
Will be different for 30 series
WL
BL
Arch | WL |  |  |  | BL |  |  | 
 | S | R | C | I | S | R | C | I
S15B 2Kx4K | 2 | 1 | 1 | 2k | 1 | 1 | 1 | 8k
20s/30s WL First 4Kx4K | 2 | 2 | 4 | 8k | 2 | 1 | 1 | 8k

## Slide 5: Key Challenge: Fitting CMOS in 30 series
14nm 4Kx4K Tile
4Kx4K Tile: About 50% of area of 20s for tile circuits (assuming slice of 2 tiles)
  One idea being looked at is NN-PP select-deselect structure to make more room
  ( not good for energy; layout study in progress)
4Kx8K Tile: About 80% area as 20s for tile circuits (Preferred option with current CMOS)
14nm 4Kx8K 1/2Tile

## Slide 6: Preliminary Die Size
Item | 14nm - 256 x 32 4Kx4K array limited | 14nm - 256 x 32 4Kx4K CMOS limited | 14nm - 128x32 4Kx8K array limited | Comments
Litho (nm) | 14.0 | 14.0 | 14.0 | 
Number of active WL's | 1024 | 1024 | 2048 | 
Number of redundant WL's | 8 | 8 | 8 | 
Number of Dummy WL's | 20 | 20 | 20 | 8 next to the socket; 4 at the edge of the X/Y decoders
Number of active BL's | 1024 | 1024 | 1024 | 
Number of redundant BL's | 8 | 8 | 8 | 
Number of Dummy BL's | 20 | 20 | 20 | 
Socket Size (lambda) | 48 | 123 | 48 | 
Patch Size (WL Direction) | 637.12 | 712.12 | 637.12 | Best case based on above socket size; Have not done layout of this small patch
Patch Size (BL Direction) | 637.12 | 712.12 | 1210.56 | Best case
Patch Area (um^2) | 1014.8 | 1267.8 | 1928.2 | Best case
Number of patches (WL Direction) | 64 | 64 | 64 | 
Number of patches (BL Direction) | 64 | 64 | 32 | 
Number of patches in termination (WL Direction) | 5.5 | 5.5 | 4 | 
Number of patches in termination (BL Direction) | 4 | 4 | 3 | 
PCU Area per partition (um^2) | 108000 | 108000 | 108000 | Estimated
Partition Area (mm^2) | 4.904 | 6.1 | 4.697 | 
Partitions | 32 | 32 | 32 | 
Core Area (mm^2) | 156.9 | 195.2 | 150.3 | 
Periphery (mm^2) | 9.56 | 9.56 | 9.56 | 
PADs (mm^2) | 3.52 | 3.52 | 3.52 | 
Scribe & Seal Ring (mm^2) | 2.56 | 2.56 | 2.56 | 
Best case Die Area (mm^2) | 173 ( Can’t fit CMOS) | 211 | 166 | 

## Slide 7: Key Challenge: WL/BL resistance
Max Array Resistance = (Max cross point voltage – Voffset)/Icell
= (6.8 – 2)/(105*0.6) = ~ 76K
( 20nm array resistance for 4Kx4K tile size = 40K
WL resistance = 30K; BL resistance = 10K with Quilt benefit )
=>
For 14nm 4Kx4K tile:
WL/BL Resistance per cell < 1.9x 20nm WL/BL Resistance per cell
For 14nm 4Kx8K tile size:
WL/BL Resistance per cell < 1.5x 20nm WL/BL Resistance per cell

## Slide 8: Prelim window
Lower leakage translates to lower Vt’s => Lower spike and lower energy
Column1 | 20s POR | 20s Lower Vt | 30 Series 4Kx4K same leakage as 20s | 30 Series 4Kx8K same leakage as 20s | 30 Series 4Kx8K 10x lower leakage as 20s
WL resistance | 30000 | 30000 | 60000 | 48000 | 48000
WL path resistance | 7500 | 7500 | 15000 | 15000 | 15000
BL resistance | 10000 | 10000 | 20000 | 32000 | 32000
BL path resistance | 10000 | 10000 | 25000 | 15000 | 15000
Median SET Vt | 4.8 | 4.3 | 4.6 | 4.8 | 4.3
Delta VT | 1.4 | 1.4 | 1.4 | 1.4 | 1.4
Median Reset VT | 6.2 | 5.7 | 6 | 6.2 | 5.7
Max Set VT | 5.5 | 5 | 5.3 | 5.5 | 5
Max Reset VT | 7.3 | 6.8 | 7.1 | 7.3 | 6.8
Inhibit bias | 3.6 | 3.2 | 3.3 | 3.4 | 3.3
Vt sigma | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
C-cell bias | 0.8 | 0.8 | 0.8 | 0.8 | 0.8
Inhibit bias as a % of set Vt | 0.75 | 0.74 | 0.71 | 0.7 | 0.76
Ith | 2.00E-07 | 2.00E-07 | 2.00E-07 | 2.00E-07 | 2.00E-08
Set Drift | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
Reset Drift | 0.6 | 0.6 | 0.6 | 0.6 | 0.6
Reset Read Disturb | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
Write |  |  |  |  | 
Row leakage drop | 0.094 | 0.081 | 0.104 | 0.072 | 0.017
WL path leakage drop | 0.188 | 0.162 | 0.209 | 0.181 | 0.043
Column leakage drop | 0.062 | 0.054 | 0.069 | 0.193 | 0.046
BL path leakage drop | 0.251 | 0.217 | 0.349 | 0.362 | 0.087
E1 Margin | 0.318 | 0.256 | 0.3165 | 0.3415 | 0.29
E4 Margin | 0.622 | 0.3325 | 0.2135 | 0.1675 | 0.5685
# of Cells needing c-cell (sigma) | -2 | 1 | 2 | 2 | -1
(VPP-VNN) for Selection | 7.624 | 7.126 | 7.624 | 7.832 | 6.878
Read |  |  |  |  | 
WL/BL bias | 2.8 | 2.7 | 2.7 | 2.8 | 2.55
Bias as percentage of Set VT | 0.58 | 0.62 | 0.58 | 0.58 | 0.59
E2/E3 margin | -0.01 | -0.05 | -0.09 | -0.1 | -0.01

## Slide 9: Key Challenge: Active Energy
Goal is 30% lower energy than 20 series
Lower cell current should get us ~10-12%
Need to figure strategy for the rest
Here are some potential enablers:
Lower supplies (requires lower selection window and reset current drop
Lower routing metal cap
Better CMOS ( shorter channel lengths )

## Slide 10: Key Challenge: Selection Spike
  Selection Spike resulting in Read Disturb and over reset expected to be a big challenge on 30 series due to reduced thermal latency and larger tile size
  Some potential options:
  Lower selection voltage window
  Lower array capacitance
  Cell magic
  Smaller tile (CMOS limits this)

## Slide 11: BACK UP

## Slide 12: 14nm Challenge – CMOS under array