## Slide 1
Problem Solving Rank Oder |  |  | Level–1: Yield/functionality |  |  |  | Level–2: Performance |  |  | Level–3: Rel | 
 |  |  | RWB gap widens due to PM vertical scaling | Read energy reduction using VHH , consistent with Set Vt DTS | Read functionality RBER and RD (G) due to Non-scalable Ihold | Memory Effects empirical, model & success criteria | 10 uA reset current scaling beyond DTS | 80ns Read Latency – 10ns Tsense reduction | Nucleation time increases with scaled nucleation volume | RD due to eSSR current delivery | R2R Write Disturb to meet 512 NW
Strategy |  | Issues |  |  |  |  |  |  |  |  | 
Impact count Risk |  |  | 1.5 | 3 | 2.53 | 2.5 | 1.5 | 2 | 1.5 | 3 | 1.5
1 | Reduce Set Vt by -350mV (CR7.76 ) with 5X inhibiting leakage reduction |  |  | X |  |  |  |  |  |  | 
1 | 10s based silicon RWB assessment, all components, fresh to EOL |  |  |  |  |  |  | X |  |  | 
1 | Design WL/BL transient to match S15 |  |  |  |  |  |  | X |  |  | 
1 | Improve ISSR current delivery |  |  |  | X |  |  |  |  |  | 
1 | Segment/Quantify RBER gap incurred due to Ihold > ISSR |  |  |  | X |  |  |  |  |  | 
1 | Segment/Quantify RDG gap incurred due to resnap Ihold > ISSR (Resnap) |  |  |  | X |  |  |  |  |  | 
1 | Quantify eSSRn current delivery requirement by ED |  |  |  |  |  |  |  |  | X | 
1 | Ensure eSSR resnap only if iSSR snapped |  |  |  |  |  |  |  |  | X | 
1 | Quantify 14nm tnuc gap |  |  |  |  |  |  |  | X |  | 
4 | Transfer function matches with 10s level capability thru Ambient/liner/seal/fill/anneal |  | X |  |  | X |  |  | X |  | X
5 | New PM material |  | X |  |  | X | X |  | X |  | X
1 | Write Algo to double nuclei density |  |  |  |  |  |  |  | X |  | 
1 | Optimize/reallocate write completion overhead |  |  |  |  |  |  |  | X |  | 
3 | Quantify/Segment memory effects in RWB and Rel & scaling |  | X |  |  | X | X |  |  |  | 
5 | New SD material |  | X | X |  | X | X | X |  |  | 
2 | Thermal profile engineering thru vertical electrical/thermal resistance |  |  |  |  | X |  |  |  |  | X
1 | Write-2-Write spec relaxation |  |  |  |  |  |  |  |  |  | X
1 | Explore memory effects |  | X |  |  |  |  |  |  |  |