## Slide 1: NVL PX/MX Intercept
CPG/GEMS/FTE presenting
By courtesy of Team Electric Pond, Dany Ly-Gagnon, Mike Goldsmith, Jason Zhang and Long Wang

## Slide 2: System in Package Mockup: Inspired by PX Processer
CPU-PX
GPU-PX
PCD-P
LPDDR
LPDDR
Substrate (UCIe-S)
CPU-PX
GPU-PX
PCD-P
LPDDR
LPDDR
Substrate
i16 Si Interposer/MiM* (UCIe-A)
CPU-PX
GPU-PX
PCD-P
LPDDR
LPDDR
Substrate
Si Interposer / MiM / i3FV SLC
CPU-PX
GPU-PX
PCD-P
LPDDR
LPDDR
Substrate
SLC
DTC
SLC
MCP
Packaging cost baseline $8~$10
Passive interposer
(FOV, 2.5D)
Active interposer for eLLC / SLC
(Active FOV, 2.5D)
Fanout Package w/ Embedded Chiplet (2.3D-BT2)
For $25 addition
$4~$6 packaging process adder
$20 256MB SRAM of N6, SF4 or N4P
1¢/µF optional DTC or ISC for PDN
For $25 addition:
$7~$8 packaging process adder
$10~$20 Interposer & MiM of P1227
For > $150 addition
$7~$8 packaging process adder
$150~$200 Interposer, MiM & 400MB SRAM of I3FV

## Slide 3: Base Die (Advanced Packaging) Technology: 2.5D (Si Interposer)  2.3D (Fan-out)
Capability
2.3D provides flexible low parasitic interconnect of heterogenous technology integrating features for performance augmentation with TTM advantage
Cost
2.5D degrades feature utilization efficiency hence higher cost ~420mm2 I3FV (~$150) vs. ~120mm2 N6 (~$20)
Silicon interposer (TSV + BEOL) is 20% higher ($2~$3) in cost of making than Fanout packaging (TMV + RDL)
Additional 2.3D cost reduction opportunities in development
Capacity of 2.3D Family
TSMC’s InFO-3D and SPIL’s FO-3D are under development (Intel’s ODI ZBB’d)
Topics under evaluation in 2.3D
D2D IP design and performance difference between 2.5D and 2.3D (UCIe and beyond), including R/W latency, IO, ESD, power/thermal and PDN
Explore unknowns in Chip-Package Interaction using "Electric Pond" for 2.3D integration flow flushing
CPU-PX
Si Interposer / MiM / SRAM
CPU-PX
SRAM
DTC

## Slide 4: Disaggregated SRAM
256MB System Level Cache organization
  8MB channel: 32 banks in 8 bank groups, 256KB/bank 64B ECC Full Duplex DQ @ 1.6MT/s, 0.2pJ/b 102 MB/s for read/write @ 3ns latency
  32 channels deliver max BW 6.6TB/s @ 11W
  "Electric Pond": 2MB channel in FO-3D package for SV
Choices of technology and die capacity
  64MB/die yields the best cost due to yield
Emb. SRAM is estimated < 3˚C (∆T) higher than top die
  Feasibility in reducing ∆T with 25µm-Pitch bump/underfill optimization and “thermal chimney” design (dummification TFM) development
  Early Engagement between suppliers and design team to achieve STCO before design start
256MB SRAM | N6 | SF4 | N4P
Density [MB/mm2] | 2.16 | 2.57 | 2.77
Footprint [mm2] | 118 | 100 | 92
4x 64MB/die | $19.79 | $20.27 | $21.65
2x 128MB/die | $20.85 | $21.89 | $22.75
1x 256MB/die | $23.54 | $25.30 | $25.35
CDµB
tµB
PitchµB
Embedded SRAM Chiplet
25µm Pitch
µBump connect to top die
9µm Pitch
TSVs connect to Substrate

## Slide 5: 2.3D BT2 Chip-Last Mockup Flow (SPIL/FO-3D, TSMC/InFO-3D)
Discrete CPU-PX DTC not shown)
GPU-PX
PCD-PX (HBI DTC not shown)
Bridge
Bridge
Emb. 64MB
Emb. 64MB
Emb. 64MB
Emb. 64MB
A
A’
2
3
3
4
5
6
2
2
2
1
1
7
64M SRAM
GPU-PX N3P
Bridge
A
A’
N6/N4P
DTC
DTC
CPU-PX N3P/N3X/N2
Power Delivery
Small chiplet embedded in 2.3D-BT2 package enables flexibilities for PDN optimization for parasitic insertion loss (I·R, di/dt·L) reduction and noise de-coupling by effective capacitor placement within proximity of consumption.
TSMC DTC and SF ISC are the high-density de-cap choices for CPU/GPU in scaling path.
PCD
DTC
PCD
DTC
GPU
Carrier Prep
Top Die Attachment
Em. Chiplets Attachment
SRAM
Bridge
Mold, RDL
RDL, Cu Pillar
C4
1
6
5
2
3
Micro Bumping
9 µm HBI
25µm µB
80µm C4
Top Carrier Bond,
Back Carrier Debond.
Bumping
CPU
4
IPD not shown
7
25µm
Bumping