## Slide 1: Modular Technologies optimized for System in Package
Challenge to Active Foveros –
  Low utilization of high functionality results in high cost.
  Eg. Effective density erosion due to interposer and MiM sharing the same wafer  $/bit increase
Resolution Strategy –
  Modular Technologies to prevent from function overload and cost overburden.
  Improve cohesion and reduce dissimilarity of contents in one module
  Increase coupling and decrease entanglement within and between modules
SPIL’s FO-EB-T presents the foundation for modular integration
  Heterogeneous chiplet Integration of dissimilar technologies (ie. logic, memory, passives, mixed-signal, PMIC, passives and etc.)
  Scalable in First Level interconnect and formfactor; high flexibility with lateral and vertical Tx/Rx between chiplets
  Low cost, low loss power delivery network to chiplets
Capability and Capacity insurance –
  FTE’s OSAT ecosystem engagement ensuring multiple suppliers’ 3Cs.
  Disagg. Cache focus team evaluating multiple nodes from TSMC, SF and GF.
  De-coupling cap exploration with PTL team on TSMC, GF DTC and SF ISC.
Substrate
36µm µB FOV + 16nm SoC + ADM + MiM
CPU
GPU
N3E CPU
N3E GPU
Substrate
TSMC 6nm SoC
DTC
DTC
POR
SPIL FO-EB-T for Interposer
TSMC HBI-DTC for MiM
TSMC N6 SRAM for ADM
1
2
3
Intel’s Product roadmap drives external technology pathfinding to win the competition
Notes: Add some speaker notes

## Slide 2
Substrate
36µm µB FOV + 16nm SoC + ADM + MiM
CPU
GPU
CPU
GPU
Substrate
Memory, MS-SOC, passive
DTC
DTC
POR
SPIL FO-EB-T for Interposer
TSMC HBI-DTC for MiM
Embedded Chiplets for act. Foveros
1
2
3