## Slide 1: Agenda
Tightly coupled memory (TCM) options
Interconnect/Integration eco system capabilities and competition mapping
Memory eco system capabilities and Intel engagements
Other Considerations
  Power and thermals
  Data movement power and arch options (common LLC or memory) vs distributed …
  Supply chain and business model

## Slide 2: Tightly Couple Memory Options
Interconnect/integration and vendor options
  2.5D – memory (mono or 3D stacked) on the side – OSATs, TSMC, Samsung, Intel, ??
  3D – memory (mono or 3D stacked) on the bottom or on the top – TSMC, T1 DRAM vendors, Intel, XMC (no memory wafer supply from non Chinese vendors are likely)
Memory type and vendor options:
  SRAM: Intel, TSMC, Global Foundries (GF), Samsung,
  DRAM (standard or custom):
    Samsung, SK Hynix, Micron – Tier 1 with active TCM programs
    Winbond, Powerchip – Tier 2 with active TCM programs
    Nanya, CXMT – Tier 2 with no known TCM programs,
    UMC?
  STT/MRAM – TSMC, Samsung, GF
  ADM/eDRAM – Intel
  eDRAM – IBM/GF
  Alternative technologies - All in research/dev phases
Memory usage model/architecture options
  Global/shared memory
  Local memory/clustered memory/distributed

## Slide 3: Interconnect/Integration Options and Eco System

## Slide 4
Potential Foundry competitive offering
prashant majhi, FTE

## Slide 5
Potential Foundry competitive offering
Samsung X-Cube
TSMC
Samsung, Micron, SKH
Winbond
AP Memory
Winbond
AP Memory, Powerchip
Winbond
TSMC*
TSMC
TSMC
TSMC, Samsung, GF
TSMC
IMEC
IMEC, ARM
Samsung, GF
Samsung, GF
* In pilot production status, unclear customer/node
AP Memory
TSMC
Samsung, Micron, SKH
Samsung, Micron, SKH
IMEC, ARM
prashant majhi, FTE

## Slide 6
TSMC
Samsung
Intel
XMC ??
UMC

## Slide 8: Bonding Landscape: R&D and HVM
Chart: 
| 0.02 | 0.03 | 0.05 | 0.06 | 0.108 | 0.13500000000000001 | 0.2 | 0.3 | 0.6 | 1 | 10 | 10 | 7
#Connections (#) | 100000000 | 70000000 | 52600000 | 34500000 | 17200000 | 4310000 | 2160000 | 1000000 | 100000 | 4000 | 1000 | 4000 | 816
Pitch (um)
Connections/mm2
C or W
C or W
INTEL CONFIDENTIAL
Current 2.5D/3D products
uBump [CoW]
Hybrid Bonding HB [WoW]
Monolithic 3D
Hybrid Bonding [CoW, CoC]
Global Foundry [WoW]
Note: Samsung claims competitive offering as other foundries
TSMC SOIC [CoW]
TSMC SOIC [CoW]
TSMC SOIC+ [CoW, WoW]
DRAM HBM/3DS [CoC, WoW];
eFlash-Logic [WoW]
Prashant Majhi , GSC-EID
CIS [WoW]
CIS [WoW]
YMTC 3DNAND
[WoW]
CPU/Cache
Disagg
CMOS/Interconnect
disagg
NMOS/PMOS
disagg
SRAM or DRAM
Array/Peri Disagg
Std Cell IP Disagg
Hybrid Bonding (HB) in HVM
HB R&D [Path Validation]
HB R&D [Concept/ Early Research]
Update with latest announcements
Add source

## Slide 10: TSMC CoWoS® Platform for High-Performance Computing
TSMC has 10+ years of silicon interposer production and assembly
Increasing size of interposer and multiple HBMs (typically with 8 DRAMs per HBM)
  TSMC expected to introduce CoWoS for up to 8 HBM + 2 logic die in 2021 in 70mm x 78mm package, up to 12 HBMs in 2023
CoWoS process with RDL and LSI (silicon bridge) referred to as CoWoS-L
Source: TSMC.

## Slide 11: Samsung’s Packaging Roadmap for Mobile and HPC
offering many package options developed internally, but also partners with OSATs
Source: Samsung.

## Slide 12
2 die HB at TSMC but 8 high may be challenging for producion

## Slide 13: Samsung’s Cube Package Options for Foundry Customers
I-Cube (silicon interposer) offered with OSAT
X-Cube is developed internally
R-Cube will be developed with OSAT
E-Cube (embedded bridge) will be offered using the panel line for the embedding of bridge chip
  RDL will be fabricated on top
Source: Samsung.

## Slide 14
EMIB
Foveros
CoEMIB
Die to Die connection
on advanced package with EMIB
Die to Die connection
On Active/Passive Silicon Base Die
Die to Die connection
With EMIB and Foveros
ATTD Advanced Packaging Architecture Portfolio
Foveros Omni (ODI)
Foveros Ultra (HBI)
Die to Die connection via bridge in ODI complex.
Can also enable 3D Active Die connection
Die to Die solder less connection
On Silicon Base Die at <10um bump pitch
(Bridge can include TSV)

## Slide 15
ATTD POR
(Product Aligned)
Left Edge
HVM Ready
Directional Technology (No products Aligned))
IPM Alignment with Packaging Architectures

## Slide 16: Memory Eco System Capabilities and Intel Engagements

## Slide 17
Company | Scope | Lead | Sponsor | Notes
Samsung | DRAM/Broad | Wilfred | Raja | 
SK Hynix | Interposer and stacked DRAM | WIlfred | Raja | 
Micron | High bandwidth, low capacity | Kujit |  | 
Winbond | Stacked DRAM | Wilfred |  | 
AP Mem | cDRAM – Cache DRAM, low capacity, high BW, 2.5/3D VHM – Very HBM, 0.6-4.5GB, 2.4/4.5TB/s | n/a | n/a | AP is a design house using Powerchip as DRAM foundry
TSMC |  |  | Boyd | 
GF |  |  | Raja | 
SunRise | 3DS QVM on logic. Scope TBD |  |  | 
Nantero |  |  |  | 
… |  |  |  | 

## Slide 18: Performance Comparison of High Capacity Memories
SRAM and e-DRAM need increased capacity while maintaining latency and BW to enable large model sizes (is it really doable)
 | HBM3 (Samsung) | LL DRAM (Renesas) | ADM e-DRAM | SRAM
Bandwidth (GB/s) | 512 per 8GB | 288 per 4GB | >4000 per 1 GB | >8000 per 128 MB
Min capacity (GB) | 8 | 4 | 0.5 | <0.12
Density (GB/cm2) | 2 | 2 | 0.45 | ~0.29
Latency (ns) | 30 | 10 | 15 | 1.5
Energy (pJ/bit) | 4 | 3 | 0.4 (block-level) | 0.1 (block-level)
SRAM
Need to prepared to use each memory where it fits best instead of trying to come up with a “do it all” memory
(DDR, LPDDR, GDDR, RLDRAM, HBM, LLHBM, SRAM, eDRAM, ….)

## Slide 19
DRAM Technology in Tier-2
NANYA:
Thanks to the direct-collaboration with Micron,
The most advanced process is available in Taiwan.
Main production has moved to 1Ynm.
Re-started Foundry Business with 2Znm since 2020.
Winbond:
Main production is at 2Ynm level.
Process definition is slightly different from Tier-1 company.
Their 2Ynm could be 2X/3Znm Cell in Tier-1.
PWC:
Traditional DRAM foundry.
DRAM process is very old. Maybe 3Znm level.
Metal process is still AL not Cu in DRAM industry.
CXMT:
----------
…

## Slide 21: Intel Server Architecture + DRAM Interposer
Bandwidth: 2.5 – 3 TB/s
  Using SKH 128MB/128GB/s 9.9mm2 macro:
  Need 24 macros for 3 TB/s
  24 * 9.9 = ~240mm2
Capacity: 6 GB (Baseline)
  Scalability option: 2x (12GB) to 4x (24GB) capacity at same bandwidth, additional cost
  Using SKH 128MB/128GB/s 9.9mm2 macro:
  Need 48 macros for 6GB 
  Provide macro with different BW/capacity ratio. Ex. 256MB/128GB/s in 19.8mm2?
#1. Mainstream/General Purpose Perf. Segment (Cache)
Capacity | DRAM Area
6GB (1x) | ~480mm2
12GB (2x) | ~960mm2
24GB (4x) | ~1920mm2
Construction Options
  Compute area: ~1500mm2
  Baseline 6GB DRAM area: ~480mm2
  3x area delta , logic/DRAM will scale differently over time
  Scalability option for 2x – 4x capacity?
Compute
Compute
DRAM Interposer
Option 1: Interposer
Use older/cheaper DRAM node?
Compute
Compute
DRAM
DRAM
Option 2: Intel ODI Packaging
Compute
DRAM
Logic Interposer
Option 3: DRAM cube
With scalable height for capacity
DRAM
Data shared under CNDA 30991112 & CNDA 112784
Can we use the SK logic interposer without DRAM ?

## Slide 23
Parameter |  | unit | 3D DRAM 2Gb w/ ECC |  |  |  |  |  |  | 
 |  |  | Option 1 |  | Option 2 |  | Option 3 (Reference) |  | Option 3B | 
Process |  |  | D25s | D20 | D25s | D20 | D25s | D20 | D25s | D20
Size |  | mm^2 | 37.61 | 32.16 | 28.17 | 23.8 | 24.16 | 19.46 | 35.45 | 30.3
Size w/ bump pitch 25um |  | mm^2 |  |  |  |  |  |  | 33.93 | 28.83
Chip per wafers |  | est. | 1669 | 1952 | 2228 | 2637 | 2598 | 3225 | 1770 | 2071
Good Dies |  |  | 1418 | 1659 | 1894 | 2242 | 2208 | 2741 | 1505 | 1761
Stacked dies (layer) |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Channel (CH) # per Die |  |  | 16 | 16 | 8 | 8 | 8 | 8 | 4 | 4
Bank # per CH |  |  | 1 | 1 | 1 | 1 | 1 | 1 | 8 | 8
Memory per Die |  | MB | 256 | 256 | 256 | 256 | 256 | 256 | 256 | 256
Memory density |  | MB/mm^2 | 6.81 | 7.96 | 9.09 | 10.76 | 10.60 | 13.16 | 7.22 | 8.45
Memory per Channel |  | MB | 16 | 16 | 32 | 32 | 32 | 32 | 64 | 64
Peak Bandwidth* | per CH | Gbps | 256 | 256 | 256 | 256 | 128 | 128 | 256 | 256
 | per Die | Gbps | 4096 | 4096 | 2048 | 2048 | 1024 | 1024 | 1024 | 1024
 | per mm^2 | Gbps | 109 | 127 | 73 | 86 | 42 | 53 | 29 | 34
 | per 100 mm^2 | GB/s | 1361 | 1592 | 909 | 1076 | 530 | 658 | 361 | 422
Effective Bandwidth | per CH | GB/s | 2.8 | 2.8 | 2.8 | 2.8 | 1.4 | 1.4 | 22.8 | 22.8
 | per 1GB | GB/s | 182 | 182 | 91 | 91 | 46 | 46 | 364 | 364
 | per 100 mm^2 | GB/s | 121 | 142 | 81 | 96 | 47 | 58 | TBD | TBD
DQ I/O # | per CH |  | 512 | 512 | 512 | 512 | 64 | 64 | 128 | 128
 | per Die |  | 8192 | 8192 | 4096 | 4096 | 512 | 512 | 512 | 512
ECC IO # | per CH |  | 32 | 32 | 32 | 32 | 4 | 4 | 8 | 8
 | per Die |  | 512 | 512 | 256 | 256 | 32 | 32 | 32 | 32
Data Rate |  | Gbps | 0.5 | 0.5 | 0.5 | 0.5 | 2 | 2 | 2 | 2
Row Cycle time (tRC) |  | ns | 45 | 45 | 45 | 45 | 45 | 45 | 45 | 45
Memory core speed (tCCD) |  | ns | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4
Total Latency |  | ns | 21 | 21 | 21 | 21 | 21 | 21 | 21 | 21
Read Latency |  | nCK | 2 | 2 | 2 | 2 | 8 | 8 | 8 | 8
Access Time (RL + tAC) |  | ns | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9
* Under seamless read operation |  |  |  |  |  |  |  |  | * w/ Metal4 | 
Memory Solution for Intel L3/L4 Cache
Need your confirmation for the number

## Slide 24
(HBI IF)
SONY CMOS Imager
HBM1
HBM2E
8Gb
(Interposer IF)
(IF Energy?)
About C4 Bump
X-Sec Photo from the same paper
Die thickness is ~50um,
Easily to guess how much DRAM Stack uBump/TSV pitch would be?

## Slide 25
2020 Mar.: Hisilicion request the 600-700 uF capacitor and TSMC is working on Gen1 WoW solution, Gen1 DRAM also can replace by capacitor. Gen 1 now have two AI companys are working for that. Gen2 was request by a big design house and even Google intel also have highly interesting for that. Gen2 have better heating structure.
2021 Mar: 2-10 customer engagements

## Slide 26: Micron – Kuljit to provide details

## Slide 27
Architecture Options

## Slide 28
2.5D
Logic
Memory
IO Connection is Long
3D
Logic
Memory
IO Connection
is Short
Larger R & C  Larger power
Worse SI
Smaller R & C  Smaller power
Better SI
HW Trend w/o Cache Architecture Aspect
Suitable for
Global/Shared Cache Architecture.
Suitable for
Local Cache Architecture.

## Slide 29
3D
Logic
Memory
With including 2D IO Connections,
The signal length becomes Longer and complicated.
larger R & C  Larger power
Worse SI
3D HW with Global/Shared Cache Architecture
In order to get the true merit from 3D Interconnects,
Need to shift Cache Architecture from “Global/Shared” to
“Localized Somehow” = “Clustering”.

## Slide 30
For HPC/AI systems with larger memory capacity and higher BW,
scaling Global/Shared Cache Architecture is in jeopardy.
Clustering/Grouping/Partitioning approaches must be necessary
to improve the performance with less power.
Especially, in 3D Stacked Memory + Logic systems.
Sub-NUMA Clustering (SNC) is a good candidate to pursue.

## Slide 31
Capacity: 256KB per Processor Tile x 1216 Tiles = 304 MB
BW: 24 GB/s x 1216 Tiles = 30 TB/s (April 2018, 1GHz)
38 GB/s x 1216 Tiles = 48 TB/s (April 2019, 1.6GHz)
GC2 Processor Chip
24GB/s = 192 IOs x 1GHz
= 86 IOs x 1GHz x DDR

## Slide 32
Cerebras SC19 Info.
IO Block
Engine Block
Cooling System
Product: CS-1
IO Control
Device?
Key attributes:
46,225 mm2 die (=> Die size = 215 mm x 215 mm)
12 x 7 = 84 tiles (chips) on a wafer
1.2 Trillion Transistors by TSMC 16nm
400K Sparse Linear Algebra Compute (SLAC) cores
18GB On-chip SRAM Memory Capacity
9 PB/s Memory Bandwidth
100pb/s BW of 2D Mesh fabric
TSMC 16nm process
Key Readings:
Tile (chip) size is about 550mm2, still big.
9 PB/s (BW) for 18GB (Cap) in total  ~24GB/s, 47KB Local memory per Core.
3D liquid cooling and power supply seem to be MUST for 20KW.
Tile redundancy should be tricky and difficult,
Intel Confidential
Massive 400K core number and Local Memory!

## Slide 33
MIG In A100 - Hardware
33
By Jayasimha, Jay
QoS via isolation
  Compute
    SMs not shared across MIGs
  Mem bandwidth
    Non-overlapped L2 slices & mem channels across MIGs
  Configuration
    Creating/destroying one instance w/o affecting others
  Error
    Separately resettable

## Slide 34: Competition Picture

## Slide 36: Intrepretation of AMD annoucment
CCD is 80mm2 – 8 cores + 32MB L3
Up to 2 CCD for high end desktop
Up to 8 CCD for EPYC (xeon competitor)
Announced:
64 MB, 36mm2 sram chiplet, also in 7nm
Hybrid bonded (face down) to back of SOC (face down)
32MB -> 96MB L3 (192 MB client, 768MB L3 EPYC)
Dummy silicon over core, sram chiplet only covers sram

## Slide 38: Hardware for AI
Samsung and TSMC indicate Si interposer used for AI
NVIDIA’s latest A100 uses GPU + 6 HBMs
  Si interposer (∼1,600 mm2) using TSMC’s CoWoS process
  Large GPU die (826 mm2)
  Package body size 55 mm x 55 mm
Source: NVIDIA.
Typical hardware for edge application would be Intel server board
  2, 8-core CPUs + 3 NVIDIA GPU boards
  GPU + HBM
Lots of AI libraries that go with NVIDIA GPU
  Hardware must be compatible with libraries

## Slide 39: Cerebras Wafer Scale Engine for AI Compute
1.2 trillion transistors on single die (46,225mm2)
Packaged between heat spreader and power supply system
RDL used for interconnectivity within the wafer scale die and for power distribution

## Slide 41
CoWoS • 2021 Mar.: Due to the CoWoS_L is getting more and more popular and will increase more flexibility for combination of different device and also can reduce the cost. So TSMC will drop the 4X reticle size CoWoS development. • 2021 Mar.: TSMC think the CoWoS_L and CoWoS_R and CoWoS with capacitor will let the CoWoS demand growth from 8k/M to 12-13K/m by 2023. • 2021 Mar.: The Broadcom is the most aggressive for CoWoS_L and plan to will use the TPU for Google to adopt the CoWoS_L,. TSMC plan to finish to finish qualification by Q223 and Broadcom request to pull in to Q123 and even Q422. • 2021 Mar. : The AMD will have several combination products for CoWoS CPU+HBM2E/CPU+GPU+HBM2E/ CPU+ accelerator and have good forecast in the coming. Now the AMD and Xilinix CoWoS have best forecast growth rate of overall customers. • 2021 Mar.: The Microsoft Server CPU for Azure@5nm will adopt CoWoS and plan to ramp up by end of 2021. • 2021 Mar.: The Nvidia new AI chip@5nm will adopt the SoIC on CoWoS

## Slide 42
– InFO • 2021 Mar.: Apple cut 8-9M A12 and 2M around A13 demand but pill in the Apple InFO_L pilot run and mass production schedule…. • The Apple have chance to launch the iMac/iMac Pro adopt Apple own CPU@InFO _L in spring event date. • 2021 Mar.: AMD will ramp up the GPU@5nm Navu31/32/33 adopt the InFO_oS from Q421.Now total demand still forecast max is 30K/m but that will depe

## Slide 43
y : – Backend 3D IC (WoW) : • 2021 Mar.: The TSMC BD (Business development) is cooking for low end X86 CPU with wide IO for high performance computing for China market due to China-USA trade conflict. But it’s in the early stage. – Backend InFO PTI • 2021 Mar.: The PTI have high possibility will give up the panel fan out due to PTI CTO was resign and now no specific owner to be in charge of the Panel fan out. But concentrate more resource for wafer base InFO and WoW. The PTI is working on the Sony CIS+ISP solution

## Slide 46: Alternative Tech

## Slide 47: Emerging Technology in Memory Pyramid
TFT channel planar / nonplanar XTOR
2T [independent read write] Option
Si channel planar / nonplanar XTOR
MRAM [STT/SOT]
Nanostructure change
High-k Capacitor
Ferro-capacitor
Access Device
Memory Element
Resistance Change ReRAM[1D, 2D], PCM [3D]
Ferroelectrics
Magnetic
[MRAM, STT(SOT)MRAM]
Volatile filament
Ovonic Threshold
Thermionic
[diode, MIEC, ..]
Metal-Insulator Transition
Access Device
Memory Element

## Slide 48: Executive Summary
Embedded memory – 1T-STTM with low write cycle time and high endurances were demonstrated.
  TSMC-16nm, Samsung-28nm, GF-22nm and IBM-14nm improves write speed (~10ns) and reliability (106 to 1012 cycles).
  IBM-Samsung JDP demo write speed limit at 2nsec; Read disturb is problematic.
  1T-STTM density is low; Samsung’s 28nm yields 12Mb/mm2 (~Intel’s eDRAM circa ’12), shipping buffer memory in LCD display.
  2T-SOT is still in deep research.
In-Package Memory – Intel’s ADM is the leading low-latency alternative, but density is not competitive to bulk Si 1T1C solution
  Samsung, Hynix and Micron have indications of monolithic 3DIC DRAM interest but no public disclosure.
  low latency 1T-STTM technology requires large x’tor footprint or more advanced technology for high current bipolar operation.
  1T-1FeCap, 1T-nFeCap, 1FeFET and 2T-0C gain-cell (IxZO class) in research stage. Long lead time is anticipated.
3D XPoint – Intel is leading competitive landscape by 24~36 months (SLC, MLC and BiSM)
  Hynix: Although several papers published in 2020~21, no new information disclosed since IEDM18 paper (a S15-like product).
  Samsung remains silent; Macronix-IBM primarily worked on cell level research with limited array activities.
  Micron ceased SXP & SSM TD on March 16, 2021, 2y8m after ending IM-JDP. Gen-2 production at Lehi, UT ends by the end of ’21.
Alternative technologies for PM / SCM are either in primitive research, missed product milestone or dropped out.
  Fujitsu-Nantero’s 40nm selector-less NRAM: missed sampling milestone of low-latency product.
  Sony’s 20nm OTS-select CBRAM: missed sampling milestone likely due to Cu-integration, sigma, drift & disturb.
  Avalanche 1S-STTM demonstrated very high NL single cell data; still no array information; disturb, sigma are likely showstoppers.
  Crossbar/SMIC FAAST-VO+ cell has been radio-silent since their new CEO visited Intel in 2019. Co-funder’s resume is on the street.
  Bipolar RRAM, Unipolar CeRAM and FeFET (NAND string) are either dropped out or in early stage of research.
Flash Memory: SunRise 3D QVM (NOR flash), Macronix 3D AND Flash,

## Slide 49: Memory Architectures
Arch | Description | Companies
MRAM | Uses electron spin to store information; high-density, non-volatile, power efficient Challenges: Requires significant process integration to manufacture Status: Furthest along in development; Solutions already in the market (Everspin, Samsung, TSMC, GF) | Avalanche Escencia Everspin (IPOed) Spin Transfer Tech
RRAM | Changes the resistance across a dielectric solid-state material, non-volatile Challenges: Variability issues are proving to be difficult to overcome Status: Advertised as the ultimate scalable memory; Many RRAM companies trying to penetrate into the AI/ML market and worth with in-memory compute model | Crossbar Intrinsic NuMe ReBIT ReRAM Spin Memory
NRAM | Based on carbon nanotube technology for strong write-endurance, non-volatile Challenges: Have yet to deliver on promises Status: Have been around for 20+ years, Fujitsu announced to partner with Nantero to bring to market in 2019 | Nantero
FeRAM | Uses ferroelectric layer to achieve non-volatility, low power, fast write Challenges: Historically used materials that were difficult to integrate into FAB environment, lower storage densities than Flash Status: Advances made to use Hafnium Oxide to make more accessible for FAB environment | FerroElectric Memory
Other | SRAM NAND | Zeno (SRAM) Netlist Yangtze Memory Tech

## Slide 52
Mem On Bottom
Mem On Top
Adjacent
SRAM
ADM
DRAM
SRAM
SRAM
ADM
ADM
DRAM
DRAM
DRAM stacked on SRAM
LP5
HBM
HBM
Samsung
SK
Micron
Winbond
AP Mem
Samsung
Samsung
New DRAM
AP Mem
Winbond
New DRAM
7 permutations of DRAM adjacent to logic
New DRAM
Custom GDDR
Intel
TSMC
GF

## Slide 53
Focus on taking advantage ef each memory type with the best available interconnect tech.
Focus on TTM execution and quality