## Slide 1: TCM/IPM Options
Logic
Interposer
SRAM
(e)DRAM
STT/SOT-MRAM
ubump connections
Hybrid bond connections
SRAM Based High Bandwidth Solutions
(e)DRAM Based High Bandwidth Solutions
STT/SOT-MRAM Based
monolithic
2.5D with interposer
3D with ubump
3D with HB (CoW)
3D with HB (WoW)
monolithic
2.5D with interposer
3D with ubump
3D with HB (CoW)
3D with HB (WoW)
prashant majhi, FTE

## Slide 2: TCM/IPM Landscape of High Bandwidth Options for System Performance
prashant majhi, FTE
Technology (Foundry Options) | Density | Scalability | Bandwidth | Masks | Energy | Process Tech Readiness | Eco-System Readiness | 3D integration limitations | Ex-Industry Engagements | Expected Product Drivers
Monolithic SRAM |  |  |  |  |  |  |  |  | TSMC, Samsung | 
SRAM(s) chiplet ubump on Interposer |  |  |  |  |  |  |  |  | Samsung (X-Cube) | 
SRAM(s) chiplet ubump on Logic |  |  |  |  |  |  |  |  | Samsung, TSMC | 
SRAM chiplet HB (CoW) |  |  |  |  |  |  |  |  | Samsung, TSMC SOIC | 
SRAM chiplet HB (WoW) |  |  |  |  |  |  |  |  | Samsung, TSMC SOIC | 
Monolithic eDRAM / low latency DRAM |  |  |  |  |  |  |  |  | IBM, TSMC (sunset), Samsung DBM, Micron | 
DRAM(s) chiplet ubump on Interposer [HBM] |  |  |  |  |  |  |  |  | Samsung, Hynix, Micron, | 
DRAM(s) chiplet ubump on Logic [3D DRAM/Logic] |  |  |  |  |  |  |  |  | AMD..w/ ?? | 
DRAM chiplet HB (CoW) |  |  |  |  |  |  |  |  | Samsung, Hynix w/ XPERI, TSMC w/ ?? | 
DRAM chiplet HB (WoW) |  |  |  |  |  |  |  |  | Powerchip w/ logic vendor; TSMC? | 
STT/SOT-MRAM |  |  |  |  |  |  |  |  | SAMSUNG, TSMC | 
Notes: Up to 10 Gb
L1 KB
L2 100 KB
L3 10 MB
Per core? E.g. 8 core system
ADM  div between llc type perf-centric ipm; vs high cap
Energy/bit dependence on arch (MUX/data width/page size)

## Slide 3: TCM/IPM Landscape of High Bandwidth Options for System Performance
prashant majhi, FTE
Technology (Foundry Options) |  | Density (Gb/mm2) | Capacity (GB/die) | Bandwidth density (GB/s/GB) |  | Latency (ns) |  | Masks (#) |  | Array Energy (pJ/bit) |  |  | Process Tech Readiness | Limitations | Ex-Industry Engagements
 |  |  |  | R | W | R | W | Crit | Tot | Read | Write | Idle |  |  | 
eDRAM | ADM |  |  |  |  |  |  | 23 |  | 0.5 | 0.1 | 0.64 |  |  | IBM, TSMC (sunset), Samsung DBM, Micron
 | Si |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SRAM | 6T |  |  |  |  |  |  |  |  | 0.17 | 0.1 | 0.64 |  |  | high reliability TSMC, Samsung
 | 3T |  |  |  |  |  |  |  |  |  |  |  |  |  | 
DRAM | HBM |  |  |  |  |  |  | 17 |  |  |  |  |  |  | Samsung, Hynix, Micron,
 | DBM |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | LL-DRAM |  |  |  |  |  |  |  |  |  |  |  |  |  | 
STT/SOT-MRAM | Classic STTM |  |  |  |  |  |  |  |  |  |  |  |  |  | SAMSUNG, TSMC
 | SOT |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Notes: Command/Data Energy
Up to 10 Gb
L1 KB
L2 100 KB
L3 10 MB
Per core? E.g. 8 core system
ADM  div between llc type perf-centric ipm; vs high cap
Energy/bit dependence on arch (MUX/data width/page size)

## Slide 4: TCM/IPM Landscape of High Bandwidth Options for System Performance
prashant majhi, FTE
Technology (Foundry Options) |  | Density | Scalability | Bandwidth | Masks | Energy |  |  | Process Tech Readiness | Eco-System Readiness | 3D integration limitations | Ex-Industry Engagements
 |  |  |  |  |  | Macro | PHY | I/O |  |  |  | 
SRAM | Mono |  |  |  |  | 0.2 | 0.3 | 0.2 |  |  |  | TSMC, Samsung
 | WoW |  |  |  |  |  |  |  |  |  |  | 
 | DoW |  |  |  |  |  |  |  |  |  |  | 
 | Bumps |  |  |  |  |  |  |  |  |  |  | 
eDRAM | Mono |  |  |  | 23 | 0.5 | 0.67 | 0.2 |  |  |  | IBM, TSMC (sunset), Samsung DBM, Micron
 | WoW |  |  |  |  |  |  |  |  |  |  | 
 | DoW |  |  |  |  |  |  |  |  |  |  | 
 | Bumps |  |  |  |  |  |  |  |  |  |  | 
DRAM | Mono |  |  |  |  |  |  |  |  |  |  | Samsung, Hynix, Micron,
 | WoW |  |  |  |  |  |  |  |  |  |  | 
 | DoW |  |  |  |  |  |  |  |  |  |  | 
 | Bumps |  |  |  |  |  |  |  |  |  |  | 
STT/SOT-MRAM | Mono |  |  |  |  |  |  |  |  |  |  | SAMSUNG, TSMC
 | WoW |  |  |  |  |  |  |  |  |  |  | 
 | DoW |  |  |  |  |  |  |  |  |  |  | 
 | Bumps |  |  |  |  |  |  |  |  |  |  | 
Notes: Up to 10 Gb
L1 KB
L2 100 KB
L3 10 MB
Per core? E.g. 8 core system
ADM  div between llc type perf-centric ipm; vs high cap
Energy/bit dependence on arch (MUX/data width/page size)

## Slide 5: TCM/IPM Landscape of High Bandwidth Options for System Performance
prashant majhi, FTE
Technology (Foundry Options) | Density | Scalability | Bandwidth | Masks | Energy | Process Tech Readiness | Eco-System Readiness | 3D integration limitations | Ex-Industry Engagements | Expected Product Drivers
Monolithic SRAM |  |  |  |  |  |  |  |  | TSMC, Samsung | 
SRAM(s) chiplet ubump on Interposer |  |  |  |  |  |  |  |  | Samsung (X-Cube) | 
SRAM(s) chiplet ubump on Logic |  |  |  |  |  |  |  |  | Samsung, TSMC | 
SRAM chiplet HB (CoW) |  |  |  |  |  |  |  |  | Samsung, TSMC SOIC | 
SRAM chiplet HB (WoW) |  |  |  |  |  |  |  |  | Samsung, TSMC SOIC | 
Monolithic eDRAM / low latency DRAM |  |  |  |  |  |  |  |  | IBM, TSMC (sunset), Samsung DBM, Micron | 
DRAM(s) chiplet ubump on Interposer [HBM] |  |  |  |  |  |  |  |  | Samsung, Hynix, Micron, | 
DRAM(s) chiplet ubump on Logic [3D DRAM/Logic] |  |  |  |  |  |  |  |  | AMD..w/ ?? | 
DRAM chiplet HB (CoW) |  |  |  |  |  |  |  |  | Samsung, Hynix w/ XPERI, TSMC w/ ?? | 
DRAM chiplet HB (WoW) |  |  |  |  |  |  |  |  | Powerchip w/ logic vendor; TSMC? | 
STT/SOT-MRAM |  |  |  |  |  |  |  |  | SAMSUNG, TSMC | 
Notes: Up to 10 Gb
L1 KB
L2 100 KB
L3 10 MB
Per core? E.g. 8 core system
ADM  div between llc type perf-centric ipm; vs high cap
Energy/bit dependence on arch (MUX/data width/page size)

## Slide 6
Array-based
System-integration based

## Slide 7: TSMC on High Bandwidth Memory
TSMC @ ERI , 2020
prashant majhi, FTE

## Slide 8: TSMC Enabling/Developing(?) High Bandwidth In-package Memory
prashant majhi, FTE

## Slide 10: Adamantine:

## Slide 11
Samsung @ SAFE
prashant majhi, FTE

## Slide 12: 3D Stacked SRAM: Rambo (Intel) vs Foundries
Samsung 3D SRAM (SAINT-S, X Cube)
prashant majhi, GSC-EID
Note: Not indicative of memory density as it is test chip w/ other functions included

## Slide 13: Renesas HBLL

## Slide 14: HBM with WOW and FG-DRAM

## Slide 15
prashant majhi, GSC-EID