## Slide 1: System/Technology Co-design Methodology for Energy-efficient Multi-tier 3D IC DNN Accelerators
September 15 , 2022
Presenter: Srivatsa RS
Gauthaman M, Dileep Kurian, Adel A Elsherbini, Tanay Karnik (Manager)
Heterogeneous Platforms Lab (HPL)

## Slide 2: Today`s presentation
Re-architecting ML accelerator for higher throughput per mm2
Architectural simulations using ScaleSim/STONNE for motivation
Modified DELPHI (SPH`s ICE) architecture simulator to study the benefits of re-architecting DELPHI
3D Accelerators
Architecture and design space exploration
Exploration of benefits of hybrid bond interconnects (HBI) for 3D accelerator

## Slide 3: Overview
Current ML accelerator trends
Re-architecting ML accelerator
2D accelerator case study
3D ML accelerator architecture and design space exploration
Future work

## Slide 4: How does DRAM BW affect the throughput?
Chart: Mapping ResNet50 on Eyeriss, SRAM BW: 64B, SRAM Capacity: 128 KB
| 16 | 32 | 48 | 64
Layer 1 | 1 | 0.875 | 0.875
Layer 3 | 1 | 0.735 | 0.735
Layer 5 | 1 | 0.5625 | 0.5625
Layer 14 | 1 | 0.57143 | 0.57143
Layer 15 | 1 | 0.71053 | 0.49123 | 0.46053
Eyeriss – A fixed interconnect
accelerator

## Slide 5: Memory BW vs Throughput Analysis
MAERI – a flexible
interconnect architecture
#Convolution layer in SSDMobileNetv1 (left) and ResNet34 (right)
Effect of SRAM BW on execution time

## Slide 6: Case study: Commercial 2D Inference Engines
TPU v3: 64k MAC units
Offers ~100TOPS theoretical throughput
Practical PE utilization on ResNet50 ~30%
SPH: 48k MAC units
Offers ~48-92 TOPS theoretical throughput
~48% PE utilization on ResNet50
G-GPU
T-TPU

## Slide 7: Case study: SpringHill (SPH) high level architecture
4K MAC units per compute grid (DELPHI/ICE)
Each ICE unit has a 4MB DeepSRAM
A 3MB LLC is shared by two ICE units
https://en.wikichip.org/wiki/intel/microarchitectures/spring_hill
https://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=8875671
Notes: ØPerforma as a post processing step.
Ø Flow
ØWhile computing L1 fetch L2 data also.
ØAfter the compute while streaming out L1 data DELPHI can perform element wise addition.
ØReLU befor eand after element wise addition
Ø
ØThroughput 64 elements per cycle.
Ø
ØOverhead : Fetch of L2 data from memory.
ØIf the layer is input BW limited – Delay in compute

## Slide 8: Case study: DELPHI (ICE within SpringHill)
PE-0
PE-1
PE-N
BRAM
Buffer 0
OSRAM
Buffer
OSRAM
Buffer
OSRAM
Buffer
PE-0
PE-1
PE-7
BRAM
Buffer 0
OSRAM
Buffer
OSRAM
Buffer
OSRAM
Buffer
PE-0
PE-1
PE-15
BSRAM
Buffer 0
OSRAM
Buffer
OSRAM
Buffer
OSRAM
Buffer
ISRAM
ISRAM
Buffer
ISRAM
Buffer
BSRAM Write
Ctrl
ISRAM
Write
Ctrl
Load unit
Store unit
OSRAM
Read/Write
Ctrl
GEMM Ctrl
CNN Ctrl
DNN/FC Ctrl
Nonlinear Ctrl
AXI/CVE interface
………
…………
IP Registers
Tile-0
Tile-31
GEMM Ctrl
IP Registers
CNN Ctrl
GEMM Ctrl
IP Registers
Broadcast across tiles, 32KB
1.Broadcast across PEs
2.CNN-Kernels, 4 KB per tile (total 128 KB)
1.Unique per tile per PE
2.Holds output data
3. 8KB per tile (total 256KB)
8 MACs
MEM
DELPHI
Notes: Ø Flow
ØWhile computing L1 fetch L2 data also.
ØAfter the compute while streaming out L1 data DELPHI can perform element wise addition.
ØReLU befor eand after element wise addition
Ø
ØThroughput 64 elements per cycle.
Ø
ØOverhead : Fetch of L2 data from memory.
ØIf the layer is input BW limited – Delay in compute

## Slide 9: Case study: DELPHI (JBL Version)
PE-0
PE-1
PE-N
BRAM
Buffer 0
OSRAM
Buffer
OSRAM
Buffer
OSRAM
Buffer
PE-0
PE-1
PE-7
BRAM
Buffer 0
OSRAM
Buffer
OSRAM
Buffer
OSRAM
Buffer
PE-0
PE-1
PE-15
BSRAM
Buffer 0
OSRAM
Buffer
OSRAM
Buffer
OSRAM
Buffer
ISRAM
ISRAM
Buffer
ISRAM
Buffer
BSRAM Write
Ctrl
ISRAM
Write
Ctrl
Load unit
Store unit
OSRAM
Read/Write
Ctrl
GEMM Ctrl
CNN Ctrl
DNN/FC Ctrl
Nonlinear Ctrl
AXI/CVE interface
………
…………
IP Registers
Tile-0
Tile-31
GEMM Ctrl
IP Registers
CNN Ctrl
GEMM Ctrl
IP Registers
Broadcast across tiles, 32KB
1.Broadcast across PEs
2.CNN-Kernels, 4 KB per tile (total 128KB)
1.Unique per tile per PE
2.Holds output data
3. 8KB per tile (total 256KB)
8 MACs
SMEM
(16 MB)
DELPHI
AXI
(512b)
Notes: Ø Flow
ØWhile computing L1 fetch L2 data also.
ØAfter the compute while streaming out L1 data DELPHI can perform element wise addition.
ØReLU befor eand after element wise addition
Ø
ØThroughput 64 elements per cycle.
Ø
ØOverhead : Fetch of L2 data from memory.
ØIf the layer is input BW limited – Delay in compute

## Slide 10: Why tiling isn’t a great solution?
control logic
ISRAM:
40 RF instances
Area: 260um x320um
2048 MACs
16 PEs
16 Tiles
2048 MACs
16 PEs
16 Tiles
BSRAM: 32KB
BSRAM: 32KB
BSRAM: 32KB
BSRAM: 32KB
OSRAM: 64KB
OSRAM: 64KB
OSRAM: 64KB
OSRAM: 64KB
1.11 mm
1.35 mm
4mm
4mm
16 MB

## Slide 11: Scaling trends in DELPHI
Simulations performed with modified tightly coupled memory (ISRAM, BSRAM, OSRAM) bandwidth
Chart: 16 PEs DELPHI performance
| 32 | 64 | 128
Exec. Cycles | 1192152 | 857421 | 810077
 | 0 | -0.28078 | -0.32049
Notes: Assuming we have enough routing resources

## Slide 12
Chart: DELPHI performance
| 32 | 64 | 128
16 PEs | 1192152 | 857421 | 810077
32 PEs | 916795 | 774349 | 771702
64 PEs | 852791 | 752920 | 758244
128 PEs | 839228 | 747380 | 752756
Saturates after 40% improvement
Scaling trends in DELPHI

## Slide 13: Scaling 2D DELPHI and Mapping ResNet50
Tiles | 64
#MACs | 8K
Design Frequency | 500 MHz
Average PE utilization | 48%
Theoretical throughput | 8 TOPS
Effective throughput | 3.93 TOPS
Throughput per area | 1.75 TOPS/mm2
ResNet50 Model
Notes: BW limited due to routing resources

## Slide 14: Avoiding Deep SRAM/SMEM
ISRAM Buffer
Write From DRAM
Read to PEs
OSRAM Buffer
Write From PEs
Read to Adder and quantizer
Adder + quant
Write to DRAM
Output FIFO

## Slide 15: Memory/Near-memory accumulator Architecture
From PEs
Output FIFO
To NMAQ
16 x 32b
Write 512b to OFIFO
Write 512b to OFIFO
Write 512b to OFIFO
Write 512b to OFIFO
Read 512b from OFIFO
Read 512b from OFIFO
Read 512b from OFIFO
Read 512b from OFIFO
From PE
adder/quant
Write 512b to OFIFO
Write to ISRAM
16 x 32b
32-bit adder
32-bit adder
32-bit adder
32
32-bit Quant.
32 –bit Quant.
Quant.
1
2
16
Controller EN
9-bit Quant.
9-bit Quant.
9-bit Quant.
16 x 9b
ISRAM Buffer
8 KB
8 KB
To I/P NW Config.
8 x 9b
2:1
From NMAQ
Write 144b to ISRAM every #IFMs cycle
Write 144b to ISRAM every #IFMs cycle

## Slide 16: Tightly coupled PEs and Memories
PE with 8 MAC units
ISRAM 1
(16 KB)
ISRAM 2
(16 KB)
ISRAM 3
(16 KB)
ISRAM 4
(16 KB)
PE1-1
PE1-2
PE1-15
PE1-16
PE1-17
PE1-18
PE1-31
PE1
32
PE1-33
PE1-34
PE1-47
PE1-48
PE1-49
PE1-50
PE1-63
PE1-64
OFIFO 1
(128 B)
OFIFO 2
(128 B)
OFIFO 3
(128 B)
OFIFO 4
(128 B)
NMAQ 1
NMAQ 2
NMAQ 3
NMAQ 4
To ISRAM 1-1
To ISRAM 2-1
To ISRAM 3-1
To ISRAM 4-1
72b
72b
72b
72b
72b
72b
72b
72b
512b
512b
512b
512b
512b
512b
512b
512b
144b
144b
144b
144b
x3
x3
x3
x3
Inputs from other PE blocks
144b
144b
144b
144b
144b
144b
144b
144b
A 64 PE tile design
Divided into 4 groups (4 sets of PEs and ISRAM)
OFIFO of depth 2 – to enable store and accumulate
ISRAM – 64 KB to store outputs from a single PE block
Additional 128 KB required to store outputs from different tiles – to enable next layer computation.

## Slide 17: Benefits of Re-architecting
Feature Maps
3 MB
Weights
1.25 MB
PE1
PE2
PE16
PE3
PE1
PE2
PE16
PE3
PE1
PE2
PE16
PE3
PE1
PE2
PE16
PE3
x64
Near memory adder and quantizer
Tiles | 64
#MACs | 8K
Design Frequency | 500 MHz
Average PE utilization | 89%
Theoretical throughput | 8 TOPS
Effective throughput | 7.29 TOPS
Throughput per area | 3.24 TOPS/mm2

## Slide 18: 3D accelerator architecture exploration
PE - 8
PE - 7
PE - 5
PE - 6
OFIFO
ISRAM
Weight SRAM
Near-memory accumulator
& Quantizer (NMAQ)
8K MAC 3D accelerator architecture
PE - 1
PE - 4
PE - 3
IP NW Config
PE - 2
PE - 9
PE - 10
PE - 12
PE - 11
PE - 15
PE - 16
PE - 13
PE - 14
Hybrid bonds
Weight SRAM
Input SRAM
Output FIFO
Controller
Compute tier
Memory tier
OFIFO | Read to (stride 1) | Stride 2 | To DRAM (stride2 – stride 1)
OFIFO 1 | ISRAM 1, 15, 16 | ISRAM 1, 8, 9, 16 | 8, 9
OFIFO 2 | ISRAM 1, 2, 16 | ISRAM 1, 9 | 9
OFIFO 3 | ISRAM 1, 2, 3 | ISRAM 1, 2, 9, 10 | 9, 10
OFIFO 4 | ISRAM 2, 3, 4 | ISRAM 2, 10 | 10
OFIFO 5 | ISRAM 3, 4, 5 | ISRAM 2, 3, 10, 11 | 2,10, 11
OFIFO 6 | ISRAM 4, 5, 6 | ISRAM 3, 11 | 3, 11
OFIFO 7 | ISRAM 5, 6, 7 | ISRAM 3, 4, 11, 12 | 3, 4, 11, 12
OFIFO 8 | ISRAM 6, 7, 8 | ISRAM 4, 12 | 4, 12
OFIFO 9 | ISRAM 7, 8, 9 | ISRAM 4, 5, 12, 13 | 4, 5, 12, 13
OFIFO 10 | ISRAM 8, 9, 10 | ISRAM 5, 13 | 5, 13
OFIFO 11 | ISRAM 9, 10, 11 | ISRAM 5, 6, 13, 14 | 5, 6 , 13, 14
OFIFO 12 | ISRAM 10, 11, 12 | ISRAM 6, 14 | 6, 14
OFIFO 13 | ISRAM 11, 12, 13 | ISRAM 6, 7, 14, 15 | 6, 7, 14, 15
OFIFO 14 | ISRAM 12, 13, 14 | ISRAM 7, 15 | 7, 15
OFIFO 15 | ISRAM 13, 14, 15 | ISRAM 7, 8, 15, 16 | 7, 8, 16
OFIFO 16 | ISRAM 14, 15, 16 | ISRAM 8, 16 | 8
Only 4 layers in ResNet50 have a stride of 2

## Slide 19: Area and 3D connection analysis based on 7nm technology – Per Single PE block
Metrics (per bank) | Values
Bits | 72
Words | 912
Size | 8.015 KB
Unit Memory Area | 4589 um2
Total memories required | 12x2banks
Total Area for 24 banks | 0.11 mm2
ISRAMs within a PE block
PE - 1
PE - 4
PE - 3
crossbar
PE - 2
Path | #3D Connections per PE group
ISRAM to PE | 72x12 = 864
PE to OSRAM | 32x64 = 2048
Total | 2912
Silicon Area | 112,500 um2
Hybrid bond pitch 9 um | 99x12 = 1,188
Hybrid bond pitch 5 um | 179x24 = 4,296
Power/GND connection NOT included
Hybrid logic+memory integration technology required

## Slide 20: Memory on Logic Integration
Path | #3D Connections per PE group
ISRAM to PE | 72x12 = 864
PE to OSRAM | 32x64 = 2048
OSRAM to NMAQ | 32x64 = 2048
NMAQ to ISRAM | 9x64 = 576
Total | 5,536
Silicon Area | 112,500 um2
Hybrid bond pitch 9 um | 99x12 = 1,188
Hybrid bond pitch 5 um | 179x24 = 4,296
Hybrid bond pitch 2 um | 449x61 = 27,389
Hybrid bond pitch 1 um | 899x124 = 111,476
PE - 1
PE - 4
PE - 3
crossbar
PE - 2
NMAQ moved to bottom tier

## Slide 21: Learnings from the architectural exploration
3D architecture can offer 85% practical throughput improvement (based on ResNet50)
INT8: >50k connections between PEs and memories
Such heavy 3D connections are impossible to achieve using micro-bumps
Higher computation precision and higher compute logic requires more and more 3D interconnects to achieve maximum PE utilization
Finer 3D hybrid-bond pitches are required for better accelerator hardware scaling
Further scaling can be enabled through chipletization

## Slide 22: Summary
Design | 2D DELPHI | Proposed 3D Architecture | ∆%
Tiles | 64 | 64 | 
#MACs | 8K | 8K | 
Design Frequency | 500 MHz | 500 MHz | 
Average PE utilization | 48% | 89% | 41%
Theoretical throughput | 8 TOPS | 8 TOPS | 
Effective throughput | 3.93 TOPS | 7.29 TOPS | 85.4%
Throughput per area | 1.75 TOPS/mm2 | 3.24 TOPS/mm2 | 85.4%

## Slide 23: Thanks for listening!